## Slide 1
José Manuel Blanes Martínez
Universidad Miguel Hernández de Elche
Deep Space Microsatellite Power System Design and Development
ASFAE/2022/021
Space Power and Electronics System Group
SPES
Reunión Final del Plan Complementario de Astrofísica y Altas Energías
Noviembre 2025, Santander

## Slide 2
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Presentation Outline
Introduction
Project Objectives
SPES PCDU Architecture
Facilities and Equipment Acquired
PCDU Validation and Test Results
Summary and Conclusions

## Slide 3
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Introduction – Rise of Cubesats
Traditionally used in the past by universities for educational purposes.
Exponential growth in recent years driven by the “New Space” paradigm.
Cost-effective platforms (Reduced Complexity - COTS components).
Faster development cycles.
Reduced complexity but with increased mission risks
1U
12U

## Slide 4
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Introduction – Cubesats in Deep Space Missions
Deep Space

## Slide 5
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Introduction – Cubesats in Artemis I (Deep Space)
6U Cubesats
BioSentinel
EQUULEUS
Argomoon
LunaHMap
Lunar IceCube
CuSP
LunIR
Omotenashi
Team Miles
NEA Scout
High Risk-High Reward
Lessons Learned:
More reliable Cubesats are needed for Deep-Space

## Slide 6
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Introduction – Cubesats Failures
Electrical Power Subsystem (EPS) + Unknown Failures > 50 %
More recent reliability studies and state-of-the-art reviews agree that improving the robustness of the EPS is essential for Deep-Space Cubesats.
Subsystem contribution to Cubesats Failures

## Slide 7
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Project Objectives
Deep Space Exploration Microsatellite PCDU system development.
  Very low temperature .
  Harsh Radiation Environment.
  Use of commercial components (COTS)
    Identify electronic components and battery cells.
    ”Careful COTS approach” - System level design
  High reliability
    Protections and Redundancy for critical functions.
    Optional Rad-Hard version of critical components in the same PCB.
Validation System development.

## Slide 8
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
PCDU Architecture – Solar Array Regulator (SAR)
COTS: Extended temperature range automotive qualified components
Analog MPPT
Integrated PWM controller (rad hard version option)
Double control loop
µController (rad tol version available)
Redundancy and Protections
Fault-Free Operation TID > 70 kRads
Fault-Free Operation TVAC -40ºC-60ºC
C. Torres, J. M. Blanes, A. Garrigós, D. Marroquí and J. A. Carrasco,
"High-Reliability Solar Array Regulator for Deep Space Exploration Micro-Satellites" in IEEE Access, vol. 11, pp. 94138-94147, 2023

## Slide 9
PCDU Architecture – Battery Management System (BMS)
COTS: Extended temperature range automotive qualified components
Single Point Failure Free
Battery Cell Thermal Management
Cell Balancing - Switched Capacitors Equalizers (SCE)
OV + OC protection
Remove Before Flight + Deployment Switches
µController (rad tol version available)
Fault-Free Operation TID > 70 kRads
Fault-Free Operation TVAC -40ºC-60ºC
Casado, P.; Blanes, J.M.; Garrigós, A.; Marroquí, D.; Torres, C. “COTS Battery Charge Equalizer for Small Satellite Applications”. Appl. Sci. 2025, 15, 8228. https://doi.org/10.3390/app15158228
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.

## Slide 10
PCDU Architecture – Battery Pack
COTS: Extended temperature range automotive qualified components
Li-ion Commercial 18650 cells
4 Independent Heaters
4 Cell temperature sensors
2S2P (other conf: 2 x 1S1P+1S1P, 4S1P)
Over temperature protection
Fault-Free Operation TID > 70 kRads
Fault-Free Operation TVAC -40ºC-60ºC
P. Casado, J.M. Blanes, A. Garrigós, D. Marroquí, C. Torres,
“Evaluation of commercial Li-Ion 18650 battery cells for deep space applications”,
Journal of Power Sources, Volume 638, 2025
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.

## Slide 11
PCDU Architecture - Power Distribution Unit (PDU)
COTS: Extended temperature range automotive qualified components
PCDU Payload/Avionics backplane connection
Outputs: Vbat, 5V, 3.3V outputs
OC and UV protections (LCL)
OBC dedicated supply lines
Integrated PWM controller (rad hard option)
µController (radtol version available)
Fault-Free Operation TID > 70 kRads
Fault-Free Operation TVAC -40ºC-60ºC
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.

## Slide 12
PCDU Architecture - DC Transformer (DCX)
COTS: Extended temperature range automotive qualified components
EMI filter
Planar transformer - Isolated outputs
Si MOSFET or GaN FETs
Zero voltage and zero current switching
µController (radtol version available)
OC and UV protections (LCL)
Fault-Free Operation TID > 70 kRads
Fault-Free Operation TVAC -40ºC-60ºC
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.

## Slide 13
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
PCDU Architecture – Modular Design
1.SAR
2.SAR
3.BMS
4.DCX
7.DCX
5.PDU
6.PDU
0.BAT

## Slide 14
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
PCDU Architecture – Modular Design
1.SAR
4.DCX
3.PDU
0.BAT
2.BMS
selecting, testing, and designing around the commercial components.

## Slide 15
PCDU Architecture - Integration
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
PCDU – Aluminium Enclosure

## Slide 16
PCDU Architecture – Structure Integration
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
6U Cubesat Structure
4x8S1P – SAS
Cesi CTJ30-SCA

## Slide 17
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Facilities – Battery Characterization System
12 different battery cells characterized
Hioki BT4560
Battery Impedance Meter
June 2024

## Slide 18
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Facilities – SAS, Bat & Sun Simulator
LED LARGE AREA SOLAR SIMULATOR 25x50 cm2
32 Channels
G2V SUNBRICK
SMU KEITHLEY 2461
4xSAS ITECH IT2100
4xBat ITECH M3612
SOLAR ARRAY SIMULATOR
BATTERY SIMULATOR
SOURCE MEASUREMENT UNIT
SUN SIMULATOR

## Slide 19
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
PCDU Validation – In-House Functional Tests - OK

## Slide 20
PCDU Validation – Thermal Vacuum Chamber (TVAC) Tests
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Fault Free Operation TVAC -40ºC-60ºC

## Slide 21
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
PCDU Validation – Total Ionizing Dose (TID) Radiation Tests
Fault Free Operation TID > 70 kRads

## Slide 22
PCDU Validation - Vibration Tests
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
PASSED

## Slide 23
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Conclusions
6U Modular/Scalable HiRel PCDU ready – TRL 6
Technology ready for integration in future space missions.
Validated advanced “Careful COTS” and “New Space” methodologies for power conversion and distribution.
Consolidated a technological capability in high-reliability satellite power systems within the Valencian Community.
Research group specialized in power systems for space applications.
Facilities and Know-How for Space Power Electronics.

## Slide 24
Deep Space Microsatellite Power System Development
ASFAE/2022/021
José Manuel Blanes Martínez
Universidad Miguel Hernández de Elche
Space Power and Electronics System Group
SPES
Reunión Final del Plan Complementario de Astrofísica y Altas Energías
Noviembre 2025, Santander

## Slide 25
The ASFAE’s research projects acknowledge the financial support from the MCIU with funding from the European Union NextGenerationEU and Generalitat Valenciana.
Backup Slides – ASFAE 2022/21 Results
1 Post-Doctoral researcher hired
1 Pre-Doctoral researcher hired
1 PhD Thesis on-going
5 Papers in indexed Journals
7 Conferences Proceedings
1 Private company collaboration
Consolidated a technological capability in high-reliability satellite power systems within the Valencian Community.