## Slide 1: New methods and instrumentation to exploit CNA and CERN synergies in experimental nuclear physics
J. Bartolomé-Sarsa*, G. Auñón, B. Fernández, J. Ferrer, J. García-López, J. Gómez-Camacho, C. Guerrero and A. Vegas
Universidad de Sevilla, 41012 Seville, Spain
Centro Nacional de Aceleradores (CNA), 41092 Seville, Spain
Plan Complementario de Astrofísica y Física de Altas Energías (ASTRO+FAE)
Congreso final en Santander, 25-27 de noviembre de 2025
*Doctoral student funded by MRR ASTRO-FAE @CNA/USevilla

## Slide 2: The Centro Nacional de Aceleradores (CNA) in Seville
MiCaDaS
3 MV Tandem
18/9 MeV Cyclotron
PET/TC Scanner
Micro PET and Micro TC scanner (Animals)
1 MV AMS (SARA)
Radiofarmacy Labs
Co-60 Irradiator

## Slide 3
Nuclear reactions at CNA and CERN

## Slide 4: Nuclear reactions at CERN/ISOLDE and CNA/FNB
12C(6Li,α0)14Ng.s
excitation function
12C+197Au
target
PIPS detectors
Silicon DSSSD
+
⁶Li
¹²C
α
14N
Vb= 4.5 MeV
Light targets nuclear reactions studies at energies around the coulomb barrier Vb.
α-scattering on unstable proton-rich tin isotopes for the astrophysical p-process.
108,110,112Sn(a,a) at Ec.m = 18.8 MeV in inverse kinematics using “solid” 4He targets @ SEC (Scattering Experiments Chamber) of HIE-ISOLDE

## Slide 5: Neutron induced reactions at CERN/n_TOF and CNA/HiSPANoS

## Slide 6
Plan Complementario de I+D+i de
Astrofísica y Física de Altas Energías @CNA

## Slide 7: Magnetron-Sputtering to make solid-gas targets for CNA and CERN
plasma
5 cm
metal target
Sample holder
Magnetron Sputtering
Industrially well established
Large areas feasible
Wide range of substrates
Control of microstructure
Control of composition
Gas
element
Gas
element
Gas
element
Gas
element
solid
matrix
UNIVEX 250 for RF sputtering
by Leybold
Self supported Si-He target
Many of the isotopes of interest in nuclear reactions correspond to gaseous elements, which poses a serious problem
=> A solution is to “grow” s samples that incorporate the gas into sustrate in sufficient amounts, which has been demosntrated by our group and now at CNA we will be able to make such targets for nuclear physics experiments at CNA, CERN/ISOLDE, TRIUMPH, LNS, etc.
MRR ASTRO-FAE:
Magnetron-Sputtering system

## Slide 8: New manipulator for accurate sample positioning at CNA/FNB
Precise target positioning is essential for achieving high-accuracy nuclear reaction measurements: s(E,θ)
New manipulator system:
Remote contolled motorized movement
3D positioning with 10 µm precision.
360º rotation
MRR ASTRO-FAE:
Manipulator for CNA/FNB
Física Nuclear Básica (FNB) reaction chamber

## Slide 9: Cyclic neutron activation at CNA/HiPANoS and CERN/n_TOF (short t1/2)
Neutron activation is used to measured te integral cross section of recations of intersts, mainly in astrophysics. Often, the product nucleus is short lived and thus cyclic activation is required.
MRR ASTRO-FAE:
Fast Linear Stager at CNA
n-moderator for beam shaping at CNA
Contract student and trips to CERN

## Slide 10: New buncher to measure (a,n) by Time-of-Flight at CNA/HiSPANoS
MRR ASTRO-FAE:
Design, construction and installation with NEC of new beam buncher
Contract student
The MANY Collaboration: Measurements of (A,N) Yields
Renewed interest in measuring (a,n) recations for astrophysics, nuclear Technology, rare-events background assesment.
Current pulsing systems for ToF only for 1H and 2H beams.
In collaboration with NEC:
=> design a unique 3 stage buncher for 1H, 2H and 4He beams to <2ns.

## Slide 11
Conclusions
This work is part of the ASTRO21/1.3/3 project, funded by the Plan Complementario de I+D+i de Astrofísica y Física de Altas Energías, Plan de Recuperación, Transformación y Resiliciencia (MRR)
MRR ASTRO-FAE (Actuación 1.3 and part of 1.1):
New Magnetron-Sputtering system for making solid targets of gaseous elements for CNA, ISOLDE, TRIUMPH, …
High precision sample manipulator for nuclear reaction studies at CNA
Fast linear stager and moderator for cyclic neutron activation at CNA/HiSPANoS and CERN/n_TOF-NEAR
New beam buncher for CNA/HiSPANoS suited for 4He in addition to 1H and 2H
24 months contract of doctoral student on the last two topics