## Slide 1
Space-charge saturation effect
and correction at high gain
in CYGNO GEM-based detectors
Giorgio Dho on behalf of Antonietti, Baracchini, Benussi, Bonali, Capoccia, Caponero, de Carvalho, Cavoto, Costa, Croce, Dané, Di Marco, D'Astolfo, D'Imperio, Fiorina, Iacoangeli, Islam,
Jùnior, Maccarrone, Mano, Gregorio, Marques, Mazzitelli, McLean, Messina, Meloni, Monteiro, Nobrega, Pains, Paoletti, Petrucci, Piacentini,
Pierluigi, Pinci, Renga, Russo, dos Santos, Saviano, Scamporlino, Silva, Spooner, Tesauro, Tomassini, Tozzi
Istituto Nazionale di Fisica Nucleare (INFN-LNF), Frascati (RM), Italy
G. Dho, LNF Feb 23 2026
CYGNUS workshop 2026

## Slide 2
CYGNO Experiment
G.Dho 1
See Fiorina’s presentation earlier this morning
He:CF4 gas 60/40:
room temperature
atmospheric pressure
F gives spin dependent sensitivity He for low DM mass sensitivity CF4 scintillates in visible range
TPC
Amplification Stage
Optical readout
Gas Electron Multipliers
(GEMs)
Grants large gains with high granularity O(50) um
READOUT
Optical readout
PMT
sCMOS cameras
Decoupled from gas less contamination
z axis
CYGNO project aims to construct a large directional detector, O(10-100) m3, for rare event searches (DM, Solar neutrinos)

## Slide 3
Higher gain allows to:
      Improve energy threshold
      Detect all the low energy deposits of a recoil
Optical readout with camera requires high gain
Why Do We Need Large Gain
G.Dho 2
Conversion efficiency
0.07 ph/secondary e-
He:CF4 with isobutane %
N: lens aperture I: magnification
Solid angle coverage
Pro: Large area framed by camera
Price: Little solid angle coverage
Amaro et al., EPJC, https://doi.org/10.1016/j.physletb.2024.138759

## Slide 4
You want more gain? Put more GEMs!
Technically works, but increases the number of transfer gaps
Not an efficient process
Diffusion from amplification stage increases
Balance Between Tracking and Gain
G.Dho 3
STD of light distribution caused by amplification stage of short round tracks
Measured with CYGNO prototype: MANGO
Dho et al., EPJC, https://doi.org/10.1140/epjc/s10052-024-13471-5
Bad for a directional detector

## Slide 5
So just push GEM voltage to the limit of sparking
      This is what we do
Push GEM voltage
G.Dho 4
Numbers in our gas mixture:
LNF (1000 mbar): max 460 V each GEM
LNGS (910 mbar): max 440 V each GEM

## Slide 6
So just push GEM voltage to the limit of sparking
      This is what we do
However, data with 55Fe source (5.9 keV photoelectrons) as a function of drift distance in LIME (@ LNGS):
Push GEM voltage
G.Dho 4
Numbers in our gas mixture:
LNF (1000 mbar): max 460 V each GEM
LNGS (910 mbar): max 440 V each GEM
Light yield (AU)
Drift distance z (cm)
Drop of 40% from 33 cm to 4 cm

## Slide 7
Sort of know problem when too much charge undergoes avalanche
Space-charge saturation effect
Charge density is key events closer to anode diffuse less more saturated
What Is Going On?
G.Dho 5
Oliveri et al., NSS/MIC, https://doi.org/10.1109/nssmic.2015.7581778
Colour: ion density
Electric field from GEMs is shielded by ion field
Can we model this?

## Slide 8
Start from GEM charge generation in GEM: Townsend equation
Space-Charge Effect Model
G.Dho 6
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7

## Slide 9
Start from GEM charge generation in GEM: Townsend equation
First order linear dependence on electric field of Townsend coeff
Space-Charge Effect Model
G.Dho 6
Golovatyuk et al., NIM A, https://doi.org/10.1016/S0168-9002(00)01172-4
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7

## Slide 10
Start from GEM charge generation in GEM: Townsend equation
First order linear dependence on electric field of Townsend coeff
Assume the electric field is shielded by n itself
Space-Charge Effect Model
G.Dho 6
Golovatyuk et al., NIM A, https://doi.org/10.1016/S0168-9002(00)01172-4
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7

## Slide 11
Start from GEM charge generation in GEM: Townsend equation
First order linear dependence on electric field of Townsend coeff
Assume the electric field is shielded by n itself
Solve equation for 1 GEM
Space-Charge Effect Model
G.Dho 6
Golovatyuk et al., NIM A, https://doi.org/10.1016/S0168-9002(00)01172-4
Unsaturated Gain
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7

## Slide 12
Start from GEM charge generation in GEM: Townsend equation
First order linear dependence on electric field of Townsend coeff
Assume the electric field is shielded by n itself
Solve equation for 1 GEM
Space-Charge Effect Model
G.Dho 6
Golovatyuk et al., NIM A, https://doi.org/10.1016/S0168-9002(00)01172-4
Unsaturated Gain
~ 0: no effect
~ 1: no gain
0<< && <<1: saturation
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7

## Slide 13
In CYGNO,
    We use 3 GEMs: between each stage there is extraction and collection efficiency All accounted in 
    The charge density reaching the GEM holes depends on electron cloud size: diffusion 
Rewriting the previous expression:
Space-Charge Effect Model II
G.Dho 7
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7

## Slide 14
In CYGNO,
    We use 3 GEMs: between each stage there is extraction and collection efficiency All accounted in 
    The charge density reaching the GEM holes depends on electron cloud size: diffusion 
Rewriting the previous expression in 4:
Space-Charge Effect Model II
G.Dho 7
Parameter: Townsend coefficient α
Parameter: geometrical and saturation
Parameter: total efficiency
Measurable: Diffusion coefficient
Parameter: V0
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7

## Slide 15
In CYGNO,
    We use 3 GEMs: between each stage there is extraction and collection efficiency All accounted in 
    The charge density reaching the GEM holes depends on electron cloud size: diffusion 
Rewriting the previous expression:
Space-Charge Effect Model II
G.Dho 7
Parameter: total efficiency
Measurable: Diffusion coefficient
Parameter: V0
Can we measure/test this?
Parameter: geometrical and saturation
New paper! Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7
Parameter: Townsend coefficient α

## Slide 16
CYGNO prototype at Laboratori Nazionali Frascati (LNF)
Gas TPC with 10x10 cm2 readout area and 23 cm drift
Triple GEM amplification stage
2 PMTs, 1 ORCA Quest2 camera with EHD lens
Field cage made of PET sheet with deposited copper strips
Movable source 55Fe holder (5.9 keV x-rays)
GIN Detector
G.Dho 8
Camera sensor
Movable source holder

## Slide 17
Data is taken with and without the 55Fe source
Source movable along 11 different positions along z (drift direction)
Analysis of clusters allows to retrieve: energy, sigma of the spatial distribution.
GIN Detector Data Acquisition
G.Dho 9

## Slide 18
Exploiting data taken with different VGEM, and position a combined fit of our model can be performed
Model Fit
G.Dho 10
Amaro et al., EPJC, https://doi.org/10.1140/epjc/s10052-026-15318-7
Model works on separated dataset!
PAPER:

## Slide 19
This model has been included in our detector simulation yielding very promising results
Model into Simulation
G.Dho 11
Amaro et al., eprint, https://arxiv.org/pdf/2601.01435

## Slide 20
How does Saturation appear
G.Dho 12
Energy non-linearity
To be measured different sources are needed
Topology changes along the energies
Under study by LNGS group
Non-exponential gain
It naturally occurs for GEMs in wide ranges of VGEM
Absolute saturation measurable only in small VGEM ranges
z-dependence of light yield
Complicates the energy determination
Dependent on drift field as well due to absorption
Topological deformation Worsening ER/NR discrimination
Light yield (AU)
Light yield (AU)

## Slide 21
How Do We Work Around This
G.Dho 13
Lower VGEM and drift field
Reduces the spread in z
Diffusion increases lowering drift field
Lower light yield (about half)
Some data with LIME at LNGS taken in this configuration
V-Bond GEM
Procedure to modify GEM structure
Visible effect: opaque copper
Intense electric field below last GEM
Extra electrode to distort electric field below last GEM
Saturation reduced to about ~ 20%
Tackle experimentally
Dho et al., EPJC, https://doi.org/10.1140/epjc/s10052-024-13471-5

## Slide 22
How Do We Work Around This
G.Dho 13
Lower VGEM and drift field
Reduces the spread in z
Diffusion increases lowering drift field
Lower light yield (about half)
Some data with LIME at LNGS taken in this configuration
V-Bond GEM
Procedure to modify GEM structure
Visible effect: opaque copper
Intense electric field below last GEM
Extra electrode to distort electric field below last GEM
Saturation reduced to about ~ 20%
Tackle experimentally
Dho et al., EPJC, https://doi.org/10.1140/epjc/s10052-024-13471-5

## Slide 23
V-Bond GEM
G.Dho 14
After the GEM is etched the V-Bond procedure is applied
Bath of chemicals which etches non perfect Cu crystals generating small valleys
Depth about 500 nm, width similar
Generation of small film of 10 nm of organic copper film (unknown)
Originally thought to remove reflections seen in LIME data
Intense tracks were reflecting over window and smooth copper
With V-Bond GEM become opaque: NO reflections
https://www.mec-co.com/en/product/electronic-substrate/sekisou/

## Slide 24
In GIN detector GEM3 (closest to optical readout) was replaced with a V-Bond GEM
A simple VGEM scan showed interesting hints of lower saturation
Gain Scan
G.Dho 15
Light yield (AU)

## Slide 25
As this GEM might behave differently, we modified GIN to measure saturation
Two scintillators added above and below GIN to tag muons (about 30x7x2 cm3)
System is movable along z, to perform drift gap scans with muons
Modified GIN Setup
G.Dho 16
Simulated distribution of z coordinate of muon with respect to nominal centre of scintillator
Average: 0 with error of < 100 µm Sigma: 1.2 cm

## Slide 26
To correct for absorption along the drift we employ muons tagged by the system
Muons have the least energy deposit density, no saturation
Intensity (ISC) estimated with truncated method on Landau distributions
Attenuation Length
G.Dho 17
λabs = (200 ± 40) cm
VGEM = 440V
Edrift = 1 kV/cm

## Slide 27
Now, a similar scan in z with 55Fe source
After correcting for attenuation length (blue points) real saturation can be extracted
Drift Distance Scan
G.Dho 18
No saturation @ 440 V LNF with V-Bond GEM
Peak-to-peak fluctuation = 1%

## Slide 28
Study repeated with 450 and 460 V.
Used muons to estimate non saturated gain increase when increasing GEM voltage
Absolute Saturation
G.Dho 19
Paper in preparation
Saturation appears back again
At maximum voltage saturation is below 20%
Effectively reduced saturation but keeping the same light yield

## Slide 29
Study repeated with 450 and 460 V.
Used muons to estimate non saturated gain increase when increasing GEM voltage
Absolute Saturation
G.Dho 19
Paper in preparation
Selected solution for CYGNO-04 demonstrator

## Slide 30
Within the CYGNO experiment it is really important to increase as much as possible the amplification gain while keeping the best detector performances
Pushing the GEM to maximum voltage causes the onset of space charge saturation effects which limit the detector uniform response
An effective modelisation of the phenomenon appears to work consistenly with data taken with a prototype at LNF laboratories
The V-Bond procedure applied to GEM was tested with a modified version of the same CYGNO prototype
Saturation is measured reduced by more than half while preserving the same light output which already guarantees 0.5 keVee energy threshold
Other R&D activities are under study with possibly even better results
Conclusion
G.Dho 20

## Slide 31
Backup
G.Dho

## Slide 32
Reconstruction algorithm of CYGNO based on DBSCAN and fittin procedure to merge pieces of long tracks
Reconstruction
G.Dho
Muon
55Fe electron recoils

## Slide 33
Modification of amplification stage adding an extra electrode 3mm below the last GEM
New electrode: ITO (indium-tin-oxide) transparent sheet (85%)
Very strong electric fields applied in this induction gap (<15 kV/cm)
Lowering the GEM HV, above a certain field, the light yield increases exponentially
Studies with ITO I
G.Dho
Dho et al., EPJC, https://doi.org/10.1140/epjc/s10052-024-13471-5
MANGO prototype @ LNGS

## Slide 34
Simulation of electric field with Ansys of GEM hole region
Large deformation of field intensity below GEM hole when Eind is high
A wider region has electric field strong enough to generate amplification, yet with low intensity
Light yield achieved is larger than using triple GEM and with reduced intrinsic diffusion
Studies with ITO II
G.Dho
LY vs diffusion

## Slide 35
Exploting GEM1 voltage scan with low voltage GEM configuration for GEM2/3 and 55Fe source (1 cm away from GEMs)
Absolute unsaturated behaviour of GEM1 scan is obtained (how much the gain should increase every 10 V more I power up GEM1)
Studies with ITO III
G.Dho

## Slide 36
Different configuration with 3 GEMs and ITO are tested and absolute saturation is calculated
Studies with ITO IV
G.Dho
Low VGEM no Eind: LY 9800 ± 150 Sat 0%
Low VGEM high Eind: LY 31300 ± 200 Sat (1.7 ± 1.5)%
Med VGEM high Eind: LY 64700 ± 400 Sat (29.1 ± 1.5)%
High VGEM no Eind: LY 30700 ± 200 Sat (34.5 ± 1.6)%
Paper in preparation

## Slide 37
The V-Bond technique is likely causing rough copper crystals around the GEM holes to be removed.
This might place the electrodes further from the holes
Why Less Saturation with V-Bond?
G.Dho
Reducing electric field
Indeed, applying the same voltages, the light gain is lower than standard GEM
Widening the amplification region
This could be similar to ITO studies causing the wider region the imprint less saturation