## Slide 1: Environmental neutron measurement and development of analysis techniques using nuclear emulsion detector
T. Shiraishi - Kanagawa Univ.
23 Feb. 2026 CYGNUS2026 @Kobe

## Slide 2: Motivation of Environmental Neutron Measurement
DAMA/LIBRA signal : 2 – 6 keVee
R. Bernabei et al., Nucl. Phys. At. Energy 19, 307 (2018)
Neutron measurement over a wide energy range is necessary
> 22 years annual modulation
Background Study
  Nuclear recoil by Neutron
   background in direct WIMPs search
  γ, p, α emission via nuclear reactions （e.g. AN + n  A+1N + γ）
   background in rare event searches
Demonstration of low mass dark matter search (e.g. Boosted Dark Matter)
N
n
 Assuming this signal as Na recoil by neutron, its energy corresponding to 80 – 250 keV
(especially sub-MeV)

## Slide 3: Neutron Detection Principle by Nano Imaging Tracker (NIT)
880 keV Neutron
10 mm
θ
Proton range
Ep ~ 600 keV
NIT film
Optical Microscope Image
10 mm
H atomic fraction ~ 40%
Neutron
5 mm
Sub-micrometric
3D tracking
T. Shiraishi, et al., PTEP 2021 4, 043H01 (2021)

## Slide 4: High-resolution Readout and 3-dimensional Tracking
Latest Analysis System (Kanagawa Univ.)
High-speed Camera
Z-drive
Epi-illumination microscope
Light guide
Objective lens
XY-drive
Achieve high speed (1.3 kg/year) while maintaining high resolution
5 Mpixels & 700 fps
(50 Gbps)
T. Shiraishi, et al., Phys. Rev. C 107, 014608 (2023)
Improve analysis speed
50 Gbps Image Acquiring
3D Tracking

## Slide 5: 3D Convolutional Neural Network （3D-CNN）
Training Samples
Proton or alpha
Dust
Multi-prong
input image size
128 x 128 x 20
feature maps1
64 x 64 x 128
Convolution &
Max-Pooling
feature maps2
32 x 32 x 256
Convolution &
Max-Pooling
feature maps3
16 x 16 x 512
feature maps4
8 x 8 x 256
Convolution &
Max-Pooling
Flattened
・・・
・・・
1024
layers
Dropout
0.2
Dropout
0.5
256
layers
proton
dust
multi
Convolution &
Max-Pooling
Signal
Noise
Reduce the noise by a factor of 10⁴ with 95% efficiency

## Slide 6: Evaluation using Monochromatic Fast Neutron Beam
Track Range
2025
2022
Scattering Angle
Beam Energy
(0.88±0.02) MeV
Proton Energy
Reconstructed Neutron Energy
Monochromatic 0.88 MeV neutron via T(p n)3He reaction @ AIST
Geant4 simulation

## Slide 7: Environmental Neutron Measurement @LNGS
H. Wulandari et al., Astropart. Phys. 22 (2004) 313.
Almost of measurements used moderators and thermal neutron captures.
  No energy resolution
   Uncertainty of moderations
Unknown angular distribution.
Neutron flux is different for each measurements.
   Annual modulation of water content in the rock, or Location affects it?
No spectrum and directional data in sub-MeV

## Slide 8: Environmental Neutron Measurement by NIT @ LNGS
n-Run1
(Nov. 2021)
Surface ground
Without shielding!
because of no sensitivity to muon and gamma
Underground
n-Run2
(May 2022)
n-Run3
(Jan. 2023)
n-Run4
(Nov. 2023 )
8
Refrigerator Box
Sample2
Compressor
12cm
Thermal
Insulator
10cm
Sample1
*Radon reduction

## Slide 9: Results of Neutron Measurement
(n-Run4)
210Po
sub-MeV
Preliminary
238U
234U, 230Th, 226Ra
210Po
Result of n-Run4 0.52 kg*day
Thermal n
14N(n p) 14C
In sub-MeV region, both surface ground and underground measurements are consistent with predictions
Radon reduction is needed for MeV region
MC Simulation using NeuCBOT, PHITS, and GEANT4
(α n) reaction in the rock by 238U, 232Th
Spontaneous fission of 238U
* Assuming the water content in the concrete is 8%
H. Wulandari et al., Astropart. Phys., 22, 313-322 (2004)
sub-MeV
Surface ground
Underground

## Slide 10: Effects of Radon Reduction in Air
sub-MeV
234U, 230Th, 226Ra
210Po
238U
214Po
NEWSdm facility (@ Hall-F)
n-Run3
Rn Level ~ 100 Bq/m3
Rn Level ~ a few Bq/m3
 Further radon reduction and humidification are needed
Radon free room (CR1 @ Hall-C)
n-Run4
α-ray background has decreased, however the energy resolution is worse than in the previous run (n-Run3)
 Damage to the sample due to rapid drying at low humidity in CR1?

## Slide 11: Radon Filtering System
Gas circulation compressor
Globe box
Humidification
+
NIT film preparation
4A type zeolite
(for water trap)
Ag-zeolite*
(for Radon trap)
*provided from Dr. Ogawa
222Rn
218Po+
a
PIN-PD
GND
−HV
a
Radon Detector
MFC
Circulation
Now trying to reduce Rn in air…

## Slide 12: Neutron Detection Methods for Various Energies
Nuclear Reaction
Proton Elastic Scattering
Deep Inelastic Scattering
Neutron Energy
Sub-GeV −
100 keV (~ 1 µm)
meV (thermal neutron)
3 fragments
Nuclear recoil
10 µm
70 µm
0.88 MeV neutron
θ
Recoil proton
0.58 MeVproton
(Monochromatic)
Reconstruct 3D trajectory with sub-micron accuracy
 can obtain position, energy and direction
6.5 µm
σN(n p)C ~ 2 barn
@ 26meV
n + 14N  p + 14C + 0.62 MeV
N atomic fraction ~ 3.7% in NIT
JENDL-4.0

## Slide 13: Demonstration of Thermal Neutron Detection
proton 2.49 MeV
Li
Neutron source: RANS-Ⅱ beamline @ RIKEN
*Neutron energy is broad spectrum due to 100 µm thick of Li target
PE moderators
Proton signal created by
thermal neutrons via 14N(n p)14C
fast neutrons (elastic collision)
Gold foil
7Li(p n)7Be
Thermal neutron monitor
Measured by Ge detector

## Slide 14: Confirmation of Thermal Neutron Signal
Red (8cmPE) ×10 scale
Blue (14cmPE) ×100 scale
Thermal neutron signal
Thermal neutron
Fast neutron
Fast neutron
Confirmed the characteristic 0.584 MeV peak from the 14N(n p)14C reaction is enhanced by moderators
Neutron spectra expected by Geant4 simulation
Data (proton energy spectra)
w/o moderator
w/o moderator

## Slide 15: Data/MC Comparison of Thermal Neutron Signal
w/o moderator
PE 8cm
PE 14cm
Thermal neutron signal
Confirmed the expected sensitivity to thermal neutrons
 Sensitive over a wide energy range

## Slide 16: Luminescence and Track Formation in AgBr:I Crystal
Microscope
60keV C ion
NIT type
200 nm OPERA type
20 nm UNIT type
0.5 µm
Silver filament
Light yield ~ 40 photon/keV
@ 88K (241Am γ-ray)
T. Shiraishi et al., Nucl. Inst. Meth. A 927 (2019) 202
NIT film
Track formation
Luminescence
via Iodide

## Slide 17: Luminescence and Track Formation in AgBr:I Crystal
Microscope
60keV C ion
NIT type
200 nm OPERA type
20 nm UNIT type
0.5 µm
Silver filament
Light yield ~ 40 photon/keV
@ 88K (241Am γ-ray)
T. Shiraishi et al., Nucl. Inst. Meth. A 927 (2019) 202
NIT film
Track formation
Luminescence
via Iodide
High-efficient
luminescence
sub-micron
track
Get BOTH responses

## Slide 18: Luminescence and Track Formation in AgBr:I Crystal
Microscope
60keV C ion
NIT type
200 nm OPERA type
20 nm UNIT type
0.5 µm
Silver filament
Light yield ~ 40 photon/keV
@ 88K (241Am γ-ray)
T. Shiraishi et al., Nucl. Inst. Meth. A 927 (2019) 202
NIT film
Track formation
Luminescence
via Iodide
High-efficient
luminescence
sub-micron
track
Get BOTH responses

## Slide 19: Luminescence α – β Comparison @105K
241Am 70 Bq
60Co 30 Bq
T. Shiraishi et al., Nucl. Inst. Meth. A 927 (2019) 202
T. Shiraishi, Doctor Thesis (2019), Nagoya Univ.
50 < total p.e. < 200
Fast (540nm)
Slow (560nm)
Averaged Waveforms

## Slide 20: Temperature dependency
Slow component drastically quenched by arising temperature
Fast component is comparable even at RT.

## Slide 21: Luminescence Study with Ion Implantation System at Cryogenic Temperature
Now, upgrade and measurement on going

## Slide 22: Summary
3D sub-micrometric tracking technique has been developed for NIT analysis
  Achieved analysis speed of 1.3 kg/year/machine with 1 µm ( p 100keV) threshold
Neutron run in Gran Sasso
  Surface ground run (n-Run1, nRun2)
    Succeeded to measure neutron spectrum and direction in sub-MeV region
    Thermal neutron signal was indicated
      Confirmed using RANS-Ⅱ beamline @ RIKEN
  Underground run (n-Run3, nRun4)
    Environmental neutron signal in sub-MeV region has been observed with 0.52 kg*day scale analysis
    More scaling up is available, but Radon background contamination also observed in MeV region with current scale
       Constructing Radon filtering system using Ag-zeolite
Luminescence of NIT
  Luminescence characteristics are studying using Ion implantation system
 T. Shiraishi et al., Phys. Rev. C 107, 014608 (2023)
 T. Shiraishi et al., PTEP 2021 4, 043H01 (2021)

## Slide 23: Backup

## Slide 24: For the Verification of DAMA Signal
D. Cintas et al, J. Phys.: Conf. Ser. 2156, 012065 (2021)
DAMA claims signal around 2 – 6 keVee
R. Bernabei et al., Nucl. Phys. At. Energy 19, 307 (2018)
Assuming DAMA signal as neutron background, its energy corresponding to 80 – 250 keV
 Neutron spectrum measurement including sub-MeV region is needed to verify the DAMA signal!
Many experiments agree that quenching factor of Na is ~20%
22 years annual modulation

## Slide 25: Establishment of Neutron Energy Reconstruction
Ep = 0.85 MeV, cosθ = 0.98
 En = 0.89 MeV
Ep = 0.59 MeV, cosθ = 0.86
 En = 0.80 MeV
Ep = 0.31 MeV, cosθ = 0.60
 En = 0.86 MeV
10 µm
0.88 MeV neutron
Neutron Energy
Neutron direction is “known”
Neutron direction is “unknown”
Predict original distribution from observed distribution using Unfolding Method
Data
Response function
Original Energy
Used spontaneous fission of 252Cf
Neutron energies can be reconstructed event by event

## Slide 26: Establishment of Neutron Energy Reconstruction
Ep = 0.85 MeV, cosθ = 0.98
 En = 0.89 MeV
Ep = 0.59 MeV, cosθ = 0.86
 En = 0.80 MeV
Ep = 0.31 MeV, cosθ = 0.60
 En = 0.86 MeV
10 µm
0.88 MeV neutron
Neutron Energy
Neutron energies can be reconstructed event by event
Neutron direction is “known”
Neutron direction is “unknown”
Predict original distribution from observed distribution using Unfolding Method
Data
Response function
Original Energy
Used spontaneous fission of 252Cf

## Slide 27: Luminescence

## Slide 28: Event discrimination by using multi-signals
CDMS Experiment (Charge + Phonon)
XENON Experiment (Photon + Charge)
S. Fallows, Univ. of Minnesota Doctor Thesis, Dec 2014
XENON Collaboration, E. Aprile et al, Phys. Rev. D 97, (2018) 092007

## Slide 29: Cryostat and DAQ
241Am 66 Bq
Two-photon coincidence method
  MPPC measure intensity and decay time
  PMT & Monochromator measure spectrum
Spectrum and waveform analysis with ultra-low noise at photon counting levels
Cryostat
T. Shiraishi, et al., Nucl. Inst. Meth. A 927 (2019) 202
T. Shiraishi, Doctor Thesis (2019), Nagoya Univ.

## Slide 30: Cryostat and DAQ
241Am 66 Bq
Two-photon coincidence method
  MPPC measure intensity and decay time
  PMT & Monochromator measure spectrum
Spectrum and waveform analysis with ultra-low noise at photon counting levels
Cryostat
T. Shiraishi, et al., Nucl. Inst. Meth. A 927 (2019) 202
T. Shiraishi, Doctor Thesis (2019), Nagoya Univ.
MPPC signal at a-ray exposed
 First observation of AgBr:I luminescence for charged particles

## Slide 31: Results of AgBr:I luminescence study so far
Spectrum
a-ray
405nm LED
Decay Time
These differences probably come from excitation density between alpha rays and photoexcitation
Comparison of light yield with 241Am γ
Capable of application as a scintillation detector, giving time resolution, and so on…
Light yield at liquid nitrogen temperatures is comparable to NaI:Tl scintillators
Possibility of particle identification from luminescence characteristics
Understanding electronic properties under high-density excitation
T. Shiraishi, et al., Nucl. Inst. Meth. A 927 (2019) 202
T. Shiraishi, Doctor Thesis (2019), Nagoya Univ.

## Slide 32: Luminescence
Current understanding
There is no doubt that iodine acts as an isoelectronic trap for holes
Slow components are tunneling recombination between shallow trapped electrons and trapped holes
Fast components are predicted as direct recombination between conduction electrons and trapped holes (high-density excited states in α-rays)
Wavelength shift is observed
Decay time is quite different
Comparison of α – photo excitation
Fast/Slow ratio depends on excitation density?
NIT
NIT

## Slide 33: Why can indirect transition-type AgBr luminous?
Before, luminescence of emulsion was reported only by photo-excitation
Ag core
Luminescence
(Recombination)
Conduction band
Valence band
E
Electrons
Holes
Hole trap
(Iodide)
Surface defects
Ag+
Energy
Hole is captured by difference in electron affinity between Br and I
Very short range potential same order of Bohr radius
   Hole is localized very close to Iodide
Iodide acts as isoelectronic trap
If hole is trapped
Localized to Iodide
Hole can spread in wavenumber space because of the uncertainty principle
E
k
I- trap
Excitation
Luminescence
Wavenumber space
Bohr radius
Potential for electron in GaP:N

## Slide 34: Combined detection may be possible?
Locate the recorded track position in emulsion with mm accuracy
Dust and fog don’t luminescent
Identify particle property from luminescence information (intensity, life time, spectrum, …)
NIT
Y axis
X axis
MPPC Array
Setup Example

## Slide 35: Energy deposition of low-velocity nuclear recoil
Energy deposition of low velocity nuclear recoil (β~10-3, ≈ fermi velocity of electrons) in solid is very complex
  The nucleus becomes neutral covered with electrons, no longer a simple ionization loss
  Rutherford scattering (Nuclear Stopping Power, NSP)
    Lattice defect generation
    Collision cascade
  Molecular orbital formation (Velocity Matching)
  …
Ga (15keV)
 | ESP in AgBr:I crystal (keV/mm) | NSP in AgBr:I crystal (keV/mm)
30keV C＋ | 240 | 130
10keV β線 | 6.5 | 0
1MeV β線 | 0.5 | 0
Lattice defect of potassium iodide
Proceedings of the Royal Society, A 332, 167 (1973)

## Slide 36: Luminescence Study with Ion Implantation System at Cryogenic Temperature

## Slide 37: Accelerators in our laboratory
Low Velocity Ion Implantation
Acceleration Voltage : 5 ~ 200 kV
Temperature : –196 ~ 1000℃
Ion : H, He, B, C, N, O, F, Si, P, Ar, Ti, Fe, Co, Ge, Kr, Xe, CO, CD4, ...
Valence : 1, 2, 3, (4)
Beam size : φ 10 cm (max.)
Beam density : 106 ~ 1013 ion/cm2
1MV Tandem Pelletron Ion Accelerator
Acceleration Voltage : 0.5 - 1 MV
Ion : He++, H, Li, B, C, O, Si, Ni, Cu, ...
Valence : 1, 2, ???
Detector : Si semiconductor detector x 2
Analysis : RBS-channeling, PIXE, Nuclear Reaction, ERDA

## Slide 39: Comparison of Nuclear Emulsion
60keV C ion
200nm crystal
500nm
44nm crystal
500nm
OPERA type
Nano Imaging Tracker (NIT) type
AgBr:I crystal (SEM)
AgBr:I crystal (SEM)
Optical microscope image
Optical microscope image
1 µm
100mm
60keV C ion
Range ~ 200nm
1 µm
100mm
500MeV/n Fe ion
500MeV/n Fe ion
Ion
Ion

## Slide 40: High Energy Ion Track in NIT
C 290 MeV/n
Ar 500 MeV/n
Fe 500 MeV/n
Xe 150 GeV
Pb 150 GeV

## Slide 41: Environmental neutron measurement

## Slide 42: 1st Surface Run (n-Run1) for Environmental Neutron Measurement @ LNGS
Motivation
Demonstration of spectrum measurement for environmental neutron and CR-DM search
There is no detailed data in the sub-MeV region even on the surface
* Recoil protons are accumulated O(2) events /(g month) on the surface
Refrigerator Box
Sample2
Compressor
12cm
Thermal
Insulator
10cm
Sample1
n-Run1 Setup

## Slide 43: Event Classification
External a-rays are excluded by fiducial volume cut, then events are topologically classified to Single-prong and Multi-prong
Unfortunately, n-Run1 samples accumulated a lot of Radon daughters, we focused on sub-MeV region (2~14mm  0.25~1MeV) of Single-prong event to analyze with background free

## Slide 44: Single-prong Analysis Result (n-Run1)
Range spectrum of Single-prong signal
0.25 < En < 10 MeV
9.0 x 10-3 cm-2 s-1 @ LNGS surface
Assumed neutron spectrum expected by PARMA model
T. Sato, PLOS ONE 10, e0144679 (2015)
T. Sato, PLOS ONE 11, e0160390 (2016)
Observed signal increase consistent with environmental neutron signal
Detectable neutron spectrum with 2 < R < 14 mm
(0.25 < Ep < 1 MeV)
14N(n p)14C reaction
(Q = 0.62 MeV)

## Slide 45: Data/MC Comparison (n-Run1)
Proton Energy
Plane Angle
Zenith Angle
 Due to low efficiency for vertical
Number of Events
MC : 11.9±0.5 event/g/day
Data : 11.1 ± 0.6(stat.) ± 2.4(sys.) event/g/day
Zenith (= Z)
qZenith
f
X
Horizontal sample
Neutron Flux [0.25 ~ 10 MeV]
PARMA model : 9.0 x 10-3 cm-2 s-1
Data : (8.4±1.8) x 10-3 cm-2 s-1
T. Shiraishi, et al., Phys. Rev. C 107, 014608 (2023)

## Slide 46: MeV Region (n-Run1)
n-Run1
210Po
214Po
sub-MeV
Sub-MeV
Proton Energy
Track Range
214Po
(short life-time)

## Slide 47: Reduction of 214Po Contamination at Drying
n-Run1
n-Run4
(Radon free room, CR1 @ Hall C)
210Po
214Po
sub-MeV
Hall F (NEWSdm facility)
n-Run1
(granite table)
n-Run2, n-Run3
(climatic chamber)
1 order
more 2 order
Proton Energy

## Slide 48: n-Run1 and n-Run2 Result
210Po
(Long life-time)
214Po
(short life-time)
14N + n  p 584keV + 14C 42keV
track range ~ 6.5mm
As expected
  sub-MeV signal increase
  210Po-alpha increase
  Offset background in MeV decrease
Thermal neutron signal can be seen significantly
Thermalized due to surrounding materials?
or attenuation by water contained in rock was suppressed?
14N(n p)14C
Q=626keV
Sub-MeV region
Track Range
Sub-MeV

## Slide 49: n-Run1 and n-Run2 Result
210Po
(Long life-time)
214Po
(short life-time)
14N + n  p 584keV + 14C 42keV
track range ~ 6.5mm
As expected
  sub-MeV signal increase
  210Po-alpha increase
  Offset background in MeV decrease
Thermal neutron signal can be seen significantly
Thermalized due to surrounding materials?
or attenuation by water contained in rock was suppressed?
14N(n p)14C
Q=626keV
Sub-MeV region
Track Range
Sub-MeV

## Slide 50: Surface Run Result (*after reference subtraction)
Proton energy spectrum (linear scale)
(log scale)
Reduced offset background makes MeV spectrum similar to the simulation
14N(n p)14C
210Po
214Po

## Slide 51: 2nd Surface Neutron Run (n-Run2)
 | Condition | Exposure Time on Surface (day) | Analyzed Mass (g) | Average Rainfall in Assergi (mm/day)
n-Run1 (Run start from 24 Nov. 2021) | Dried on granite table Run @ -20℃ | 2 | 0.65 | 4 **
 |  | 29 | 1.35 | 4 **
n-Run2 (Run start from 25 May 2022) | Dried in chamber Run @ -15℃ | 0 | 0.95 | ---
 |  | 58 | 1.08 | 1.4
** Estimation from Nov. – Dec. 2022 data

## Slide 52: Neutron Flux
Linear
Log
Angle-integrated neutron flux on LNGS surface with water fraction in rock = 20%
PARMA model take into account the neutron reflection by surface ground
Especially, epi-thermal neutrons flux depends on water fraction in rock
*Expected by PARMA model
fast
epi-thermal
thermal

## Slide 53: Underground Neutron Sources
(α n) reaction in the rock by 238U, 232Th(, 235U)
Spontaneous fission of 238U
m spallation
  Negligible in <10MeV region at LNGS underground
H. Wulandari et al., Astropart. Phys., 22, 313-322 (2004)
ρ = 2.71 g/cm3
Estimate myself using NeuCBOT and GEANT4 simulation

## Slide 54: Neutron Spectrum at LNGS Underground
Neutrons attenuated by water contained concrete
Spectrum spread to thermal region
Original
After attenuation
Attenuation
Tunnel structure by GEANT4
n

## Slide 55: m spallation
J.M. Carmona et al., Astropart.Phys. 21 (2004) 523-533
Underground muon rate is about 6 order less than Surface
Almost negligible

## Slide 56: Monochromatic Neutron Calibration

## Slide 57: Calibration with Monochromatic Sub-MeV Neutron
Monochromatic 880 keV neutron exposure from T(p n)3He reaction at AIST
Exposed 7.9 hours with a stable temperature at -26℃
En cos2θ
Data of recoil proton
Range cut (1 mm)

## Slide 58: Simulation of Neutron Exposure
Color corresponding to neutron energy
Energy
Fluence
Considering energy and fluence for each angle

## Slide 59: Correlation of Proton Energy and Range in NIT (GEANT4)
E ≈ 60.68 + 553.16 - 474.59 (keV)
NIT density : 3.2 g/cm3

## Slide 60: Calibration of α-ray detection

## Slide 61: Calibration of alpha-ray Energy (Ea) by Th star
228Th (6±1) mBq/kg
(Ge Detector)
Th star event is useful for calibration of run condition, such as brightness or E-R relation
It should be accumulated during run, and 5 prong event can be identified as 228Th to 208Pb
  5.423, 5.685, 6.288, 6.779, [8.785 or 6.051] MeV
10 mm
Th Decay Chain
~64%
~36%
Suggested by Valeri
 15 events/(g 28day)
2002年アイソトープ手帳

## Slide 62: a-energy calibration with Th star
n-Run1 Sample 2 & 3
228Th
224Ra
212Bi (36%)
216Po
212Po (64%)
220Rn
Geant4 Simulation
DEa,FWHM / Ea ~ 5%

## Slide 63: Concerning the excess in MeV region - Understanding for 210Po contamination -
Multiplicity of a in 1event | Expected number of event (31day * 0.71g) | Number of event from Data
5 (228Th to 208Pb via 212Po) | 6.4 (Ge) | 5
5 (228Th to 208Pb via 208Tl) | 3.6 (Ge) | 3
4 (224Ra to 208Pb via 212Po or 208Tl) | ~1 (Ge) | 1
4 (226Ra to 214Bi) | 1.5 (Ge) | 2
3 (222Rn to 214Bi) | ~0.1 (Ge) +222Rn contaminated | 3
1 (238U, 234U, 230Th) | respectively 1.5 (Ge) | Respectively < 3
1 (210Po) | 1.5 (Ge) +222Rn contaminated | 80?
226Ra 0.8 mBq/kg (Ge)
228Th (6±1) mBq/kg
(Ge Detector)
Contaminated from air

## Slide 64: Ea Spectrum
210Po peak (5.304MeV) have time dependence
 Accumulate during the Run
214Po peak (7.687MeV) ???
 214Po should be 3prong!
Can this seem as
internal 1prong???
U decay chain
No time dependence excess
 Short life time alpha decay?
2002年アイソトープ手帳

## Slide 65: Intrinsic Activity (Chamber dry & Underground)
α source | Energy (MeV) | Event Rate (events/g/4month) | Total Activity (mBq/kg)
218Po, 214Po (Rn short decay) | 6.003, 7.687 | 50 +- 12 | 
210Po (Rn long decay) | 5.304 | 1138 +- 56 | 10.97 +- 0.54
234U, 230Th, 226Ra | 4.775, 4.668, 4.784 | 103 +- 17 | 10.0 +-1.6
238U | 4.198 | 33 +- 10 | 3.2 +- 0.9
These activities are almost 3.3 mBq/kg respectively
Confirmed to be 2 orders less by CR1 dry
According to Fabio’s paper (Astropart. Phys. A 80, 16 (2016)),
226Ra activity is 2.4 mBq/(1kg high deionized gelatin)  0.8 mBq/(1kg NIT)
Because of radiative equilibrium, 234U, 230Th, 226Ra, 238U should be same activity
n-Run3 4 month sample
Contaminated from air
Accumulated during Run