## Slide 1: Drift Properties of Noble Gases in Negative Ion Drift TPCs
Elizabeth Tilly – The University of New Mexico
CYGNUS workshop – Feb 24, 2026
tillyeg01@unm.edu

## Slide 2: Noble Gases as Ideal Targets
Gaseous Xe for neutrinoless double beta decay
  K. Mistry, D. R. Nygren, (2025) arxiv:2512.19290
  I.G. Irastorza et al JCAP 01 033 (2016)
Gaseous He, Ar, Xe, CF4 in Migdal Effect searches
  D. Yi et al. Nature 649, 580–583 (2026)
  H.M. Araújo et al. (MIGDAL collaboration), Astropart. Phys. 151 102853 (2023)
  K.D. Nakamura et al PTEP 1 013C01 (2021)
Gaseous Ar in collider-based neutrino experiments
  R.M. Amarinei, et al JINST 18 P12001 (2023)
Gaseous He, Ar, Xe and CF4 for WIMP DM searches
  J.F. Castel et al JINST 19 C05029 (2024)
  F.D. Amaro et al Particles 4 343-353 (2021)
  S.E. Vahsen et al (2020) arxiv:2008.12587
  C. Deaconu et al Phys. Rev. D 95 122002 (2017)
  K. Nakamura et al JINST 7 C02023 (2012)
And the list goes on…
Far from a comprehensive list (I’m sorry if I’ve missed your paper)

## Slide 3: Negative Ion Drift Low-Pressure Gas TPCs
Amplification Plane
Cathode
+V
-V
(2) Ionization electrons are captured according to
forming negative ions
(1) Recoiling particle ionizes gas creating track
(3) As charge cloud drifts, it is diffused with a characteristic
(4) In order to amplify, the ions must be stripped of their electrons
(5) Resulting track is read out via optical or charge readout
Lower diffusion
Longer Tracks
Better Directional Resolution

## Slide 4: Advantages of Negative Ion Drift (NID)
CF4
CF4+CS2
CF4
CF4+CS2
Gains for these tracks are on the order of 105!
Notes: Comparable gas gains but the light is lower so the G is a good estimate using two gGEMs like in MIGDAL ** mention MPII

## Slide 5: Thermal Drift
At low electric fields, ions are nearly in thermal equilibrium with the gas, giving rise to the following diffusion coefficient
Typically, in this regime, mobility is constant with E/P
At higher fields, these relationships break down and things deviate from thermal
  Mobility and diffusion are larger at higher fields
  Diffusion is axially dependent
= drift velocity, = mobility, = Electric Field, = ion charge, = thermal energy, = diffusion coefficient
Electric Field
D
E-field
Plots created using desmos.com

## Slide 6: Optimizing/Testing Different Gas Mixtures
Goal: Explore gas mixtures maximizing target gas maintaining negative ion benefits
Target Gases: Xe, Ar, He, CF4 NID gases: SF6 and CS2
  Of interest to Migdal searches, Directional Dark Matter searches, Neutrino Studies, etc
Properties of interest for Noble Gas NID TPCs:
  Diffusion = Track broadening from stochastic motion within the gas  NID is narrower
  Mobility = Proportionality constant between drift velocity and field  NID is slower
  Gain = Stable operation and amplification capability  NID has lower gain but higher stability
  Attachment Length = Mean distance before electrons are captured in the gas  Must have short attachment length

## Slide 7: The Detector
N.S. Phan et al 2017 JINST 12 P02012

## Slide 8: Relative Gains
Peak lies at 5.9 keV
Strongly electronegative SF6 and CS2 ions must be stripped before amplification
CS2-based mixtures had higher gains, in general, than SF6-based mixtures
20% for CS2 and 25% for SF6
Stable operation resolving 5.9 keV peak from 55Fe with as little as 3 Torr SF6 and 5 Torr CS2!
All numbers in labels are in Torr
All numbers in labels are in Torr
Notes: Pitch 0.5mm hole diam 0.3mm

## Slide 9: Laser-based Measurements
60 cm
55Fe
N2
RFI Signal induced by Laser firing  t0
Signal from charge cloud  ta
Current [au]
19+1 Torr Xe+SF6
SF5-
SF6-

## Slide 10: Mobility
  N and No are gas density in detector and at STP, vd is drift velocity, E is Electric Field
Mobilities are roughly 2 orders of magnitude lower than in the pure noble gases
Many minority species were noted with mobilities around ~10-20% of the primary species
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED* () | NID ()
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Preliminary
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/

## Slide 11: Mobility
  N and No are gas density in detector and at STP, vd is drift velocity, E is Electric Field
Mobilities are roughly 2 orders of magnitude lower than in the pure noble gases
Many minority species were noted with mobilities around ~10-20% of the primary species
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED* () | NID ()
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Preliminary
11
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/

## Slide 12: Waveform Shape
Fitting Functions Used to model Diffusion (and attachment)
Gaussian:
Exponentially Modified Gaussian:
Step + Gaussian:
Current [au]
Current [au]
Current [au]

## Slide 13: Longitudinal Diffusion
  DL is longitudinal diffusion coefficient
Diffusion can be suppressed by ~ an order of magnitude with as little as 1 Torr SF6 or 5 Torr CS2
In many cases it’s nearly thermal!
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED Dlong* () | NI Dlong ()
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
13
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/
Preliminary

## Slide 14: Aside: Attachment in CF4

## Slide 15: Aside: Attachment in CF4
Multiple peaks?
  Can we measure the different species?
    Extract the electron energies right before capture?
    Do they match the cross-sections?
Exponential leading edge
  Can we measure attachment?
I. Iga, M. V. V. S. Rao, S. K. Srivastava, and J. E. Nogueira, Z. Phys. D 24, 111 (1992).

## Slide 16: Aside: Attachment in CF4
Multiple peaks?
  Can we measure the different species?
    Extract the electron energies right before capture?
    Do they match the cross-sections?
Exponential leading edge
  Can we measure attachment?
I. Iga, M. V. V. S. Rao, S. K. Srivastava, and J. E. Nogueira, Z. Phys. D 24, 111 (1992).

## Slide 17: Aside: Attachment in CF4
By measuring the exponential portion of the waveform, we reconstruct measured attachment to within 8%
L. G. Christophorou, J. K. Olthoff, M. V. Rao, J. Phys. Chem. Ref. Data 25, 1341–1388 (1996)
S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/
Preliminary
Preliminary

## Slide 18: Aside: Attachment in CF4
By measuring the exponential portion of the waveform, we reconstruct measured attachment to within 10%
L. G. Christophorou, J. K. Olthoff, M. V. Rao, J. Phys. Chem. Ref. Data 25, 1341–1388 (1996)
S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/
This confirms that the exponential component in waveforms corresponds to attachment!
Preliminary
Preliminary

## Slide 19: Attachment Length in CS2 Mixtures
Attachment could only be measured in a subset of the data
CS2 + Ar and CF4 mixtures had large attachment lengths!
Consequences of high attachment for tracking detectors:
Exponentially modified waveforms along drift axis
“Mixed Drift” waveforms if drift length too short
  Leads to waveform distortion
  Leads to mixed gain for ED and NID components of the waveform
Preliminary

## Slide 20: Conclusions
Negative ion drift properties in mixtures of Xe, Ar, He, and CF4 with either SF6 or CS2 have been measured with very low partial pressures of the NID component
Stable gain for Fe-55 peak noted in many of the mixtures
Diffusion was suppressed by ~1 order of magnitude
Mobility was slowed by 2 orders of magnitude
In some cases, attachment length could also be measured!
Fermilab/DOE
GIRA Award
Awarded to E.Tilly
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED Dlong* () | NI Dlong ()
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/

## Slide 21: Backups

## Slide 22: The Future of these studies
Paper coming soon!
Development of a novel low-pressure NI TPC
  10cm x 10cm 2D strips at 200 μm pitch
    Gas Electron Multiplier (GEM) at 140 μm pitch to amplify the signal from the tracks
  Front-end electronics assembled, adapted, tested and characterized with collaborators at Boston University
Alex Madorsky
Lila Smith
Ed Kearns

## Slide 23: Contaminants in the CF4
Detector was opened in May, right before this data was taken
After each measurement, detector was pumped on continuously until the next measurement
Clear evolution of right-hand side and relative peak heights of the 2 dominant peaks

## Slide 24: Minority Species Area
Preliminary
Charge Ratio is defined as the area under the minority peak divided by the area under the primary peak

## Slide 25: Measuring Electron Energy
Under a very simple assumption:
We can use the area ratios to get approximate electron energies (pre-capture)
  Note: different electronegativities mean these two species probably have different gains
    Thus, this is more likely an upper limit on the energy
Preliminary

## Slide 26: Dealing with Water
Small amounts of water in detector lead to ‘water-shelves’ on left side of waveform
Compromises measurement of minority area and diffusion sigma of main peak
Include 1 or 2 step functions in fit:
  For minority area:
  For main peak diffusion:

## Slide 27: Exponentially Modified Gaussian
λ = mean free path of attachment (i.e. attachment length)
σ = diffusion
Fit Residuals
Fits well at all measured
Has a fairly small ‘good-fit’ region

## Slide 28: Bridging the Gap Between Exponential Fit and EMG
Exponential fits on CF4 waveforms reproduced Christophorou’s recommended attachment length to within 8%
Measurements made in Ar+CS2 found very good agreement between exponential and EMG fits 
EMG fits were chosen instead of exponential fits in order to measure both attachment and diffusion width
  Exponential fits could not be verified on waveforms with
    This region falls roughly in our EMG ‘good-fit’ region, thus it was straightforward to use EMG results

## Slide 29: Light Yield in NID
Courtesy of D. Loomba RD51 Collab. Meeting 6/14/22

## Slide 30: Negative Ion Species Cross Sections
Standard capture and dissociation process for SF6:
Standard dissociation processes for CF4:
CS2 is can form 5 different NI species, but none of the cross-sections match well with the measured area ratios.
I. Iga, M. V. V. S. Rao, S. K. Srivastava, and J. E. Nogueira, Z. Phys. D 24, 111 (1992).
L. G. Christophorou, J. K. Olthoff, Int. J. of Mass Spectrom. 205 (1) 27–41 (2001)

## Slide 31: Select Averaged Waveforms with Attachment
40 + 10 Torr Ar + CS2
40 + 5 Torr CF4 + CS2

## Slide 32: Energy Resolution
Preliminary
Preliminary