## Slide 1: Experimental and Simulation Studies of Non-linear Resonances in the ISIS Synchrotron
Esmaeil Ahmadi
Chris Warsop
Hayley Cavanagh
ISIS Neutron and Muon Source · STFC Rutherford Appleton Laboratory
Session A-4 · Beam Loss and Halo Dynamics · Oxford · 2 October 2026
SPACE CHARGE 2026 · 7TH ICFA BD MINI-WORKSHOP

## Slide 2: MOTIVATION THE ISIS TUNE FOOTPRINT SAMPLES NON-LINEAR RESONANCES
The incoherent tune spread at injection is 0.4 to 0.5 — the footprint simply cannot avoid all the low-order lines
ISIS operation is not about avoiding these resonances — it's about choosing where the footprint sits and how fast particles sweep across the lines
ISIS loss budget
Measurement-based setup on benchmarked models — we are measuring the machine in more detail than ever. Better models give a better basis for operations, improved understanding, and push the high-intensity limit

## Slide 3: Measurement meets the model?
At ISIS the dipole bending radius is small and the aperture large — so fringe fields are strong.
How do we model the machine's nonlinearity?
Sliced model of the lattice
MEASUREMENTS
Does the model reproduce the measurements?
Dynamic tune scan:
A fingerprint of the machine's error content
Up/down crossing asymmetry
Stop band width

## Slide 4: Ramp the tune, record everything, simulate the same ramp(Coasting beam, low intensity)
METHOD
1
Ramp the tune
Dynamic Qh and Qv ramps across the resonance, from below and from above; fiducial-corrected tunes
2
Record the loss
Ring-summed beam-loss monitors plus the intensity monitor, through the crossing
3
Watch the halo
R6HPM1 / R6VPM2 profile monitors: tails and halo forming as the beam crosses
4
Simulate the ramp
The identical dynamic tune ramp in Xsuite (two trim families) — not a static tune grid
Q ramp
Beam loss while approaching the resonance
Beam Profile (RGI)

## Slide 5
Sextupole compensation of the residual 3Qₓ = 13 error
Beam loss vs Qx along the ramp
Beam profile with residual
Sextupole exciting 3Qx=13
Beam profile after sextupole compensation
3=13
Nonlinear model calibration
Loss from residual sext error
Over drive with sextupole
Compensate by one DC sextupole
Qx=4.333
Tune ramp direction

## Slide 6
Octupole compensation of the residual 4Qₓ = 17 resonance
BLM and intensity vs Qx across the 4Qx = 17 crossing
A single DC octupole at 50 A partially compensates the crossing — k₃L = 1.10 m⁻³ at the null (0.15701·I·L_eff / Bρ, L_eff = 0.1719 m)
Beam profile with residual
octupole
Beam profile after octupole compensation
Loss from residual octupole error
4=17
Nonlinear model calibration
Qx=4.25
Tune ramp direction

## Slide 7
Sextupole-driven third-order resonance:
For:
Octupole-driven fourth-order resonance:
Residual machine error as a phasor:
The trim magnet also generates its own resonance-driving term:
Why one magnet is enough: 13 and 17 are not multiples of P = 10, so symmetric magnet families cancel at these harmonics — the residual is symmetry-breaking, and a single symmetry-breaking trim can null it
Null condition:
Compensation theory: one phasor per resonance

## Slide 8
Modelling nonlinearity near resonance 3Qx=13
Initial distribution from fitting profile monitor data
The initial coasting beam is a hollow beam.

## Slide 9
Modelling nonlinearity near resonance 3Qx=13
simulation
experiment
Profile:
Beam survival
Only the compensating sextupole is included in the model.
Intensity (N=8.5e11pp)effect included via PIC calculation
Initial distribution
Final distribution (Experiment and model)

## Slide 10: Modelling nonlinearity near resonance 3Qx=13
Phase space near resonance with only sextupole
The separatrix shrinks as the tune ramps — particles are peeled off along it.

## Slide 11: Modelling nonlinearity near resonance 3Qx=13
Additional fixed points appear when the octupole error is added
Appearing more fixed points by adding octupole error to the model

## Slide 12
Modelling nonlinearity near resonance 3Qx=13
the predicted octupole error had to be increased by a factor of two to fit the model to experiment.
simulation
experiment

## Slide 13
How 3Qx=13 compensation works with increasing beam intensity
N=8.0e11 ppp
N=1.5 e12 ppp
N=3.3 e12 ppp
N=2.0 e12 ppp

## Slide 14: Tune footprints under space charge at different tune points
The footprint touches 3Qx = 13 before the set point does, so the beam crosses a resonance the tune programme never does
Set tune

## Slide 15: Phase space near resonance during tune ramp
Zero intensity
Intensity = 8.5×10¹¹ ppp
3Qx = 13 island chain sweeps through the beam and transports trapped particles to large amplitude — with space charge the islands broaden and carry more of the core.
Tune ramp direction

## Slide 16: Summary and conclusion
Measured tune loss maps fingerprint the machine: loss concentrates on 3Qx = 13 and Qx + 2Qy = 12, with a strong up/down crossing asymmetry — the observable everything else must explain
One DC magnet per resonance: a single sextupole at 40 A flattens 3Qx = 13; a single octupole at 50 A nulls 4Qx = 17 — coasting beam, tunes held; |f₃₀₀₀|, |f₄₀₀₀| of the bare machine measured at the nulls
The residual error reproduces the crossing by chromatic selection — mechanism right, magnitude wrong: the same sextupole strength does not give the same loss in the simulation
Measurement-anchored PIC: the footprint reaches 3Qx = 13 before the set point does— redistribution starts early and ends in a flat halo plateau.
The mechanism is resonant trapping–transport: the beam deforms into the 3Qx = 13 triangle and trapped particles ride outward; space charge broadens and feeds the chain
Next: Study stopband position, coherent vs incoherent — a stability diagram to optimize the operational tune program.

## Slide 17
Add space charge: measurement-anchored PIC
Solver
Xsuite PIC on the same dynamic tune ramp · averaged 2.5D FFT solver · 200 space-charge interaction nodes · verified against internal deposition, field and kick tests
Beam, anchored to monitors
Horizontal: fitted painted annulus 48.5–63.2 mm (R6HPM1) · Vertical: fitted hollow profile (R6VPM2) · Bounded parabolic δ, edge 3.0×10⁻⁴, mean 1.55×10⁻³
Scan
Intensity 0 → 2.5×10¹² ppp across the 3Qx = 13 crossing, multi-seed ensembles
Self-consistent kicks distributed around the ring; core–halo charge density solved each pass

## Slide 18: MAGNET MODELLING
Limited measurements available for ring magnets
Matched OPERA simulations to measurements
Produced models of each magnet type
Incorporating non-linear multipole components into simulations, including fringe fields
  Better TEAPOT/PTC PyORBIT models
Q QT Q QT RF Q BF (dipole)
One of 10 ISIS Super periods
Improved fringe fields
Dean Adams, Iker Rodriguez, Steve Jago et al.
ISIS Combined Function Dipole
ISIS Quadrupole

## Slide 19: Space charge with waterbag distribution