## Slide 1
Notes: To edit the background image, select ‘Format’ from the PowerPoint menu and ‘Slide Backgound’ from the drop-down menu. Within the new list of options that appears on the right of the screen, select the ‘File’ button under ‘Insert picture from’ and select your image from your file browser.

## Slide 2: Benchmarking Experience with PTC-PyORBIT for High-Intensity Synchrotron Studies
Haroon Rafique, Chris Warsop
7th ICFA Space Charge Workshop
02.10.26
B: Machine Design and Numerical Modelling of Beam Dynamics
B-2: Benchmarking and Experiments
How we can confidently utilise ‘AI’ to support benchmarking

## Slide 3: Contents
What is PTC / PyORBIT?
What do we use it for?
History
Compiling PTC-PyORBIT3
Benchmarking
3

## Slide 4: What is PTC-PyORBIT?
ORBIT
Macro-particle simulation code developed by SNS @ ORNL (+ CERN, GSI) for single bunch particle tracking with physics processes
PTC-ORBIT
2010 developed @ KEK (E. Forest, A. Molodeozhentsev)
PyORBIT
Python wrapping of (C++) ORBIT: used python 2.7 with custom C++ and MPI bindings, original code uses TEAPOT tracker, PTC integration carried over from PTC-ORBIT
ESS developed Python 3.0 version (referred to as PyORBIT3) in 2023
  Still under active development and usage by multiple facilities
PTC-PyORBIT
2017 (ish) forked by CERN (+ PTC library) for LIU (H. Bartosik, JB. Lagrange, et. al.)
Benchmarked on CERN injectors for various space charge studies
@ ISIS:
  ORBIT code used for beam dynamics, later TEAPOT-PyORBIT (python 2.7)
  PTC-PyORBIT (python 2.7) used since 2020, running on SCARF (HPC)
PTC
Single-particle accelerator optics/tracking code developed principally by Etienne Forest (KEK), with major CERN collab/integration by Frank Schmidt et. al.
Fortran 90 symplectic integrator / ‘kick code’ in similar element-by-element tradition to TEAPOT, SixTrack.
Element models integrated symplectically with user selectable integration order / slicing, allowing controllable numerical accuracy.
Built around Forest’s Fully Polymorphic Package (FPP)
  Variables can represent ordinary floating point numbers or Taylor Series
  Enables high-order transfer maps, differential algebra/TPSA, Lie methods and normal form analysis useful for tracking and non-linear optics
Detailed geometrical representation of accelerator
  3D magnet placement / orientation
  Access to optics quantities inside thick elements
  Sector and rectangular bends, recirculators and other non-trivial beam-line topology
  Forward and backward propagation
Integrated into MAD-X as MAD-X/PTC, giving MAD-X access to PTC tracking, higher order maps, and nonlinear optics. Also integrated into BMAD.
PTC provides the accelerator model and tracking,
PyORBIT provides the macro-particle beam and collective effects

## Slide 5: What do we use PTC-PyORBIT for?
Goals:
Understand the accelerator to improve operation (reduce losses / increase efficiency)
Develop end-to-end digital twin for operational optimisation and training humans to operate
PTC-PyORBIT used for ISIS RCS:
Operational lattice model development
  Defining the bare lattice
  Misalignment studies
  Injection painting studies
  Tune control
  Misalignments
High intensity studies
  Resonance crossing studies
  Non-linear dynamics
PTC-PyORBIT is one of our tools for high intensity RCS beam dynamics studies
Simulated (left) and measured (right) horizontal profiles for similar painting parameters
Benchmark: Code vs Measurement behaviour

## Slide 6: 2025: Python 2.7 obsolescence
Can no longer run legacy PTC-PyORBIT on newer systems (required for ‘security’)

## Slide 7: 2025: Python 2.7 obsolescence
Can no longer run legacy PTC-PyORBIT on newer systems (required for ‘security’)
Need to fit PTC (Fortran90 wrapped in C++ wrapped in python) into PyORBIT3

## Slide 8: LLMs and Agentic AI
LLMs:
ChatGPT
Gemini
Meta AI / Muse
Copilot
Claude
Grok
Deepseek
Qwen / Qianwen
Doubao
Le Chat
Kimi
Agentic AI:
ChatGPT Work / Codex
Gemini Spark
Muse
Claude Cowork
Copilot + Agents
Manus
Genspark Super Agent
Perplexity
GitHub Copilot coding agents
Cursor
Devin / Cognition
Z.ai / GLM
Google Antigravity
 | Large Language Model (LLM) | Agentic AI
What is it? | Model trained on text/code to understand context and generate useful response | System using LLM for reasoning and planning to take actions towards a goal
Typical interaction | Prompt -> Response | Goal -> Plan -> Act -> Inspect -> Adapt -> Repeat
Can it use tools? | Not inherently | Usually: code execution, files, web, APIs, databases, other models/agents
State / workflow | Primarily responds to current context | Can maintain task state and execute multi-step workflows
Accelerator Example | “What is the SIS18 frozen space charge benchmark?” | “Plan a new repository for the complete SIS18 benchmark using PTC-PyOBIT3, based on the completed PTC-PyORBIT2.7 SIS18 benchmark repository, using the website reference plots to produce side-by-side outputs. Use the superpowers brainstorming skill, the existing repository is here …, the agent should start with step 1 and not progress until the user confirms the result.”

## Slide 9: Human vs AI
Learned meson build
Support from ISIS Scientific Computing (Dr. Sam Tygier)
StackOverflow
Debugging with LLMs (browser based)
Successful compilation after intermittent effort over months
Runtime segmentation fault
  Didn’t have time/resource to resolve

## Slide 10
Human vs AI
Using agentic command line interface (CLI)
Iterative approach needed
  AI is not intelligent
Developed good practice
  AI requires robust and rigid safeguards, rules, objectives, resources (repos, documentation, instruction)
Able to achieve more than initial intention
  Wrapped PTC in python standalone (pyPTC)
  Compiled PTC-PyORBIT3
  Exposed more PTC functionality to PyORBIT
  Developed better tests/benchmarks
Made mistakes
  More than a human (?) but different types
  Human must remain authority
  Regular guidance → Documented rules

## Slide 11: PyPTC
Standalone python library wrapping PTC
Provides independent tracking/benchmarking asset
GitHub Repo: https://github.com/HaroonRafique/PTC/tree/master/PyPTC
Apertures agree between design, MAD-X, pyPTC
Misaligned orbits: expected path difference inside PTC thick elements
Benchmark: Code vs Code consistency
ISIS RCS: 6 Scintillator BLMs inside each main dipole have shown localised loss. Ops need for modelling trajectories inside thick elements
Notes: Used Agent to wrap PTC in python, exposed parts not previously connected to PyORBIT
Benchmarked against cpymad – expected difference in orbit inside thick elements observed

## Slide 12: PTC-PyORBIT3 Benchmarking
Aperture consistent between all codes
Chromaticity behaviour similar between model and measurement
Consistent results between code versions
PTC-PyORBIT(2.7)
PTC-PyORBIT3
Apertures agree between design, MAD-X, PTC, TEAPOT
Bare tunes in agreement with measurement by design
Benchmark: Code vs Code consistency
Benchmark: Code vs Measurement Behaviour
Notes: Used agents to compile PTC with PyORBIT3 in mesonbuild
Additional PTC functionality exposed to PyORBIT3
Benchmarked linear optics and apertures etc

## Slide 13: SIS18 Frozen Space Charge Benchmark

## Slide 14: PTC-PyORBIT3: SIS18 frozen space charge benchmark
Step 1: validate that all codes reproduce the same third-order-resonance Poincare topology and dynamic-aperture boundary with frozen space charge
Step 2: Sextupoles off, benchmark amplitude dependent tune shift from frozen space charge
Step 3: Sextupoles on at Qx=4.338 to verify the combined space charge and non-linear detuning before islands enter sampled range
SIS18 Benchmark: G. Franchetti, S. Machida, I. Hofmann
HB06 Paper
Notes: Performed the entire SIS18 benchmark without writing any code
Only possible due to having the PTC-PyORBIT2.7 benchmark repo – LLMs are excellent at porting code, bad at physics

## Slide 15: PTC-PyORBIT3: SIS18 frozen space charge benchmark
Step 4: Move closer to 3rd order resonance at Qx = 4.3504 to expose amplitude dependent tune structure associated with islands
Step 5: Compare space charge plus sextupole phase space topology, including central orbit, physical extent, and three stable islands
Step 6: Follow 1 particle through slow 15,000 turn synchrotron oscillation to test adiabatic resonance trapping through its normalised horizontal invariant
SIS18 Benchmark: G. Franchetti, S. Machida, I. Hofmann
HB06 Paper

## Slide 16: PTC-PyORBIT3: SIS18 frozen space charge benchmark
Step 7: Increase synchrotron tune to Qs = 10-3 to show transition from adiabatic trapping to fast scattering
Step 8: Extend fast-regime single particle case to long storage and compare resulting scattering/trapping action evolution across codes
Step 9: Track a full Gaussian bunch at Qs = 10-3 to benchmark long term transverse RMS emittance growth from the collective trapping/scattering dynamics
SIS18 Benchmark: G. Franchetti, S. Machida, I. Hofmann
HB06 Paper

## Slide 17: PTC-PyORBIT3: PIC space charge benchmark
Coasting KV (Kapchinskij-Vladimirskij) distribution
  Exact self consistent solution of the Vlasov-Poisson system for a beam in linear periodic focusing, with its self-generated space charge field remaining linear and preserving the distribution.
  No longitudinal variation -> no variation in line density
  Expect a tune depression, but no tune spread
  Tune depression linearly dependent on Intensity

## Slide 18: Agentic AI approaches to benchmarking
Convergence testing
  How many macro-particles are needed to resolve behaviour?
  What space charge grid size best balances prediction and run time?
  Needs well defined metrics
Test: Can I perfectly match a KV distribution?
  Used to perform convergence on initial distribution to minimise; beta-beating, emittance growth, and centroid motion
Things Agentic AI does well (with the correct guidance)
Code porting
Automated testing
Implement existing well documented benchmarks
Applying working methods to new environments

## Slide 19: Lessons from Agentic AI usage
Set rules, boundaries, goals, dependencies, expectations in AGENTS.md: keep it focussed
  Rule: Read the AGENTS.md, WORK_DIARY.md, and README.md files before any execution, refer to these files and store important information in the relevant file to minimise dependency on context windows
Work in Git repositories; Agents delete a lot of useful things that have to be retrieved
  Rule: All completed code changes and generation of input/output artefacts should be committed as separate git commits, the user should be prompted for confirmation before committing any files larger than 1MB
Store all prompts and summaries of agent outputs in a WORK_DIARY.md: record decisions, process and reasons behind them, constraints that may change in time or with further development
  Rule: All prompts and summaries of Agent outputs must be stored in the timestamped WORK_DIARY.md for provenance, the Agents.md should be updated with rules and constraints as provided by the user, and the README.md file should be kept up to date by the agent without prompting as part of each prompt resulting in file changes.
Don’t rely on the ‘context window’: store plans in .md files
  Rule: Store complete plans in .md files, refer to these in the README.md, and AGENTS.md, including their status. Ensure that these plan .md files are updated as part of their implementation.
Use Superpowers and Skills
  Rule: Use the superpowers skills in all execution, this can be found in <directory>
Don’t use agents to run simulations
  Rule: All simulations should be run by the user, the agent should implement all simulations with smoke tests to debug using small particle numbers, turns, grid sizes, etc. to minimise unnecessary usage

## Slide 20: Summary
Porting legacy codes to modern frameworks seems to be a recurring theme in my career
  Complex, tedious, time consuming, requires dedicated commitment

## Slide 21: Summary
Porting legacy codes to modern frameworks seems to be a recurring theme in my career
  Complex, tedious, time consuming, requires dedicated commitment
Evidence based approach to understanding, porting, wrapping, compiling, and benchmarking Acc. Phys./S.C codes with Agentic AI
  LLMs are well suited to such language-based problems, not to be trusted with much else
  Agentic AI (LLMs that can execute commands to achieve goals) are better suited
    Requires very clear boundaries, rules, babysitting
    Copilot – humans must define correct, provide feedback, direct investigation, be authority

## Slide 22: Summary
Porting legacy codes to modern frameworks seems to be a recurring theme in my career
  Complex, tedious, time consuming, requires dedicated commitment
Evidence based approach to understanding, porting, wrapping, compiling, and benchmarking Acc. Phys./S.C codes with Agentic AI
  LLMs are well suited to such language-based problems, not to be trusted with much else
  Agentic AI (LLMs that can execute commands to achieve goals) are better suited
    Requires very clear boundaries, rules, babysitting
    Copilot – humans must define correct, provide feedback, direct investigation, be authority
Working with code-aware copilots, we can focus more on the science
  New approaches and methods to be considered: trust and provenance are key
  Plan to use similar approach to systematically benchmark suite of codes at ISIS

## Slide 23: Summary
Porting legacy codes to modern frameworks seems to be a recurring theme in my career
  Complex, tedious, time consuming, requires dedicated commitment
Evidence based approach to understanding, porting, wrapping, compiling, and benchmarking Acc. Phys./S.C codes with Agentic AI
  LLMs are well suited to such language-based problems, not to be trusted with much else
  Agentic AI (LLMs that can execute commands to achieve goals) are better suited
    Requires very clear boundaries, rules, babysitting
    Copilot – humans must define correct, provide feedback, direct investigation, be authority
Working with code-aware copilots, we can focus more on the science
  New approaches and methods to be considered: trust and provenance are key
  Plan to use similar approach to systematically benchmark suite of codes at ISIS
pyPTC available as standalone access to polymorphic tracking
PTC-PyORBIT3 compiled with meson build, benchmarking ongoing
PTC-PyORBIT3 SIS18 benchmark completed
Question: What does the future of modelling look like?

## Slide 24
Thank you
Questions?
Connect with me on LinkedIn
Haroon.Rafique@stfc.ac.uk
2024 RAL Open Days: ISIS Target Station 2 Accelerator Zone #WheresWally #WheresWaldo

## Slide 25: Abstract
PyORBIT has recently been ported to Python 3 and migrated to a Meson-based build system. This creates both an opportunity and a practical challenge for compiling PyORBIT together with the PTC libraries, which enable realistic lattice tracking, including nonlinear machine effects, within multi-particle space-charge studies.
This contribution will discuss ongoing work and experience with PTC-PyORBIT workflows, motivated by ISIS RCS applications including injection painting and chopped-beam measurements. These examples will be used to discuss benchmarking against previous simulations and machine data, together with practical lessons from compiling, validating, and applying PTC-enabled PyORBIT workflows in a Python 3 environment.