## Slide 1: Benchmarking PIC Simulations at the SNS Beam Test Facility
October 2, 2026 | Space Charge 2026
Tony Wood
Oak Ridge National Laboratory
Notes: - improved distribution-level modeling is important for SNS
BTF provides measurements that we can benchmark models against
Pick up from there and talk about the status of the benchmarking effort

## Slide 2
The Beam Test Facility
Initial Beam
Final Beam
Diagnostics reconstruct the initial beam
Measurement tests the prediction
Measurement
PyORBIT v3.1
x–x′
y–y′
Notes: - BTF is ~10m
- equipped with diagnostics capable of HDR measurements of initial/final beam
- dual slit and camera system to reconstruct transverse phase spaces
1. Initial diagnostic suite reconstructs the measured upstream transverse and longitudinal phase spaces.
2. PyORBIT transports the assembled input distribution through the BTF model
3. The measured phase space at the end provides the downstream benchmark.
Quadrupoles are all linear fields. All nonlinearities present in simulation come from space charge.
The small downstream heatmaps show the matched horizontal case as an example.
Diagram has 2 cameras; we mostly uses the one camera pointing down the dipole and changes between two gain setting
The HDR measurements are 3x 2D measurements for the initial beam.
- Going up in dimensionality sacrifices dynamic range.
- 4D measurements indicate that coupling between transverse coordinates is small.
- 6D measurements sacrifice
We’re maybe smearing out the long. emittance. We usually take the measurement from a single transverse slice; doesn’t really seem to make a huge difference if we do a 4D scan to map out the full space. The most important feature is the energy spread of the initial beam, which is current dependent.

## Slide 3: Outline
Given the measured initial beam, how well do the models predict the downstream phase spaces?
How does model agreement look across different simulation frameworks?
  e.g., PyORBIT vs. ImpactX
What are the gaps in our models?
Notes: - How well do models generalize for a variety of optics settings?
- What are the gaps in our models that prevent us from describing the tails of these distributions?

## Slide 4
PyORBIT Nominal Configuration
Component | Specification
Beam energy | 2.5 MeV
Beam current | 50 mA
Numerical resolution | 100 million macroparticles
Space charge | 3D FFT w/ multi-bunch solver, 64x64x64 grid
Quadrupoles | Standard: Soft-profile PMQs, Hard-profile EMQs Pure quadrupole fields
Notes: Put plot of the soft edge vs. hard edge profile.
The standard configuration uses hard-edge EMQs and soft-edge PMQs.
Frequency is 402.5 MHz
- We do not use full field maps because maps are missing for the Radiabeam quadrupole family. For the family with available maps, the differences were found to be negligible.

## Slide 5
How we compare measurement and model
PyORBIT output is projected onto the measurement grid and cropped to the measured range.
Each complete 2D profile is normalized to peak and overlaid with log contours for shape comparison
Contours: log10(f / fmax) = −0.05, −1, −2, −3, −4 -> 10%, 90%, 99%, etc.
Core shape checks dominant transport. Outer structure probes nonlinearities and halo
Notes: The paired plots show the matched horizontal phase space on the same measurement grid and range. The heatmaps and log contours are independently peak-normalized. Core shape checks dominant transport; the outer structure shows where nonlinear fields, scraping, offsets, or halo population may matter.
Carry the. contours through to other plots

## Slide 6
Data vs. Model Comparisons
Increasing mismatch
The model captures the core across the three cases, while differences grow in the outer contours.
Contours: log10(f / fmax) = −0.05, −1, −2, −3, −4
Notes: abilty to measure and benchmark against a variety of optics cases
Shown here demonstrates the effect of introducing varied levels of mismatch in the fodo line

## Slide 7
Quadrupole and energy uncertainties don’t cover disagreement
Gray contours are a visual sensitivity envelope
Next: nonlinear field components and transverse offsets.
Contours: log10(f / fmax) = −0.05, −1, −2, −3, −4
Notes: The matched x-x' comparison is shown. Gray contours are a representative subset of Gaussian parameter throws: quadrupole strengths use sigma_PMQ = 0.2% and sigma_EMQ = 0.5%; beam energy uses sigma_E = 0.01 MeV. Black is the nominal PyORBIT v3.1 result and ochre is the measurement. The contour spread is a sensitivity envelope, not a confidence region. These two sampled uncertainties do not span the observed data-model difference. Next hypotheses include nonlinear field components and transverse offsets.

## Slide 8: Cross-code benchmark with ImpactX
Core agrees well up to 90% of the beam
Beyond: modeling differences start to appear in the tails  appears to be tied to energy spread.
Contours: log10(f / fmax) = −0.05, −1, −2, −3, −4

## Slide 9
Summary
• The BTF enables us to benchmark models against measurements
• The models agree well at the RMS-level, but are less successful at predicting the evolution of the full beam distribution
5D measurement available on Zenodo:
Hoover, A., Ruisard, K., Aleksandrov, A., Zhukov, A., & Cousineau, S. (2023). Five-dimensional phase space measurement at the Spallation Neutron Source Beam Test Facility (Version 0.1.5) [Dataset]. Zenodo. https://doi.org/10.5281/zenodo.10368144
PyORBIT SNS-BTF Benchmark
Ruisard, K., Hoover, A., & Thompson, T. (2025). SNS-BTF simulation benchmark (Version 0.0.2) [Figure]. Zenodo. https://doi.org/10.5281/zenodo.14902814

## Slide 10: Discussion Points
s-based vs. t-based?
Magnetic field modeling
PyORBIT’s paraxial transport vs. ImpactX’s exact Hamiltonian
Differences in the space charge solve?
  Point-based Green’s function vs. integrated
Is the full 6D initial distribution important?
Contours: log10(f / fmax) = −0.05, −1, −2, −3, −4
Notes: PyORBIT tracks through magnets using exact profiles. Not 100% sure what ImpactX’s SoftQuadrupole does just yet.
BTF bunch large amplitudes and angles -> truncated Hamiltonian possible doesn’t work as well. But then you’d expect worse agreement with data not better…

## Slide 11: Thank you for your attention

## Slide 12
Vertical phase-space uncertainty
Matched y-y′ phase space; gray contours show representative Gaussian parameter throws.
Visual sensitivity envelope, not a calibrated confidence region.
Notes: Highlight stability of first few contours. But the outer portions are pretty sensitive to these relatively small errors.

## Slide 13
BTF Diagnostics
Slit pairs resolve transverse coordinates; the dispersive slit selects energy; the bunch-shape monitor resolves RF phase.
z–ΔE
Notes: We’re maybe smearing out the long. emittance. We usually take the measurement from a single transverse slice; doesn’t really seem to make a huge difference if we do a 4D scan to map out the full space. The most important feature is the energy spread of the initial beam, which is current dependent.

## Slide 14
Measurement and model phase spaces
Cyan contours: log10(f / fmax) = −0.05, −1, −2, −3, −4.

## Slide 15
RMS beam sizes along the BTF
All-soft-edge PyORBIT model for matched, α = 5, and α = 10 optics.

## Slide 16
Hard Profiles w/ SC
Hard-edge optics remove the soft-field-profile difference. Residual outer-contour differences remain.
Notes: This control keeps the same 100-million-particle input, apertures, and single-bunch three-dimensional FFT space charge while replacing the soft-edge quadrupoles with hard-edge models. ImpactX recorded 99,913,460 survivors and PyORBIT 99,913,584, a difference of 124 particles out of 100 million. The control removes overlapping soft-edge profiles but leaves differences in integration and space-charge discretization.

## Slide 17
Hard profiles w/o SC
Contour differences remain without the space-charge solve, so space charge is not their sole source.
Notes: Both runs use the same 100-million-particle input, hard-edge optics, and apertures with space charge disabled. ImpactX recorded 99,986,506 survivors and PyORBIT 99,986,517, a difference of 11 particles. The squared Hellinger distances are 0.001011 horizontally and 0.001953 vertically. The residual can come from element maps, coordinate conventions, lattice splitting, or histogram sampling.

## Slide 18: 6D bunch predicted to have small effect
Initial bunch
Quadrupoles
Dynamics
Hoover et al, High Brightness Workshop, CERN (Oct 2023)
Beam distribution (1D profiles) evolving with/without full 6D beam (simulated):
As inferred from simulations with PARMTEQ initial bunch. We have never tracked a bunch based on full-and-direct 6D measurement!
10-7 (~99.99999%)
10-2
(~99%)

## Slide 19: Iron-core quadrupole model
Initial bunch
Quadrupoles
Dynamics
No gridded 3D fields!
Pure quadrupole field
Soft-edged profile modeled with Enge function
Gradient/current curves from rotating coil measurements
Notes: We’re uncovered errors amounting to 5-10% gradient errors by re-checking old data

## Slide 20: Permanent magnet quadrupoles
Initial bunch
Quadrupoles
Dynamics
Pure quadrupole field
Soft-edge modeled with analytic expression from Halbach
in rotating coil gradient measurement
Halbach permanent magnet quad
9”