## Slide 1: Welcome to the session on Benchmarking and Experiments!
Benchmarking PIC simulations against the SNS Beam Test Facility
Tony Wood, ORNL
Space-charge dynamics in bare IOTA: Benchmarking among simulations and experiment
Nilanjan Banarjee, FNAL
Benchmarking Experience with PTC-PyORBIT for High-Intensity Synchrotron Studies
Haroon Rafique, RAL
Space Charge Effects in the Alternating Gradient Synchrotron at injection energies
Yichao Jing, BNL
Beam Dynamics in the SNS Linac and Beam Test Facility
Kiersten Ruisard, ORNL

## Slide 2: Beam Dynamics in the SNS Linac and Beam Test Facility
October 2, 2026 | Trinity College, Oxford
Kiersten Ruisard
Oak Ridge National Laboratory

## Slide 3: Spallation Neutron Source
2 MW target
0.7 MW to 2nd target station
1.4 MW baseline design
2 MW
All new cavities installed
DTL
CCL
SCL
SCL
RFQ
1300 MeV
186 MeV
2.5 MeV

## Slide 4: Increased beam loss at 2+ MW increases lost beam and radioactivation in tunnels

## Slide 5: Intrabeam stripping loss was a major hiccup in initial commissioning of SNS
A. Shishlo, J. Galambos, A. Aleksandrov, V. Lebedev, and M. Plum, PRL 108, 1 (2012)

## Slide 6: Beam dynamics mechanisms for LINAC beam loss
Dominated by halo
Dominated by
intrabeam stripping
Beam optics (~ bunch size)
Beam loss
design
Real operating point
Model prediction

## Slide 7: Production optics have been empirically tuned away from design
Settings for warm linac cavities from 2015-2025.
(MEBT cavity amplitude settings are approximated, due to missing data)

## Slide 8: Beam is not matched!
Shishlo, LINAC2014
Beam Longitudinal Profile at End of SCL
Shishlo, 2023 HB
Transverse phase space at end of SCL

## Slide 9: MEBT model is also benchmarked – we don’t understand the tails here either
Dots = wire scanner profile measurements
Phase space diagnostic

## Slide 10: Spallation Neutron Source
Ion source
LEBT
RFQ
MEBT
FODO
beamstop
320 m, 1.3 GeV H-
Beam Test Facility
13 m, 2.5 MeV H-

## Slide 11: Extensive phase space diagnostics give detailed picture of initial bunch distribution
Up to 6D phase space
2D high dynamic range
“input bunch”
Hoover et. al (2023). PRAB 26, 064202
5D measurement of initial bunch

## Slide 12: Extensive phase space diagnostics give detailed picture of initial bunch distribution
Up to 6D phase space
2D high dynamic range
“input bunch”
2D high dynamic range
“output bunch”
dipole
slit 1
slit 2
H- beam
0.95 m
2 cameras for range-stitching
H+

## Slide 13: We are currently studying dependence of halo on mismatch and current density
Up to 6D phase space
2D high dynamic range
“input bunch”
rms y [m]
s [m]
Increasing mismatch
Plot shows 5 optics cases with varying level of mismatch:

## Slide 14: Summary
SNS linac model has not been used to explain H- losses
  There is no trusted global model
  We cannot predict or control losses using model (and we have not matched)
Reduce losses by matching
Reduce losses empirically
Reduce losses with model?
2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
SNS Beam Test Facility can validate PIC model for bunch evolution
  Particularly on formation and transport of nonlinear tails and halo
  Some BTF diagnostics being implemented for SNS MEBT
Will better physics knowledge improve operations?
Development of better tools, diagnostics, PyORBIT
BTF beam dynamics project

## Slide 15: Thanks for your attention
Remaining slides show additional materials

## Slide 16
DTL
CCL
SCL
SCL
RFQ
HEBT
402.5 MHz
805 MHz
387 MeV
1300 MeV
186 MeV
2.5 MeV
OpenXAL envelope model is online model
This model is useful for tuning and choosing operating point:
Transverse centroid model is benchmarked for whole linac, model-based orbit correction works (to within 0.1 mm)
Model-based tuning of cavity phases/amplitudes is fast and reproducible
  Re-scaling around tripped cavity achieves accuracy of 1.5 MeV (0.1%)
  Cavity phase/amplitudes known to within 1˚ / 1%
  Require only phase scans to calibrate energy, cavity phase, cavity amplitude
Model for rms Twiss is useful in the HEBT
Phase scan of DTL1 fit with OpenXAL model

## Slide 17: PARMILA – PyORBIT X RMS (3D Waterbag, 3D FFT SC)
1 mA
15 mA
38 mA
Horizontal RMS size

## Slide 18: Transport to WS14 – 6 mA (No Quads – just Drift)
Horizontal
Vertical
Points – three times measurements of WS14 for all last 4 quads off
Red curve – PyORBIT emittance distribution tracking
Simulations show too narrow shapes

## Slide 19: MEBT/DTL/CCL
MEBT1
DTL1
CCL1

## Slide 20: Simulations: Design vs. “Real” RF Settings (PyORBIT)
CCL1
near
end
Horizontal and Vertical RMS sizes do not show anything dramatic
Longitudinal RMS is awful at MEBT and in general
Beam loss started in CCL1

## Slide 21: MEBT model is not consistent across cases/diagnostics
Phase space device
Phase space device
Dots = wire scanner profile measurements

## Slide 22
2D measurement, high dynamic range
MEBT
6D phase space measurement
Hoover et al, High Brightness Workshop, CERN (Oct 2023)
10-7 (~99.99999%)
10-2
(~99%)
simulate
compare

## Slide 23: Predicting loss rates is only part-way to predicting detected losses or radiation
Signals of ionization and neutron detector loss monitors along linac:
BLM
BLM
BLM
Beam 