## Slide 1: Plans for Space Charge Compensation with Electron Lenses at GSI
M. Kirk
GSI Helmholtzzentrum für Schwerionenforschung GmbH
Space Charge 2026, 7th ICFA Beam Dynamics Mini-Workshop, 30th Sept. - 2nd Oct., University of Oxford

## Slide 2: Acknowledgements
GSI:
K. Schulte-Urlichs, K. Thoma*, D. Ondreka, P. Spiller, O. Boine-Frankenheim
FNAL:
G. Stancari
CERN:
G. Khatri
Riga TU:
A. Ratkus, G. Pirkus, A. Moisejevs
Goethe University Frankfurt:
O. Meusel, M. Droba, H. Podlech, S. Artikova, K. Thoma*
University of Oxford:
A. Oeftiger
LLNL:
W. Stem

## Slide 3: Basic concept of an electron lens
Modulation to match longitudinal bunch profiles:
'Toroid'
Main (interaction) Solenoid
Reduced tune footprint (SIS100):
Primary beam (ions):
Compensation by electrons:
Just enough E (ion - e-) to avoid cooling
the primary beam
'Toroid'
Primary beam:
Solenoids
Solenoids†
Artikova, Boine-Frankenheim et al., 2021:
1st publication: Burov et al., FERMILAB-TM-2125, September 2000
† "Gun" and "expansion" solenoid

## Slide 4: Motivation
Primary Beam Intensities at GSI and FAIR |  |  |  |  | 
 |  | p | Ar | Xe | U
Charge number | GSI | 1 | 18 | 48 | 73
 | FAIR | 1 | 10 | 21 | 28
Energy [GeV/u] | GSI | 4.7 | 1.7 | 1.3 | 1.0
 | FAIR | 28.8 | 6.6 | 4.0 | 2.7
Intensity [Ions/s] | GSI | 1011 | 8·1010 | 2·1010 | 4·109
 | FAIR | 1013 | 1012 | 5·1011 | 3·1011
FAIR designed to increase intensity limits of GSI:
  Primary beam intensities up by factor 10-100
  Lower charge states to avoid space charge limit
GSI facility… as injector for FAIR
"Numerical studies for SIS100 have shown that a few symmetrically distributed electron lenses could increase the space-charge limit by up to 50%, while a larger number potentially enables increase up to x 2" [1]
[1] A. Oeftiger and O. Boine-Frankenheim, “Pulsed Electron Lenses for Space Charge Mitigation”, Phys. Rev. Lett., vol. 132, p. 175001, 2024, doi: 10.1103/PhysRevLett.132.175001
Oeftiger et al., 2024 [1]
Later module (> 2028)

## Slide 5: E-Lens Requirements for SIS18
Ion beam envelopes in e- lens section (ELEGANT code):
Synchrotron Cycle
  Parameters determining modulation to superimpose ion and e- bunches
    Tune spread peaks shortly after start of ramp
    Cavity RF and  bunch length vary strongly
Electron Lens Design
  RF-modulated e- gun
    Up to 15 A (peak) electron beam current for space charge compensation
    0.4 - 1 MHz to follow longitudinal bunch profile, required bandwidth 10 MHz
    Transverse homogeneous e- beam density with circular cross section
  Collector
    Reduce e- beam power density by deceleration and e- beam expansion in a cusp-form B-field
    Mitigation of secondary electrons
Injection
Bunching
Accele-ration
Longitudinal Bunch Structure (time)
Evolution of bunch length & RF
Longitudinal ion bunch profiles
Evolution of peak tune spread
Electron lens design underway. Demonstration with SIS18 e- cooler to come
Profiles:
A: Single h RF,
B: dual h RF,
C: Beam blow-up
A
B
C
Cycle time (t)
Solenoid
Solenoid
e- beam
e- beam

## Slide 6: RF-Modulated Electron Gun
'Target' grid
'Honey comb' grid
Electrostatic Analysis:
Max. 10 kV / mm vacuum:
Max. 1.5 kV / mm air:
Gun-Solenoid
Gun-Solenoid
invisible for illustration
1.5 kV / mm
10 kV / mm
Air
Being
assembled

## Slide 7: Electron Collector
Design by G. Pikurs, A. Ratkus and A. Moisejevs, RTU, 2026
Collector Parameter |  | 
electron current, max. | 15 | A
bias potential, max. | -6 | kV
collector area | 1452 | cm2
inner radius , max. | 215 | mm
outer radius, max. | 242 | mm
beam radius | ≥ 215 | mm
DC power deposition, max. | 90 | kW
power deposition within cycle, max. | 30 | kW
chamber height | 66 | mm
weight | >50 | kg
B-field, max. | 0.4 | T
Maximum Power Deposition in Cycle:
E-lens is used at low B of SIS18 cycle thus reducing power deposition by ~0.3
Secondary Electron Mitigation:
Efficiency 99.8%
SE backflow:
11.1 mA
Distribution T C:
This project received funding from the European Union’s Horizon Europe Research and Innovation Programme under GA No. 101290927
-29 kV
0 kV
Electrons
35 keV, 15 A

Additively manufactured

## Slide 8: SIS18 e- Cooler as Test-Bed
Modification of SIS18 e-cooler:
Max. B-field: e- & ion-beam region 0.15 T, gun & collector 0.4 T
CO simulation indicates that the 0.15 T is feasable for experiments
Gun and collector designs adapted to e- cooler
Experiments on e- cooler carried out with more to come.
Questions:
  Kicks to particles from toroids
  e- beam‘s influence on ions
  'Gridded' e- beam current density distribution
  Compensation of coupling between transverse planes
  Resonance compensation
SIS18 e-cooler at present:
Modified SIS18 e- cooler design:
SIS18 closed orbit at 0.15 T, CST  ELEGANT with FTABLE* element:
HS
HS
HS
H-Steerer
(HS)
Solenoid
* Ref. FTABLE: A. Xiao, M. Borland et al., “Tracking particles through a general magnetic field", PAC11
M .Kirk

## Slide 9: Further Reading
S. Artikova, D. Ondreka, K. Schulte-Urlichs, P. J. Spiller, “Design and Beam Dynamics of the Electron Lens for Space Charge Compensation in SIS18”,
IPAC'21, pp. 3614–3617
K. Schulte-Urlichs et al., “Status of the Electron Lens for Space Charge Compensation in SIS18”, IPAC'21, pp. 1880–1883
A. Oeftiger and O. Boine-Frankenheim,
“Pulsed Electron Lenses for Space Charge Mitigation”,
Phys. Rev. Lett., vol. 132, p. 175001, 2024,
doi: 10.1103/PhysRevLett.132.175001
A. Xiao, M. Borland et al.,
“Tracking particles through a general magnetic field”,
Conf. Proc. PAC11
I. Lobach, Y. Li,
“Using neural-network Ansatz for the generating function in the Hamilton-Jacobi equation to obtain symplectic transfer maps for elements with any magnetic field configuration”,
IPAC’26

## Slide 10: History of Electron Lenses for Space Charge Compensation
A. V. Burov, G. W. Foster, V. D. Shiltsev, “Space-Charge Compensation in High-Intensity Proton Rings,” FERMILAB-TM-2125, September 2000
S. Machida, 2001, KEK PS simulation
Y. Alexahin, “Effects of Space Charge and Magnet Nonlinearities on Beam Dynamics in the Fermilab Booster”, PAC 2007, DOI 10.1109/PAC.2007.4440463
M. Aiba, M. Chanel, U. Dorda, R. Garoby, J.-P. Koutchouk, M. Martini, E. Métral, Y. Papaphilippou, W. Scandale, F. Zimmermann, V. Shiltsev, G. Franchetti, “Space-Charge Compensation Options for the LHC Injector Complex”, Proceedings of PAC'07, Albuquerque, 2007, pp. 3390–3392
M. Aiba, “Benchmark of ACCSIM-ORBIT codes for space charge and electron-lens compensation”, CERN, 2008
Y. Alexahin and V. Kapin, “Study of Possibility of Space Charge Compensation in the Fermilab Booster with Multiple Electron Columns,” Fermilab Beams-doc-3108, June 2008
V. N. Litvinenko and G. Wang, “Compensating Tune Spread Induced by Space Charge in Bunched Beams”, Physical Review Special Topics — Accelerators and Beams 17, 114401 (2014)
O. Boine-Frankenheim and W. D. Stem, “Space charge compensation with pulsed electron lenses for intense ion beams in synchrotrons”, Nuclear Instruments and Methods in Physics Research A 896 (2018), 122–128. DOI: 10.1016/j.nima.2018.04.014
S. Artikova et al., “Pulsed electron lenses for space charge compensation in the FAIR synchrotrons”, 2021 JINST 16 P03044. https://doi.org/10.1088/1748-0221/16/03/P03044
Y. Alexahin and V. V. Kapin, “On possibility of space-charge compensation in the Fermilab Booster with multiple electron columns”, Journal of Instrumentation 16 (2021) P03049. DOI: 10.1088/1748-0221/16/03/P03049
The references above are up to about the point when work at GSI began.

## Slide 11: Summary & Outlook
Symplectic transfer map for e-lens*
Resonance and coupling compensation
Electron lens is under development
Electron gun will be ready for testing at GSI
Prototype electron lens in SIS18 synchrotron will follow
* I. Lobach, Y. Li, Using neural-network Ansatz for the generating function in the Hamilton-Jacobi equation to obtain symplectic transfer maps for elements with any magnetic field configuration, IPAC’26

## Slide 12: Reserve slides …

## Slide 13: Transport Simulations with ELEGANT
Lattice with EDRIFTs, CSBENDS (EDGE*_EFFECTS = 3), KQUADS. SOLEnoids at 0 mT. Tunes (4.28, 3.3), 12C6+ 11.5 MeV/u
Single particle in phase space
tracked for 10k turns
1k-ion waterbag tracked for 10k turns
0.3% drop in emittance
Horizontal
Vertical
8 mrad
12 mm
4 mrad
40 mm
92.55 m2
4D RMS emittance vs. turn

## Slide 14: RF-Modulated Electron Gun – Choice of Materials
Body parts: Stainless steel
Insulators: Alumina
Dispenser cathode: BaO, type 311XM by Spectra-Mat Inc.
Modulation grids: Molybdenum or graphite (SIGRAFINE®)
Focusing electrode: Molybdenum

## Slide 15: RF-Modulated Electron Gun
Thermomechanical analysis

## Slide 16: Collector – Stress Distribution
Structural Analysis
Notes: Top fig. total deformation in mm. 0.07 mm max. (top of color scale)
Bottom fig. equivalent stress in Pascals.
[Artjom CAS]
ANSYS (Riga TU)

## Slide 17: Collector - Cusp Design
transverse velocity vs. longitudinal velocity
Cusp field
Approx. 7% losses

## Slide 18: RF-Modulated Electron Gun
Electron gun parts & assembly: NTG GmbH & Co. KG
A
B
A
B