## Slide 1
Lead talk: High-Intensity Linacs
“Proposal of a 1‑ampere deuteron single‑cell linac”
Hiroki OKUNO
MS10 Okuno project PM
RIKEN Nishina Centr for Accelerator-based Science
1995～
Design, Development, Construction, and Operation of Superconducting Ring Cyclotron (Cyclotrons, Superconducting Magnets, and Helium Refrigeration Systems)）
2008～
Development of a Charge-State Stripper System for High-Intensity Operation of the RIBF
Accelerators for Societal Applications:
2015～
Research on the Treatment of High-Level Radioactive Waste (ImPACT Program, Fujita Program)
2021～
Development of n-Type Diamond Semiconductors through Nuclear Transmutation (Canon Foundation)
2023～
Establishment of a Japanese Helium Recycling System (JST PM Training Program) 2024～
Development of Core Technologies for Compact Artificial High-Intensity Muon Production (JST K Program)
2024 Oct. ~ PM for Moonshot goal 10 ”Fusion energy”
Windowless Helium Charge Stripper
The World's First Superconducting Ring Cyclotron
１
How should we design a next-generation highest-intensity linac?
Notes: “Let me begin.
I would like to respond directly to the request from the chair — to discuss how we should design a next‑generation highest‑intensity linac in this session.
Today, I will present our concept for a 1‑ampere deuteron single‑cell linac, developed within the Moonshot Goal 10 program for fusion‑energy research.”
“Before going into the technical details, let me briefly introduce myself because I joined this workshop for the first time.
My background is mainly in high‑intensity accelerator technology — superconducting ring cyclotrons, charge‑state strippers for uranium ion beams, and several accelerator‑based applications.
I should also mention that beam‑dynamics simulation is not my primary specialty. I work closely with colleagues who are experts in this area, and one of my goals in this session is to learn from your experience and understand how we can refine the beam‑physics aspects of this concept.
Since October 2024, I have been serving as the project manager for Moonshot Goal 10: Fusion Energy. This background naturally leads to today’s topic — the design of a highest‑intensity front‑end linac.”

## Slide 2: Contents
Introduction
  Fusion‑science motivation
  Requirement to the accelerator
Proposal of 1-ampere class single cell linac
  no RFQ (can accelerate large size beam)
  Concept of 1-ampere single cell linac
Low beta section
  Ion source + LEBT
  Tune depression(compared with EES and DONES)
  TTF problem (Low frequency rf system and broad)
  Bunching of of 1A beam in 3D simulation
Medium beta section
  Lattice structure
  the 3D bunching simulation, (Solenoid or FODO lattice)
Halo Analysis and Suppression Toward Completion of the 1 A Linac Design
CARA (Cyclotron Auto Resonance Accelerator)
Summary
2
Notes: “Here is the outline of my talk.
I will begin with the motivation from fusion materials science, then describe the requirements for the accelerator.
After that, I will introduce the concept of a 1 ampere single cell linac, followed by the low beta section, medium beta section and halo analysis and suppression toward completion of its design.
I will touch with CARA (cyclotron auto resonance accelerator)

## Slide 3: Motivation: Fusion Materials Science
Fusion reactors require materials that survive extreme neutron damage
High‑flux irradiation → requires high‑power deuteron beams
DONES (125 mA) is currently under construction and will be capable of irradiating materials up to 50 dpa/fpy; however, it is intended only for the irradiation testing of a very limited amount of materials for Euro-DEMO.
1‑A deuteron beam → pathway to next‑generation fusion materials testing
3
Notes: “Fusion reactors require structural materials that can withstand extremely high neutron damage. This is not just a matter of high dpa — the materials must survive under high temperature, high flux, and long‑term exposure.
To evaluate such materials properly, we need irradiation facilities capable of producing very high neutron fluxes over a meaningful sample volume.
DONES will reach 125 mA and about 50 dpa per full‑power year, but only for limited sample volumes. This is an important step, but not sufficient for DEMO‑class qualification.
To expand the irradiation capability and move toward next‑generation fusion materials testing, we need a much higher beam power.
A 1‑ampere deuteron beam at around 40 MeV is one promising approach to achieving this.”

## Slide 4: Comparison of Accelerator Performance Worldwide
Particle ：Deuteron
Output Energy ：40 MeV
Current ：1A
Beam Power ：40MW
Requirements to the accelerator
Energy per nucleon (MeV/u)
For fast neutron
Beam Power
Energy per nucleon (MeV/u)
Average current (mA u)
For Low energy neutron
(Deuteron、1A⇒0.1A, 400MeV)
IFMIF
MS10
Deuteron 1A 40MeV
~x4
ITER NBI
Deuteron 1MeV 20A
4
Notes: “This slide summarizes the global context.
Our target is: 40 MeV, 1 ampere of deuterons, and 40 megawatts of beam power.
This is four times the IFMIF beam power. ITER’s neutral beam injector operates at 1 MeV and 20 A, but that system is designed for plasma heating, not materials irradiation.
So the 1 A, 40 MeV linac fills a unique role as a high power neutron source for fusion materials science.”

## Slide 5
Technical issue: beam size
Plasma
1A beam
RFQ
(radiofrequency quadrupole)
Size of 1A beam >10cmf >> 1cm: typical acceptance of RFQ
Cross sectional view of RFQ
The area which beam can
go through.
RFQ (radio-frequency quadrupole) linacs are widely used as front-end accelerators in the high-intensity, high-energy proton (deuteron) linacs. It works as a buncher of DC beam from ion source, electrical transverse focusing elements, accelerator.
We can’t use RFQ！!
5
Notes: “One of the first challenges is the beam size.
A 1‑A deuteron beam extracted from a cusp‑field ion source has a diameter exceeding 10 centimeters.
In contrast, a typical RFQ aperture is about 1 centimeter.
Therefore, an RFQ cannot be used for a 1‑A front end. We need a different approach.”

## Slide 6
Concept of Single‑Cell Linac for 1A beam
Single-cell cavities + magnetic focusing elements (without RFQ)
Merits：
1: It can accept large beams because it uses magnet focusing elements free from discharge.
2: Low current density owing to the large beam size mitigates space charge force.
3: Voltage and phase of each cell can be independently selected to compensate for the longitudinal space charge effects, and also to implement an efficient bunching function for a
36.5MHz
イオン源
73MHz
219MHz
6
Notes: “Our solution is the single‑cell linac.
Instead of an RFQ, we use single‑cell cavities combined with magnetic focusing elements such as solenoids.
This approach has three advantages:
The large bore can accept large beams without discharge.
The low current density mitigates space‑charge forces.
The RF phase and voltage of each cell can be independently adjusted, allowing RFQ‑like bunching and compensation.
This makes it possible to reproduce the essential functions of an RFQ while maintaining a large aperture.”

## Slide 7
コア
Challenge 1: Development of a Low-Energy Front End Enabling RF Acceleration of Large-Aperture
Challenge 2: Achieving the Required Beam Loss Level (10⁻⁸)
Approach: Develop a new beam halo analysis methodology to meet the beam loss requirement corresponding to 1 W/m.
Challenge 3: Demonstration of a 1-A Deuteron Beam from the Ion source
Challenge 4: Scaling Superconducting RF Cavities to Large Aperture and High Power
Challenge 5: Advancing the Target Concept to the Conceptual Design Stage
Challenge 6: Improving Electrical efficiency of the accelerator
These challenges define the core of the MS10 accelerator R&D project
Key Technical Challenges and
Solutions for a 1-A Deuteron Linac
Limit the beam power
Core
7
Notes: “To realize a 1‑A linac, we need to address several technical challenges.
We need a low‑energy front end with a large aperture.
We must meet the beam‑loss requirement of 10⁻⁸, which corresponds to about 1 watt per meter.
We need to demonstrate a 1‑A deuteron beam from the ion source. We need large‑aperture superconducting cavities. We need a realistic target concept. And we need to improve electrical efficiency.
These challenges define the core of the MS10 accelerator project.”

## Slide 8: Ion source + LEBT(low energy beam transport)
Ion source: A cusp-field confinement type Ion source used for NBI (Neutral beam injector) in Tokamak fusion reactors. Extraction from the multi hole is inevitable.
Beam envelope in the LEBT
(no neutralization is assumed.)
Plan view of LEBTp
Multi-holes for beam extraction (14mmf x 37)
Emittance of extracted beam
X (m)
X ‘(rad)
12p mm mrad
< 25p mm mrad
KV-distribution
Gaussian
studying on beam halo with various initial conditions
This multiple beamlet cause mismatch resulting in Beam halo?
8
Notes: This slide explains ion source and LEBT.
We use a cusp‑field ion source similar to those used in neutral‑beam injectors for tokamaks. Multi‑hole extraction is unavoidable at 1 ampere. — 14‑mm holes, 37 of them —
The extracted rms emittance is around 12π to 25π mm·mrad.
However, multiple beamlets can cause mismatch, and mismatch can lead to halo formation. This is an important topic for further study.”

## Slide 9: Low b section (adiabatic rf capture)
> 90 cells (Single gap with S.C. solenoid)
Longitudinal Beam behavior: Adiabatic rf capture
（DC→bunched beam）
rf ギャップ
2m
超伝導
ソレノイド
Phase（rad)
Phase（rad)
Energy （MeV/u)
All Phase Energy Zoom
All Phase Energy
Energy [MeV/u]
Energy [MeV/u]
Phase [rad]
Phase [rad]
Key issues
(1) Strong space charge forces
Make Tune depression small, placing the beam near resonance conditions.
(2) Transit time factor reduction
Large apertures broaden the energy distribution across the RF gap. Low RF frequency is required to maintain adequate TTF.
(3) Adiabatic capture
RF frequency, gap voltage, and synchronous phase must be carefully chosen.
9
Single gap
S.C. solenoid
Notes: “The low‑beta section consists of more than 90 single‑gap cavities, each paired with a superconducting solenoid.
We use adiabatic RF capture to gradually convert a DC beam into a bunched beam. Simulations show smooth phase compression and stable longitudinal motion.”
Slide 9 — Key Issues in the Low‑β Section
“There are three key issues in the low‑beta section.
First, strong space‑charge forces which make Tune depression becomes small, and the beam can approach resonance conditions. This requires careful lattice design.
Second, the transit‑time factor. Large apertures broaden the energy distribution across the RF gap, so low RF frequency is required to maintain adequate TTF.
Fourth, adiabatic capture conditions. RF frequency, gap voltage, and synchronous phase must be carefully chosen to ensure smooth capture without exciting large oscillations.”

## Slide 10: Tune depression at injection energy
Tune depressions of 1A deuteron linac are large compare with those another high power linac because of large aperture.
10
Notes: “Thanks to the large aperture, the tune depression of the 1‑A linac is much larger than in other high‑power linacs such as ESS or DONES.
This is a major advantage because high tune depression means the beam behaves more linearly and is less sensitive to resonances.”

## Slide 11: Problem of TTF (Transit Time Factor) at injection
Large bore broad E distribution Low rf frequency is required to keep TTF larger
11
36.5MHz
Notes: “Large bore leads to broad energy distribution across the RF gap. To maintain a reasonable transit‑time factor, we need low RF frequencies.
This is why we use RF frequencies around 36.5 MHz in the low‑beta section.”
But this ttf is improved when beam energy increases

## Slide 12: 3D beam envelope simulation in the low b section
TRACK code (developed by P. Ostroumov, et al.,):
that includes the space charge effect and non-linear phenomena owing to this effect
After 3rd cell
After 6th cell
After 9th cell
After 12th cell
Phase (rad)
Phase（rad)
Energy （DW/W)
After 3rd cell
After 6th cell
After 9th cell
After 12th cell
Energy （DW/W)
Transverse beam envelope
without longitudinal s.c. forces
with longitudinal s.c. forces
12
Notes: “We use the TRACK code to simulate the 3D beam envelope including space‑charge effects.
We observe longitudinal distortion and some transverse envelope changes, but overall the beam remains stable.
The acceleration efficiency is about 82 percent with 1‑MeV injection and 25π mm·mrad normalized RMS emittance.”

## Slide 13
Acceleration efficiency 82.4%
Injection Energy 1MeV
Normalized RMS emittance 25πmmmrad
3D beam envelope simulation in the low b section
13
Notes: The acceleration efficiency is about 82 percent with 1‑MeV injection and 25π mm·mrad normalized RMS emittance.”

## Slide 14: To reduce the length of the low-beta section.
Increase Injection (200keV →400keV, 1000keV)
  Improve small TTFs
  Improve efficiency (Cell length (40cm) > βλ/2 (~8cm) at 200keV injection)
IH linac in solenoid or giant RFQ will be study
These studies are going
14
Notes: To shorten the low‑beta section, we are studying several options:
Increasing the injection energy from 200 keV to 400 keV or even 1 MeV. Improving the transit‑time factor. Improving acceleration efficiency. Considering IH linacs in solenoid lattices. And exploring giant RFQ concepts.
These studies are ongoing.”

## Slide 15: Medium b section (10-40 MeV)
Structure of the cavity (30 quarter-wave resonator until 40MeV)
QWR 73MHa
QF or Sol.
QF or Sol.
QD or Sol.
15
Beam bore 200mmφ
Notes: “The medium‑beta section uses 30 quarter‑wave resonators to accelerate the beam from 10 to 40 MeV.
This is a lattice for medium beta section.

## Slide 16
Beam pipe= 5 x σrms ~300mm
Design study of Superconducting Cavity started with the bore from the solenoid based lattice
FODO lattice vs Solenoid based lattice (IMPACT-X)
Beam pipe= 5 x σrms ~120mm
Solenoid field ~ 3T
16
FODO
Solenoid
Notes: These are results of 3d simulations using IMPACTX in the case of FODO and solenoid lattice. We have begun superconducting cavity design based on the solenoid‑focused lattice.
We set the beam pipe size 5 RMS to avoid halo hitting the pipe, which corresponds to about 300 millimeters in the case of FODO 120mm in the case of solenoid.
solenoid lattices show smoother envelope behavior.”
Design study of Superconducting Cavity started with the bore from the solenoid based lattice,120mm

## Slide 17: Halo Analysis and Suppression Toward Completion of the 1A Linac Design
Objective
Halo analysis and suppression for both low-beta and medium-beta sections
Beam dynamics simulation with approximately 10⁸ macro-particles
Support the completion of the 1 A linac design
Physics Issues to be Studied
1. Coherent Resonance
Check coherent resonance using Stop Band Diagram
Identify mechanisms of halo formation
Evaluate impact on beam loss and emittance growth
2. LEBT and Mismatch Effects
Investigate halo generation due to Multi-hole LEBT
Study beam mismatch at section transitions
Quantify contributions to halo growth and beam degradation
Expected Outcome
Understanding of dominant halo formation mechanisms
Validation of beam dynamics design with large-scale simulations
Establishment of halo suppression strategy for the 1 A linac
17
Notes: “To complete the 1‑A linac design, we are performing halo analysis with about 10⁸ macro‑particles.
This large number is necessary because halo formation is a rare but critical event. We need sufficient statistics to evaluate beam loss at the 10⁻⁸ level.
We study coherent resonance, mismatch from the multi‑hole LEBT, and mismatch at section transitions.
The goal is to identify dominant halo mechanisms and establish a suppression strategy.”

## Slide 18
Background
1. This acceleration concept was proposed in the 2000s by Hirshfield and colleagues at Yale University. The original concept targeted beam energies of approximately 1 GeV.
2. Its realization has been hindered by the requirement for a large-aperture, high-field solenoid magnet. Although the concept has been experimentally demonstrated with electron beams, it has not yet been realized for high-current ion beams.
In the present
3. project, the goal is to demonstrate the concept in the non-relativistic energy regime up to approximately 1 MeV (40MeV deuteron).
Key Features
1. Mitigates space-charge concentration in the low-energy section of the accelerator.
2. Enables acceleration of a continuous-wave (CW) beam without bunching, thereby alleviating space-charge effects.
3.Beam extraction without disperse is difficult
4.Provides a compact beam trajectory, with the kinetic energy imparted in the direction tangential to the circular orbit.
イオン源
CARA (cyclotron auto-resonance Accelerator)
sorry for not linac but cyclotron
・Cyclotron frequency = Resonance frequency
→ Resonant acceleration is achieved
・By utilizing a helical beam trajectory, this concept enables compact CW-beam acceleration while mitigating space-charge effects in high-current, low-energy beams.
TE111 in the resonactor
Cyclotron resonance frequency
CARA中の軌道(1例)
18
Notes: “In parallel to 1A ampre, we are studying the CARA concept proposed by Hirshfield at Yale university.
CARA uses cyclotron auto‑resonance acceleration with a helical trajectory.
It mitigates space‑charge concentration and enables continuous‑wave acceleration without bunching.

## Slide 19: Beam Extraction Method from CARA
Acceleration in CARA
(DC Acceleration, Continuous Acceleration）
Cusp Magnetic Field (Rotational Motion → Linear Motion)
Extraction of a Ring-Shaped Beam
Extraction without an Electrostatic Deflector or Stripping Foil
Injection without an Electrostatic Inflector
Beam Intensity Can Be Increased by Orders of Magnitude!
出願日：2025年4月16日
出願番号：特願2025-67406
発明者：奥野広樹、三宅泰斗
Without the Cusp Magnetic Field (Beam Diverges and Is Lost)
RIKEN SRC (Superconducting Ring Cyclotron) Beam Extraction Port: 12 mm
19
Notes: “
Beam extraction from CARA is very important when we use it because Most of the beam energy is in rotational motion.
We have developed a new extraction method using a cusp magnetic field.
It converts rotational motion into linear motion, allowing extraction of a ring‑shaped beam without electrostatic deflectors or stripping foils.
We can expect beam intensity can be increased by order of magnitude

## Slide 20: dCARA (40MeV, 100ｍA!!, deuteron）
7T, 53.4 MHz (CST studio）
DONES length 40m、dCARA length 1.8m
We are investigating why CARA is capable of accelerating such high-intensity beams and evaluating its beam stability.
Cavity(1.8m)
Injection energy 80keV
Final energy 40MeV
20
Round beam in PSI injector 2 cyclotron
Notes: “Here is an example of dCARA:
40 MeV, 100 mA, 7 Tesla, 53.4 MHz, and only 1.8 meters long — compared to 40 meters for DONES.
We are investigating why CARA can accelerate such high‑intensity beams and evaluating its stability.”

## Slide 21: Ion CARA verification test (World’s first)
21
Beam
Recycled 3T MRI magnet
Resonator with a pair of electrodes
We will have the first beam in the autumn of 2027.
1MeV 1mA proton
Notes: We will have a plan to do the world’s first ion CARA verification test.
The preparation is goin on.
The recycled 3T MRI magnet is in preparation of cool-down.
Specially prepared resonator for this test is in fabrication.
We will have the first beam in the next autumn.

## Slide 22: Summary 1
Fusion materials science requires 1 ampere class deuteron beams.
RFQs cannot handle such large apertures.
The single cell linac provides a scalable solution.
High tune depression ensures stability.
Halo suppression is a key research direction.
And CARA offers a complementary high intensity concept.
22

## Slide 23: Summary 2
Three talks in this session.
Jibong Hyun (QST):
Reduction of longitudinal rms emittance through nonlinear space-charge forces
Abhishek Pathak (Fermi National Accelerator Laboratory):
Space-Charge Stability and Beam-Loss Margins in the PIP-II Linac
Dong-O Jeon (Institute for Basic Science):
Parametric instabilities in actual high-intensity linear accelerators
These three presentations focus on instabilities in space-charge-dominated beams, which are regarded as critically important research topics for advancing toward even higher beam intensities.
22
Notes: “The three talks in this session — Hyun, Pathak, and Jeon — focus on instabilities in space‑charge‑dominated beams.
These topics are essential for advancing toward higher beam intensities and closely related to our 1‑A linac program.”

## Slide 24: Questions for discussions from authors
Hirokii Okuno
1: What is the current limit for RFQ for deuteron? (deuteron 500mA?)
2: Solenoid lattice or FODO lattice?
3: Polarity of Solenoid (+++++++ or +-+-+-+- which is better?)
4: Why is the beam from CARA so stable?
Hyun Jibong
1: Can the predicted emittance reduction be confirmed experimentally?
2: Can this mechanism be applied for beam-quality control?
3: Can the concept of the force nonlinearity parameter be extended to predict beam halo formation?
Abhishek Pathak
Dong-O Jeon
My question is whether parametric instabilities are observable in actual circular accelerators, especially high order ones. As I shall present tomorrow, high order parametric instabilities are not observable in actual linear accelerators.
24