## Slide 1: a network of 43Ca+ optical clocks for entanglement-enhanced metrology
A. Agrawal*, S. Chen, E. M. Ainley, A. R. Martinez,
E. Malinowski, J. A. Blackmore, M. Mallweger, D. P. Nadlinger, P. Drmota, G. Araneda, D. M. Lucas, R. Srinivas
Precision physics of Simple Atomic Systems (PSAS), 21 May 2026
Towards
A network of 43Ca+
optical clocks for entanglement-enhanced metrology
Notes: Thanks for the introduction, and to the organisers for giving me the opportunity to speak at this very interesting event.
My background is quite different from that of most people here – I’m here from the Oxford Ion Trap Group which primarily focuses on quantum computing applications, but have adapted our existing setup for entangled spectroscopy.
And I’m happy to point out that we have some preliminary data, [animation] so we can change the title of the talk slightly

## Slide 2: Optical atomic clocks
[1] McGrew et al., Nature 564, 87 (2018)
[2] Safronova et al., Rev. Mod. Phys. 90, 025008 (2018)
Notes: I don't think I need to motivate the importance of atomic clocks here. As you're all aware, optical atomic clocks are some of our most accurate and precise tools for measuring anything humans have ever built.
The last year has been especially competitive, with multiple groups reporting systematic uncertainties at the 10^-19 level

## Slide 3: Ion clocks
Low systematic uncertainty: ~ 10-19 [1]
Higher instabilities (statistical noise)
Entanglement-enhancement: improve from SQL to Heisenberg limit!
[1] M. C. Marshall et al, Phys. Rev. Lett. 135, 033201
Notes: - The performance of an atomic clock is characterised by two main parameters:
- the systematic uncertainty (in the observed laboratory frequency compared to that of an isolated atom)
- and the instability (tells you how long you need to measure to average down your measurement),
ion clocks: easier to isolate from environment, have some of the lowest systematic uncertainties (as shown on previous slide).
But usually only have one or two atoms, short-term instabilties are generally 2-3 orders of magnitude larger than systematics.
Without entanglement, clock stability given by SQL (1/sqrt(N)). With entanglement, Heisenberg limit (1/N), giving gain of sqrt(N)

## Slide 4: Differential spectroscopy
  Navigation
  Properties of dark matter [1]
  Variation of fundamental constants [2]
  Relativistic geodesy [3]
[1] A. Derevianko and M. Pospelov. Nat. Phys., 10(12):933–936, 2014
[2] Safronova et al., Rev. Mod. Phys. 90, 025008 (2018)
[3] McGrew et al., Nature 564, 87 (2018)
(a)
Changing constants
Need ability to compare time and frequency!
Notes: Measurements from a single clock have little use without ability to compare to another equally stable reference -- either for cross-validation, or because it is the inherent quantity of interest, e.g. for navigation, geodesy or fundamental physics searches.
And this is what we are going to focus on today -- frequency comparisons between two independent clock systems

## Slide 5: Ramsey spectroscopy
pulse
pulse
Limited by laser phase noise
Notes: Let me first just reintroduce the fundamentals of Ramsey spectroscopy:
Goal is to measure the detuning of a light field (such as a laser) from a narrow-linewidth transitions
Start with a pi/2 pulse, creating a superposition of the excited and ground state.
Let it evolve for a probe duration T, accumulating a phase proportional to the detuning
Finally closing pi/2 pulse to complete the interferometry, followed by state detection
The clock stability scales as inversely with the Ramsey duration -- longer probe durations give you higher sensitivity.
Can in principle measure the absolute detuning of each clock individually. The difference frequency stability adds in quadratures.
In practice, current technological limitations in laser technology due to laser dephasing generally limit the probe duration to 10s of ms

## Slide 6: Correlation spectroscopy
Common
probe laser
Sacrifice contrast for resistance to common laser phase noise
Notes: For frequency difference comparisons, it is possible to get around laser phase noise limitations using a technique known as correlation spectroscopy.
Interrogate both clocks with the same laser with a simultaneous Ramsey. LPN becomes common-mode to both clocks, and causes 0 and 2 excitation components to dephase. The single excitation subspace, however, is insensitive to common-mode noise.
This evolves with the difference frequency of the two atoms. This enables probes much beyond laser coherence limit by sacrificing 50% contrast (as only half the state participates in this)
Been used in many measurement campaigns to interrogate at lifetime limit

## Slide 7: Entangled correlation spectroscopy
Ramsey delay
Common
probe laser
Notes: Now naturally, question arises, if only the single-excitation component of the state contributes to difference frequency, why can't we just create that state directly?
And you'd be right. We can! Then the sequence looks something like this: First, we entangle two clocks into a Bell state residing in a decoherence-free subspace resistant to sigma z errors.
Let it evolve for the probe duration gaining a phase dependent on the frequency difference of the two clocks.
Then, as with conventional x-spec, use the same laser to do a second Pi/2 pulse and measure the spin parity sigma_z cross sigma_z.

## Slide 8: Comparison methods
State | Entangled | Uncorrelated | Unentangled correlation
Uncertainty |  |  | 
Insensitive to common mode laser phase noise? | Yes | No | Yes
State | Entangled | Uncorrelated | Unentangled correlation
Uncertainty |  |  | 
Insensitive to common mode laser phase noise? | Yes | No | Yes
Notes: So the entangled state gives best of both worlds
1. maintains LPN insensitivity, enabling long probe times like the unentangled x-spec and
2. Doesn't sacrifice contrast
But also,
3. The correlations in the state give a further improvement of sqrt(2) from the Heisenberg limit over the SQL
Practically can gain >20x over uncorrelated clocks and ~2x over unentangled correlation spectroscopy

## Slide 9: Quantum networks
Entanglement enhancement demonstrated locally[1-3]
Entanglement over a network is hard
  High-fidelity (contrast ≈1)
  High-speed generation (maximise duty cycle)
98% fidelity at 300 Hz!
[1] D. Leibfried et al. Science 304, 1476–1478, (2004)
[2] C. F. Roos et al. Nature 443, 316–319 (2006)
[3] E. Pedrozo-Peñafiel et al. Nature 588, 414–418 (2020)
Notes: Entanglement enhancement has been demonstrated within a single system many times
However, doing it over a network is hard:
1. need...
Thankfully, we can do both in our lab – producing an entangled Bell state of 98% between our two nodes at a rate of up to 300 Hz

## Slide 10: Previous work: 88Sr+ clocks
Heisenberg scaling with entangled 88Sr+ clocks[1]
Limited by magnetic field noise
~10-15 level
[1] B.C. Nichol, R. Srinivas et al., Nature 609, 689–694 (2022)
entangled
unentangled
Notes: Did this with two entangled Sr88 clocks a few years ago:
Did show Heisenberg scaling
See on the right, get a much tighter measurement bound with the entangled (green) vs unentangled (orange)
Measurement at 1e-15 level: Hz resolution
Great proof of principle but probe duration severely limited (~15 ms), duty cycle

## Slide 11: 43Ca+ Clocks
 | Sr | Ca
Transition wavelength | 674 nm | 729 nm
Sensitivity | ~10 Hz/nT | ~ 0
Ramsey duration | 12 ms | ~ 500 ms
Entanglement generation duration | 9 ms | ~ 30 ms
Stability at 1s | ~10-13 | ~ 10-14
Resolve gravitational redshifts: 10-17 ~ 10 cm
Long term: tests of GR with entangled clocks?
Benhelm et al., Phys. Rev. A 75, 032506
729 nm
Notes: - Now extending it to Ca43 clocks on the optical S1/2 to D5/2 transition (point to transition) at 729 nm
- rich hyperfine structure
- intermediate field regime even at 5 Gauss, field-insensitive clock transition (shown on the right)
- much longer coherence time
- [next animation] Enables probes at much longer Ramsey durations, expect to be limited by excited state lifetime, which is ~1.1 s.
- Massively improves duty cycle, even though slower more cooling
(for data, 80 ms but definitely reduce massively < 30ms)
improvement of 1 order of magnitude in clock stability.
Expect to average down to 1e-17 from a preliminary evaluation of our drifts
- [next animation] Enables resolution of gravitational time dilation shifts at the 10 cm height difference.
Long term: first test of GR using entanglement, if GR changes quantum phase? Don't expect to see any deviations, but never been done before

## Slide 12: Entanglement scheme
Two nodes
Co-trapped 88Sr+ and 43Ca+
  Strontium – networking qubit
  Calcium – memory/clock qubit
Notes: Setup contains two nodes: alice & bob
each node has 2 co-trapped ions
88Sr: simple energy level structure, good for networking. But b field sensitive, bad for coherence
43Ca: Hyperfine structure, good for storing quantum information and will be used as our clock
All communication across nodes is between the Sr
Ca only interacts directly within the same node with the Sr

## Slide 13
13
Bob
Alice
~ 2 m
Entangling station
Notes: This is what our apparatus looks like:
See alice and bob on either side, approx 2 m free space (3m fibre) apart.
Entangling station with the Bell state analyzer in the back

## Slide 14: Entanglement scheme
Ion-photon entanglement
5S1/2
5P1/2
422 nm
~5 ps
Ca
Sr
Ca
Sr
Notes: How do we generate entanglement between sr?
Prepare Sr in ground state
ps excitation pulse to P1/2 state
Decays back to ground state, emitting a photon
Photon polarisation entangled with Sr state
Do simultaneously on both Alice and Bob

## Slide 15: Entanglement scheme
Ion-photon entanglement
Collect photons with high-NA
Notes: Then collect single photons via a high NA lens focused into an optical fibre
Have about ~2% efficiency of photon emission to end of fibre in each node
Probability of collecting a photon from both nodes simultaneously is 2% squared, but we attempt this generation at GHz rates
Now have two pairs of ion-photon entanglement from each trap

## Slide 16: Entanglement scheme
Ion-photon entanglement
Collect photons with high-NA
Photon bell-state measurement
Project Sr-Sr onto Bell state
Notes: Then do entanglement-swapping protocol:
- Measure photons with a bell state analyzer
- collapses the two Sr into a Bell state
Takes less than 4000 attempts for one herald (250-300 Hz)

## Slide 17: Entanglement scheme
Ion-photon entanglement
Collect photons with high-NA
Photon bell-state measurement
Local entangling gate maps entanglement to Ca-Ca
Local SWAP gate
Local SWAP gate
Notes: Then do local entangling gates to map Sr bell state onto two Ca ions

## Slide 18: Entanglement scheme
Ion-photon entanglement
Collect photons with high-NA
Photon bell-state measurement
Local entangling gate maps entanglement to Ca-Ca
Map to optical transition
Clock transition
Local SWAP gate
Local SWAP gate
Notes: The Ca-Ca entanglement is in the microwave qubit, we now map this onto the optical qubit
[animation]
[animation]
finally left with an entangled Bell state between the optical clock qubits

## Slide 19: Optical qubit entanglement
Remote Ca-Ca entanglement with 93% fidelity on microwave qubit [1]
Map to optical transition with 729 nm laser
[1] D. Main et al., arXiv:2506.14334 (2025)
Prepared bell state
Notes: Starting with Sr-Sr 98%
Have shown 93% fidelity on microwave
We've now set up the quadrupole 729 nm laser for the optical mapping, and preliminarily we see 94% parity contrast

## Slide 20: Preliminary results
Coherence > 125 ms
~2x higher contrast with entanglement
Ca
125 ms Ramsey duration
Sr
15 ms Ramsey duration
Notes: We have some preliminary results that we took last week
Blue curve is unentangled correlation spectroscopy, orange with entanglement. See parity contrast is almost 2x
See almost ~60% contrast at durations of up to 125 ms, well beyond the laser coherence time (measured ~5ms)
[animation]
Compare this to our previous Sr results, where we had lower contrast at 10x shorter probe, so it's a clear step forward

## Slide 21: Preliminary results
Ca
Initial contrast | 94.1(8) %
Coherence time | 260(20) ms
Sr
Notes: This is plot of the contrast vs ramsey duration
As mentioned earlier, start with approx 94% contrast
The contrast decays a bit lower than we expect: at 125 ms expect 85% from fidelity and excited state lifetime. Gives effective lifetime 1/4 of true decay rate
We know almost all of it (some 20-25%) comes from motional heating of the crystal leading to out-of-lamb-dicke effects in the closing pi/2 pulse, so should be able to push up to the full 500 ms with sympathetic cooling of the Ca ions
But even then, comparing to our previous results using Sr, significantly longer coherence and better starting fidelity

## Slide 22: Detecting spontaneous decay
Entangled state decays faster => same limit
Adds projection noise, no signal
Detection can improve stability by 2x
arXiv
Notes: [check time]
A subtlety to note about the entangled state near the lifetime limit:
- entangled state decays 2x as fast, so loses the factor of sqrt(2) gain over uncorrelated clocks when excluding laser decoherence
[animation x2]
- If you can detect the decay, improve sensitivity by further 2
by discarding those points.
[animation]
Details are in a paper on the arxiv with collaborators at NIST

## Slide 23: Detecting spontaneous decay
Teleported CNOT [1] between Ca atoms
  Control has phase information
  Target encodes whether state has decayed
Erasure detection outside clock subspace [2]
[1] D. Main et al., Nature 638, 383–388 (2025)
[2] R. Shaniv et al., arXiv:2604.01099 (2026)
Notes: 2 ways of doing this:
- controlled not (CNOT) gate between ca atoms -- separates information about phase and decay onto two different atoms. We can do this using protocol called "Quantum Gate Teleportation", which we demonstrated in our 2025 Nature paper [point to reference]
- in real atoms, have > 2 levels, can directly detect decays to state other than the ground state
Combining both, should be able to detect all spontaneous decay, and something we want to try in the lab

## Slide 24: Fibre length stabilization
~ 40 dB
1 github.com/OxfordIonTrapGroup/stabilizer
2 github.com/OxfordIonTrapGroup/stabilizer-ui
Firmware1
UI2
GitHub
Notes: And as a last quick note, we've developed an open-source fibre length stabilization system with a desktop applet, so if this is of interest to anyone here happy to happy to discuss more in the break

## Slide 25: Summary and outlook
Show entanglement is a practical way to improve frequency comparisons
  Proof of principle with 88Sr+
  Demonstrated 125 ms with 43Ca+, pushing to 500 ms
Evaluating systematics…
Test GR with entanglement??
Larger networks with longer distances??

## Slide 26
People and Funding

## Slide 27: Teleported gate
Ion-ion entanglement
Local Ca-Sr entangling gate
Measure Sr + local corrections

## Slide 28
cooling
…
cooling
…
State prep
ps pulse
SWAP gate
Cooling + State prep
Entanglement generation attempt
Herald
Map to correct Bell state
S (F=4) → D
S (F=3)
→ S (F=4)
clock
Readout
SWAP gate
Readout
abort?
Ca
Sr
Ca
Sr
Alice
Bob
clock

## Slide 29: Fidelities
Pair | Fidelity (%)
Sr-photon | 97.2(2)
Ca-photon | 93(2)
Sr-Ca (local) | 98.0(2)
Sr-Sr (remote) | 96.6(2)
Sr-Ca (remote) | 94.0(5)
Ca-Ca (remote) | 92.9(7)

## Slide 30: Performance Power spectrum
 | Free-running | Stabilized
Linewidth broadening | ~20 Hz | < 0.3 Hz
Coherence time | ~50 ms | > 3 s
Integrated phase noise* | 1.33 rad | 0.058 rad
Jitter* | 2.6 ns | 0.01 ns
*Integrated from 0.3 Hz to 1 MHz
Notes: The key performance parameters are summarised in the table on the slide.
We see that the integrated phase noise reaches 1 rad when integrated above ~20 Hz,
whereas with the cancellation enabled, the noise is still only ~58 mrad when integrated above 0.3 Hz, implying a coherence time of over 3 s between the fibre output and input.
We think that this performance is limited by the internal clock of the feedback electronics driving the DDS, and that it may be possible to boost performance further by switching to an external reference Rubidium clock and adjusting some of the multiplier settings on the electronics. However, as the cancellation we got was already better than other limiting factors, we did not try this in the lab.

## Slide 31: Entanglement loop
State preparation
Pulsed Excitation
Photon emission
Entanglement!
Detector click(s)?
NO
YES
~1 µs

## Slide 32: Measurement instability
Nichol, B. (2022), Doctoral Thesis
Without laser phase noise
With laser phase noise
a)
Notes: Plots show the stability enhancement from entanglement (green line) over conventional unentangled techniques (plotted in blue and orange).
See that entanglement improves stability, although its minimum instability is the same as without entanglement as the state decay rate is also twice as high.
A practical system however, is severely limited by laser phase noise on the laser, in the presence of which the enhancement provided by entanglement is much more substantial, as the entangled state produced is resistant to common-mode phase phase errors.