## Slide 1: Towards XUV Frequency Comb Spectroscopy of the 1s-2s Transition in He+
Jorge Moreno
PSAS 2026, ÖAW Vienna
Florian Egli
Muhammad Thariq
Erdem Yilmaz
Johannes Weitenberg
Theodor W. Hänsch
Thomas Udem
Akira Ozawa

## Slide 2: Testing QED by precision spectroscopy of Hydrogen-like systems
α: electron g-factor, atomic recoil shift experiments
Penning trap experiments, molecular spectroscopy
 Two parameters left for laser spectroscopy: and
 Measure two transition frequencies to determine and
Rydberg constant
Fine structure constant
Electron/nucleus mass ratio
Nuclear charge radius
E. Tiesinga et al., Rev. Mod. Phys. 93, 025010 (2021)
D. Hanneke et al., Phys. Rev. Lett. 100, 120801 (2008)
L. Morel et al., Nature 588, 61 (2020)
S. Alighanbari et al., Nature 644, 69–75 (2025)

## Slide 3: Target: 1s-2s Transition in He+
Independent QED test (in combination with µHe+ measurements)
Sensitive to higher order QED corrections (∝ Z5-7)
Trapped and cooled target  small systematics
2s
1s
Γ ≈ 2π × 84 Hz
2 x 61 nm
J. Moreno et al., Eur. Phys. J. D 77, 67 (2023)
J.J. Krauth et al., Nature 589, 527–531 (2021)
3

## Slide 4: Scanning Range
Parameters | Contribution to Uncertainty (He+ 1s-2s)
m-He spectroscopy [1, 2]
Mass ratio measurements
in Penning traps
Atomic recoil (atom interferometer)
g-2 measurement
Hydrogen spectroscopy
m-H + H (1s-2s), CODATA2022
Rydberg constant
Nuclear charge radius
Fine structure constant
Nucleus/electron mass
Uncertainty from He+ QED: 4x10-12 (36 kHz)
Expected observational linewidth: 1 kHz
[1] J.J. Krauth et al., Nature 589, 527–531 (2021)
[2] S. S. Li Muli et al., Phys. Rev. Lett. 134, 032502 (2025)
1x10-12 (10 kHz)
7x10-12 (74 kHz)
5x10-15 (45 Hz)
2x10-14 (166 Hz)

## Slide 5: He+ Spectroscopy for Testing QED
Measuring the 1s-2s transition:
  Better than ⁓ 400 kHz (4x10-11)
  Determine and contribute to the proton radius puzzle
  Better than 74 kHz (7x10-12)
  Determine charge radius, compare to µ-He measurement
  Better than 36 kHz (4x10-12)
  QED theory uncertainty will be limitation in extracting charge radius and
Measuring more transitions in 4He+: QED test independent from µ-He and Hydrogen
Measuring 3He+: Get charge radii difference, compare with neutral He and µ-He
Sun, Y. R. and Hu, S.-M., National Science Review 7, 1818–1827 (2020)
The CREMA Collaboration, arXiv.2305.11679 (2023)

## Slide 6: Direct Frequency Comb Spectroscopy
Line width of a single comb mode
Efficient nonlinear frequency conversion due to high peak power of pulsed laser
As efficient as CW laser of same average power
6
XUV comb at 61nm
1S
2S
2 x 61 nm
He+
Spectroscopy signal: He2+
< 91 nm

## Slide 7
He+ spectroscopy setup: overview
High-power IR
frequency comb
Yb:KYW laser + amplifiers
@1030 nm
300 W Innoslab amplifier
(Fraunhofer ILT)
Trapped He+ ions
Intracavity
high-harmonic generation
17th harmonic
Frequency comb
at 61 nm
HHG
IR frequency comb
1030 nm
Odd-order harmonics
XUV frequency comb
61 nm
17th harmonic
High-harmonic generation

## Slide 8
30 µW at 61 nm
Yb:YAG amplifier (Innoslab)
270 W, Dl = 1.6 nm, 𝜏 = 1.1 ps
Yb:KYW oscillator (frequency comb)
40 MHz, 10 mW, l = 1030 nm
f
Yb:LuAG preamplifier x2
2.7 W Dl = 2.3 nm
(+ double-pulse generation)
61 nm laser system
HHG
Intracavity high-harmonic generation
(non-collinear geometry)
5 kW, < 100 fs
XUV comb
to He+ trap
Seed laser
Amplification
&
compression
XUV comb
generation
Multi-pass-cell spectral broadening
(two stages)
230 W , 1010 - 1060 nm, 59 fs

## Slide 9
Enhancement Resonator for HHG
Xe gas for HHG
Mirror with slit
Comb frep = 40 MHz
Cavity FSR = 20 MHz
Wedge mirror
Side view
Wissenberg, S. H. et al., Phys. Rev. Res. 7, 023071 (2025)
Segmented input coupler
9
frequency comb
at 61 nm

## Slide 10
H9
115nm
H11
H13
H15
H17
61nm
H19
H21
H23
H25
41nm
~30 µW at 61 nm
Optical frequency comb at 61 nm
~ 0.1 Hz signal rate (ionization)

## Slide 11: XUV beam delivery to trapped He+
HHG chamber
Ion trap
XUV focusing mirrors
(R=30% @ 61 nm)
XUV grazing incidence mirror
(R=70% @ 61 nm)
recoil- and Doppler-free
Anti-collinear excitation
11

## Slide 12: Single Ion Laser Excitation in Harmonic Oscillator
carrier
Laser
Excite electronic transition:
F. Egli et al., arXiv:2605.07942 (2026)
Laser

## Slide 13: Spatial and Temporal Alignment of the XUV Beam
Linear chain of Be+
Harmonics + IR leak
Linear chain of Be+
IR (1030 nm)
SHG
➤ Drive Raman transition in Be+ with 515 nm pulses

## Slide 14: Pulse Overlap: Raman Transitions in Be+ ground state HFS
F=1
F=2
Virtual state
GHz
Paschke, A.-G. et al., Phys. Rev. Lett. 122, 123606 (2019)
40 MHz
1.25 GHz
87 MHz
29
515 nm
Comb 1
Comb 2
AOM

## Slide 15
Achieved:
- Comb at 515 nm with ⁓ 4W (SHG from IR)
- Double pass AOM setup
HHG chamber
Ion trap
XUV focusing mirrors
(R=50% @ 515 nm)
Beam Switcher
(rotational stage with mirrors)
XUV Spectrometer
After losses: Power @ ions ~300 mW
Estimated π-time ~250 ms
Grazing Incidence Plate (GIP)
Pulse Overlap: Raman Transitions in Be+ ground state HFS
SHG
1030 nm
515 nm

## Slide 16
XUV frequency comb source
Ion trap

## Slide 17: Single Ion Laser Excitation in Harmonic Oscillator
carrier
Laser
Excite electronic transition:
F. Egli et al., arXiv:2605.07942 (2026)

## Slide 18: Carrier Revival in Linear Ion Chains
MHz
MHz
mK
Sidebands
detuning
F. Egli et al., arXiv:2605.07942 (2026)

## Slide 19: The He+ team
Florian Egli
Jorge Moreno
Akira
Ozawa
Johannes Weitenberg
Thomas Udem
Muhammad Thariq
Erdem
Yilmaz
Theodor W. Hänsch
Savely Karshenboim

## Slide 20
Uncertainty due to QED theory for He+ 1s-2s transition
Total QED uncertainty : 36 kHz (4x10-12) (preliminary)
Contribution | Uncertainty (in kHz)
Relativistic Recoil | 0
Nuclear Polarizability | 3
Self Energy | 0
Vacuum Polarization | 1
Two Loop Corrections | 32
Three Loop Corrections | 9.5
Four Loop Corrections | 0
Nuclear Size Correction to Self Energy | 0
Nuclear Size Correction to Vacuum Polarization | 0
Radiative Recoil | 12
Nuclear Self Energy | 0.6
Total | ~36 kHz
[1]
[3-7]
[3,4]
[8]
[9]
[1] Yerokhin A. and Shabaev V. M , Phys. Rev. A 93, 062514 (2016)
[2] Pachucki K. and Moro A. M, Phys. Rev. A 75, 032521 (2007)
[3] Karshenboim S. G et al. , Physics Letters B 795, 432–437 (2019)
[4] Karshenboim S. G et al. , Phys. Rev. A 100, 032515 (2019)
[5] Karshenboim S. G et al. , Phys. Rev. A 98, 022522 (2018)
[6] V. Yerokhin et al. , Annalen der Physik 531, 1800324 (2019)
[7] A.Czarnecki et al. , Phys. Rev. A 94, 060501 (2016)
[8] S. Laporta, Physics Letters B 800, 135137 (2020)
[9] Karshenboim S. G and Shelyuto V. A. , Phys. Rev. A 100, 032513 (2019)
[2]

## Slide 21: Helium: Difference of Squared Charge Radii
Sun, Y. R. and Hu, S.-M., National Science Review 7, 1818–1827 (2020)
The CREMA Collaboration, arXiv.2305.11679 (2023)

## Slide 22: Helium Ions: Alpha Charge Radius
µHe +
e- scattering
Krauth et al., Nature 589, 527–531 (2021).

## Slide 23: Understanding spectral broadening
GDD
Second-order dispersion
TOD
Third-order dispersion
SPM
Self-phase modulation
Not considering self-steepening, intrapulse Raman scattering…
Notes: To understand and simulate spectral broadening, one needs to consider mainly two effects. The most important, self-phase modulation, is an intensity and time dependant phase in time domain, that causes modulation and broadening in frequency domain. But also chromatic dispersion or chirp play an important role, mainly through its leading term: the second order dispersion or GDD. This modulates the pulse amplitude in time domain by adding a frequency dependant phase in frequency domain. And one can also consider the next leading term in dispersion, which is the third order dispersion or TOD, which is the first term that introduces asymmetries in the pulses. In principle one can think that SPM affects only the spectral amplitude and dispersion affects only the pulse shape in time domain, but when acting together, they all affect the properties of the pulses both in time and frequency domains.

## Slide 24
Simulating multi-pass cell spectral broadening
Simulation of MPCSB
GDD + SPM act together in Split-step Fourier method
Asymmetry only explained with strong TOD   0.5 ps3 present before MPCSB!
Agrawal, G. Nonlinear Fiber Optics. (Elsevier Inc, Cambridge, 2019)
GDD
GDD
GDD+SPM
Notes: In order to calculate the spectral broadening, we can assume Gaussian pulses come into the MPCs and propagate such that they accumulate GDD in the focusing mirrors, and GDD and SPM simultaneosuly in the nonlinear element. This can be simulated via the Split-step Fourier method, where you split the propagating medium in small distance steps and you apply GDD to your pulses in frequency domain, then perform a Fourier transform to time-domain, apply your SPM phase and Fourier transform back. Then move to the next distance step and repeat this process until you have propagated your pulses through the whole medium. In principle, these MPCs are designed with specific values for GDD and SPM in mind, but when simulating the spectral broadening, we see that the asymmetry of the spectrum cannot be reproduced with these effects only. One could also include the TOD from the propagation in the nonlinear element, but this contribution is actually quite small. In order to reproduce this asymmetry, I had to make the initial pulses non-gaussian, with a very strong third order phase corresponding to a TOD of -0.5 ps3. We can then reproduce the spectrum quite well. We believe that this strong TOD contribution comes from the very strong gain narrowing in the previous amplification stages, but this is something that still needs to be studied in more detail.

## Slide 25: XUV Spectrometer
resolution 0.18 nm
repeatability 0.0015 nm
Response function obtained from He+ lamp spectroscopy
(second order diffraction of 1s – 2p emission at 30.4 nm)

## Slide 26: Comb stabilization
Fixed point (depends on noise source)
f
Cavity-stabilized cw laser (ECDL)
Comb mode locked at
f
Noise cancelled by two-photon excitation
Yb:KYW oscillator