## Slide 1: CERN’s Experimental Areas
Fabian Metzger (BE-EA-LE) with input from many others!
28.11.2025

## Slide 2: Introduction
Overview about CERN
North Experimental Area
East Experimental Area
Modelling & Simulations
Beam Dump Facility and Search for Hidden Particles

## Slide 3: CERN and the Accelerators
H. Pekeler
E. Lopienska

## Slide 4: Proton Synchrotron
The oldest operating synchrotron at CERN
(Small) circumference of 628m
Accelerates from 2GeV to max. 26GeV
Various extraction techniques and cycle lengths possible
Sends beam to:
  SPS
  East Area
  Antimatter Facility
  nTOF

## Slide 5: Super Proton Synchrotron
Normal-conducting accelerator
6.9km circumference and about 30m underground
Accelerates up to 450GeV with intensities up to 5×1013 protons per cycle
Provides slow extracted beam to the North Area
Fast extraction to LHC, AWAKE and HiRadMat

## Slide 6: What Do We Do in Our Group?
Operation & Engineering / Scientific Support
Technical Services & Supply
100-150 User Teams
linking to equipment and service groups
10 Beamlines
~30 Experimental Areas
~8km
Staff, Fellows, Associates, Students, Contractors 1/3 – 1/3 – 1/3
Group Members
~80
Design, Operation, Coordination, Support
Experiments & Facilities / Users
~20 / 2000
Areas & Machines, Experiments, Users
Fixed Target Experiments
LHC Experiments & Forward Detectors
Providing technical and engineering support
User, physics and service oriented
GL: M. Brugger
DGL: R. Folch

## Slide 7: North Area

## Slide 8: North Area Secondary Beamlines
SPS beam
@400GeV/c
EHN1
NA62
AMBER
NA64
MUonE
ECN3
EHN2
NA61
NA64
The 400GeV/c primary beam is slowly extracted to three primary targets  T2, T4 and T6
Spill duration: 4.8s flat top
Typically: 2 cycles / SPS supercycle for NA and
~ 3000 spills/day
Supercycle structure depends on the physics program of all the facilities served by the SPS including LHC, AWAKE, HiRadMat and the Machine Development program

## Slide 9: How to Make Three Primary Beams - Splitting
We serve three production targets starting from one proton beam from the SPS
Depending on user schedule, sharing between targets needs to be adapted
Making use of splitter magnets
  Beam is smeared vertically over the magnet aperture
  Beam going through uniform field gets deflected
  Beam going through hole continues straight ahead
  Smearing is adapted when different sharing is needed
Septum hole
Uniform field
J. Kurdej

## Slide 10: Secondary Beams
500mm
240mm
Secondary beams are produced from interaction of primary beam in a target
  We use typically beryllium due to high melting point
  Secondary particles go mostly in forward direction
  Multiple species are produced, not only one
With magnets, one can define momentum and beam shape
  After momentum selection particles have same momentum but different velocity
Collimators define beam shape and particle rate
Hadron beams consist mostly of:
  Pions
  Kaons
  (Anti)Protons
  Muons (typically from decays) are constant background

## Slide 11: How to Make Multiple Secondary Beams - Wobbling
The general idea is quite simple: Excurse the primary beam in a way to collide with the target at an angle and offset such that a spectrometer selects desired momenta for various beamlines
In this note, all the information about the geometry can be found
The task is: Find a set of magnetic fields to serve the beamlines
  We use the “Wobbling Configurator” → There is an analytic solution!
  Beam momenta of all beamlines strongly coupled!
B1
B2
B3
T4
Front-face of the target attenuator
Primaries
H6
H8
P42
P42
H8
H6

## Slide 12
Current T4 Region
Beam Direction
B1
B2
T4 Target + Diagnostics
B3
VXSS
XTAX
P42 MSNs
TBIU
TBID
The “Wobbling”
Quad
B1
B2
B3
TAX
T4
TBIU
TBID
Primaries hit the target off-centre with an angle → Produced secondaries of desired momenta go to H6/H8 while primaries need to follow P42 line
Number of protons defined by needs of NA62 and chosen T4 target length (set by needs of test beam users)
In future: two different cycles that relax these constraints!
Not to scale!
XTAX: Target Attenuator
VXSS: Big Vacuum Chamber
TBIU/D: Target Beam Instrumentation Up/Down-stream
y
s
x
s

## Slide 13: How to Make Multiple Secondary Beams - Wobbling

## Slide 14: How to Make Multiple Secondary Beams - Wobbling

## Slide 15: Beam Characteristics
Parameter | T2 Target |  | T4 Target | 
Beamline | H2 | H4 | H6 | H8
p attenuated primary / secondary beam in GeV/c | 400 / 360 | 400 / 360 | - / 205 | 400 / 360
Maximum Δp/p in % | ±2.0 | ±1.4 | ±1.5 | ±1.5
Maximum intensity/spill (hadrons/electrons) | 107 / 106 | 107 / 107 | 107 / 105 | 107 / 105
Available particle types | Primary protons or pure electrons or pure/mixed hadrons or pure muons |  |  | 
Ion beam availability | Yes | Yes | No | Yes
T6 target  Serves the M2 beam that is currently used for the AMBER experiment
  < 4.8×108 hadrons/spill with < 280GeV/c (requires additional shielding around target); increase to 109 with improved shielding in future
  < 2×108 muons/spill with < 280GeV/c
  NA64 and MUonE will continue physics and test runs
P42 beam also originates from the T4 target and transports the proton beam that has not interacted onto the T10 target to produce typically 75GeV/c kaon beams guided via K12 to NA62

## Slide 16
ECN3
H2
H4
H6
H8
EHN1
EHN2
B. Parsamyan

## Slide 17: East Area

## Slide 18: East Area Secondary Beamlines
Spill duration: 0.4s flat top
Usually : 1-2 cycles per minute per East Destination
Max 3.3×1010 protons/second per destination (limited by RP for secondary lines)
Max 6.6×1010 protons/second for T08
Supercycle structure dependent on all users (SPS, nTOF, …)

## Slide 19: Beam Characteristics
Parameter | T09 | T10 |  | T11
pmax of secondary beam in GeV/c | 16 | 12 | 3.5 | 
Δp/p in % | ±0.7 to ±15 |  |  | 
Maximum intensity/spill (hadrons/electrons) | 106 |  |  | 
Available particle types | Pure electrons (T09 only) or mixed electrons (T10) or mixed/pure hadrons or pure muons |  |  | 
Multi-target configuration
30-35 mrad vertical production angle
T11 serves the CLOUD experiment which is a permanent installation

## Slide 20
T10
T09
Beam
T08
Beam
T09
T10
T11
T09
T10
T11
T08
Beam

## Slide 21: Modelling & Simulations

## Slide 22: Simulation of Secondary Beamlines
Experiment
p
#
Converter Target
Beam Dump
Target
Multi-Species Beam Spectra
Secondary beams can provide a wide range of particles over a wide range of momenta
    Useful for detector calibration and development
Exploit particle-matter interaction
Composite spectra based on beamline and materials
Several ten to hundred components along the line (up to 1km long!)
Experiments rely on knowledge of beam properties and background

## Slide 23: Geant4
Use a 3D radiation transport model to predict detector response and compare to data using Monte Carlo
Detailed 3D geometry - complex and specialised to an experiment
Often includes magnetic field for particle identification
Geant4 is one of the most common software libraries for creating these models
  Open-source C++, regular development by community
  All subatomic particles, huge array of physics models
Simplified ATLAS Geometry
http://geant4.web.cern.ch
Constructive Solid Geometry
L. Nevay

## Slide 24: FLUKA
FLUKA is typically used for radiation shielding applications and machine protection
  Also used for variety of nuclear applications
Certified for radiological protection by many organisations
  Therefore, they often require a FLUKA model at some point
Written in Fortran, but huge efforts are there to translate to C++
  Would mean rewriting a lot of Geant4 code → Decided to make use of the existing libraries
Uses combinatorial geometry without hierachy
https://fluka.cern
L. Nevay

## Slide 25: BDSIM
Automatic Geant4 models of accelerators
Library of scalable accelerator components
  Make a model in minutes to weeks, not years
  Convert from other accelerator codes easily
Applied to many experiments and machines
  CERN North & East Areas, ILC / CLIC, AWAKE, XFEL undulators, LHC collimation, Laserwires, FASER, KLEVER, NA62, ATLAS non-collision backgrounds, MAGIX at MESA, FCC MDI, LhARA
Benefit from community-driven Geant4
  Physics models constantly updated and improved
Comp. Phys. Comm. (252), July 2020, 107200
L. Nevay

## Slide 26: Customisation
Generic geometry is not always suitable
  Ability to include custom geometry
Can overlay E or B or combined EM field maps → 1D to 4D with numerical interpolation
Supports all Geant4 physics lists
Cross-section biasing per volume
Beam distribution generator for accelerators
3D scoring meshes and beam loss monitor scoring
Automatic tunnel building following beamline
Custom field map attached to geometry
Field map interpolation
L. Nevay

## Slide 27: pyg4ometry
Ability to import / place it in a Geant4 model
Creation of geometry from scratch
Conversion of detailed geometry from another format (different mathematical form)
Place custom components in Geant4 / BDSIM
Have parity with models in Geant4 & FLUKA
Python Geant4
STL from vacuum
company
GDML from BDSIM
CAD/STEP
FLUKA
Laser vacuum chamber
Gate valve
Quadrupole triplet
Sector bend
Faraday cup
10.1016/j.cpc.2021.108228
10.18429/JACoW-IPAC2024-MOPS24
S. Boogert

## Slide 28: M2 Beamline
XTAX
Hadron Section
Muon Section
Target
Protons
Experiment
400GeV/c protons to produce hadrons and electrons
  Hadron beams for AMBER
  Pions decay to produce muon beams for AMBER/NA64/MUonE
  Electron mode also possible
Multi-stage simulation
Custom geometry and field maps throughout

## Slide 29: M2 Beamline
Simulation
Electron spectrum
Measurement
Muon spectrum at end of hadron section
Simulations start with protons on target
  Full particle production included
Use biasing techniques for muon mode
  Muon splitting for enhancement of muon rate
  Cross-section biasing for estimation of hadron contamination in muon beam
No biasing possible for electron mode

## Slide 30: Calorimetry
Transverse shower along beam axis for 150×1011 protons with 400GeV/c on P4 XTAX
Jura
Saleve
Beam parameters | 
Number of protons | 1.5×1013
Momentum | 400 GeV/c
Cycle length | 14.4s
Total beam power | 67kW
FLUKA
Geant4
Temperature evolution simulated with ANSYS based on energy loss from Geant4/FLUKA
[A. Petrellese]
Power at front face
For the “positive” wobbling of +120/+180 GeV/c
H6
H8
P42
Primary protons
Positive secondaries
Negative secondaries
Neutrals
Vacuum chamber
Spectrometer shadow

## Slide 31: What comes next?

## Slide 32: Beam Dump Facility / Search for Hidden Particles
Direct search for Feebly Interacting Particles
Exploit 4×1019 protons (400 GeV/c) per year for 6×1020 POT over 15 years
SHiP Physics Proposal: Rep. Prog. Phys. 79 (2016) 124201 published 2016
SPS Beam Dump Facility Comprehensive Design Study: CERN-2020-002 published
M. Fraser
High ppp & POT Overcome small cross-section of hidden particles
High ρ, Z & A Maximize p+ interaction
Shortest λ Force absorption of K & π to reduce muon & neutrino background

## Slide 33: Beam Delivery to BDF/SHiP
BDF/SHiP
We need to transport 400×1011 protons per spill to BDF
Today, we typically extract about 250×1011 to the whole NA
Compared to today’s P42 operation mode, we will have about 90× higher power transported in SHALLOW tunnels
Need to minimise losses due to multiple reasons:
  Radiation protection (we transport 2MW)
  Meet proton requirements for BDF/SHiP
  Minimise background
Complete redesign of the transfer line happening in LS3

## Slide 34: Beam Transport Through T4
To minimise losses, we need to reduce material seen by the beam as much as possible → But we still go through the secondary target area!
Axis of machine
HI-ECN3 beam
Fixed-target
beam
Target plates
Target box
Stay clear region:
y
s
x
s

## Slide 35: Background for BDF/SHiP
SHiP will operate with a magnetic muon shield to remove any background from the experiment
  Works very well for particles created in the beam dump
  Beam-induced background can be problematic as potentially off-axis
We talk about 104 muons generated from 4×1013 protons → We need to make use of dedicated techniques to estimate the background properly: rate plus spatial and angular shapes
  Biasing techniques to enhance muon production
  Muon splitting
  Still, optics designed to transport 7σ without losses! → Dedicated simulations needed to estimate distributions

## Slide 36: Conclusion
How to make mutiple primary and secondary beams starting from one primary beam
  Splitting and Wobbling
Characteristics of beams in the East and North Area
  Up to 24GeV/c available in the East and up to 400GeV/c in the North Area
  Primary and secondary beams possible
  Ion momenta up to 150GeV/c/n
Methods for simulating secondary beams with BDSIM/Geant4
  Programmatic model building
  Estimation of beam and background distributions
Design of a new beamline for the Beam Dump Facility and SHiP experiment
  Minimise beam losses for background reduction and mitigation of radiation protection constraints
  Dedicated studies to estimate (low) background necessary

## Slide 37
Our Group
BE-EA
HI-ECN3
Physics Beyond Colliders
Carrer Possibilities
Student Opportunities
Doctoral Student Programme
Graduate Programme
Additional info for Germans
Contact me in case of any question:
fabian.metzger@cern.ch

## Slide 38: HI-ECN3 and BDF
The unique neutron-dominated radiation field generated around the BDF spallation target is of interest for:
  Electronics and Materials irradiation
  Nuclear astrophysics
  “CERN’s RME Strategy Panel is mandated to assess interest from the scientific community and recommend possible synergies for irradiation testing that can be carried out parasitically at the BDF once the SHiP experiment is operational after LS4.”
Beam characteristics:
  300kW average power
  2.3MW total beam power over 1s → Competing with spallation sources
  Transporting the beam through shallow transfer tunnels challenging due to RP
HI-ECN3 Irradiation Opportunities Workshop
M. Fraser

## Slide 39: HI-ECN3 and BDF
Position | TID in Gy/yr | Si1MeVNeq in cm-2/yr | HEHeq in cm-2/yr | Particles’ fraction
BHFIM1 (4 x 1019 POT/year) | 107 - 108 | 1020 | 1017 | Neutrons (N): 66% Photons (Ph): 33% Charged Hadrons (CH): 1%
BHFIM2 (4 x 1019 POT/year) | 107 | 1019 | 1016 | N: 79% Ph: 20% CH: 1%
R2E@4m (2 x 1016 POT/hour) | 101 | 1013 | 1011 | Neutrons (N): 99% Charged Hadrons (CH): <1%
R2E@10m (2 x 1016 POT/hour) | 100 | 1012 | 1011 | N: 99% CH: <1%
R2E@20m (2 x 1016 POT/hour) | 10-1 | 1011 | 1010 | N: 99% CH: <1%
R2E@10m
Z
X
R2E@20m
Atmospheric-neutron channel
R2E@4m
BHFIM2
BHFIM1
Beam
SHiP experiment
P. Pelissou