## Slide 1
Preliminary Electromagnetic Design of a 15 T HTS Racetrack Superconducting Magnet
Author: Yuan cheng
SSRF Science Center, Shanghai Advanced Research Institute, Chinese Academy of Sciences
Date: Oct 27, 2026

## Slide 2
Overview of Institute and Research Group
Shanghai Synchrotron Radiation Facility (SSRF)
432 m, 3.5 GeV, user operation started from 2009
Shanghai Soft X-ray FEL facility (SXFEL)
532 m, 1.5 GeV, user operation started from 2023
Shanghai Hard X-ray FEL facility (SHINE)
3.1 km, 8 GeV, under construction

## Slide 3
Overview of Institute and Research Group
SSRF is a 3.5 GeV third generation light source, opened to users in May 2009， now it has 38 beamlines and 55 end-stations in operation for user experiments.
3.5GeV Storage Ring C=432m
Booster C=180m
150MeV Linear Accelerator
Beamlines and Experimental Stations
SSRF operation Parameter | Value
Storage Ring Energy | 3.5 GeV
Circumference | 432m
Natural Emittance | 4.2 nm-rad
Multi-bunch Single-bunch | 200-300 mA 20 mA
Coupling | 0.3 ~ 0.7%
RF Voltage | 4-5 MV
Beam Lifetime | 10 ~ 20 hrs
Linac Energy | 150 MeV
Booster Output Energy | 3.5 GeV
Injection interval | 10 min (top-up)

## Slide 4
Overview of Institute and Research Group
NbTi wiggler in SSRF
The model coil of NbTi wiggler
The superconducting wiggler at SSRF is a home-developed high-field insertion device with a peak field of 4.2 T. It serves as the photon source for the BL12SW hard X-ray beamline

## Slide 5
Overview of Institute and Research Group
HTS wiggler in SSRF
The model coil of undupator
As China’s first SCU with storage-ring beam commissioning, the SSRF superconducting undulator prototype has a 16 mm period, 9.5 mm gap and 50 periods, with 0.67 T design peak field and 0.57 T measured field.

## Slide 6
Overview of Institute and Research Group
LTS: NbTi
Tc：<10K
Bc：<15T
Engineering application realized
？
HTS: REBCO tape
TC：>25K
Bc：>25T
So far, SSRF has limited experience in HTS magnet applications. We aim to build up relevant technical capabilities starting from the design of a 15 T HTS racetrack coil.

## Slide 7
1. Requirements of the 15 T HTS coil
Main parameter for 15 T HTS coil
Parameters of Thin-substrate HTS Tapes of SST | 
width（mm） | 4
thickness（µm） | 50
Ic （77 K，自场） | 200 A
Ic （4.2 K，15 T） | 200*2.29 A
Bending radius（mm） | 5
Central Field | >10 T
Bmax of coil | <20 T
Arc Radius | 5 mm
Max. Stress | <600 MPa
Cooling Method | LHe bath cooling
Operation temperature | 4.2K-20 K
- | VPI
- | Stycast 2850+CAT 24LV
Iop/Ic | ≤50%

## Slide 8
2. EM Optimization of the 15 T Racetrack Coil
图 匝数优化
Double-pancake optimization shows saturated field and cost-efficiency at 7 pancakes (600 turns, 1 mm inter-pancake gap, 50 mm straight length, 4 mm arc radius, 200 A operating current).
Turn optimization reveals saturated field and cost-efficiency at 600 turns (5 DBs, 1 mm gap, 50 mm straight length, 4 mm arc radius, 200 A operating current).
Conclusion: 7 double pancakes with 600 turns each DP minimize HTS tape consumption.

## Slide 9
Straight-section length | 50 mm
Arc radius | 5 mm
Number of DPs | 7
Turns | 600×7
Iop | 300 A
Ic | 326 A
Length of HTS tape | 120*7
Bmax | 20.4
Bcenter | 19.7
Hoop stress | 220 MPa
Radial stress | 50 MPa
On-axis Magnetic Field Distribution
2. EM Optimization of the 15 T Racetrack Coil
EM results for HTS coil（Bmax=20.4 T)

## Slide 10
2. EM Optimization of the 15 T Racetrack Coil
Straight-section length | 50 mm
Arc radius | 5 mm
Number of DPs | 7
Turns | 600×7
Iop | 235 A
Top | 4.2 K
Ic | 478 A
Bmax | 15.7
Bcenter | 15.1
The previous current and magnetic field were near the coil’s performance limit. Based on simulation results, we adjusted it to a central field of ~15 T at 235 A.

## Slide 11
3. Structural Design of the 15 T Racetrack Coil
Conduction-cooled
board
Conduction-cooled collar
G10 board
winding former
Current Led
HTS joint
Double pancake

## Slide 12
Bridge-joint structure: adjacent double pancakes bridged by 12 mm-wide tape, Sn63Pb37 solder, melting point 183 °C
DP coil#1
12 mm HTS tape
DP coil#2
Adjacent double-pancake leads
（4mm HTS tape）
3. Structural Design of the 15 T Racetrack Coil

## Slide 13
Thank you for your attention！