## Slide 1: FAST – Fast actuator using superconducting technology
Mathijs van Gorcum
mathijs.van.gorcum@vdletg.com

## Slide 2: Facts and Figures VDL ETG
12
VDL ETG
consists of 12 companies
> 5,000 Employees in 6 different countries
2006
Production surface area > 250,000 m²
A global design & manufacturing company, cooperating with high-tech companies
VDL ETG was acquired by VDL Groep in 2006
1953
1900
Unique combination of technical design knowledge and manufacturing craftmanship under one roof
Production and staff > 4,300
T&D Engineers > 700

## Slide 3
Manufacturing
Design and Engineering
Business Development
VDL ETG USA
VDL ETG USA
VDL ETG SWITZERLAND
VDL ETG ALMELO
VDL ETG EINDHOVEN
VDL ETG PRECISION
VDL GL PRECISION
VDL ETG PROJECTS
VDL ETG T&D
VDL ETG
VDL ETG SUZHOU
VDL ETG VIETNAM
VDL ETG SINGAPORE

## Slide 4: Value Chain
From sketch to design to (volume) manufacturing to usable product for society
First sketch
Concept
Functional model
Release for volume

## Slide 5: Why superconductivity at VDL?
Off the shelve components
  Cryocoolers
  HTS tapes
  Oxygen free copper
  MLI
  Vacuum pumps

## Slide 6: Cryogenics & superconductivity at VDL
6 years of Frozen
Ongoing project for several years with approx. 10 people
Conduction-cooled set-up: up to 2 kA, down to 10 K
NI pancake coil duet: 10 T peak field
Developed and assembled in-house
Re-use parts of set-up for FAST
  Superconducting linear motor
Control rack
Vacuum vessel
Inside vacuum chamber
Coils
Coolers & pumps

## Slide 7
FAST project
100G linear motor

## Slide 8: Project overview
Linear motor
FAST project aim:
  Design and fabrication of a superconducting linear motor
    Conventional AC mover & DC HTS stator
    Enable a much higher acceleration than possible with conventional technology
A linear motor provides linear motion (i.e. along a straight line)
  Essentially an ‘unrolled’ rotary motor
  Track with N/S poles and AC mover -> Lorentz force
  Widely used in (semicon) industry
  Experience with such systems at VDL ETG
Mover
Stator
Source: https://commons.wikimedia.org/wiki/File:Linearmotorprinzip.png

## Slide 9: Design overview
Mover flange
(thin wall)
3-phase mover
Radiation shield
HTS coil array
(stator)
Force frame
Powerlead and
1-stage cryocooler
2-stage cryocooler

## Slide 10: Main Thermal Challenges
Focus of this talk
Large forces on superconducting stator
  Needs strong force-frame
Sufficient cooling at target current
Thin wall cryostat
  Minimize distance between atmospheric mover and HTS stator
Thermal model

## Slide 11: Force frame
Stiff in actuation direction
Thin in y-direction to decrease heat transport
Titanium
293K connection
50K intermediate temperature
25K stator coil array

## Slide 12: Cooling force-frame
Conduction cooling through powerleads
First stage of 2-stage for additional cooling

## Slide 13: Cooling force-frame
Conduction cooling through powerleads
First stage of 2-stage for additional cooling

## Slide 14: Thin wall cryostat
Thin ‘air’ gap crucial to maximize magnetic field at mover coil position
  Design for ≤ 11 mm mover-stator distance
  Incl. vacuum wall, MLI, and heat shield
Challenge to minimize radiation heat leak
  Multi-layer insulation
  Actively cooled heat shield
Vacuum wall thickness optimized
  Withstand 1 bar pressure difference
  Thin wall section above stator coils
  Minimize total thickness
Thin cryostat wall
3 phase mover coils
Heat shield
To 1st stage cooler
To 2nd stage cooler
Stator coils
z
x
MLI
Vacuum wall
≤ 11 mm

## Slide 15: Thin wall cryostat
HTS coil array
Force frame
Bottom shield
Top shield
~293K
~50K
~25K
(Internal shield)
Mover flange

## Slide 16: Block-based model
Nodes simulated with thermal connections

## Slide 17
Questions
Contact us at our stand or via:
Mathijs van Gorcum – mathijs.van.gorcum@vdletg.com
Aernout Kisteman – aernout.kisteman@vdletg.com
Cees Maris – cees.maris@vdletg.com