## Slide 1: Design of the main ring beam position monitors for FCC-ee
E. Howling, CERN, John Adams Institute & University of Oxford
Supervisors: P. N. Burrows, John Adams Institute & University of Oxford
M. Gasior, CERN
With thanks to N. Chambers, R. Kieffer, T. Lefevre, B. Moser, A. Novokhatski, B. Spear, H. Sullivan, C. Zannini, CERN
18/12/2025 JAI Fest
Emily Howling

## Slide 2: Table of contents
2
Introduction
  FCC-ee BPM requirements
  Response to different FCC-ee modes
Geometrical studies
  Varying parameters of a simplified button
  Different geometries of a circular button
  Non-standard geometries
Thermal studies
Bench-marking
Conclusions
Emily Howling

## Slide 3: Table of contents
3
Introduction
  FCC-ee BPM requirements
  Response to different FCC-ee modes
Geometrical studies
  Varying parameters of a simplified button
  Different geometries of a circular button
  Non-standard geometries
Thermal studies
Bench-marking
Conclusions
Emily Howling
Find 5 festive John Adamses!
(not including this one)

## Slide 4: Introduction: FCC-ee BPM requirements
Electrostatic button BPMs (see Fig.1), one rigidly fixed to each quadrupole.
Shall provide orbit, turn-by-turn and bunch-by-bunch measurements .
High resolution requirements (see Table. 1).
Low beam impedance to prevent excessive heating of the button electrodes and to ensure beam stability.
Need to be reliable and have rad tolerant electronics.
~10’000 needed across accelerator complex → must have suitable cost for mass production.
Table 1: Requirements for FCC-ee arc BPMs [2].
Fig 1: Diagram showing the principles of an electrostatic button BPM. [1].

## Slide 5: Introduction: Response to different FCC-ee modes
FCC-ee will run at several different beam modes, summarised in Table 2.
The BPM must have sufficient resolution at the lowest beam intensity mode and acceptable impedance at the highest beam intensity mode.
The lower intensity beam (~10% of nominal) during initial injection/commissioning and the variation of bunch charge during top-up injection (+/- 5%) must also be considered.
Table 2: Beam parameters of the different running modes of the FCC-ee collider from the CDR [3].

## Slide 6: Introduction: Response to different FCC-ee modes
I simulated a simplified BPM in CST at different FCC-ee modes, voltage results shown in Figs 2-4.
There was up to a factor 30 difference between the raw peak to peak voltage of the lowest and highest intensity beams.
Fig 5: The Voltage signal from a simplified pickup for the SR FCC-ee beam modes, with a 75 MHz filter applied.
Fig 4: The voltage signal from a simplified pickup for the most extreme FCC-ee beams, with a 75 MHz filter applied.
Fig 3: The voltage signal from a simplified pickup for the most extreme FCC-ee beams.
Fig 2: A simplified BPM model in CST, with FCC-ee beampipe.

## Slide 7: Geometrical Studies

## Slide 8: Geometrical Studies: Varying Parameters of a Simplified Button
The effect of 4 parameters on 4 different properties was studied.
Peak-to-peak voltage: increases significantly with the electrode radius, increases slightly with gap size, and decreases slightly with back gap size, whilst height has a negligible effect.
Wake-loss factor: increases with both pickup radius and gap size, whilst gap and height have negligible effect.
Fig 8: Voltage signal for different pickup gaps, Z (BS) mode, with a 75 MHz filter applied.
Fig 7: Voltage signal for different pickup radii, ttbar (SR) mode, with a 75 MHz filter applied.
Fig 10: Wake-loss factor vs pickup gap, Z (BS) mode.
Fig 9: Wake-loss factor vs pickup radius.
Fig 6: Simplified flat pickup with geometric parameters labelled.

## Slide 9: Geometrical Studies: Varying Parameters of a Simplified Button
Resonant peak amplitudes in the wake impedance spectrum: increase with radius and gap. Increasing the back gap slightly decreases the amplitude of the largest peak.
Resonant peak frequencies in the wake impedance spectrum: increase as radius decreases, and increase slightly in frequency as height decreases and back gap decreases. Gap size has negligible impact.
Fig 11: The largest peaks in wake impedance as a function of frequency for different pickup heights, ttbar (SR) mode.
Fig 12: Wake impedance as a function of frequency for different pickup back gaps, ttbar (SR) mode.
Fig 5: Simplified flat pickup with geometric parameters labelled.

## Slide 10: Geometrical Studies: Different Geometries of a Circular Button
Fig 15: Cross-sections of some of the geometric models used. From top left clockwise: flat, stepped, conical and trapezoid.
Conical pickups pushed the resonant peaks in the impedance spectrum to higher frequencies compared to a flat pickup, which is beneficial due to the beam spectrum having a lower amplitude at higher frequencies.
Stepped buttons had no advantage.
Fig 14: Wake impedance of conical and stepped buttons (solid lines) simulated in CST, along with the beam spectral content for two operational modes (dashed lines).
Fig 13: The initial voltage signal for different pickup geometries, simulated in CST with the ttbar (SR) mode.

## Slide 11: Geometrical Studies: Different Geometries of a Circular Button
Trapezoid pickups had a similar effect to conical pickups, whilst being easier to manufacture.
CST results comparing a 1 mm tall flat button and a trapezoid button with a 1 mm parallel section and 1 mm cone are shown in Figs. 14-15.
The trapezoid has a beneficial effect on the impedance and a similar voltage signal to the flat button.
Fig 15: Cross-sections of some of the geometric models used. From top left clockwise: flat, stepped, conical and trapezoid.
Fig 16: The largest impedance resonant peaks for a flat and a trapezoid pickup, simulated in CST with the ttbar (SR) mode.
Fig 17: The initial voltage signal over time for a flat and a trapezoid pickup, simulated in CST with the ttbar (SR) mode.

## Slide 12: Geometrical Studies: Non-Standard Geometries
A study by A. Novokhatski suggested that elliptical buttons had a smaller wake-loss factor than round buttons of the same area [3].
In CST, I simulated elliptical buttons of various ratios with FCC-ee beam parameters and beam pipe. The results suggest a reduced wake-loss factor for ellipses with a longer axis along z axis. There was negligible impact on voltage results.
Fig 18: Voltage signal simulated after a 75 MHz filter for different ratio ellipses.
Fig 19: Wake loss factors for different ratio elliptical buttons for ttbar and Z modes.
Fig 20: Elliptical button with ratio 4 modelled in CST, sliced at z=0.

## Slide 13: Geometrical Studies: Non-Standard Geometries
The wake potential was smaller to start for larger ratios, but rang for longer.
This could cause issues if the wake potential is still significant when the next bunch arrives – there is a 25 ns gap foreseen between bunches (equivalent to 7.5 m).
Fig 21: Wake potential simulated for different ratio ellipses over 10 m, using the ttbar mode beam parameters.
Fig 22: Ringing in wake potential simulated for different ratio ellipses between 9 and 10 m.

## Slide 14: Geometrical Studies: Non-Standard Geometries
Elliptical buttons were also compared to pill-shaped and rectangular pickups, using a ratio of 4, keeping the area of the pickup the same, and using the ttbar mode.
The rectangle had the lowest wake-loss factor – but would sharp corners cause heating issues?
Shape | Wake-loss factor, V/pC
Ellipse | 1.29E-03
Pill | 1.38E-03
Rectangle | 1.01E-03
Fig 24: The wake impedance spectrum of different non-circular pickups.
Fig 25: The voltage after a 75 MHz filter of different non-circular pickups.
Fig 26: The wake potential of different non-circular pickups.
Fig 23: Pill-shaped button with ratio 4 modelled in CST, sliced at z=0.
Table 3: The wake-loss factor of different non-circular pickups.

## Slide 15: Thermal studies

## Slide 16: Thermal Studies
Due to the high beam intensities expected in FCC-ee during runs with the Z mode, it is vital to model the BPM heating, to ensure it remains within acceptable limits.
The first model submitted for power loss and thermal simulations is shown in Fig 16. The thermal studies suggested this would reach temperatures well beyond the acceptable limit.
The BPM was redesigned as shown in Fig 17. The seal material was changed to alumina as this has higher thermal conductivity than borosilicate glass.
Fig 27: A cross-section of the initial pickup model used in thermal studies.
Fig 28: A cross-section of the improved pickup model used in thermal studies.
Table 4: Results from simulating different pickups. The voltage is after a 75 MHz filter, and the temperature is from simulations of the Z mode.

## Slide 17: Bench-marking

## Slide 18: Bench-marking
Tests of an existing BPM at AWAKE have been used to benchmark CST results against measurements with beam.
The result is shown in Fig. 19. The peak to peak voltage is similar but significantly more ringing is present in the measured signal. This could be due to structures not included in the simulation.
Other benchmarking measurements have been taken at SwissFEL and CLEAR.
Table 5: Summary of the CST and AWAKE eBPM benchmarking.
Fig 29: Cross-section of the CST model of the AWAKE eBPM. Model courtesy Bethany Spear.
Fig 30: Measured voltage response over time of AWAKE eBPM compared with CST results, compensated for the cable and oscilloscope responses.

## Slide 19: Conclusions
Summary
Thermal simulations show that beam-induced heating will be significant in the Z mode operation, but could be mitigated by optimising the pickup geometry and selecting an insulator material with high thermal conductivity.
Geometry of the button has a significant impact on performance – for now a trapezoidal button is favoured, but other more ‘non-standard’ designs are being explored.
Future Work
Further iterations of design modifications and thermal studies will be undertaken and data from additional benchmarking measurements will be analysed.
Once studies converge to a promising model, prototypes will be built and tested both in the laboratory and with beam.

## Slide 20: Thank you for your attention! Merry Christmas!
Emily Howling
Joined a fanfare band on the sousaphone
Other developments during my doctoral studentship…
Learned the alphorn
Discovered sledging in Switzerland is more hardcore than in the UK…
Sang about science at the Ri
18/12/2025 JAI Fest

## Slide 21: References
M. Wendt, “A brief introduction to beam position monitors for charged particle accelerators,” IEEE Instrumentation and Measurement Magazine, vol. 24, no. 9, pp. 21–32, Dec. 2021, issn: 19410123. doi: 10.1109/MIM.2021.9620043.
A. Abada et al., “FCC-ee: The Lepton Collider,” CERN,Geneva, Switzerland, 2019
A. Novokhatski, F. Fransesini, M. Boscolo, et al., “JACOW : The design and electromag-netic analyses of the new elements in the FCC-ee IR vacuum chamber,” JACoW IPAC,vol. 2024, WEPR18, 2024. doi: 10.18429/JACOW-IPAC2024-WEPR18. [Online]. Available:https://cds.cern.ch/record/2913547.

## Slide 22
Colors
Backgrounds
Radiant Blue
Flash
Energy
Green
Red
Deep Blue
Use for Layout
Background Blue
Background Purple
Background Yellow
Background Grey

## Slide 23
Graphical Elements
Badges
Infographics
Separation lines 1.5 pt
Arrows
Use light badges on dark backgrounds
Use blue badges on light backgrounds
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!
This information is a badge because it is important!