## Slide 1: Beam stacking and RF knockout in Fixed Field Accelerators
Carl Jolly, D.J.Kelliher, J.-B. Lagrange, A. P. Letchford, S. Machida, D.W. Posthuma de Boer, C.T. Rogers, A. Seville
JAI fest 2025
18/12/25

## Slide 2: Contents
ISIS Neutron and Muon Source and ISIS-II
What are FFAs?
Beam stacking
  KURNS experiment to demonstrate beam stacking.
RF knockout during stacking and experiments at ISIS.

## Slide 3: ISIS and ISIS-II
ISIS is a pulsed Neutron and Muon source at the Rutherford Appleton Laboratory.
The ISIS accelerator is a 50Hz rapid cycling synchrotron (RCS) built in 1984.
ISIS parameters | Value
Circumference | 163 m
Energy Range | 70 – 800 MeV
Repetition Rate | 50 Hz
Charge | 2.5 – 3.0e13 protons-per-pulse

## Slide 4: ISIS and ISIS-II
More beam power = more neutrons
Various options for the proton accelerator are under consideration including an RCS, Accumulator ring or even an FFA.

## Slide 5: FFAs
Fixed Field alternating gradient Accelerator  FFA.
  In an FFA the bending field is fixed.
  The closed orbit moves to a higher radius with increasing energy.
  The magnets are generally a combined function element.
From: Topp-Mugglestone, M. E. (2024). Scaling fixed field accelerators: theory and modelling of horizontal- and vertical-excursion accelerators [PhD thesis]

## Slide 6: FFAs for spallation neutron sources
The goal of the accelerator in a spallation neutron source is to deliver as much beam power as possible with the specified time structure – typically 10s of Hz.
  Beam stacking allows an FFA to accumulate more beam in a single pulse.
  High power beam  low loss operation.
  Cost/power efficiency.
  More sustainable?

## Slide 7
Beam Stacking
The fixed field of an FFA allows you much more freedom to manipulate the beam.
  Techniques such as beam stacking become possible.

## Slide 8: Beam Stacking
Inject beam 1
Time
Energy
The fixed field of an FFA allows you much more freedom to manipulate the beam.
  Techniques such as beam stacking become possible.

## Slide 9: Beam Stacking
Inject beam 1
Time
Energy
Accelerate
The fixed field of an FFA allows you much more freedom to manipulate the beam.
  Techniques such as beam stacking become possible.

## Slide 10: Beam Stacking
Inject beam 1
Time
Energy
Accelerate
Debunch
The fixed field of an FFA allows you much more freedom to manipulate the beam.
  Techniques such as beam stacking become possible.

## Slide 11: Beam Stacking
Inject beam 1
Inject beam 2
Time
Energy
Accelerate
Debunch
Accelerate
Debunch
The fixed field of an FFA allows you much more freedom to manipulate the beam.
  Techniques such as beam stacking become possible.

## Slide 12: Beam Stacking
Inject beam 1
Inject beam 2
Time
Energy
Accelerate
Debunch
Accelerate
Debunch

## Slide 13: Beam Stacking
Debunch
Inject beam 1
Inject beam 2
Time
Energy
Accelerate
Debunch
Accelerate

## Slide 14: KURNS FFA
Located near Osaka in Japan.
  The KURNS FFA was the proton driver for a prototype accelerator driven nuclear reactor.
Now (temporarily?) shutdown.
  Our beam stacking experiment was one if its final runs!

## Slide 15: Demonstration of beam stacking at KURNS FFA in 2023
Schottky signal from 2 stacked beams
Second beam
First beam, the area of the peak is smaller as some of the beam has been lost.
Results published in Physical review accelerators and beams here: T. Uesugi et al. - Beam Stacking Experiment at a Fixed Field Alternating Gradient Accelerator
Beam stacking was first demonstrated at the MURA FFA in the 1960s
We attempted to make a more systematic measurement at KURNS.

## Slide 16: Beam loss during stacking
Investigating the cause of beam loss:
  The loss only happened in beam 1  so likely not caused by some transverse effect/aperture limitation.
  The loss still happened even if the beam 2 RF bucket was empty  implied that the loss was related to the RF.
Beam loss happens here.
Inject beam 1
Inject beam 2
Energy
Accelerate
Debunch
Accelerate
Time

## Slide 17: What caused the beam loss?  RF knockout
In a scaling FFA, the orbit is dispersive everywhere in the ring.

## Slide 18: What caused the beam loss?  RF knockout
In a scaling FFA, the orbit is dispersive everywhere in the ring.
Every time the particle gains energy from the cavity, the equilibrium orbit moves because of the finite dispersion.
   Equivalent to an instantaneous, horizontal displacement when passing the cavity.

## Slide 19: What caused the beam loss?  RF knockout
In a scaling FFA, the orbit is dispersive everywhere in the ring.
Every time the particle gains energy from the cavity, the equilibrium orbit moves because of the finite dispersion.
   Equivalent to an instantaneous, horizontal displacement when passing the cavity.
If these displacements synchronise with the horizontal tune then they could build up turn by turn.

## Slide 20: RF knockout mechanism

## Slide 21: RF knockout mechanism

## Slide 22: RF knockout mechanism
The RF knockout resonance condition is:

## Slide 23: To recap
Beam stacking allows an FFA to accumulate more beam and deliver to the target.
But the beam stacking RF program can cause beam loss through RF knockout.
RF knockout happens when the horizontal tune synchronises with the RF knockout displacements.
  The displacements build up like an integer resonance.
Inject beam 1
Inject beam 2
Time
Energy
Accelerate
Debunch
Accelerate
RF knockout loss happens here.

## Slide 24: Mitigating RF knockout

## Slide 25: How can we prevent RF knockout driven beam loss?

## Slide 26: How can we prevent RF knockout driven beam loss?
All depends on removing the driving force from RF knockout.

## Slide 27: How can we prevent RF knockout driven beam loss?
How can we remove the driving force?
  Reduce the RF voltage or accelerate faster.
All depends on removing the driving force from RF knockout.

## Slide 28: How can we prevent RF knockout driven beam loss?
How can we remove the driving force?
  Reduce the RF voltage or accelerate faster.
  Cancel out the RF knockout displacement with down stream cavities (local cancellation).
All depends on removing the driving force from RF knockout.

## Slide 29: How can we prevent RF knockout driven beam loss?
How can we remove the driving force?
  Reduce the RF voltage or accelerate faster.
  Cancel out the RF knockout displacement with down stream cavities (local cancellation).
  Leverage the properties of the RF knockout process to cancel out the beam oscillation (global cancellation).
All depends on removing the driving force from RF knockout.

## Slide 30: Experiments at ISIS
ISIS is of course a synchrotron and not an FFA.
  We cannot perform “proper” beam stacking in ISIS but we can imitate a beam stacking RF program using “storage ring mode”.
  Allows for the investigation of RF knockout mitigation methods without an FFA.
  … It turns out that the ISIS RF cavity layout is very convenient for testing RF knockout.

## Slide 31: No mitigation case
This scenario is equivalent to the situation at the KURNS FFA beam stacking.
ISIS fundamental RF cavity layout

## Slide 32: No mitigation case
Beam loss when the RF knockout conditions are met.
This scenario is equivalent to the situation at the KURNS FFA beam stacking.
ISIS fundamental RF cavity layout

## Slide 33: 2 opposite cavities (global cancellation)
This RFKO condition is not cancelled.
This one is cancelled
2 RF cavities on exact opposite sides of the ring
By using more cavities, more conditions will be cancelled.
ISIS fundamental RF cavity layout

## Slide 34: Summary
FFAs are one option for the proton driver for ISIS-II.
Beam stacking allows an FFA to accumulate beam and deliver more beam power to the target.
RF knockout can cause beam loss during the beam stacking RF programme.
Through a series of experiments at ISIS we’ve shown it is possible to mitigate the loss from RF knockout.
  Results published here and submitted to PRAB.

## Slide 35: Back ups

## Slide 36: Experimental confirmation of RF knockout at ISIS
Procedure:
Set the magnets to a constant field (ie no acceleration).
Inject 70 MeV coasting beam.
Run this RF program to imitate a Beam Stacking RF program.

## Slide 37: Experimental confirmation of RF knockout at ISIS
Procedure:
Set the magnets to a constant field (ie no acceleration).
Inject 70 MeV coasting beam.
Run this RF program to imitate a Beam Stacking RF program.
Beam loss when the RF knockout conditions are met.
2.9*
2.1*

## Slide 38: Global cancellation
Using the symmetry of the lattice, it is possible to cancel some of the RF knockout resonances…
Driving force from one cavity only.
Add term for cavities
cavity position in the ring.
C = ring circumference
i.e /C = angular cavity position.
harmonic number

## Slide 39: Global cancellation
Using the symmetry of the lattice, it is possible to cancel some of the RF knockout resonances…
Driving force from one cavity only.
Add term for cavities
For two cavities on opposite side of the ring:
cavity position in the ring.
C = ring circumference
i.e /C = angular cavity position.
harmonic number

## Slide 40: Global cancellation with two opposite cavities
Then the total force becomes:
When is an odd number the RF knockout driving force is zero.

## Slide 41
As the two voltage from the two cavities becomes more unequal, the RF knockout displacements return.
  Zooming into the mitigated condition.
    Still a small kick even with equal voltages  probably because of the error in the gap volts.
Global cancellation results

## Slide 42
As the two voltage from the two cavities becomes more unequal, the RF knockout displacements return.
  Zooming into the mitigated condition.
    Still a small kick even with equal voltages  probably because of the error in the gap volts.
  Unlike the local cancellation this method does not effect the acceleration of the second beam.
     But it does not cancel every condition.
Global cancellation results