## Slide 1: Neutron transmission as a surrogate to tightly constrain neutron capture rates on radionuclides*
10th Workshop on Nuclear Level Density and Gamma Strength, Oslo, Norway
May,18th – 22nd, 2026
LA-UR-26-xxxxx
Experiendo cognoscitur
Th. Stamatopoulos1, P. Koehler1, C. Blough2, E. Bond3, S. Chasapoglou1, A. Couture1, B. DiGiovine4, S. Essenmacher1, M. Hochanadel5, D. Kral1, A. Marenco6, A. Matyskin7, V. Mocko3, T. Morrow1, J. Morrell3, E. O’Brien3, E. Renner1, G. Rusev3, D. Schmidt2, J. Svoboda1, J. Ullmann1, C. Vermeulen3
Physics Division, Los Alamos National Laboratory, 87545, NM, USA
Materials Science and Technology Division, Los Alamos National Laboratory, 87545, NM, USA
Chemistry Division, Los Alamos National Laboratory, 87545, NM, USA
Weapons Engineering Verification & Validation Division, Los Alamos National Laboratory, 87545, NM, USA
Sigma Division, Los Alamos National Laboratory, 87545, NM, USA
Plutonium Supply and Disposition Division, Los Alamos National Laboratory, 87545, NM, USA
Radiation Science & Engineering Center, College of Engineering, Pennsylvania State University, 6801, PA, USA
*Funded by LANL/LDRD-DR,OES, NCSP

## Slide 2: Table of Contents
Motivation
Neutron transmission measurements
Neutron transmission at LANL
A few highlights
A sneaky peak in the future

## Slide 3
Neutron-induced reaction studies

## Slide 4
The what-we-know
Capture cross sections at thermal are known mostly for stable isotopes and actinides
Notes: This work is focused on the (n,g) process. Measuring neutron capture rates it not trivial for radioactive nuclei. Just for fun look at the known (n,g) cross section for 25meV neutron energy. All the grey boxes are unknown. The gray squares are typically radionuclides.

## Slide 5
Neutrons impinge on a sample
Gamma detectors are close to the sample and detect the gammas from the de-excitation.
Works fine for stable or moderately radioactive samples.
What about unstable nuclides?
A new indirect technique is proposed:
  Neutron transmission experiments to measure the (n,tot) cross section
  R-Matrix fits of the resonances seen in the transmission spectrum
  Fit results to calibrate the Nuclear Statistical Model and tightly constrain (n,γ)
Neutron capture measurements

## Slide 6
The technique in a nutshell
Resonances can be used across an energy region ΔΕ to calculate the 3 ingredients needed to extract or constrain the average capture cross section
Average level spacing (N: number of resonances in the ΔΕ interval).
Neutron strength function for s-waves , where
  g is the spin factor for a resonance with spin J
  Γ0n is the reduced neutron width
Average radiation width <Γγ>
The capture cross section is related to these quantities
k : Wave number
W : Width fluctuation factor
Notes: n the Hauser-Feshbach formalism, the width fluctuation factor represents the effect of the statistical fluctuations in the nuclear levels on the width (or probability) of a particular reaction channel. It accounts for the fact that the widths of these levels are not fixed values but can vary due to the uncertainty principle of quantum mechanics. Essentially, it helps to adjust the predicted cross sections for nuclear reactions to better match experimental data.

## Slide 7
The technique in a nutshell

## Slide 8
Proof of principle: in brief
Data on 151Sm(n,tot) from Kirouac and Einland (10.1103/PhysRevC.11.895)
Resonance data up to 300 eV (120 resonances)
Resonances were fitted with SAMMY
13 Γγ values were obtained
<Γγ> = 96.5(14) meV
Level spacing D0 = 1.10(7) eV
Strength function 104xS0 = 3.58(59)
TALYS was adjusted to these values and compared with recent (n,γ) data
  Level density parameter α(Sn)
  Optical model potential depth
  Optical model potential diffuseness
  Photon strength function was normalized to give the <Γγ> value https://nds.iaea.org/talys/tutorials/talys.pdf
Good agreement with the data in EXFOR

## Slide 9
Neutron transmission measurements

## Slide 10
Traditional transmission measurements: How to
~10m
~10m
Neutron
detector
Neutron
beam
Collimator
The neutron spectrum (Cout) and backgrounds (Bout) are recorded by a neutron detector (sample out)
A sample, (~cm in diameter), is installed and absorption dips appear (sample in)
The transmission T is the ratio sample in/out
Transmission measurements provide information on the total (Γ) and neutron (Γn) widths and the level spacing (D0) Γ : Transmission dip width Γn : Transmission dip depth D0: Distance between transmission dips
Γ
Γn
D0

## Slide 11
Example: we only have 1mg of Au and our collimator is 1cm in diameter
  Cylindrical Au sample: 1 cm diameter  Length = 0.7μm  areal density = 3.882e-6 at/b.
  The sample is too thin to observe resonances.
  We need to have a longer (or thicker) sample to see resonance dips.
  If areal density = 1e-3 at/b  Length = 169 μm (chose “any” value)  30μm diameter
Traditional transmission measurements: Challenges
Limited mass
  Hard to produce large amounts of radioactive materials (budget, half-lives)
  Dose rates
Given mass and length restrict the volume.
Reducing the diameter seems to be a solution

## Slide 12
Sample cycling is needed therefore a positioning system must be utilized.
Positioning systems have a finite accuracy and that’s a serious bottleneck, in cycling small and radioactive samples
  Repositioning precision and risk mitigation
Precise repeatability of the sample’s position, relative to the collimation system, is not necessarily ensured.
Traditional transmission measurements: More challenges
What if…the sample didn’t have to move…?

## Slide 13
Binocular mode of operation: Simultaneous measurement of sample in and out
2 non-parallel beam lines, 1mm in diameter that point to the same area on the neutron production target.
No precise repositioning concerns, as long as the sample is precisely positioned beforehand: metrology network ~10μm and ~10 mdeg accuracy
  Knowing where a pencil lead is positioned across the length of a basketball court
Added bonus: measurements are completed in half the time!
Neutron
detectors
Neutron
beam
Collimator
Non-traditional measurements: Binocular approach
Target/moderator
~15m
~15m
Not to scale

## Slide 14
Neutron transmission at LANL

## Slide 15
1 km long LINAC
Up to 800 MeV protons
Multi-user proton (p) and neutron (n) facility
  Isotope Production Facility (IPF) (100 MeV p)
  Proton irradiation (pRad) (800 MeV p)
  Ultra Cold Neutrons (UCN) (<300 neV n)
  Lujan Center (meV – keV n)
  WNR (keV – MeV n)
  Target 4 (500 - 800 MeV p)
LANSCE: The Los Alamos Neutron Science Center

## Slide 16
800MeV protons impinge on a 3-way split W target.
DICER points to the H2O moderator and the target
Mark-IV (M4) : New neutron target at Lujan, est. 2022
Simulation
P. Koehler

## Slide 17
Neutron spectrum
Mark-IV provides an enhanced keV spectrum compared to Mark-III
Mark-IV is expected to improve the neutron energy resolution
Preliminary
S. Chasapoglou
Th. Stamatopoulos

## Slide 18
Description of the apparatus:
Device for Indirect Capture Experiments on Radionuclides
A. Stamatopoulos et al., NIMA (1025) 166166, 2022
A. Stamatopoulos et al., IEEE Trans. Nucl. Science 70, (2023)
A. Stamatopoulos et al., Neutron News 33, 12 – 14 (2022)
P. Koehler
Th. Stamatopoulos
A. Couture
B. DiGiovine
G. Rusev
J. Ullmann

## Slide 19
Sophisticated collimation system
Rotating beam blocker
Binocular collimator
Aperture stop
Rotating inner cylinder with 3 holes
30 cm in length
Provides 0 - 2 beams
Stepped design to avoid neutron stream paths
Remotely controlled
Divided in a top and bottom part
Sample is installed in the collimator in the Maxwell kinematic stops
1.5 cm length, 1 cm diameter sample envelope
1 mm collimation
Kinematic stops ensure repeatability when installing the top part.
Cuts off the beam penumbra
Ensures two sharp beam spots at a 31 m, 9.5 cm in diameter

## Slide 20
Sophisticated collimation system
Rotating beam blocker
Binocular collimator
Aperture stop

## Slide 21
Single pixel detectors
A commercial 235U loaded fission chamber is installed at ~7.8 m from the neutron source, to monitor the flux.
Two types of single pixel 6Li-glass neutron detectors are available
  ORELA type: Dual PMT detector. - Chi-nu type : Single PMT detector. Less material in beam PMT in contact with glass Poorer light collection More material in beam
Currently exploring a detection system based on CLYC

## Slide 22
Multipixel detector
The Large Area Picosecond Photo-detector (LAPPD) is a multi-channel plate (MCP) based detector, able to provide spatial information (nominally ~mm)
8 x 8 pads, 20 x 20 cm total coverage area
20 cm
20 cm
B. DiGiovine
A. Couture
Th. Stamatopoulos
D. Kral

## Slide 23
A few highlights

## Slide 24
Laundry list
191Ir
193Ir
natCl
natCd
natGd
natBi
197Au
239Pu
95Mo
natCu
147Sm
149Sm
88Zr
133Cs
63Cu
103Rh
151Sm
88Y
natY
40Ar
239Pu (keV–MeV)
167-171Tm
73,74,75As
56,57,58Co
85Kr
36Ar
40K
70Zn
72,73Ge
77,82Se
98,99Ru
107Pd
145-156Eu
153,157Gd
160,161Tb
163,166Ho
169Er
175Yb
179,180mTa
173,174Lu
185W
186Ru
191Os
110mAg
Measured
Will be measured in the near future
134Cs
147Nd
147Pm
135Xe
35Cl
Could be measured

## Slide 25
The curious case of 88Zr (t1/2 = 83.4 days)
LLNL: σγth = 0.861(69) Mb Shusterman et al., Nature 565, p 328 (2019)
LLNL: Iγ = 2.530(280) Mb Shusterman et al., PRC 103 124614 (2021)
Systematic study taking data from Mughabghab reveals that this is an odd combination

## Slide 26
The curious case of 88Zr (t1/2 = 83.4 days)
It’s even hard to model such combination
SAMMY with different combinations didn’t yield such an enormous Iγ.

## Slide 27
DICER - IPF synergy: The 88Zr case – LANL Directed Research
The radioactive sample fabrication relies on the synergy between DICER and IPF
Proton irradiation of a suitable bulk material
Chemical separation and purification (600 mCi, 10 mL 88Zr + D2O●6mol/L DCl )
Gamma spectroscopy
A. Matyskin et al, Scientific Reports 13, 1736 (2023)
A. Stamatopoulos et al., EPJ., Conf. 260, 03006 (2022)
A. Stamatopoulos et al., J. Rad. Nucl. Chem. 331, (2022)
A. Matyskin
V. Mocko
B. DiGiovine
Th. Stamatopoulos

## Slide 28
Results
Compatible cross section: σthDICER = 771(31) kb vs σthLLNL = 861(69) kb
Incompatible resonance integral: IDICER = 15.21(67) kb vs ILLNL = 2530.0(280) kb
1 keV MACS in agreement with LANL evaluation MACSDICER = 1.6(12) b. vs MACSLANL = 1.1 b

## Slide 29
The curious case of 88Zr (t1/2 = 83.4 days)

## Slide 30
The curious case of 88Zr (t1/2 = 83.4 days)
Results published in Phys. Rev. Lett. and C.
Already compiled in EXFOR (2025ST03)
Next ENDF

## Slide 31
n+149Sm : Capture and transmission – Nuclear Criticality Safety Program
Detector for Advanced Neutron Capture Experiments (DANCE)
~4π calorimeter
DANCE to get the capture yields
DANCE also provides multiplicities
Different multiplicity distributions for different spins
DANCE is used as a spinometer

## Slide 32
R-Matrix analysis : Resonance parameters
Fits in capture and transmission data using SAMMY
About 40 spins were incorrectly assigned
Resolved 58 new resonances (215 vs 157 in evaluations)
Resolved doublet @ 15 eV
Evaluated Γn is too large

## Slide 33
Non-Statistical behavior
Statistically significant change in the Γγ distributions around 200 eV was observed.
Findings will be submitted for publication to Phys. Rev. Lett. (similar findings in 147Sm)
Phys. Rev. Lett.
Phys. Rev. C

## Slide 34
Non-Statistical behavior - more
Sm work gave rise to an interesting observation
Neutron-capture cross sections are exhibiting a statistically significant oscillating behavior

## Slide 35
A few more highlights
239Pu data are needed for criticality safety (<1% unc)
Hard due to 240Pu
Identified 100 mg 99.99%
DICER only needs 1 mg!
Improving evaluations
239Pu
133Cs data are needed for criticality safety (<1% unc)
Hard to do a measurement on pure Cs: pyrophoric
Hazard minimization
133Cs
Through the PARADIGM project, we’re employing ML to identify differential and integral experiments and reduce time in nuclear data evaluations: 3 vs 25 years!
Cost reduction
63Cu
Phys. Rev. X 15, 021086

## Slide 36
A sneaky peak in the near future – 88Y

## Slide 37
Development of a 0.1 mm collimator
A smaller collimator will enable measurements on even smaller/more radioactive/more exotic samples i.e. 88Y
  1 mm / 15 mg  200 Ci / 7.4 TBq
  0.1 mm / 150ug 88Y -> 2 Ci/74 GBq
Beta version fabricated and tested
Currently fabricating the collimator
Enclosed in 250 kg of Tungsten for shielding purposes

## Slide 38
Development of microjet printing
Radioactive sample fabrication through “3D” printing
Custom-made printer for use in hot-cells
Capability to characterize the sample
Grain of salt

## Slide 39
Chemistry development
Challenging to identify a chemical compound that is suitable for transmission
YCl3 could work but there is too much Cl
YOCl is great but hasn’t been verified
We developed a chemical process and verified the conversion of YOCl from YCl3 at 650 oC
  X-Rays beams at SLAC
  Hyper Spectral X-Ray Imaging at LANL
  Neutron beams at LANL/DICER
HXI
DICER

## Slide 40
Experiment
Experiments scheduled in the following months
  Irradiation of SrCl2 in IPF to make 88Y through (p,n) reactions
  Neutron transmission of 88YOCl at DICER
SrCl2
Inconel
casing
Test 88Y solution
Sample loading
with a robotic arm
Robotic arm
3D printed collimator

## Slide 41
Development of DICER64
Through an early career award, a new DICER variant at 64 m is being developed
Data taken to understand the performance and assess the feasibility of a new instrument
Promising results: significantly improved signal/background compared to DICER
Testing the idea of simultaneous transmission and prompt-gamma activation analysis (PGAA)/neutron capture measurements

## Slide 42
Justin Jorgenson
Evelyn
Bond
Ryan Amberger
Nataly Panczyk

## Slide 43
Thank you for your attention!

## Slide 44
Thank you for your attention!

## Slide 45
9Back-up slides

## Slide 46
The technique in a nutshell
Cases where the most probable reactions are capture and scattering
Scattering
Capture
Total
Each resonance can be analytically described by its Energy and Width
Similar to cross sections, resonance widths are:
Scattering
Capture
Total
At resonance energies:
At intermediate energies (keV):

## Slide 47
Metrology and alignment
Stations have 5&6 Degrees of Freedom: precision alignment systems
Collimators are fiducialized
  Fiducials: red fixed points on the elements that need to be positioned in a reference system
Laser trackers are used to locate the position of the collimators in the flight path cave
Alignment over the 30 m length must be held to very tight tolerances.
Alignment to better than 20um and 0.0100
Universal Spatial Metrology Network (USNM)
“Monuments” are installed in the flight path cave: blue fixed points in the flight path aka the reference system.

## Slide 48
Flux monitor
Sanity checks
Binocular collimator
Paddle configuration: should not affect the flux monitor
Does the binocular idea work?
Flux * efficiency: Left vs Right

## Slide 49
Example
What can be extracted from a resonance:
Assuming a single Breit-Wigner resonance, the capture cross section is proportional to:
If Γn >> Γγ then σ ~ Γγ . In that case the radiation width can be extracted from the resonance, but the neutron width can’t.
If Γn << Γγ then σ ~ Γn . In that case the radiation width can’t be extracted from the resonance, but the neutron width can.

## Slide 51
Development of filling station
Operations have to take place in a hot cell with a remote handling capability

## Slide 52
WNR – High energy neutrons
PFNS
Scattering
(n,z)
LENZ
Chi-nu, CoGNAC
Irradiation of Chips
Electronics
Irradiation of Chips
Electronics
General purpose
SREFT (n,f), SPIDER and LENZ
(n,f), FY, (n,z), …
(n,z)

## Slide 53
The Los Alamos Neutron Science Center - LANSCE
500-800 MeV protons
meV – keV neutrons
keV – MeV neutrons

## Slide 54
Lujan Center – Low energy neutrons
Lujan Center
DANCE (n,γ), (n,f) tag
DICER (n,tot), “(n,γ)”
SPIDER (n,f), FY, ...
LENZ (n,z)

## Slide 55
800MeV protons impinge on a 2-way split W target.
Nominally 20 Hz duty cycle (tunable down to 1 Hz)
Nominally 145 ns proton pulse width FWHM (tunable down to 9 ns)
DICER pointed to the liquid hydrogen moderator
Upper target for nuclear physics
Lower target for material science
The Mark-III (M3) neutron source (RIP in 2022)

## Slide 56
PARADIGM