## Slide 1: LC with Energy Recovery
K. Yokoya
EPFL meeting 2025-1210

## Slide 2: Introduction
Most popular direction of extension of linear colliders beyond Higgs is the energy upgrade
It is also possible to go to much higher luminosities using the energy recovery technology
Several ideas have been proposed. Among them ERLC, ReLiC and Ghost Colliders are being considered
I am giving an introduction to these ideas with emphasis on beam dynamics issues. Obviously, very, very brief in 20 minutes.

## Slide 3: Two Schemes
Deceleration after beam collision is essential for energy recovery
What to do after deceleration?
  Put the beam into a damping ring (DR) and wait (milliseconds) until the beam quality, damaged by the beam-beam interaction, is restored. Then, accelerate the beam again
    ReLiC
  After a weak damping (e.g., by wigglers), reaccelerate the beam again
    ERLC, Ghost Collider
acc
dec
dec
acc
DR

## Slide 4: Energy Transfer
There are many varieties of energy transfer schemes from the beam to be decelerated and the beam to be accelerated
Must be in the same RF cavity or in the two electrically connected cavities
  How to avoid collision in cavities?
ReLiC
ERLC,
Ghost 1
Ghost 2
2 right and 2 left going beams
Don’t care collision
Timing difference
Twin-Axis cavity

## Slide 5: Common Problem: Tail of Beamstrahlung
High-energy tail of beamstrahlung causes low energy electrons/positrons
They cannot be accepted by the DR (or the beam transport line for [B])
  Energy compressor (bunch expander)
The important parameter is the critical energy (divided by E0)
The number of photons with energy > is

## Slide 6: ReLiC
2 linacs each accelerates e+/e- and decelerates e+/e-
Beams cooled every cycle in DR
  linear collider concept
  Do not care about beam-beam tune shift
Avoid collisions of oppositely running beams by time separation
2IPs, e+/e- and e-/e;
polarized e+e- Recycling Linear Collider with high high-energy, high luminosity reach (V. Litvinenko, T.Roser, et.al.)
SNOWMASS2021
See V. Litvinenko LCWS2025 for the latest

## Slide 7: Acceleration/Deceleration Scheme
All 4 beams (acc e+, acc e-, dec e+, dec e-) all go through cavity center
  180 degrees of for e+/e- same direction
  acc and dec beams do not encounter in cavities
  They encounter in the sections between cavities where acc and dec beams are separated by electro-magneto separators
  h must be estimated. Original value too small

## Slide 8: Beam Current Limitation
Energy loss by synchrotron radiation in DR
  EDR = 2.5 GeV, for example
  Each particle stay in DR for 2 damping time  energy loss 2x2.5 = 5 GeV
Every particle loose 5GeV from IP to IP
If beam current is 100 mA, for example, the total radiation loss = 100mA x 5GeV = 500MW
Max beam current < ~10mA per beam
  Parameters in the next page say the beam current in linacs = 12mA
  This presumably means 3mA for each beam
Must go to large bunch population
  In contrast, ERLC must go to low bunch population to avoid HOM loss  too high beam current
Accordingly,
  Very high disruption
  Very small vertical emittance
    Note: horizontal beam size must be large to suppress Upsilon

## Slide 9: Suggested Parameters of ReLiC
CM Energy | GeV | 250 | 550
Length of 1 accelerator | km | 14.25 | 14.25
Accel. gradient | MV/m | 12.55 | 27.6
Bunches per train |  | 5 | 21
Particles per bunch | 1010 | 2.5 | 2.5
Collision frequency | MHz | 1.5 | 1.5
Beam currents in linacs | mA | 12 | 12
ex, norm | mm.rad | 4 | 4
ey, norm | nm.rad | 1 | 1
bx | m | 2.2 | 4
by (matched) | mm | 0.19 | 0.36
sx | mm | 6 | 6
sy | nm | 0.9 | 0.9
Disruption param Dx |  | 0.01 | 0.01
Disruption param Dy |  | 87 | 88
Total luminosity | 1034 | 140 | 153
https://agenda.linearcollider.org/event/10624/attachments/40242/63966/LCVision_Generic_backup_EPPSU.pdf
Cavity Q0 4x1010
Temperature 4.5K (Nb3Sn)
sz not found
Parameters are changing
Here, I use

## Slide 10: Key Technologies for ReLiC
CW cavity
  High Q (>1011 if 1.5K). Ideal if Nb3Sn cavity developed
  HOM damping
  But twin-axis cavity not needed
DR:
  Very low vertical emittance (eny=1nm),
    Cf. eny=20nm in ILC DR
  Short damping time (~ 1ms)
  large energy acceptance (>~10%)
  Bunch separation O(ns), beam current > 1A
  Sokolov-Ternov polarization (Vladimir says possible)
  MHz rate injection/extraction kicker, O(ns) rise/fall
Bunch compressor: ~15x at 10GeV

## Slide 11: Key Technologies for ReLiC (cont’d)
Small emittance increase in the main linacs
  Increase of normalized emittance << 1nm
    (ILC ~15nm in single pass)
Flat beam control (emittance ratio ~4000)
  Design of Final Focus System
High disruption (Dy ~ 100)
  Luminosity loss
  How much (transverse) damping time needed to restore the emittance?

## Slide 12: ERLC (Energy Recovery Linear Collider)
Proposed by V. Telnov
  LCWS21 telnov-lcws21.pdf
  arXiv: 2105.11015 (May 2021)
  JINST 16 (2021)12, P12025
  At first proposed for Ecm=250GeV
  Possible energy upgrade has been discussed in the v3
  e-e- Collider is proposed recently (LCWS2025) I do not touch it here.

## Slide 13: Outline of ERLC
ILC-like structure plus
  Inverse FFS (Final Focus System) after collision
  Decelerating linac from 125GeV to ~5GeV
  Bunch length decompressor
  Turn around, wiggler (1/200 = 25MeV loss), another turn around
Energy Recovery : Electrons during deceleration create RF which accelerates positrons (vice versa)
Deceleration and acceleration linacs must be “linked”
  “link” by couplers (LCWS) is almost impossible due to high power
  So, “link” by Twin Axis Cavity  To be discussed later
In spite of the name “ERLC” and its shape, the principle of the entire system is more like circular collider
  Concept of the beam-beam tune-shift limit plays an important role
  Must also work as damping rings

## Slide 14: Basic Conditions (1)
Energy spread due to the beamstrahlung
  The energy spread created by one collision
  Equilibrium with the damping (dEwiggler /EDR = 1/200)
  Gives the equilibrium
  Then, the constraint at IP

## Slide 15: Basic Conditions (2)
Beam-beam tune-shift limit
  Same as in circular colliders

## Slide 16: Basic Conditions (3)
Beam lifetime due to the beamstrahlung tail
  Beamstrahlung creates long low-energy tail of electron/positron distribution
  They are lost when the momentum bandwidth of the ring is exceeded, causing beam lifetime
  After beam-beam, the beam is decelerated 125GeV  5GeV (relative energy spread increased).
  Bunch decompressor necessary after deceleration: assume energy spread x 1/10, bunch length x 10)
  Assume the momentum bandwidth of 5GeV line ~ 3%
  Then, the acceptance at IP is h = 0.03 x 10/25 = 1.2%
  Required lifetime ncol ~ 106 turns
Telnov, LCWS2025

## Slide 17: Latest Parameters of ERLC (250GeV)
Telnov, LCWS2025
Beam current 235 mA
Too high !!

## Slide 18: Latest Parameters of ERLC (500GeV)
Telnov, LCWS2025

## Slide 19: AC Power and Cost
In the first version,
  Refrigeration 92 MW
  RF compensation of HOM loss 30M W
  Compensation of energy loss in wiggler 5.3 MW
  Total Wall Plus Power ~130 MW (Others --- DR, BDS, etc, may be ~15 MW)
More detailed estimation strongly depends on the HOM extraction, cavity Q0, choice of duty cycle (ideally, CW), refrigeration efficiency, etc.
Cost: presumably more than 2 x ILC
Evaluation by European Strategy for Particle Physics -- Accelerator R&D Roadmap
https://arxiv.org/abs/2207.02095
Page195

## Slide 20: TW Twin-Axis Cavity
ERLC requires twin-axis cavity
Travelling Wave idea
    S. Belomestnykh, et.al. arxiv 2307.06248.pdf. 2209.01074.pdf
  SW = TW(right)+TW(left)
  TW(left) does not contribute in acceleration
  Use waveguide for the return wave
This idea can be adopted in ERLC twin-axis cavity
    KY LCWS2024, ERL2024
  Can effectively gain factor ~1.7

## Slide 21: Beam Dynamics Issues (1): General
The entire system is a damping ring with extraordinary long insertion (~ 20km) of
  BC (bunch compressor)
  Acceleration linac
  FFS
  IP (beam-beam)
  FFS
  Deceleration linac
  BD (bunch decompressor)
Damping time
  25MeV energy loss by wigglers and arc magnets
  Longitudinal : 200 turns
  Transverse : 400 turns

## Slide 22: Beam Dynamics Issues (2) Transverse
Damping time is 400 turns
Stochastic effects accumulate over 400 turns, e.g.,
  Dogleg in FFS (to create dispersion necessary for chromaticity correction)
  Linacs due to the geoid-following orbit (ILC)
  Bunch compressors
Emittance increase in the linacs due to misalignment and wakes
  ERLC adopts 35nm of vertical normalized emittanceat IP (same as ILC)
  ILC expects ~15nm increase in the linac (20nm  35nm)
  Crazy number if multiplied by 400
  Major part of ~15nm would not accumulate
  But how large is the cumulative component?
    Chromatic filamentation
    Ground motion faster than ~10 kHz
    Also, beam-beam disruption?
  Careful studies are needed

## Slide 23: Bending Fields in ILC (1)
Bunch compressor
Vertical bend by off-center orbit in the quads to follow the earth’s curvature
Dogleg for positron generation 
Bends in Final Focus System
  To create dispersion
  ILC FFS is designed for Ebeam=500 GeV
  Dexn at 250GeV is 1/64, but not small enough compared with 1/400
   must be a bit longer

## Slide 24: Bending Fields in ILC (2)
2.2km
14mrad
Linac tunnel
Crossing angle 
  The beam line must come back to the main linac tunnel after IP
  A rough calculation shows this is marginal for ECM=500GeV (no problem for ECM= 250GeV)
  One more km may be needed
  Telnov proposes (nearly) head-on collision
Need a good optics design
Note: hor/ver emittances in Telnov’s parameter set are the same as in ILC TDR
LCF@CERN should think about
  Crossing angle
  Terrain-following linacs
  Tunnel crosssection

## Slide 25: Summary of ERLC
There are many issues to be studied but there seems to be no showstopper
  Emittance preservation
But
  High AC power consumption
  High cost, > 2 x ILC
Required R&D
  Twin-axis cavity. TW type suggested.
  Cryomodule design with efficient HOM absorber
  Higher Q? Other SC material?
  How many years? 10 years? 20 years?
If these problems are solved, ERLC may be a candidate of future luminosity upgrade of ILC
  But, perhaps, too expensive for energy upgrade

## Slide 26: Ghost Collider (1)
Modify Telnov’s ERLC like (idea by Erk Jensen)
  Split each linac into 2 (4 linacs of half length)
  Turn around at reach end at the energy Emax/2
  Electron and positron in the same bucket, one accelerated and the other decelerated
  Energy transfer within each cavity (twin-axis cavity is not needed)
  Almost no longitudinal HOM
  Disadvantage
    High energy arc at E=Emax/2 (synchrotron radiation loss)
      Energy upgrade extremely expensive
    Large energy ratio between electron and positron at the same location
    BPM for 4 beams (right/left going, electron/positron)
    Transverse HOM may be excited (electron and positron orbits may split due to misalignment, etc) but may be milder (?)
This is not DR

## Slide 27: Ghost Collider (2) (A. Hutton)
Further improvement for higher luminosity
Charge mixture at the IP
  Collision of mixed (e+ plus e-) bunches
  No beamstrahlung (1st order)
  To do this, insert chicanes after linac to make a delay of l/2
Problems
  Mixed-charge FFS
    Round beam ?? bx = by, ex = ey
  Energy upgrade difficult

## Slide 28: Ghost Collider(3) : Even more greedy idea
Single linac
  All 4 beams in the same linac
    Right (left)-going electron (positron)
  Don’t care about collisions in the linac
    Neutral beams !!
IP
Arc
Arc
SRF Linac
SRF Linac
Chicanes
LCWS2025
I cannot make a list of beam dynamics issues

## Slide 29: Summary
ReLiC, ERLC, Ghost Collider, all evolving
Each having many R&D items
  SCRF
Beam dynamics issues
  ReLiC
    Design of DR
    Preserve 1nm emittance
    Beam-beam interaction Dy~100
  ERLC
    High current beam dynamics (HOM, etc)
    Horizontal emittance
  Ghost Collider
    Too many