## Slide 1
Basic Principles of Silicon Microstrip Detectors
C. García y C. Escobar

## Slide 2
Setup components @ Lab.
EASY
Components of a silicon microstrip detectors
Sensor + ASIC
HV power supply
Trigger
Laser
Control unit
Data acquisition and monitoring
Radioactive source
Source of particle
ASIC: application-specific integrated circuit

## Slide 3
EASY system
EASY
Control unit
Data Acquisition Control.
Processing of the sensor and trigger data
Adjustable HV unit for microstrip sensor bias, with voltage and current display.
Include the laser source
Communication with computer software via USB
Sensor unit
Silicon microstrip sensor and the Beetle chip.
Opaque carbon fibre window to place radioactive source.
Laser micropositioner and focus system.
A diode placed under the detector provides a trigger signal.

## Slide 4
EASY system
EASY
Silicon microstrip
P-on-N Detector
Size: 20x20 mm2
Thickness: 300 µm
Channels: 128
Interstrip pitch: ??? μm
Beetle Characteristics
Low noise ASIC developed for CERN/LHC experiments
128 channels
Laser source
Wavelength: 980nm
Pulse width: 5 ns
Laser Spot: 20 μm
Micropositioner resolution: 10 μm

## Slide 5
Trigger
EASY

## Slide 6
Basic principle
EASY
Charge collected is proportional to the depletion area
Exercise 1
Drift
Recombination
Strips of p-type silicon on a n-type substrate.
Each strip creates a p-n juntion
Notes: Our divice consist of an 300 microns thick n type bulk. and thin layer of strips of p type silicon,. The abrupt junctions are formed between the strips and the bulk silicon. The depletion zone grows from the strips to the backplane so that, the device can operate partially depleted.
We nned amplification and shaping for full processing

## Slide 7
Basic principle
EASY
EASY sensor
Notes: Our divice consist of an 300 microns thick n type bulk. and thin layer of strips of p type silicon,. The abrupt junctions are formed between the strips and the bulk silicon. The depletion zone grows from the strips to the backplane so that, the device can operate partially depleted.
We nned amplification and shaping for full processing

## Slide 8
Basic principle
EASY
Exercise 2
Laser
Steps of 10µm
Notes: Our divice consist of an 300 microns thick n type bulk. and thin layer of strips of p type silicon,. The abrupt junctions are formed between the strips and the bulk silicon. The depletion zone grows from the strips to the backplane so that, the device can operate partially depleted.
We nned amplification and shaping for full processing

## Slide 9
EASY
Charge collection
Strip i , Event k
Beetle chip
Sampling
ADC (i,k)
TDC (i,k)
Charge
time

## Slide 10
EASY
Charge collection
ADC(i,k)= Offset (i)+ Common Noise (k)+ Electronic Noise (i) + Charge (i,k)
Strip i , Event k
N events
128 channels

## Slide 11
EASY
Depletion Voltage
Exercise 1

## Slide 12
EASY
CCE mip vs Laser
Exercise 1
1000mm sensor

## Slide 13
EASY
Charge Sharing
LASER
Exercise 2
Exercise 2

## Slide 14
EASY
Charge Sharing
LASER
Exercise 2

## Slide 15
EASY
Charge Sharing
LASER
Exercise 2

## Slide 16
EASY
Charge Sharing
LASER
Laser beam Spot
Strip width
Pich

## Slide 17
EASY
LASER
Laser beam Spot
Strip width
Pich
Charge Sharing

## Slide 18
EASY
Spatial resolution

## Slide 19
EASY
Spatial resolution

## Slide 20
EASY
Spatial resolution

## Slide 21
EASY
Spatial resolution
η-algorithm