## Slide 1
Valencia, June 18th, 2026
Muon Detectors
Cristina F. Bedoya
TIDPAN 2026

## Slide 2
Muon Detectors – TIDPAN 2026 - June 18th, 2026
2
C. F. Bedoya
What is a muon?
and why do I want to detect it?

## Slide 3
Muon Detectors – TIDPAN 2026 - June 18th, 2026
3
C. F. Bedoya
MUON
ELECTRON
Charge -1
Spin ½
Mass ~ 0,511 MeV/c2
MUON
Charge -1
Spin ½
Mass ~ 105,66 MeV/c2
Life-time τ = 2.2 μs
x 207
Highly penetrating
Travel macroscopic distances
Their clean experimental signature makes them one of the most valuable particles in modern physics experiments.
Decay:
Leptons:
No strong force

## Slide 4
Muon Detectors – TIDPAN 2026 - June 18th, 2026
4
C. F. Bedoya
Muons as key observables
1974 → J/ψ → μμ (3.1 GeV) 1977 → Υ → μμ (9.46 GeV) 1983 → W → μν (80.4 GeV) 1983 → Z → μμ (91.2 GeV) 2012 → H → ZZ* → 4μ (125 GeV) 2021-2022 → Bs → μμ precision era 2023-2024 → H → μμ observation
The physics became visible because the muons could be reconstructed precisely
They may be rare decays, but the topology is easy to reconstruct and the background is small
Clean final states

## Slide 5
Muon Detectors – TIDPAN 2026 - June 18th, 2026
5
C. F. Bedoya
Muon Production
Same way we produce muon beams:
Proton beam + target+ decay+ concrete
Atmosphere is a gigantic muon source:
Primary cosmic rays (90% protons, 9% Helium, 1% heavier, e, etc)
Secondary: collision with N2 or O2 (15-20 km) => pions, kaons => muons
At sea level:
~1 muon/cm2 min-1
τ ~ 2.2 µs
c·τ ~ 660 m
????
PSI, Fermilab, J-PARC and CERN.
Close to speed of light, their time is slower
µ+/µ- ~1.3
p(uud)
(ud)
(du)

## Slide 6
Muon Detectors – TIDPAN 2026 - June 18th, 2026
6
C. F. Bedoya
LHC COLLISIONS at CMS
COSMICS at CMS
Muons can be:
Calibration source (cosmic ray data taking routinely at CMS, LHC)
Muons for calibration

## Slide 7
Muon Detectors – TIDPAN 2026 - June 18th, 2026
7
C. F. Bedoya
Muons in underground neutrino detectors play a dual role:
unwanted background: few thousand meters water equivalent
signature: Muon neutrinos will most of the time interact via charge-current reactions
      ν N –> μ + X
energetic muon in the final state
(muon detected by Cherenkov radiation)
Muons can be:
Calibration source (cosmic ray data taking routinely at CMS, LHC)
Background in dark matter experiments and others => underground
      Even if the muon is detected and vetoed, its by-products mimic rare physics signals.
Muons as signal and as background
https://scoap3-prod-backend.s3.cern.ch/media/files/72139/10.1140/epjc/s10052-022-10658-6_a.pdf

## Slide 8
Muon Detectors – TIDPAN 2026 - June 18th, 2026
8
C. F. Bedoya
How Muons loose their energy?
i.e., how to detect them?

## Slide 9
Interaction with atomic nuclei
Charged particles: electromagnetic interaction
Excitation: Electrons are excited to higher energy states when they absorb energy and subsequently emit photons as they return to lower energy states.
Ionization: the atom looses electrons
Excitation
Ionization
Elastic collisions:
- Multiple scattering: elastic collisions with atomic nucleus.
  Higher Z, larger dispersion
  Higher pt, smaller dispersion
Radiative effects: Photon emission (Bremsstrahlung)
- The particle is slowed down or deflected as it interacts with the nucleus, and it may emit a photon, thereby losing energy.
  interaction with the atomic electrons
  (Inelastic collisions)
e-
e-
e-
photon
Muon Detectors – TIDPAN 2026 - June 18th, 2026
9
C. F. Bedoya

## Slide 10
Average energy lost per unit path length in a material due to collisions with atomic electrons, resulting in ionization and excitation of the medium.
Radiative region: Energy loss through bremsstrahlung radiation caused by the particle's deceleration or deflection.
Polarization of the medium reduces the ionization energy loss (polarization depends on medium density)
Bethe & Bloch formula -dE/dx Stopping power
MIP (minimum ionizing particle)
Particle charge and speed: z2 / β2
Medium properties: Z / A, I(ionization pot), densidad
Relativistic effects : β·γ and médium polarization (δ)
Muon Detectors – TIDPAN 2026 - June 18th, 2026
10
C. F. Bedoya
Energy loss in a material by a charged particle
↑ β => ↓ Energy loss

## Slide 11
Muon Detectors – TIDPAN 2026 - June 18th, 2026
11
C. F. Bedoya
Surface => 1
100 m rock => 10-1
1000 m rock => 10-3 - 10-4
LNGS, Canfranc => 10-6
Muons are often considered Minimum Ionizing Particles (MIPs) because, over a wide range of energies, their energy loss in matter is close to the minimum of the Bethe–Bloch curve.
Differently from electrons, bremsstrahlung becomes only
important above a few 100 GeV
They are the most penetrating charged particles :
in one meter of iron they lose only ≈1.5 GeV
(for muons in few GeV to a few tens of GeV)
Muons loose little energy
Heavy enough not to shower, light enough to be produced abundantly, and long-lived enough to cross entire detectors.

## Slide 12
Muon Detectors – TIDPAN 2026 - June 18th, 2026
12
C. F. Bedoya
Cloud chamber
A Little bit of history…
(Nobel prize for positron discovery in 1936)
Ionizing particle → creates ions (condensation nuclei) → supersaturated vapor condenses on the ions → droplets form along the particle track
Wilson received the 1927 Nobel Prize for the invention of the cloud chamber.
From cloud chambers to modern muon detectors, the underlying principle remains the same: charged particles ionize matter and leave measurable signatures.
Phys. Rev. 50 (1936) 263
Muons were discovered by Carl D. Anderson and Seth Neddermeyer in a cloud chamber experiment at CalTech in 1936

## Slide 13: A Brief History of Particle Physics and Detector Instrumentation
Muon Detectors – TIDPAN 2026 - June 18th, 2026
13
C. F. Bedoya
1960-1985: Bubble chambers (liquid instead of gas, vapor instead of drops)
>1980: Solid state detectors (Silica, Ge, etc)
>1970: Multiwire chambers (MWPCs and drift chambers)
~1930:
Photomultipliers, Geiger-Müller tubes, emulsions
~1910:
cloud chambers
Bubble chamber ‘61
1960: Spark and streamer chambers (trigger)

## Slide 14
Radiation detectors
Ionization
Excitation
Gas/Liquid
Scintillation
Semiconductors
Indirect detection of radiation :
Radiation generates light that in turns, generates electricity through a photosensor
Direct detection of radiation :
Radiation generates electrons that are sent to an electronics system
Ionization/excitation typical energies:
1-5 eV semiconductors
10 eV scintillation
30 eV gaseous
  Electron- ion pair (gas/liquids)
  Electron- hole (semiconductors, metals)
Muon Detectors – TIDPAN 2026 - June 18th, 2026
14
C. F. Bedoya
Muons can be detected by all of them!!!

## Slide 15
Radiation detectors
Muon Detectors – TIDPAN 2026 - June 18th, 2026
15
C. F. Bedoya
Gaseous
Liquid scintillator
Solid state
Plastic scintillators
Gaseous
Muons can be detected by all of them!!!

## Slide 16
How to detect a muon?
Muon Detectors – TIDPAN 2026 - June 18th, 2026
16
C. F. Bedoya
Usually you want to make sure the signal from your detector is not noise.
This is usually granted by the coincidence of signals from neighbouring detectors
Muon detection
layer
Muon detection
layer

## Slide 17
How to identify a muon?
Muon Detectors – TIDPAN 2026 - June 18th, 2026
17
C. F. Bedoya
Absorber
To ensure it is a muon, you need to make sure it is the only particle left.
Enough absorber that will stop all particles except muons and neutrinos (but you will not detect them…)
Muon detection
layer
Muon detection
layer
High Z materials
Usually instrumented (calorimeter)
Interaction length (λI):
distance over which a high-energy hadron (proton, pion, kaon, neutron, etc.) travels in a material before undergoing a strong nuclear interaction.
  After 1 λI => 37% survive
  After 2 λI => 14% survive
  …
  After 6 λI => 0.25% survive
Usually 12 λI calorimeters at LHC energies
Iron = 16.8 cm, copper = 15 cm..

## Slide 18
How to measure a muon?
Muon Detectors – TIDPAN 2026 - June 18th, 2026
18
C. F. Bedoya
Absorber
Now you are sure you have a muon, but likely you want to say something about its energy…
Curvature of the muon in the magnetic field is proportional to the momentum of the muon
Muon detection
layer
Muon detection
layer
Muon detection
layer
Curvature in a magnetic field:
100 GeV muon in 1T field, 333 m….
Large fields, large muon systems
Positive and negative muons bend in opposite direction
High Z materials
Usually instrumented (calorimeter)

## Slide 19
How to measure a muon?
Muon Detectors – TIDPAN 2026 - June 18th, 2026
19
C. F. Bedoya
Bending in an homogeneous field
Sagitta
s = R - R cos(θ/2) = R ( 1 - cos(θ/2))
For small angles:
cos(x) ≈ 1 - x2/2
s ≈ R θ2/8
s ≈ L2/ 8 R
s ≈ 0.3 B L2/8 pT
The momentum resolution is directly determined by how accurately the sagitta can be measured.
Difficult to measure high energy muons with precision, they bend little
Large muon detectors, and ALIGN LARGE ESTRUCTURES (civil engineering problem)

## Slide 20
Multiple scattering
Muon Detectors – TIDPAN 2026 - June 18th, 2026
20
C. F. Bedoya
Charged particles: large number of small
scattering processes when traversing matter
They are small, but many, they accumulate
They result in a change of the particle’s direction (Θ) and a displacement of its position (or exit point)
Highland formula
Lower momentum => More scattering
Greater thickness and density of material => More scattering

## Slide 21
Muon Detectors – TIDPAN 2026 - June 18th, 2026
21
C. F. Bedoya
How to measure a muon?
Muon systems: large, external part of the detector, embedded or after enough absorber, inside a B field
Muon systems: type of magnet (iron-core, air-core, …) , precision requirements, area to be covered, cost & maintenance
Price usually determines technology (gaseous detectors)

## Slide 22
Muon Detectors – TIDPAN 2026 - June 18th, 2026
22
C. F. Bedoya
Gaseous detectors
A charged particle ionizes the gas molecules, creating ion–electron pairs.
They move in all directions and lose their energy through collisions with the gas molecules (thermalization).
If an electric field is applied to the gas, ions and electrons experience forces in opposite directions and drift along the field lines: ion→cathode electron→anode
E field
Anode (+)
Cathode (-)
ions
+
+
+
+
electrons
-
-
-
-
Multiple ionizing collisions follow Poisson distribution
A second ionization process can occur with δ ray electrons: primary electrons with enough energy to ionize the gas: effects on the total number of ionization electrons !! (and spatial resolution as well )

## Slide 23
Gaseous detectors: Ionization
Muon Detectors – TIDPAN 2026 - June 18th, 2026
23
C. F. Bedoya
In gaseous detectors typically ~100 ion/electron pairs are produced by a MIP in 1 cm of gas
To be compared to ≈24.000 hole/electron pairs produced in 300 μm of Si.
The typical noise level of a signal amplifier is ~1000 e-
Ex , Ei : first excitation and ionization potentials
Wi : average energy per ion pair
NP , NT : primary and total ion pairs per cm for 1 proton
We need amplification!!
W≈25−35 eV/pair
MIP in Argon => ~100 electrons/cm

## Slide 24
Gaseous detectors: Avalanche Multiplication and Gas Gain
Muon Detectors – TIDPAN 2026 - June 18th, 2026
24
C. F. Bedoya
The gain (G), or gas amplification factor, is defined as
G=n/no n= total number of electrons after multiplication
n0=number of primary electrons in the absence of multiplication
Thus, the gain represents the factor by which the initial ionization charge is amplified within the detector.
If the electric field is sufficiently high, an electron is accelerated and gains enough energy to ionize a gas molecule, producing a new electron. The process repeats itself, giving rise to an electron avalanche.
        Electron avalanche
(a measurable charge pulse is induced on the readout electronics).
Townsend Avalanche
Near thin anode wires, GEM holes or Micromegas meshes:
E∼50−100 kV/cm
Electrons acquire enough energy to ionize new atoms.
First Townsend coefficient (α)

## Slide 25
Gaseous detectors: discharges
Muon Detectors – TIDPAN 2026 - June 18th, 2026
25
C. F. Bedoya
Avalanche growth is not unlimited.
Raether limit:
Ncrit∼107−108 electrons.
Beyond this:
Space charge builds up.
Streamer formation occurs.
Full discharge (spark) may develop.
Consequences
Dead time
Electronics damage
Detector ageing
Mitigation
Resistive electrodes (RPCs)
Segmented GEMs
Resistive Micromegas
Optimized gas mixtures
Multi-stage amplification
MSGC (1994)
Micro-Strip Gas Chambers

## Slide 26
Gaseous detectors: Operation modes
Muon Detectors – TIDPAN 2026 - June 18th, 2026
26
C. F. Bedoya
Depending on the applied voltage, different operating regimes can be identified:
Recombination region
  Electrons recombine with positive ions before reaching the anode.
Ionization region
  Electrons reach the anode, but no gas multiplication occurs.
Proportional region
  The number of electrons produced in the avalanche is proportional to the initial ionization.
  As a result, the deposited energy can be measured.
Limited proportionality region
  Saturation effects become significant.
  Strong photoemission leads to the development of secondary avalanches.
Geiger region
  Massive photoemission occurs throughout the detector volume.
  The pulse amplitude is no longer related to the initial ionization, so energy measurements are not possible.
Continuous discharge region
  The detector enters a self-sustained discharge state and can no longer operate properly.
Ionization chamber
Geiger-Müller counter
Proportional counter

## Slide 27
Gaseous detectors: Choice of gas
Muon Detectors – TIDPAN 2026 - June 18th, 2026
27
C. F. Bedoya
Gaseous detectors typically use noble gases because they require the lowest electric fields to initiate electron avalanches.
Argon is widely used due to its low cost and favorable operating characteristics.
Light
Abundant, cheap
Expensive, rare
Pure noble gases: unsuitable for proportional operation because excited atoms emit UV that can trigger secondary avalanches and discharges.
Noble gases are mixed with molecular additives such as CO₂ or iC₄H₁₀. They act as quenchers by absorbing excitation energy through non-radiative processes (vibrational, rotational), suppressing UV photon emission.
Also, some gases exhibit electron attachment and vibrational excitation channels, which reduce the probability of secondary avalanche formation (electronegative)
The combined effect of photon quenching and electron moderation allows gaseous detectors to operate stably at high gains, typically up to ∼ 104 - 105.

## Slide 28
Muon Detectors – TIDPAN 2026 - June 18th, 2026
28
C. F. Bedoya
GWP in Muon Detectors
GWP: Global Warming Potential
Several of the gases used in experiments have a very large GWP
The new EU Regulation (2023) calls for the total elimination of HFCs by 2050
Mixture cost can range from 1 CHF/m3 (Ar/CO2) to more than 100 CHF/m3 (Ar/CO2/CF4).
Typical flow 10 m3/h for about 300 days/year
Gas cost can range from 72 kCHF (Ar/CO2) up to 7.2 MCHF for (Ar/CO2/CF4)

## Slide 29
Gaseous detectors: Electron drift and diffusion
Muon Detectors – TIDPAN 2026 - June 18th, 2026
29
C. F. Bedoya
Drift
Electrons and ions move under electric field (μ mobility) vd= μ E
TYPYCAL DRIFT VELOCITY
  electrons (vd∼ cm/µs)
  ions (vd∼ cm/ms) (~1000 slower)
Diffusion
Thermal collisions broaden the cloud:
σ=2Dt​
Transversal diffusion related, typically, to spatial resolution
Longitudinal diffusion related, sometimes, to time resolution
Gas mixtures are often selected as much for their diffusion properties as for their gain characteristics.
Consequences
Spatial resolution degradation.
Limits maximum drift length.
Critical for TPCs and large drift chambers.
Drift velocities computed by Magboltz at Ar/CO2 at 3 bar

## Slide 30
Muon Detectors – TIDPAN 2026 - June 18th, 2026
30
C. F. Bedoya
Aging in Gaseous Detectors
Aging refers to the gradual degradation of detector performance caused by prolonged exposure to radiation and accumulated charge. Typical effects:
  Gain loss
  Increased dark current
  Reduced efficiency
  Higher discharge probability
  Mechanical and chemical damage
Cathode Damage
Surface modification
Increased resistivity
Secondary electron emission changes
Can lead to Malter currents and self-sustained discharges:
  Positive ion accumulation → charging of insulating layer → field emission → self-sustained avalanches
Aging Parameter
Detector lifetime is usually characterized by:
Qint=∫I dt
Integrated charge per unit length or area
GEMs: >100 mC/cm²
Mitigation Strategies
✓ Highest purity gas mixtures
✓ Careful material selection (low outgassing)
✓ Gas purification and recirculation
✓ Resistive protection layers, low currents
✓ Distributed amplification (GEMs)
✓ Extensive irradiation qualification tests
✓ Fluorinated gas additives (e.g. CF₄) to suppress polymer deposition (careful…)
Polymer Deposition
Avalanche-induced dissociation of gas molecules:
CF4, CH4, iC4H10 → free radicals
Development of deposits in the form of tiny whiskers (polymerization of chemical elements in the gas)
anode wires , GEM foils , Micromegas meshes
Main Aging Mechanisms

## Slide 31
Muon Detectors – TIDPAN 2026 - June 18th, 2026
31
C. F. Bedoya
Some examples of gaseous detectors

## Slide 32
Muon Detectors – TIDPAN 2026 - June 18th, 2026
32
C. F. Bedoya
Georges Charpak (Nobel Prize in 1992)
Ionization
Drift
Multiplication
-HV
-HV
GND
+
e-
FIRST LARGE MWPC (CERN 1970)
Nucl. Instr. Meth. 62(1968)282
Major breakthrough in gaseous detectors:
Signal can be connected to the electronics chain and into the computer
Photography scanning could be abandoned
MWPC: Multiwire Proportional Chamber

## Slide 33
Muon Detectors – TIDPAN 2026 - June 18th, 2026
33
C. F. Bedoya
Several approaches to extract the
2nd coordinate from MWPCs were used:
Crossed wire planes
Charge division: resistive wires read
out from the two sides
Time division: comparing the signal
arrival time at the two wire ends
Segmented cathode planes, picking
up the induced signal, leading to a
number of variants of the MWPCs:
Cathode Strip Chambers (CSCs)
Thin Gap Chambers (TGCs) (triggering)
From MWPC to CSC, TGCs
CSCs @ CMS
TGCs @ ATLAS
Gas: Ar/CO₂/CF₄
Gap: 5–10 mm
Gain: 105
Resolution: 50–150 μm
Timing: ~5 ns
Rate capability: several kHz/cm²
Fine coordinate → strips Coarse coordinate → wires
Fast, precise and good operation in high-background environments.

## Slide 34
Muon Detectors – TIDPAN 2026 - June 18th, 2026
34
C. F. Bedoya
RPCs are composed of two parallel resistive electrodes operated at high voltage (typically ∼9 kV) and separated by a gas gap
The resistive plates limit the current and suppress discharges.
The gas avalanche induces a charge on external readout strips.
Thanks to the fast development of the avalanche, RPCs provide excellent timing performance, with time resolutions of about 1 ns.
They can work in avalanche mode (Gain~107) or streamer mode (Gain~109)
RPC: Resistive Plate Chambers
CMS RPC system.
ATLAS RPC barrel trigger.
BELLE and many neutrino experiments.
Advantages
Excellent timing (~1 ns)
Used in the trigger
Cost-effective
Limitations
Moderate spatial resolution (~0.1-1 cm)
Rate capability limited by electrode resistivity (~700 Hz/cm2)
RPCs @ CMS
Spacer
GAS
Capacitive induction
HV
GND
Graphite
Readout strip
Resistive plane
Isolation (Mylar)

## Slide 35
Muon Detectors – TIDPAN 2026 - June 18th, 2026
35
C. F. Bedoya
DT and MTD: Drift Tubes
Drift chambers allow great precision (~100 µm) with few channels (very cost effective).
They measure the drift time between the primary ionization and the arrival of the electrons at the anode.
The electron drift velocity depends on the reduced electric field E/p and the gas mixture.
VD=Drift velocity (~50 µm/ns)
DTs @ CMS
Gas: Ar/CO₂ (85/15) CMS – (93/7) ATLAS
Voltage: ~3600 V (CMS) 3080 V (ATLAS)
Gain: 104−105
Max drift: ~400 ns (CMS) – 700 ns (ATLAS)
Single tube spatial resolution: 85 μm (ATLAS) –250 μm (CMS)
Advantages
Very precise tracking.
Reliable long-term operation.
Ideal for low-background environments.
Limitations
Slow response.
Not suitable for extremely high particle rates.
MDTs @ ATLAS

## Slide 36
Muon Detectors – TIDPAN 2026 - June 18th, 2026
36
C. F. Bedoya
MPGD: Micropattern Gas Detectors
Extremely thin amplification gap (~50–100 μm, compared to 2 mm in RPC)
Produced using PCB-like photolithographic manufacturing techniques, enabling high precision and excellent reproducibility.
Excellent spatial and time resolution, with high radiation tolerance.
Common features
Micro-fabricated amplification structures
Gain ~104
High electric fields (40–100 kV/cm)
Spatial resolution ~50–100 μm
Rate capability >10 MHz/cm²
Excellent radiation tolerance
Low ion backflow
MPGDs represent the state-of-the-art gaseous detector technology for high-rate environments at the HL-LHC.
Main technologies
GEM: amplification inside microscopic holes
Micromegas: amplification in a thin mesh-anode gap
Pile up GEMs
50 μm Kapton foil
Copper on both sides
Perforated with ~70 μm diameter holes
Conductive metallic mesh suspended above the readout plane
Amplification gap 50–150 μm
Insulating pillars defining and maintaining the gap

## Slide 37
Muon Detectors – TIDPAN 2026 - June 18th, 2026
37
C. F. Bedoya
µRWELL
Single-amplification-stage MPGD derived from GEM technology.
Amplification in WELL structures etched on a Kapton foil.
Resistive layer provides intrinsic spark protection.
Simpler construction than multi-GEM detectors.
Spatial resolution: ~100 μm.
Rate capability: O(100 kHz/cm²–MHz/cm²).
Candidate technology for large-area tracking and timing applications.
Combines GEM-like amplification with Micromegas-like spark protection in a compact and cost-effective design.
Emerging MPGD: uRWELL

## Slide 38
Muon Detectors – TIDPAN 2026 - June 18th, 2026
38
C. F. Bedoya
+trigger!
Summary of Muon detectors comparison
MWPC @ LHCb
+GEMs
RPCs @ ALICE

## Slide 39
Muon Detectors – TIDPAN 2026 - June 18th, 2026
39
C. F. Bedoya
Muography
Muon radiography uses cosmic-ray muons to obtain images of structures that would otherwise be inaccessible.
First applied by Luis Alvarez in 1970 search for hidden chambers inside the Egyptian pyramids.
http://lappweb.in2p3.fr/~chefdevi/Work_LAPP/Arche/alvarez_70.pdf
November 2017
Discovery of a big void in Khufu’s Pyramid by observation of cosmic-ray muons
https://www.nature.com/articles/nature24647
Search for hidden tunnels and cavities beneath Mount Echia (Naples). https://doi.org/10.1098/rsta.2018.0057
Scintillator bars + SiPMs.
Arqueology
Civil infrastructure
Structural stability of the dome of Santa Maria del Fiore in Florence.
https://doi.org/10.1098/rsta.2018.0136
The system employed two drift-chamber detectors placed on opposite sides of the dome

## Slide 40
Muon Detectors – TIDPAN 2026 - June 18th, 2026
40
C. F. Bedoya
Muography
Monitoring of Mount Vesuvius using muon radiography.
https://doi.org/10.1098/rsta.2018.0050
plastic scintillators + SiPMs.
Vulcanology & Mining
Nuclear industry, borders security
Border security and cargo inspection
Muon tomography, X-ray imaging, gamma-ray imaging, and combined techniques are used to inspect trucks and shipping containers.
https://doi.org/10.1098/rsta.2018.0051
Uranium and lead ore exploration in the McArthur River (Canada) and Pend Oreille (USA) mines.
https://doi.org/10.1098/rsta.2018.0061
Fukushima reactors inspection
https://arxiv.org/abs/1209.2761
Nuclear waste inspection
https://doi.org/10.1098/rsta.2018.0048

## Slide 41
Muon Detectors – TIDPAN 2026 - June 18th, 2026
41
C. F. Bedoya
Muon Detectors: Summary
Muon systems are a fundamental component of modern particle physics experiments and, due to their large dimensions and cost constraints, gaseous detectors remain the preferred technology for their instrumentation.
The operation of gaseous detectors is based on ionization, electron transport and avalanche multiplication, with detector performance strongly influenced by the gas mixture and electric-field configuration.
Over decades, gaseous detector technologies have evolved from wire chambers to modern micro-pattern detectors, providing continuous improvements in spatial resolution, timing performance and rate capability.
Detector operation is limited by phenomena such as discharges and ageing, which require dedicated mitigation strategies and careful detector design.
Modern GEM, Micromegas and emerging µRWELL detectors technologies have extended the capabilities of gaseous detectors into the HL-LHC era, and future muon systems will combine high precision, fast timing and operation in extreme radiation environments.

## Slide 42
Muon Detectors – TIDPAN 2026 - June 18th, 2026
42
C. F. Bedoya
Questions?