## Slide 1: Espectroscopía de rayos g por reconstrucción de la trayectoria de los fotones: AGATA, the advanced g-ray tracking array
Begoña Quintana Arnés
Catedrática de Física Atómica, Molecular y Nuclear
Universidad de Salamanca

## Slide 2: What will this talk be about?
High resolution g-ray spectroscopy with highly-segmented HPGe detectors

## Slide 3: The before….
n-type coaxial
HPGe crystal
e-
Li-difused contact (n+)
B-implanted
contact (p+)
Ge semiconductors band gap = 3 eV
Working T = T( LN2) = -195,8 °C
Detector + preamplifier = RC circuit
t
V(t)
Vmax = Q/C
E
DV

## Slide 4: and now…
Not only E, but also (r,q,z)
With n-type HPGe crystals with highly-segmented B contact
Position-sensitive HPGe detectors

## Slide 5: How can it be?

## Slide 6: Position sensitive HPGe detectors…
Net signal shape provides the coordinate r
r

## Slide 7: Position sensitive HPGe detectors…
Transient signal shapes in the neighbor segments provide coordinates q and z
q

## Slide 8: Position sensitive HPGe detectors…
z
Transient signal shapes in the neighbor segments provide coordinates q and z

## Slide 9: A particular case: the AGATA detectors
Volume subdivided in 36 segments + central core
  mGe ≅ 2-3 kg, V 380 cm3, n-type coaxial crystal
  Asymmetric tapered hexagonal geometry.
  The internal contact or core is Li-difussed (n-type)
  The external contact is B-implanted (p-type) and it is electrically segmented

## Slide 10: What to do with the interaction position?
First, some basics of g-ray spectroscopy
Full-energy absorption peaks:
position, area -> Eg ,pg
Spectral continuum: Compton effect of photons from the source not absorbed in the detector and bremsstrahlung of charge particles
SENSITIVITY LIMITED BY THE BACKGROUND UNDER THE PEAK
Peak-to-total (P/T)
Factor of merit : e2/B
Detection limits:
NB → B
s
FWHM
Eg
N → e

## Slide 11: What to do with the interaction position?
But, with the interaction position…TRACKING!!!
Sg
Eg1
Eg2
The “classical” method: the Compton suppression
AC-detector
HPGe
detector
Second, how to reduce the Compton background?

## Slide 12: The development of clusters of highly segmented HPGe detectors
Compound or cluster detectors were developed in Europe in the nineties and used for first time in Euroball. This is the starting point up to reach the development of highly-segmented HPGe detectors…

## Slide 13: Why?...
Experiments with stable and radioactive beams to study nuclear structure at the frontier of knowledge

## Slide 14: But, why to study the atomic nucleus?
To reveal fully the characteristics of the nuclear forces, which are the glue of matter in the Universe
Nucleus properties determine the stability of matter.
Non stable nucleus are used in many applications so useful for the society as nuclear medicine and nuclear energy.
To create new nucleus leads to discover new nuclear properties and then, new matter…

## Slide 15: Some topics…
Evolution of shells and collectivity
Magic number evolution in highly excited nucleus
Very heavy nucleus towards new magic numbers
Disintegration modes of exotic nuclei
Cross sections of nuclear reactions for new nuclei
Neutron-halo (proton-halo?)
Neutron skin
Unbound systems…
Large
g-arrays

## Slide 16: Evolution of nuclear shells and collectivity
Examples of nuclear shapes
Oblate
Prolate
Spherical
Octupole
Tetrahedric
Examples of vibrational collective nuclei
GDR (isovector)
GMR (Isoscalar)
GMR (isovector)
GQR (isoscalar)
GQR (isovector)
Examples of nuclear shape vibrations
Y20
Y22
Y30
Y31
…

## Slide 17
b3 ≠ 0
b2 ≠ 0
b2 = 0
158Er
147Gd
Where to look at into the nucleus ?
J

## Slide 18: How to generate and measure exotic nuclei? …
ION BEAM
CHARGED PARTICLE AND MASS SPECTROMETERS
REACTION CHAMBER
T ∝ 3-10 MeV/nucleon
TARGET
)
s1 ∝ 1 bar
s3 ∝ 10-2 mbar
s1>> s2 >> s3
s2 ∝ 1 mbar
COULEX
MNT+Ev
Fu-Ev

## Slide 19: How to generate and measure exotic nuclei? …
Key aspects
The nucleus to be studied “must” be in an excited state
Direct detection of the “prompt” de-excitation g-rays emitted by the nucleus of interest
The detection system needs to be installed around the reaction point
In addition to the g-ray detector, frequently, complementary detectors and ancillary devices are necessary to improve selectivity or to perform a particular measurement.
REACTION products
CHARGED PARTICLE AND MASS SPECTROMETERS
Nuclear reaction production rates ∝ 10-15 s !!
p+
n
*
*
*
*
*
*

## Slide 20
High-resolution in-beam g-ray spectroscopy to study the nuclear structure far from stability
The excited nuclear state produced in a given nuclear reaction de-excites through electromagnetic transitions among the existing nuclear states, emitting a g ray per transition in a time around 10-12 s.
Eg2
Eg1
10-12 s
In-coincidence measurements: TRIGGER with conditions
EUROBALL
  Selectivity and multiplicity
  Factors that matters are e and P/T, i.e. signal-to-noise ratios
Time window:
10 ns →500 ns
HPGe
HPGe
HPGe
HPGe
HPGe
HPGe
HPGe
HPGe
HPGe

## Slide 21: What could we expect from a “clean” g-ray spectrum?
Eg, Ig and even decay times from peak shapes

## Slide 22: AGATA (the Advanced GAmma Tracking Array)
Number of encapsulated 36-fold segmented HPGe = 180
Number of high-resolution digital electronics channels = 6660
High throughput DAQ
Position sensitive operational mode
mGe 450 kg
VGe 68·103 cm3
80-82 % of 4p
With g-ray tracking algorithms
⇩
maximum e and P/T

## Slide 23: Signal readout and processing: digitisation
Digitiser (DIGOPT12) and pre-processing specifications:
Analog electronics of very low noise to obtain signal with spectroscopic quality.
Analog-to-digital conversor: effective number of bits (ENOB) = 11,5 -12 ∿ SIGNAL AMPLITUDE PRECISSION= 1/4096
Sampling frecuency: 100 MHz, band width = 30 MHz ∿ t = 10 ns, (Teorema de muestreo de Nyquist )
PSA uses the first ms
INFN-Milano, CSNSM-Orsay, IPHC-Strasbourg, STFC-Daresbury, IFIC & ETSE-Valencia

## Slide 24: But, what to do with the pulse shapes?
Characterization of the highly-segmented detector electrical response versus interaction position
DATABASE:
pulse shapes
⇩
interaction position (r,q,z)
First step…
See Gala’s poster to know SALSA, the R&D characterisation system under development in Salamanca
DB built from simulated pulse shapes is the current method used in AGATA
Liverpool´s mechanical
scanning table

## Slide 25: And, what’s next?
Pulse Shape Comparison (PSC)
PSC algorithms use statistical criteria to compare between the experimental signals and the DB ones (c2, Wilcoxon test,…)
Signals corresponding to an experimental event in a given detector
OUTPUT
Interaction position coordinates corresponding to the pulses recorded:
(r, q, z)
TRACKING
From a set of interaction positions corresponding to a given in-coincidence event, the most probable trajectory is evaluated through tracking algorithms that are based on the Compton Scattering formula

## Slide 26: Signal readout and processing: PSA farms and data storage
Data flow, control and storage

## Slide 27: Data merging process at
AGAPRO
GAna
nptool
RootFile
TS Branch
(
)
RootFile
)
TS Branch
(
RootFile
TS Branch
(
)
Merged
RootFile
AGATA V2
Mesytec
FASTER V3
SMART
l
D. Ramos from Ganil adapted

## Slide 28: Infrastructures
General view

## Slide 29: Infrastructure: hall and rooms
Experimental hall
AGATA array + front-end electronics area + pre-processing electronics and GTS Tree
DAQ area
Pre-processing GGP
(optical links of usual lengths = 60 m)
Control room
  An area of ~25m² to install all workstations required for the experiment control, data taking and on-line analysis with fast access to the GRID network for data archive
Maintenance: Detector Laboratory and Repository area

## Slide 30
Mechanical Infrastructures
STFC-Daresbury, GANIL, INFN-Milano, INFN-Padova
3 m

## Slide 31: Basic infrastructures
LN2 autofill system for Ge cooling:
  Water-free LN2 at 1.5 bar
  ATC with 4.5 L Dewar vessel needs four filling cycles per day, 5.2 L cycle ⇨ 90 ATCs needs 1,25 m3 a day
  Additional LN2 (about 7 L, in the GANIL configuration) is used at every filling cycle to purge the unwanted N2 gas and cool the transfer line
  Total LN2 volume per week = 10 – 11 m3
  Detector Support System (DSS) to control detector temperatures
Uninterruptible Power Supply (UPS)
Detector high-voltage (HV) power supply and its control system
Digitizer and detector low-voltage power supply (LVPS), water cooling system for the electronics

## Slide 32: The AGATA Collaboration
Bulgaria: Univ. Sofia
Denmark: NBI Copenhagen
Finland: Univ. Jyväskylä
France: GANIL Caen, IPN Lyon, CSNSM Orsay, IPN Orsay, CEA-DSM-DAPNIA Saclay, IPHC Strasbourg, LPSC Grenoble
Germany: GSI Darmstadt, TU Darmstadt, Univ. zu Köln, TU München
Hungary: ATOMKI Debrecen
Italy: INFN-LNL, INFN and Univ. Padova, Milano, Firenze, Genova, Napoli,
Poland: NINP and IFJ Krakow, SINS Swierk, HIL & IEP Warsaw
Romania: NIPNE & PU Bucharest
Sweden: Univ. Göteborg, Lund Univ., KTH Stockholm, Uppsala Univ.
Turkey: Univ. Ankara, Univ. Istanbul, Technical Univ. Istanbul
UK: Univ. Brighton, CLRC Daresbury, Univ. Edinburgh, Univ. Liverpool, Univ. Manchester, Univ. West of Scotland, Univ. Surrey, Univ. York
Spain: IFIC-CSIC, IEM-CSIC Madrid, LRI-USAL
Countries > 12 Institutions > 40

## Slide 33: Thank you for your attention