## Slide 1: Materials radiopurity and radioactive assays
Roberto Santorelli
CIEMAT – Madrid
roberto.santorelli@ciemat.es
TIDPAN 2026 - Taller de Instrumentación y Detectores en Física de Particulas, Astropartículas y Nuclear

## Slide 2: Objectives of this lecture
Figure out the importance of material assays and radiopurity-related aspects for low-background techniques
Know the most important sources of natural radioactivity for rare event search experiments
  Identify the main primordial radionuclides relevant for low-background experiments
  Grasp the principles of the cosmogenic production of radionuclides
  Anthropogenic contaminants
Understand the general framework of the problems posed by Radon
Know the principle of the most commonly used assay techniques

## Slide 3: Suggested references
Heusser "Low-Radioactivity Background Techniques"
Ann. Rev. Nucl. Part. Sci. 45: 543 (1995).
Formaggio J. A., Martoff C. J., “Backgrounds to sensitive experiments underground”, Ann. Rev. Nucl. Part. Sci. 54, 361-412 (2004).
S. Cebrián, “Cosmogenic Activation in Double Beta Decay Experiments”, Universe 6 (2020) 10, 162 .
M. Wojcik, G. Zuzel, “Review of high-sensitivity Radon studies”, Int.J.Mod.Phys.A 32 (2017) 30, 1743004.
M. F. L'Annunziata, “Handbook of Radioactivity Analysis”, Elsevier.
G.R. Gilmore, “Practical gamma-ray spectrometry by Gordon Gilmore”, John Wiley & Sons.
Several “material-assay” papers from different low-background experiments (DarkSide, XENON, EXO, LZ, LEGEND, NEXT, etc) .

## Slide 4
What you are expected to know:
Principles of radioactive decay
Principles of nuclear radiation
Principles of radiation interaction with matter
Rare events searches: No worries!... We are going to quickly summarize together some general aspects related to the rare-events searches and low-background techniques

## Slide 5
Rare-event searches: solar and SN neutrinos, double-beta decay, Dark Matter particles…
eV
0
Dark Matter
Reactor & Geo 
Solar & SN 
Atmospheric 
LBL 
Typical signal energy scale

## Slide 6
Rates as low as a few events per year are predicted
Improved detector technology
Optimized detector design
Improved techniques to extract weak signals over background and noise (e.g. machine learning)
Improved detector modeling, etc…
Rare-event searches: solar and SN neutrinos, double-beta decay, Dark Matter particles…

## Slide 7
Reduce the bkg level
Increase the target mass
101
102
103
10-1
10-2
10-3
Two fundamental strategies:
Rare-event searches: solar and SN neutrinos, double-beta decay, Dark Matter particles…

## Slide 8
Although the background sources in rare-event search experiments depend on the specific experiment, the main sources are generally:
Backgrounds
  These backgrounds can be shielded and vetoed
  (more or less efficiently)
  cosmic rays
  radiation from the materials surrounding the detector
radon in the experimental hall
Notes: School topics related to underground physics.

## Slide 9
It is very difficult to mitigate this type of background
Setting the stage: material-induced backgrounds
https://me.me/i/this-seems-likea-decent-amountof-pasta-what-the-okay-im-19124040
A simple and extremely effective strategy (to some extent) is to minimize the amount of material used to build the detector
The radiopurity of the detector assembly is crucial for achieving the sensitivity required for rare-event searches
Limited impact of active/passive shielding, rock overburden ineffective…
, , , from the detector materials, especially those surrounding the active volume, can produce the ultimate background for the UG experiments

## Slide 10
In rare-event searches, the background must be carefully assessed: all detector components have to be assayed
DS-50 @ LNGS
Material radiopurity: general aspects
Cryostat, sensors, support structure, Ar…

## Slide 11
Dedicated measurements to ensure the radiopurity of the materials used in the detector’s construction:
Quantify the content of radionuclides
Multiple assays methods and facilities: gamma counting, ICPMS, radiochemistry…
Simulation and calculation of radiation emission
quantify their impact on detector background
Calculation of the yields of primary and secondary particles, particle tracking …
Radiopurity assessment strategy
Notes: Extremely low-background features are more and more required: steady progress in material sourcing, manufacturing and assaying

## Slide 12
The radiopurity of commercial raw materials from different suppliers can vary by orders of magnitude
The contamination level can differ, even in batches of the same material with different geological or chemical histories because of differences in the chemical composition of ores
Clean manufactoring: materials can be contaminated during manufacturing or synthesis through the intentional or unintentional use of radioactively contaminated catalysts, molds, lubricants, or additives.
Prevent recontamination through appropriate storage and handling of clean materials
Sample, vendor, manufacturing, storage history
Notes: Extremely low-background features are more and more required: steady progress in material sourcing, manufacturing and assaying

## Slide 13
“Selecting candidate low-radioactivity materials is as much an art
as it is a science”
(Nucl.Instrum.Meth.A 839 (2016) 6-11)
Art?

## Slide 14
Radionuclides
For light stable nuclei, the number of neutrons is approximately equal to the number of protons (This reflects the structure of nuclear energy levels, in loose analogy with electron shells)
For light stable nuclei, N≈Z up to about calcium, (Z=20). For heavier stable nuclei, neutron excess increases with Z
Above Z = 82 (or 83), no stable isotopes of the elements discovered so far
λ is the decay constant of a given radionuclide  A = N λ = N/τ
The half-life t1/2 is the time required for half of the radioactive nuclei in a sample to decay
N of parent atoms decreases exponentially with time
t1/2= (ln2)/λ = 0.693  
https://www-nds.iaea.org/relnsd/vcharthtml/VChartHTML.html

## Slide 15: α,β,,….and neutrons
α-emitters produce secondary neutrons mainly through
(α, n) reactions
+
S.F.

## Slide 16
What we have to measure?
How can we measure it?

## Slide 17
What we have to measure?
How can we measure it?

## Slide 18
Naturally occurring radionuclides
Primordial
Found on the Earth and existing in their current form since before Earth was formed
Cosmogenic
Production of unstable nuclei by cosmic rays entering the Earth’s atmosphere
Artificial radionuclides
Anthropogenic
Nuclear tests, nuclear waste, accelerators…

## Slide 19
Relevant primordial radionuclides
For low-background experiments, the relevance of primordial radionuclides is driven by:
Abundance of the chemical element in the Earth’s crust
Isotopic abundance of the radioactive isotope
Abundance of the chemical elements in the Earth's upper continental crust

## Slide 20
There are 252 stable nuclides (it depends on the definition of “stability”…)
On Earth, ∼ 4.5 × 109 yr after its formation, most of the original unstable nuclei have decayed leaving only those with t1/2 > 108 yr
34 radionuclides that have half-lives long enough to have survived since the formation of the Earth 4.5×109 years (isotopes of 28 separate elements)
These long-lived nuclei undergo either highly forbidden β decays, involving large spin changes, or α decays with Q-values that lead to half-lives in this range
Primordial radionuclides
There are only a handful of nuclides with half-lives comparable to the age of the Earth
Most of them have half-lives significantly longer than the age of the Universe
(they are practically stable, with an abundance similar to the one of the stable isotopes of their respective elements)
Notes: Our galaxy’s stock of heavy elements was mostly produced in earlier generations of stars and dispersed into the interstellar medium by various processes (e.g. supernovae explosions can eject stable and unstable nuclei into the interstellar medium)
This cloud later condensed to form the stellar systems

## Slide 21
Relevant primordial radionuclides
1011y
1010y
109y
108y
“Fundamentals In Nuclear Physics From Nuclear Structure to Cosmology” - Springer
t1/2
Radiogenic heat in the Earth
For low-background experiments, the relevance of primordial radionuclides is driven by:
Abundance of the chemical element in the Earth’s crust
Isotopic abundance of the radioactive isotope
Half-life: long enough to survive since Earth formation, but short enough to produce measurable activity

## Slide 22
U, Th, and K dominate because they combine natural abundance, suitable half-lives, and radiologically relevant decay emissions.

## Slide 23
Potassium is one of the most common elements on the Earth’s crust
40K emits detectable gamma rays
40K
1.46 MeV
from 40K
In 10.72% of events, it decays to 40Ar by electron capture (EC)
Surface
UG
K content of the body is 0.2 %
40K in humans  primary source of radiation from our body
(practically constant)
For a 70-kg person, the amount of 40K will be about 4.26 kBq

## Slide 24
They do not decay directly to a stable state: each initiates a decay chain
Altogether, these chains include ≈42 radionuclides
The mass number of the members may be expressed as four times an appropriate integer (n) plus the constant for that series. Three naturally occurring series are:
Thorium series (4n): 232Th (t1/2 =1.4·1010 y)  10 radionuclides  208Pb (232Th ≈100% natTh)
Uranium series (4n+2) : 238U (t1/2= 4.5·109 y)  17 radionuclides  206Pb (238U ≈99.3% natU)
Actinium series (4n+3): 235U (t1/2= 7·108 y)  15 radionuclides  207Pb (235U ≈0.7% natU)
238U, 235U, 232Th
The neptunium series with Np-237 (with a half-life of 2 million years) 4n+1 series do not occur naturally, because the half-life of the longest lived isotope in the series is short compared to the age of the Earth.
The Np decay chain has no long-lived nuclei heavier than 209Bi.
 The chain thus consists of a single decay 209Bi → 205Tl(stable) (t1/2 = 1.9 × 1019 y)

## Slide 25
α decay
β decay
α or β decay
238U, 235U, 232Th

## Slide 26
-spectroscopy with HPGe detectors

## Slide 27
However….
In these chains there are alpha and beta emitters, most of which do not emit detectable gamma rays:
Gamma spectroscopy alone is not sufficient

## Slide 28
Equilibrium means that the activities of the parent and daughter nuclides are the same
Equilibrium in the chain
If no progeny atoms are present at time t = 0, the number of progeny atoms, N2, at any later time t is:
N0 is the number of parent atoms present at time N1(t = 0)
λ1 is the decay constant of the parent,
λ2 is the decay constant of the progeny
The apparent half-life of the progeny reflects the simultaneous production and decay of the progeny.
The ratio of activities A1/A2 for X and Y, respectively, is
Bateman equation
If (N2)0 progeny atoms are present at time t = 0, the expression for N2 is written
Notes: Secular does not mean eternal. Looking at a very long-term all secular equilibria are transient.
At the equilibrium the # of atoms Is maximum

## Slide 29
Example: Activity Evolution
Time [y]

## Slide 30
Example: Abundance Evolution
Time [y]

## Slide 31
“Secular equilibrium”: the half-life of the parent nuclide is very long and the half-life of the daughter nuclide is considerably shorter than that of the parent
A radioactive nuclide decays at the same rate at which it is being produced:
 the number of atoms present remains constant (over a certain period of time)
Over the 4.5 billion years of the Earth’s history, all U and Th decay chains have reached equilibria between the parent nucleus and the various descendants (assuming that the system has been closed for millions of years)
Minerals that contain uranium and thorium also contain virtually all daughter nuclides in their decay chains, provided the system has remained closed for a sufficiently long time
In secular equilibrium, all nuclides in the chain have the same activity
The mass of each daughter nuclide present in the mineral is proportional to its half-life
Mass / tonne (U-238)
54 g U-234
16 g Th-230
0.3 g Ra-226
4.4 mg Pb-210
Secular equilibrium

## Slide 32
chemical, artificial or natural processes (e.g. dissolution into groundwater) can remove one or more members of the chain.
Disequilibrium in natural decay chains
Equilibrium in the decay series is rarely maintained in most surface and near-surface geological environments, as a result of physical or chemical processes:
If, for example, uranium is dissolved from a primary uranium-bearing mineral by oxidation, the remaining radionuclides in the 238U series will be supported by its most long-lived radionuclide which is 230Th. If the dissolved uranium is then precipitated somewhere out of the system a new equilibrium will begin to develop.
The time required to attain the equilibrium is governed by the most long-lived daughter radionuclide in the series, 230Th in the case of 238U series. The half-life of 230Th is 75000 years and this time is required to reach 50% of equilibrium.
The disequilibria can be utilized in dating geological events.

## Slide 33
238U chain

## Slide 34
232Th chain

## Slide 35
Cosmic rays produce radioactive nuclei via their interactions with nuclei in the atmosphere and in the Earth’s crust
Cosmogenic radionuclides
14N + n  14C + p
14N + n  12C + 3H
These radionuclides are isotopes of lighter elements, and their half-lives vary widely
In the atmosphere, the most common radioactivity produced is that of 14C
14C is mixed throughout the atmosphere and enters the food chain through CO2 ingesting plants
The total production rate R of a radioisotope is obtained by summing over all target nuclei i and over all cosmic-ray particle components j:
Ni​ is the number of target nuclei
ϕj(E) is the energy-dependent cosmic-ray flux
σij​(E) is the production cross section for isotope i induced by particle j
(integral accounts for the contribution of all incident particle energies)
The primary components of cosmic radiation are high-energy alpha particles and protons, which induce nuclear reactions when they impact on the nuclei of the atmospheric atoms (especially oxygen, nitrogen and argon)
Notes: In rare circumstances, nucleons removed in spallation reactions can combine to form nuclei. For example the radioactive tritium isotope of hydrogen can be produced by cosmic rays by (for example) the reaction n 16O → H14N t1/2(3H) = 12.35 yr . (5.14) The atmospheric tritium combines with oxygen to form water that rains down on the Earth. Prior to the atmospheric testing of nuclear weapons and the Chernobyl reactor accident, this was he primary source of naturally occurring tritium. Because of its short half-life, tritium is absent in water from deep water reserves and also in crude oil
Primary cosmic ray particles hit the earth atmosphere producing a variety of particles
Cosmic muons can
create neutrons, β and γ backgrounds without leaving any traces in the detector
increase detector dead-time (if overhead burden is inadequate)
produce unwanted radioisotopes (even UG)

## Slide 36
Cosmogenic radionuclides
Fundamentals in Nuclear Physics - From Nuclear Structure to Cosmology – Basdevant, Rich, Spiro
At sea level (and obviously U.G) the muon flux dominates
There is, however, great variation at different heights of the atmosphere and at different latitudes.
The total intensity of these secondary's reaches a maximum at an atmospheric depth of about 150 g/cm (13.7 km altitude) and then falls off gradually
Most of the cosmogenic radionuclides are attached to aerosol particles and are deposited on the ground. Some, however, are gaseous, such as 39Ar (a noble gas), and thus stay in the atmosphere.
Muon-induced spallation: a high-energy muon emits a hard photon (virtual or real), which interacts photonuclearly with the nucleus and fragments it, producing radioactive residual isotopes
Electromagnetic/photonuclear showers: muon-induced bremsstrahlung photons and e± cascades generate hard photons that activate nuclei through photonuclear reactions such as (,n)
Muon-induced neutrons: secondary neutrons produced as by-products of muon-induced spallation or photonuclear reactions in electromagnetic showers, which then activate nuclei via reactions such as (n,), (n,p), or (n,2n)
Negative-muon capture: stopped μ- are captured by nuclei, converting a proton into a neutron and leaving the nucleus excited, possibly producing radioactive isotopes
Notes: This nucleus is a secondary product of neutrons who are themselves produced by high-energy cosmic-ray protons that breakup nuclei in the atmosphere. The neutrons then either decay or are absorbed. The most common absorption process is the exothermic (n,p) reaction on abundant atmospheric nitrogen
In rare circumstances, nucleons removed in spallation reactions can combine to form nuclei. For example the radioactive tritium isotope of hydrogen can be produced by cosmic rays by (for example) the reaction n 16O → H14N t1/2(3H) = 12.35 yr . (5.14) The atmospheric tritium combines with oxygen to form water that rains down on the Earth. Prior to the atmospheric testing of nuclear weapons and the Chernobyl reactor accident, this was he primary source of naturally occurring tritium. Because of its short half-life, tritium is absent in water from deep water reserves and also in crude oil
Primary cosmic ray particles hit the earth atmosphere producing a variety of particles
The total intensity of these secondary's reaches a maximum at an atmospheric depth of about 150 g/cm (13.7 km altitude) and then falls off gradually
At sea level, the muon flux dominates
Cosmic muons can
create neutrons, β and γ backgrounds without leaving any traces in the detector
increase detector dead-time (if overhead burden is inadequate)
produce unwanted radioisotopes (even UG)

## Slide 37
Cosmogenic radionuclides
For example neutron “spallation” reactions:
A neutron with kinetic energy greater than ∼20 MeV can remove two neutrons for a germanium nucleus,
e.g. n + 70Ge → 3n + 68Ge t1/2(68Ge) = 270.7day
This reaction results in an activity of 0.3 mBq kg−1 in Ge crystals produced at the Earth’s surface
This is the most important source of intrinsic radioactivity in the HPGe crystals
A fast neutron with kinetic energy above the (n,2n) threshold can remove one neutron from atmospheric argon,
e.g. n + ⁴⁰Ar → 2n + ³⁹Ar t1/2 (³⁹Ar) = 269 yr
This cosmogenic production leads to an activity of ~1 Bq kg⁻¹ in atmospheric argon
This is the dominant intrinsic radioactive background of ArAtm in low-background LAr detectors

## Slide 38
Cosmogenic radionuclides
The activation by the hadronic component can reach specific radioactivity levels higher than the residual contamination from primordial nuclides.
Since the intensity of cosmic radiation is constant over the long-term, the production of cosmogenic radionuclides is rather constant.
Materials have to be stored underground (the production of cosmogenic radionuclides stops and the activity decays away).
Materials extracted UG should be largely depleted in cosmogenic isotopes.
Notes: tritium is absent in water from deep water reserves and also in crude oil

## Slide 39
Rates of production of long-lived radionuclides
at sea level (atoms/kg/day)
Copper
Lead
SS
(Universe 6 (2020) 10, 162)

## Slide 40
Sources of artificial radionuclides:
nuclear weapons production and explosions;
nuclear energy production;
radionuclide production by reactors and accelerators (medical application etc…)
Artificial radionuclides form the largest group of radionuclides, comprising more than two thousand nuclides.
The explosion clouds of the most powerful tests entered the upper part of the atmosphere, the stratosphere, from where the radioactive pollutants have deposited on a global scale.
Artificial radionuclides
Cs-137 (T1/2=30.2 y), along with iodine-131, xenon-133, and strontium-90, has been released into the environment by nuclear weapons tests and major nuclear accidents.
The mean Cs-137 contamination in Eastern Europe following the Chernobyl disaster was several kBq/m2.
Notes: since the 1930s
Assieme al cesio-134, allo iodio-131 e allo stronzio-90, il cesio-137 era uno dei radioisotopi che ponevano il maggiore rischio per la salute tra quelli dispersi dall'esplosione della bolla d'idrogeno del reattore e il successivo incendio della grafite.
Dal momento che il cesio-137 è un sottoprodotto della fissione nucleare dell'uranio, un tipo di reazione nucleare attualmente per la maggior parte di origine artificiale, esso non si presentava in natura in modo significativo prima che cominciasse l'era atomica
Cs simile al potassio

## Slide 41
Artificial radionuclides
Kr-85 (T1/2=10.8 y) is one of the seven common medium-lived fission products
Kr-85 is produced in small quantities by cosmic rays interactions with stable Kr-84 in the atmosphere. Natural sources maintain a steady-state inventory of about 0.09 PBq in the atmosphere.
The Fukushima accident released an estimated 44–84 PBq of Kr-85 in the atmosphere

## Slide 44
Why is Rn a problem?
Radon is a noble gas and can escape both solid and liquid materials.
220Rn, 219Rn, and especially 222Rn (together with their daughters) emit several high-energy gammas
Rn daughters plate out electrostatically onto surfaces. This effect is strongly enhanced on statically charged surfaces such as plastics or glass
222Rn feeds the long-lived isotope 210Pb (T1/2​=22 y)
Techniques based on charcoal adsorption have been used which suppress Radon (by about a factor of 104-105).
222Rn problem
Rn emanates constantly from the rock.
222Rn concentration is significantly higher in an underground facility than on surface.
It is mandatory to protect a the material surface against Rn (particularly UG)

## Slide 45
What we have to measure?
U, Th, K, Cs, Co…
How can we measure it?

## Slide 46
One banana is a source of about  20 Bq of 40K   100 Bq/kg
How radiopure?
1 Bq 238U /kg  81  10-9 gU/g (81 ppb U)
1 Bq 232Th /kg  246  10-9 gTh/g (246 ppb Th)
1 Bq 40K /kg  32.3  10-6 gK/g (32.3 ppm K)
40K in humans  primary source of radiation from our body (practically constant)
    K content of the body is 0.2 %
    Natural abundance of 0.0117 % of KNat
    K-40 specific activity ≈2.6e5 Bq g-1
For a 70-kg person, the amount of 40K will be about 4.26 kBq ( 60 Bq/kg)
14C for a 70-kg person would be about 3.08 kBq (≈44 Bq/kg)
For a low-background detector, a human body is a radioactive object: per kilogram, we are about one hundred thousand times hotter than the materials we are trying to select.

## Slide 48
Common assay techniques
Gamma counting with HPGe crystals
Mass spectroscopy
    ICP-MS
    GD-MS
    LA-ICP-MS
Neutron Activation Analysis
Emission spectroscopy
    XRF
    ICP-AES
Radio-chemical methods (210Po extraction)

## Slide 49
Gamma spectroscopy with HPGe
Gamma rays produced by the great majority of radionuclides
The typical range for -rays emitted by nuclei is 50 keV - 10 MeV (endcap - size of the crystals)
Gamma spectrometry is a non-destructive technique
Gamma spectrometry using HPGe semi-conductor detectors is one of the best techniques to identify and quantify radionuclides: very good energy resolution
Operating Ge detectors not possible at room temperature (leakage current due to the small bandgap energy)
The germanium detector preamp is normally included as part of the cryostat package.
All of the cryostat materials around the detector should be as low Z as possible to reduce photon scatter. Hence, aluminum, magnesium, beryllium, Teflon, and Mylar are used whenever possible.
Notes: Germanium is by far the most common gamma-ray
detector material. High atomic number small band gap

## Slide 50
10 cm Cu-OF
20 cm Pb (~660 bricks or “donuts”)
Methacrylate Rn box.
Door
HPGe shielding
Courtesy of LSC

## Slide 51
Gamma spectroscopy with HPGe
Compton, photoelectric, and pair production cross section of Ge for high-energy g-rays.
Photoelectric cross section (barns) of Si (lower curve) and Ge (higher curve) as a function of energy (keV).
Notes: photoelectric cross section depends roughly on the fifth power
of the atomic number

## Slide 52
Ultra-Low Background Measurements Service- Hall C
7 HPGe p-type coaxial (2 kg)-LSC
1 SAGe Well model GSW275L-LSC
1SAGe Well model GSW400-Poland
7 mounted and taking data: Asterix, GeLatuca, GeOroel, GeTobazo, GeAnayet, GeAspe, GeRysy.
Obelix and GeLaraca (SAGe)-no shielding
Courtesy of LSC

## Slide 53
HPGe: Figure of Merit
Advantages:
The best technique to assay the -emitters: K-40, middle primordial decay chains, cosmogenics … etc
Relatively simple sample preparation
Non-destructive technique
Very good sensitivity achievable (<< mBq/kg)
Limitations:
Actual sensitivity strongly depends on the mass of the sample (not suitable for small samples)
Stringent detector stability and background requirements
Only sensitive to -emitters
Several weeks are typically necessary to assay clean samples
Detailed Monte Carlo simulation to calculate the efficiency as a function of E

## Slide 54
Middle Chain
HPGe

## Slide 55: MASS SPECTROMETRY (MS)
Inductively coupled plasma mass spectrometry (ICP-MS)
Glow discharge mass spectrometry (GD-MS)
Laser ablation mass spectrometry (LA-ICP-MS)
Secondary ion mass spectrometry (SIMS),
Resonance ionization mass spectrometry (RIMS),
Accelerator mass spectrometry (AMS)

## Slide 56: MASS SPECTROMETRY (MS)
Inductively coupled plasma mass spectrometry (ICP-MS)
Glow discharge mass spectrometry (GD-MS)
Laser ablation mass spectrometry (LA-ICP-MS)
Secondary ion mass spectrometry (SIMS),
Resonance ionization mass spectrometry (RIMS),
Accelerator mass spectrometry (AMS)

## Slide 57: INDUCTIVELY COUPLED PLASMA MASS SPECTROMETRY (ICP-MS)
It allows the determination of elements with atomic mass ranges 7 to 250 (Li to U)
Concentration at very low level in a wide variety of samples
High resolution ICP-MS (HR-ICP-MS), uses a magnetic field and electrostatic analyzer, providing very low detection limits, in the pgL-1 range
Destructive analysis: a previous sample digestion is required in order to obtain a liquid solution:
  Acid digestion uses a combination of different acids in order to obtain a total simple digestion (strong mineral acids: Nitric Acid, Hydrochloric Acid, Hydrofluoric Acid, Perchloryc Acid…)
  Dry ashing: Especially suitable for samples with a high organic matter content (organic matter can be completely eliminated)
  Need to avoid contamination during sample processing (acids, tools, crucible…)
Major advantage of ICP-MS: In comparison to other alternative solid-state mass spectrometric techniques is advantageous because liquid solutions can be easily and rapidly analyzed

## Slide 58: INDUCTIVELY COUPLED PLASMA MASS SPECTROMETRY (ICP-MS)
ICP source: the inductively coupled argon plasma atomizes and ionizes the elements in the sample, producing mostly positive ions.
Interface region: sampler and skimmer cones extract ions from the atmospheric-pressure plasma into the low-pressure region.
Ion optics: electrostatic lenses focus and guide the ion beam, while removing photons, neutrals and unwanted particles.
Mass analyzer: ions are separated according to their mass-to-charge ratio, using quadrupole, sector-field or time-of-flight analyzers.
Detector: the selected ions are counted, giving elemental concentrations down to sub ppt levels for U, Th and other trace contaminants.
Sample introduction: the liquid sample is nebulized into a fine aerosol and transported by argon gas into the plasma.
Perkin, Agilent, Bruker….
Notes: plasma source in which the energy is supplied by electric currents which are produced by electromagnetic induction, that is, by time-varying magnetic fields.[2]

## Slide 59
HR-ICP-MS Thermo Element
238U AND 232Th CALIBRATION
HR-ICP-MS U AND Th SPECTRA
232Th
238U
235U
Th (ng/g) U (ng/g)
LOQ 0.052 0.580
Spectroscopic interferences (molecular ion formation) can be decreased or overcome by the use of a collision cell.
ICP-MS

## Slide 60
Concentration of the daughters too low for MS

## Slide 61
SS sample

## Slide 62
ICP-MS: Figure of Merit
Advantages:
Fast analytical technique for simultaneous determination of trace and ultra-trace elements in liquid solution ( 1 d)
Excellent sensitivity, accuracy and very low det. limits:  0.1 pg/mL
Little amount of materials needed (small sample)
Isotope ratio measurements
Limitations:
Destructive analysis
Sample preparation for solid samples (full digestion, recuperation, contamination..)
It only measures the upper chain (It cannot measure K-40)
Molecular ions interferences with atomic ions (e.g. 238UH+ and 239Pu+)

## Slide 63
Radio-chemical methods (210Po extraction)
Background component:
Surface contamination
Bulk contamination
(α,n) reaction
Radioanalytical/Radiochemical
problems:
measurement can be done only by alpha spec
High volatility of Po – only wet ashing in boiling concentrated acids and acid mixtures (problems with some polymers materials)

## Slide 64: Chemical separation of 210Po
Separation method of 210Po:
Sample etch and dissolution
Sample pre-concentration and purification (if needed) by co-precipitaion or ion-exchange chromatography (e.g. measurement of bulk 210Po in Cu samples)
Source preparation by spontaneous deposition
Radiochemical tracers:
208Po (5.115 MeV alphas)
209Po (4.883 MeV alphas)
Reagents:
HNO3
HCl
H2O2 30%
N2H4•2HCl
Silver discs
Laboratory equipment:
Glass beakers (250 ml)
Watch glasses
Stirring rods with PTFE coating
Hotplate with stirrer
Pipette 10-100 μl+ tips
Protective equipment (glasses, gloves etc.)
Courtesy of T. Mróz
Jagiellonian University in Cracow, Poland

## Slide 65: Detection of 210Po – semiconductor alpha spectrometer
Very good energy resolution (20-30 keV FWHM)
Detection limits for activity lower than for XiA
Requires radiochemical separation of 210Po
Efficiency determined with tracer
Spectrum resolution depends on the source quality
Blank runs required to control the background for each procedure

## Slide 66: Source preparation
Spontaneous deposition of Po on Ag from diluted HCl solution

## Slide 67: Alpha spectrometry sources
Thick layer deposited on source
Thin source
(~20 keV FWHM)

## Slide 68
Radio-chemical methods : Figure of Merit
Advantages:
Is the only technique able to measure the lower chain
Limitations:
Sample preparation

## Slide 69: OBJECTIVES of this lecture
After this class, you should be able to:
Know the most important sources of natural radioactivity.
Understand the principles of secular equilibrium and disequilibrium of the decay chains.
Grasp the principles of the cosmogenic production of radionuclides.
Understand the general framework of the problems posed by the Rn-222.
Figure out the importance of material assays and radiopurity related aspects for low-background techniques.
Know the principle of the most used techniques for the assays.
Thank you for
your kind attention!
Roberto Santorelli TIDPAN 2026 69

## Slide 70
Backup