## Slide 1
Instrumentation for axion searches
Igor G. Irastorza (CAPA/UNIZAR)
TIDPAN 2026 - Taller de Instrumentación y Detectores en Física de Particulas, Astropartículas y Nuclear
IFIC-Valencia, 15-26 June-2026
a
g

## Slide 2: Why axions?
Most compelling solution to the Strong CP problem of the SM
Axion-like particles (ALPs) predicted by many extensions of the SM (e.g. string theory)
Axions, like WIMPs, may solve the DM problem for free. (i.e. not ad hoc solution to DM)
Astrophysical hints for axion/ALPs?
Relevant axion/ALP parameter space at reach of current and near-future experiments
Rapidly increasing interest & experimental efforts devoted to axions
Papers with “axion” in title
Source: INSPIRE-HEP
N=4570 [1977-2025]

## Slide 3: How to detect an axion?
a
g
Photon detector
Axion
source
Magnets are central components in axion experiment
a completely new and (and even more?) important role for magnets in the low mass frontier of particle physics

## Slide 4: Magnets for axions
In axion experiments, the magnet is the detector.
Most FOMs increase with B and size of magnet.
  Helioscopes ~ B2L2
  Haloscopes ~B2V
Large magnets are expensive. Most axion experiments piggyback on existing infrastructure. Some modern projects aim at purpose-made magnets (IAXO, MADMAX,…).
Synergies with HEP accelerator & detector magnets. Technologies associated with large HEP magnets (see later)
Baseline developed at:
IAXO Letter of Intent: CERN-SPSC-2013-022
IAXO Conceptual Design: JINST 9 (2014) T05002 (arXiv:1401.3233)
IAXO magnet
Superconducting “detector” magnet.
Toriodal geometry (8 coils)
Based on ATLAS toroid technical solutions.
CERN+CEA expertise
8 bores / 20 m long / 60 cm Ø per bore

## Slide 5: Detection of axions
Source | Experiments | Model & Cosmology dependency
Relic axions | ADMX, HAYSTAC, CASPEr, CAPP, MADMAX, QUAX, RADES, ORGAN, … | High
Lab axions | ALPS, OSQAR, ARIADNE,… | Very low
Solar axions | SUMICO, CAST, (Baby)IAXO | Low
Large complementarity among categories

## Slide 6: Laboratory axions
a
g
Photon detector
g
Photon source
WALL

## Slide 7: Light-shining-through-wall (LSW)
Standard configuration 
Enhanced “resonant”
configuration (future) 

## Slide 8: ALPS-II @ DESY
24 x longer than ALPS-I
Resonant configuration
3000x better sensitivity than ALPS-I expected
First results released recently!

## Slide 9: High precision optics
ALPS-II: extreme precision optical metrology
  Sub-μHz stabilization of laser frequency differences (20 order of magnitude lower than laser frequency - 282 THz)
  Picometer-level control of coupled optical cavities.
  Active feedback with kHz bandwidth to compensate seismic disturbances.
  Interferometric sensing and control of the Production and Regeneration cavities.
Production Cavity

## Slide 10: Ultra-low background optical detection
Production Cavity (PC)
Regeneration Cavity (RC)
  Shot-noise-limited heterodyne detection with sensitivity approaching the single-photon level.
  Doppler-shifted stray-light backgrounds rejected through frequency discrimination.
    Future run will reduce the stray-light background to > 1 photon per measurement time (106 seconds). Currently 200 photons in signal frequency bin (stray light)
  Operation with ~10²⁹ photons circulating in the production cavity. Optical system designed to suppress leakage and backgrounds by ~30 orders of magnitude (at the signal frequency)

## Slide 11: Solar axions
a
g
Photon detector
Axions from the Sun

## Slide 12: Solar Axions
van Bibber PRD 39 (89)
CAST JCAP 04(2007)010
Non-hadronic “ABC” Solar axion flux at Earth
(only if axion couples to electron)
Standard Primakoff spectrum
Robust prediction from axion models. Conversion of solar plasma fotons into axion (only axion-photon coupling involed)
Redondo, JCAP 1312 008

## Slide 13: CAST: state-of-the-art “axion helioscope”
First helioscope using low background techniques & x-ray focusing
Current state-of-the-art:
CERN Axion Solar Telescope (CAST)
CAST
Axion helioscope concept
P. Sikivie, 1983
+ K. van Bibber, G. Raffelt, et al. (1989) (use of buffer gas)

## Slide 14: IAXO & BabyIAXO in a nutshell
Primary physics goal: detection of solar axions. Additional physics program IAXO as a generic ALP facility
BabyIAXO under construction at DESY. Dedicated magnet  Time-critical item, experiment timetable driven by magnet: important delays due to cable and funding issues
IAXO: longer-term goal of the community.
First concept established in 2014
SNR ~105 x CAST
BabyIAXO: intermediate scale between CAST & IAXO. Prototype for IAXO. Relevant physics reach in itself
SNR ~100 x that of CAST
CAST @ CERN: current state-of-the-art. Finished in 2021.
Best upper bound on axion-photon coupling

## Slide 15: BabyIAXO – under construction
Parts of BabyIAXO already built:
At DESY
Available, to be shipped
At DESY, modification required
In production
Order in preparation
Large vacuum beamlines just finished
1st km of BabyIAXO Rutherford-type cable
1st Micromegas x-ray detector (with shielding) taking background data at DESY
Current BabyIAXO timeline:
2026: Site activation
2027: magnetless-commissioning
2028: dark photon run
2029: magnet installation
2030+: commissioning + axion runs

## Slide 16: BabyIAXO magnet
“Common coil” configuration
  Reduce risk: known design choices as much as possible
  Cost-effective: Best use of existing infrastructure and experience at CERN
  Prototyping character: winding layout very close to that of IAXO toroidal design.
Parameter | Value
Operating current [kA] | 6.0
Free bore diameter | 0.7
Transverse magnetic field during operation [T] | 2.1
Stored magnetic energy [MJ] | 56
Inductance [H] | 3.1
Cold mass weight (preliminary) [tons] | 38
Energy density (preliminary) [kJ/kg] | 1.5
Overall coil conductor length [km] | 22
Conductor length per pancake [km] | 2.5
Peak magnetic field magnitude on the Rutherford cable [T] | 4.7
Magnet design led by CERN-EP (M. Mentink), with support from DESY, Elytt, and CAPA (cable)

## Slide 17: BabyIAXO magnet: cold-mass
Al alloy support structure to hold considerable forces
Coil bonded to structure
  Four layers stack
  Requirement on conductor: transverse yield strength of >50 MPa at 4K
System of pretensioned tie rods to hold repulsion forces (also vertical ones due to mech. tolerances)
Extensive 3D simulations to evaluate deformations/ displacements
Gap opens during ramp-up
Dimensions

## Slide 18: Conductor for large scale coils
Aluminum-stabilized Nb-Ti/Cu conductor:
Nb-Ti/Cu Rutherford cable
Aluminum
Conventional technology but no providers in recent years! (+ Russian war)  causing delay to project
Rutherford cable already under production
CERN-TE support in quality control & cabling
Al co-extrusion: possible provider found in China, first trials…
Cold-working needed to meet yield strength specs

## Slide 19: Future: HTS cables
HTS-based conductors would allow for more powerful magnets, and/or simpler cryognenics
Its use in large magnets are already a reality in fusion projects and HEP demonstrators
Lack of reliable HTS ”cable”.Industrial reality rapidly evolving.
See recent seminar by A. Ballarino at CERN: https://indico.cern.ch/event/1562652/

## Slide 20: Large scale (few K) cryogenics
Cryogenic turret (phase separator)
Service box
Cold mass, concentric thermal shields and coil suspension
Concentric thermal shields (25 and 50 K)
BabyIAXO will be the first large-scale magnet using cryo-coolers integrated into the magnet vacuum vessel itself (no external plant).
Cold items:
  Cold mass at < 5 K.
  Two concentric thermal shields, 25 K and 50 K, to mitigate low cooling budget at 4.5 K
  HTS-based lead currents at 50K, to limit heat-load to cold-mass
PROS
No need of external plant Good for movable magnet Less space Modularity, redundancy Less He consumption
CONS
Complexity Innovative design Modest power, less efficient

## Slide 21: BabyIAXO magnet: cryogenics
Cold mass (<5K), Cooled with liquid He from phase separator via thermosiphon (cryo turret)
50 K & 25 K thermal shields and HTS-based current leads, cooled with He gas circulation with cryo fan (service box).
Cryogenic turret (phase separator)
Service box
A number of demonstrating setups & tests ongoing at CERN-EP
He gas circulation with cryocoolers & cryofan HTS high-efficiency current leads. Local cryocooler-based He liquefaction and thermal syphon. Compact Zero-boil-off cryogenics Custom-designed heat exchanger

## Slide 22: X-ray optics for axion helioscopes
Focal length
X-rays are focused by means of grazing angle reflection (usually 2)
Many techniques developed in the x-ray astronomy field. But usually costly due to exquisite imaging requirements
ABRIXAS spare telescope, used in one of the 4 bores of CAST (pioneer use of x-ray optics in axion research)
First X-ray optics specifically built for axions in CAST (LLNL)
5 cm

## Slide 23: Cost-effective large-scale X-ray optics
XMM Flight Spare x-ray telescope
Property of ESA, loaned to be used in BabyIAXO. 70 cm diameters, 7 m focal length
Various technologies successfully used in X-ray astronomy:
  Slumped glass (NUSTAR)
  Aluminium foil (XRISM)
Also existing flight spare modules can be used 
Conceptual design for BIAXO co-mount need to be finalized and constructed
CSGO Assembly machine @INAF
XRISM XRT and alignment bars @NASA GSFC

## Slide 24: Ultra-low background x-ray detectors
To be placed at the focal plane of optics
Pixelization to properly image the axion signal
Lowest possible background
X-ray optics specifically built for axions
Low background Micromegas
“IAXO pathfinder” @ CAST
Phys. Rev. Lett. 133 (2024)

## Slide 25: Ultra-low background x-ray detectors
Low background techniques similar to underground DM experiments:
  Radiopure components & materials
  Shielding of external radiation
  Detailed simulations
  Offline cuts
Canfranc
(underground)
~1 count/month background in the RoI!
Simulation studies (neutron event)
System on suface to test active shielding concepts (cosmic neutron tagging)
CAPA-Zaragoza

## Slide 26: Support and drive system (SDS)
BabyIAXO in the Hera South Hall
Head extension
Elevation drive unit
Support frame
Pointing & alignment, similar to astronomical telescopes

## Slide 27: Dark matter axions
a
g
Photon detector
Axions from DM halo

## Slide 28: Detecting DM axions: “axion haloscopes”
Assumption: DM is mostly axions
Resonant cavities (Sikivie,1983)
  Primakoff conversion inside a “tunable” resonant cavity
  Energy of photon =
Axion DM field
Non-relativistic
Frequency  axion mass
Cavity dimensions smaller than de Broglie wavelength of axions
If cavity tuned to the axion frequency, conversion is “boosted” by resonant factor
(Q quality factor)
Primakoff conversion of DM axions into microwave photons inside cavity

## Slide 29: Haloscopes: current results
Pre-inflation models
Post-inflation models
Finetunned
Cosmologically interesting axion mass ranges:

## Slide 30: ADMX
- High cavity
- Large volume:
- Suited for resonance
at few
- 8T superconducting magnet
Paradigmatic axion haloscope. Long track of R&D and physics results. Sited at U. of Washington
Tuning achieved by set of movable rods
Sensitivity to few eV proven
Last results (2024): KSVZ Axion Model at nominal dark matter density excluded at 90% confidence between 1 GHz and 1.3 GHz.
DFSZ Axion Model at slightly higher densities excluded

## Slide 31: RF design & engineering
As the expected signal are at RF, we need expertise in:
  Passive elements design and FEM simulation (resonant cavities and structures)
  RF components, circuits, characterization, etc…

## Slide 32: Haloscope FOM
High-ma challenges:
higher ma  lower V  lower sensitivity
R&D to go to:
  Higher B magnets
  Larger instrumented volumes
  Lower noise sensors
  Higher Q cavities
Very active R&D in many groups!
More powerful magnets
Multicell structures:
  Phase-matched
  Filter-like
  Dielectric loading
  Photonic bandgap
  …
SC deposited cavities
Lowering T with cryogenics and novel sensing techniques
QUAX at LNL
“Pizza cavity”
at CAPP
 2008.10141
HTS coated cavity
(CAPP)
RADES project
in CAST

## Slide 33: Superconducting coatings
Coating the walls of the cavity with a superconductor material will increase (decreases the losses on the walls)
Technological challenges: the material must remain SC in the magnetic field.
Novel high-T superconductor (HTS) are difficult to handle (brittle materials, etc.)
Physical limit to improving : above it does not translate in improved FOM (the axion peak must fit in the cavity bandwidth!)
NbTi coated cavity
(QUAX experiment)
HTS coated cavity
(CAPP)
HTS coated cavity
(RADES)

## Slide 34: Millikelvin cryogenics
Dilution refrigerators use evaporation of He3 from a mixture He3/He4 mixturesto reach mK temperaturas
Commercial availability has expanded dramatically, driven by advances in quantum technologies.
https://www.insight-ihbar.com/QC_hardware_en/F.html
Commercial dilfridge BlueFors LD

## Slide 35: Quantum technologies to lower
SQUID amplifier from ADMX collaboration
Leading haloscopes use cryogenics to cool down well below .
But (contribution from the sensor technology). New technologies with lower are also needed. Quantum technology needed to profit from at reach by dilution refrigerators
But Standard Quantum Limit (SQL): when approaches , irreducible noise from vacuum fluctuations.
Quantum circuits to achieve quantum-limited amplification: SQUIDs, JPA, TWPA,…

## Slide 36: Beyond the SQL: photon squeezing
If the cavity vacuum is prepared in a squeezed state, the axion signal can be read with a noise that is effectively lower than the SQL in an amount dependent of the degree of squeezing. Concept studied in Malnou et. al 2018
First experimental application HAYSTAC at Yale (Backes et al 2021). Factor x2 effective faster scan rate obtained
  HAYSTAC experiment:
  Quantum information technologies for axion searches

## Slide 37: Beyond the quantum limit
From linear amplification (LA) to counting single photons (SPD)
LA
SQL
I
Q
axion
Linear cavity
Linear amp
Conventional haloscope: In-phase(I) and Out of phase (Q) conjugates limited by SQL
Quantum + thermal noise
[I,Q]=i

## Slide 38: Beyond the quantum limit
From linear amplification (LA) to counting single photons (SPD)
I
Q
axion
n=1
Displaced vacuum state leaks into non-zero Fock number. Detect displacement by counting the photon.
n=2
n=3 (*)
LA
SPD
SQL
Shot noise
Single-photon detector (SPD)
vs Linear Amplifier (LA)
Several orders of magnitude SNR improvement available !!!
Noise counts exponentially suppressed at low T !!!
(*) heuristic simplified picture

## Slide 39: Beyond the SQL: photon counting
But, how to implement photon counters at these energies?  quantum technologies Several promising ideas. Some examples:
QUAX+Saclay group: 2403.02321 (x20 better than SQL)
Counting photons (versus phase preserving readout): SQL is evaded as phase uncertainty is maximal…
Dixit et al (PRL 126)
RADES / DarkQuantum ERC-SyG project
DarkQuantum
minimum detectable power

## Slide 40: Qubit-based Single Photon Detector (SPD)
Superconducting qubit (trasmon) dispersively coupled to cavity:
Cavity
Qubit
Coupling
Presence of photons in cavity shifts frequency of qubit.
Interrogating the qubit “senses” the presence of single photon
Quantum-non-demolition measurement  photon not absorbed, measurement can be repeated on the same photon!
Concept proposed in the context of axions by Dixit et al. PRL126 (2021)  O(Hz) dark count rate measured, 103 better than SQL!!!

## Slide 41: First implementation in RADES
Double cavity with transmon coupled to both:
Second version with cylindrical storage cavity geometry just built at CAPA/Zaragoza 
20 um
1 mm
Readout cavity
Transmon
Storage cavity
Transmon
Josephson junction

## Slide 42: Conclusions
Boosting interest in experimental search for axions
Singular portfolio of technologies, many of them not present in conventional HEP groups/institutions
  Technologicaly exciting field
Importance of networking with neighboring fields
  Astronomical observatories and missions (e.g. x-ray telecopes)
  Precision optics, material science,…
  RF technologies and astronomy
  Quantum physics and technologies
Potential for impact of new ideas, or new synergic connections, etc…
Large fraction of parameter space at reach of near-future experiments
  chances of discovery!
  Good times for axions… stay tuned

## Slide 43: Acknowledgements
The work presented in this seminar is a review of international efforts funded by many agencies. But in particular I want to personally acknowledge support from:
The European Union’s Horizon 2020 research and innovation programme under the European Research Council (ERC) grant agreement ERC-2017-AdG788781 (IAXO+).
The European Union’s Horizon 2020 research and innovation programme under the European Research Council (ERC) grant agreement ERC-2023-SyG 101118911 (DarkQuantum).
The Spanish Agencia Estatal de Investigación (AEI) under grant PID2019-108122GB-C31 funded by MCIN/AEI/10.13039/501100011033.
The “European Union NextGenerationEU/PRTR” (Planes complementarios, Programa de Astrofísica y Física de Altas Energías), co-funded by Gobierno de Aragón
Funded by the European Union. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union. Neither the European Union nor the granting authority can be held responsible for them.

## Slide 44
Thank you for your attention
 Backup slides

## Slide 45: ADMX: next plans
1 – reach downward
Plan: Extend reach down to DFSZ at below-nominal dark matter density, by improving amplifiers to lower system noise temperature. [Started data taking in 2026)
Beyond next year: Extend sensitivity to higher masses using a multicavity system. Method: Multiple cavity system
2 – reach upwards

## Slide 46: Lower-ma haloscopes
Large V haloscopes are technologically simpler, but expensive  huge magnet needed.
Use of existing magnets could be an effective strategy
Some proposals:
RADES DarkQuantum - low frequency: aiming at BabyIAXO magnet, but first prototypes could take data at CERN’s M1
FLASH proposal to use FINUDA magnet at LNF
Also
GraHal in Grenoble
ADMX plans for lower masses (EFR)
Lowest possible frequency ultimately limited but realistic magnet/cavity size  move to different concepts
Pick-up coil and resonant circuit (DM-Radio, see next slide)
NMR resonances (CASPEr), but not sensitive to other than
FLASH @ FINUDA
RADES-DQLF

## Slide 47: Plasma haloscopes: ALPHA
bal

## Slide 48: Pick-up loop & resonant circuit: DM-Radio
A program to make a definitive search for GUT-scale axions and find a pre-inflation relic!
Now commissioning DMRadio-50L
While working on a staged R&D program for DMRadio-GUT.
Notes: Summary: Building on the success of the ABRACADABRA demonstrator, the DMRadio program aims to field the definitive search for GUT-scale/pre-inflation axions. Currently testing the 50L magnet and completing the commissioning the cryostat. The collaboration is working through an R&D plan that would allow us to field additional demonstrators at the m^3 scale and finalize the design of the ultimate experiment.

## Slide 49: DM Axion Group @ IBS, Korea (former CAPP)
DMAG-12T
(12T/96m)
TM020 + auxetic + JPA
(5.1 GHz)
Near KSVZ sensitivity
PRL 135 091804 (2025)
DMAG-8TB
(8T/165mm)
8-cell + JPA
(5.9 GHz, 400 mK)
KSVZ sensitivity
PRL 135 211801 (2025)

## Slide 50: DM Axion Group @ IBS, Korea (former CAPP)
DMAG-12TB (12T/320mm)
f > 1 GHz, V = 32 L, Tsys ~ 200 mK
df/dt ~ 2 MHz/day @ DFSZ
PRX 14 031023 (2024)
Hybrid cavity
(Cu cavity + HTS tuning rod)
DAQ since Nov. 2025 (1.3–1.5 GHz)
CAPP-8T
(8T/125mm)
HTS SC cavity + JPA
(2.3 GHz, Q ~ 3.5 M)
AQN search
PRD 112, L121305 (2025)

## Slide 51: Magnetized dish antenna
DM field + B field + boundary condition in the dish  photon emission normal to surface
No resonance (loss a factor Q) BUT may be compensated with very large areas ?
Implementation
In the BRASS Project at Hamburg
Resonance versus area
Also BREAD Project @ US
Variation: solenoidal geometry
Horns et al. JCAP 1304 (2013) 016
Jaeckel , Redondo JCAP 1311 (2013)

## Slide 52: Dielectric haloscopes: MADMAX
Effect of dish antenna “boosted” by the addition of many dielectric disks
Some “mild” resonance
  Concept between a haloscope and a dish antenna
  It needs tuning! (challenging)
Relevant sensitivity in the 10-4 eV ballpark for a ~m3 10T experiment (80 disks)
MADMAX dielectric haloscope
First results with a 3 disk prototype

## Slide 53: Helioscopes & astrophysics
… as well as a large fraction of the axion & ALP models invoked in the “stellar cooling anomaly”
But for this the gae is particularly interesting (see backup slides)
IAXO will fully explore ALP models invoked to solve the “transparency hint”
IAXO+: enhanced scenario with x10 (x4) higher FOM (MFOM) with respect to LoI
MFOM = Magnet FOM

## Slide 54: BabyIAXO: beyond baseline
BabyIAXO as a generic axion(-like) facility
BabyIAXO constitutes a great infrastructure that can be used to target other physics goals beyond Primakoff solar axions:
Other (non-Primakoff) solar axion production mechanisms
Axions from SN
Dark Matter axions: haloscope setups inside the BabyIAXO bores
Other WISPs: hidden (dark) photons, chameleons, …
post-Discovery “precision” physics
…And also high-frequency grav. waves!!

## Slide 55: ALPS-II @ DESY: status & plans
Results of first axion search science campaign published!
Optics upgrade for axion searches under way.
arXiv:2512.14110 [hep-ex]
arXiv:2601.18684 [hep-ex]
TIDPAN, Valencia, Jun-2026
55

## Slide 56: ALPS II @ DESY: beyond axion searches
Expected signal at ALPS II 600 times larger than at PVLAS.
Measure changes in the cavity resonances for orthogonally polarized states when modulating magnetic field strength at mHz frequencies. Results from 19m prototype published: arXiv:2510.14064 [physics.optics].
Measure Vacuum Magnetic Birefringence
TIDPAN, Valencia, Jun-2026
56

## Slide 57: Beyond axions
Many extensions of SM predict axion-like particles
  Higher scale symmetry breaking
String theory predicts a plenitude of ALPs
Generic ALPs parameter space 
Weakly Interacting Sub-eV Particles
(WISPs)
Hidden Photons
(HPs)
Millicharged Particles
Chameleons
Axion Like particles
(ALPs)
AXIONS
Stringy ALPs
Arion
Majoron
Familon

## Slide 58: Axion phenomenology
Mass
generic
Gluon coupling
generic
Some phenomenology depends on the “axion model”, e.g.
  KSVZ axions are “hadronic axions” (no coupling with leptons at tree level)
  DFSZ axions couple to electrons
Photon coupling
generic but value
model dependent
Fermion couplings
Electron coupling
Nucleon coupling
…
Model dependent
×

## Slide 59: Axion models
Conventional QCD axion models lie on the “yellow band”
  KSVZ, DSFZ benchmarks
Outside the band typically ALPs
BUT a lot of “model building” activity in recent years, leading to QCD axion models outside the conventional band…
  Normally populating higher gag.
  Very interesting for experiments!
P. Agrawal, ESPP 2019 Granada

## Slide 60: Axions as cold dark matter
… AND decay of topological defects.
(TD)
Axion realignment…
(AR)
Only well-known AR
BUT, initial misalignment angle unknown…
Large range of masses possible, even very low ones ( anthopically finetuned?)
TD contributes, potentially dominating…
Not initial AR uncertainty
BUT TD computation very complex
Still large range of masses possible
ALP as inflaton AND dark matter?
 Right axion DM density is possible for a wide range range of masses
PQ before or after inflation?
eV

## Slide 61: Sources of axions
Natural sources
Dark matter
Dark radiation
Stellar
Laboratory sources
Photon-ALP conversion in strong magnetic fields (axion-photon coupling)
ALP fields from macroscopic bodies (fermionic couplings)
IGI, J. Redondo, 1801.08127

## Slide 62: Other purely laboratory searches
Other LSW experiments active in the past, some at different photon energies:
OSQAR@CERN, CROWS@CERN, GammeV & REAP @ Fermilab, US, BMV @ Toulouse,…
Possible future extrapolation: JURA (& also STAX with MW)
Laser polarization experiments (sensitive to VMB): PVLAS @ Ferrara, … Future (project): VMB@CERN
Short-range axion-mediated macroscopic forces: ARIADNE
  NMR techniques
  Sensitive to (products of) fermion couplings
  Good prospects for sub-meV axion
Rotating source
mass
Rotating source
NMR sample
Arvanitaki, Geraci
Phys. Rev. Lett. 113, 161801 (2014)

## Slide 63: CAST experiment @ CERN
Decommissioned LHC test magnet (L=10m, B=9 T)
Moving platform ±8°V ±40°H (to allow up to 50 days / year of alignment)
4 magnet bores to look for X rays
LHC test magnet
Moving platform ±8°V ±40°H
2 low background Micromegas
1 Micromegas + XRT
1 Ingrid + XRT
3 X rays detector prototypes used.
X ray Focusing System to increase signal/noise ratio.
CAST: last solar axion configuration

## Slide 64: …and more solar axions
Via axion-nucleon couplings: monochromatic lines from nuclear transitions:
  E.g. 14.4 keV axions emitted in the M1 transition of Fe-57 nuclei, MeV axions from 7Li and D(p;g)3He nuclear transitions or Tm-169.
More recently proposed: photons interacting with macroscopic solar B-fields.
axions
longitudinal and transversal plasmons conversion.
Depend on !
TP depend on too
Depend on solar B-field. Poorly known but constrained:
See recent study Di Luzio et al, EPJC 82, 2111.06407 [hep-ph]
See e.g. Caputo et al 2005.00078, Guarini et al. 2010.06601

## Slide 65: BabyIAXO – superbrief status
Technologies involved: Large detector magnets, x-ray optics & detectors, low-background, vacuum, astronomical alignment, link with quantum technologies,…
Collaboration consolidated: 120 (150) members, 20 (24) institutions (associated)
Site: BabyIAXO hosted by DESY
Magnet
Optics
VGS
Detectors
Structure & drive
Funding: ERC, DESY, NSF, AEI, DFG, ANR, INAF, + good prospects for more
Promising DFG GG application

## Slide 66: IAXO experiment - summary
Next generation “axion helioscope” after CAST
Purpose-built large-scale magnet
  >300 times larger B2L2A than CAST magnet
  Toroid geometry
  8 conversion bores of 60 cm Ø, ~20 m long
Detection systems (XRT+detectors)
  Scaled-up versions based on experience in CAST
  Low-background techniques for detectors
  Optics based on slumped-glass technique used in NuStar
~50% Sun-tracking time
Large magnetic volume available for additional “axion” physics (e.g. DM setups)
IAXO conceptual design
JINST 9 (2014) T05002
~104-5 x CAST SNR

## Slide 67: BabyIAXO
Prototype: Intermediate experimental stage before IAXO
  Two bores of dimensions similar to final IAXO bores  detection lines representative of final ones.
  Magnet will test design options of final IAXO magnet
  Test & improve all systems. Risk mitigation for full IAXO
Physics: will also produce relevant physics outcome
  (~100 times larger FOM than CAST)
~100x CAST SNR
ERC-AvG 2017 IAXO+
BabyIAXO conceptual design
JHEP 05 (2021) 137

## Slide 68: BabyIAXO status
Magnet
Technical in-depth review of magnet design successfully passed at DESY PRC last april. Progress towards TDR
Magnet cable procurement: critical item, causing delays. Good progress in finding viable provider
X-ray Optics
2 detection lines in BabyIAXO with different solutions: existing XMM spare + custom-made slumped glass optics
Collaboration effort: CAPA, Columbia, INAF, DTU, MPE-Panter
First prototype sectors built!

## Slide 69: BabyIAXO detectors and beamlines
Baseline detectors:Low background Micromegas detectors of microbulk type.
Various alternative technologies being explored in te collaboration: TES, MMC, GridPix, SDDs,…
Various prototypes taking data at CAPA, LSC & Saclay
Beamline design finalized.
First procurements started

## Slide 70: BabyIAXO Micromegas detectors
Goal is to reach 10-7 c/keV/cm2/s
Achieved underground
Prototypes aboveground (CAPA) and underground (LSC) to test intrinsic limits
Simulation effort: background model
Cosmic neutrons study: collaboration with HENSA
Simulated cosmic neutron event
Development of new radiopure electronics
& low EM noise

## Slide 71: Detecting DM axions: “axion haloscopes”
Assumption: DM is mostly axions
Resonant cavities (Sikivie,1983)
  Primakoff conversion inside a “tunable” resonant cavity
  Energy of photon =
Axion DM field
Non-relativistic
Frequency  axion mass
Cavity dimensions smaller than de Broglie wavelength of axions
If cavity tuned to the axion frequency, conversion is “boosted” by resonant factor
(Q quality factor)
Primakoff conversion of DM axions into microwave photons inside cavity

## Slide 72: Solar Axions
Primakoff conversion of solar plasma photons  generic prediction of most axion models
In addition, -mediated axions (model dependent)
axions
Non-hadronic “ABC” Solar axion flux at Earth
JCAP 1312 008
(only if axion couples to electron)
Standard Primakoff spectrum
Dafni+2019

## Slide 73: CAPP to DMAG
IBS-CAPP
2013.10 ~ 2024.12
IBS-DMAG
2025.01 ~

## Slide 74: RADES
Exploratory project emerged at a later stage of CAST: use of “helioscope” magnets for “haloscope” searches
Various R&D and physics results
Strong boost by ERC-StG (B. Dobrich) in 2018
Now ultra-cryogenic setup being built at MPP-Munich
DarkQuantum ERC-SyG started 2024 (Irastorza, Kontos, Paraoanu, Wernsdorfer)
JCAP 05 (2018) 040
JHEP 07 (2020) 084
JHEP 21 (2020) 075
JHEP 04 (2025) 113
IEEE Trans. Appl. Supercond. 32 (2022) 45
New geometry concepts to scale in V but keeping high resonant f
Physics result at single f point in CAST and in SM18 magnets
Inner HTS coatings to improve Q factor

## Slide 75: DarkQuantum: quantum-enhancing RADES
DQ
LF
DQ
HF
Built on RADES plans. Add “quantum” ingredient.
  Establish link with key experts and bring them to the axion field.
Well defined roadmap of technical and physics outcome ( impact)
  Low frequency search in RADES@BabyIAXO
  High frequency search in RADES@LSC
Additional exploratory lines with great potential: 1) HTS for increasing Q, 2) low radioactive techniques / underground, 3) Machine learning, 4) Magnonics for tuning
DarkQuantum
Also QRADES project from Quantera call, further strengthen the quantum development for RADES

## Slide 76: RADES/DQ low frequency
Large V haloscopes are technologically simpler, but expensive  huge magnet needed. Use of existing magnets could be an effective strategy
RADES: use of BabyIAXO Use of (Baby)IAXO large magnetic volume for axion DM setups.
  Various 5-m long 50-cm diameter cavities
Very competitive prospects for 1-2 eV axion searches.
First prototypes under construction (1 m long)
Could already get physics from them: using M1 magnet at CERN North Area?  recent EoI to CERN SPSC submitted

## Slide 77: RADES-DQ high frequency
Beyond the standard quantum limit by counting ~10 GHz photons:
SC qubit (transmon) based sensor
Quantum non-demolition measurement
Magnonics for frequency tuning
HTS for increasing cavity Q
Going underground to reduce darkcount rate  EoI to LSC recently submitted
SPD
dark count rate

## Slide 78: DarkQuantum: quantum-enhancing RADES
Main “rationale”:
Built on RADES plans, high-frequency and low-frequency (BabyIAXO)
Add “quantum” ingredient. Establish link with key experts and bring them to the axion field.
3rd RADES Coll. Meeting & DarkQuantum KICKOFF Meeting
1 month ago @ MPP-Munich
Also QRADES project from Quantera call, further strengthen the quantum development for RADES
DarkQuantum
DQ

## Slide 79: DarkQuantum: quantum-enhancing RADES
Well defined roadmap of technical and physics outcome ( impact)
  Low frequency search in RADES@BabyIAXO
  High frequency search in RADES@LSC
Development & implementation of quantum sensors.
Very novel synergies: remain open for new ideas, unforeseen byproducts, etc…
DQ
LF
DQ
HF

## Slide 80: Haloscopes & quantum technologies
Reducing implies:
  1) reducing physical temperature &
  2) improving sensing technology (quantum sensing)
Quantum amplification technologies are needed if one want to profit from cryogenics…
But, even doing 1) and 2) the improvement suggested in above expression does not continue indefinitely: standard quantum limit SQL
ADMX coll.

## Slide 81: Beyond the quantum limit
From linear amplification (LA) to counting single photons (SPD)
LA
SQL
I
Q
axion
Linear cavity
Linear amp
Conventional haloscope: In-phase(I) and Out of phase (Q) conjugates limited by SQL
Quantum + thermal noise
[I,Q]=i
81

## Slide 82: Beyond the SQL: “counting photons”
‘No Click’
Qubit 0
Qubit 1
axion
‘Click’
From linear amplification (LA) to counting single photons (SPD)
LA
SPD
SQL
Shot noise
Single-photon detector (SPD)
vs Linear Amplifier (LA)
Several orders of magnitude SNR improvement available !!!
Noise counts exponentially suppressed at low T !!!
Linear cavity
B-resilient Qubit (B-SPD)
DQ change of paradigm  Number-Phase conjugates evade the SQL
[N,f]=i
82

## Slide 83: DarkQuantum synergies
Large-scale cryogenics
Machine learning for quantum sensing
Low radioactivity techniques and underground operation
HTS coatings
Magnonics for tuning

## Slide 84: Why going underground
Going underground to further reduce dark count rate?
  EoI to LSC recently submitted
Large scale cryogenics to cool down BabyIAXO bores
Machine What is its origin? Could radiation play a role?
Suggestive link to evidence of radiation affecting qubits properties. Synergies with ARQ/MIRQ project already operating at Canfranc (led by P.Forn IFAE) ?
QRADES: Quantera project share goals with DarkQuantum, includes P. Forn
84
DarkQuantum could open an innovative link between “low background techniques & underground labs” and “axion haloscopes”:
RADES at LSC the first underground axion haloscope?

## Slide 85: Haloscopes inside BabyIAXO
Use of (Baby)IAXO large magnetic volume for axion DM setups.
Very competitive prospects for 1-2 meV axion searches.
  4 x 5m long cavities with tuning slabs.
  Low noise (standard) amplification + DAQ
  Bores cooled down to 4-5 K
  Sensitivity to KSVZ in < 2year data.
  Other implementations (more speculative) are being discussed, BASE-like setups to much lower masses
RADES coll., Ann. Phys. 2023

## Slide 86: BabyIAXO detectors
Baseline detectors:
  Low background Micromegas detectors of microbulk type
  “Discovery detectors” (priority to low background).
  Experience in CAST
  Low background capability, radiopurity, shielding.
  Goal is to reach 10-7 c/keV/cm2/s
Improved detector design for BabyIAXO
IAXO-D0 prototype in its shielding

## Slide 87: BabyIAXO magnet
“Common coil” configuration
  Minimal risk: conservative design choices
  Cost-effective: Best use of existing infrastructure and experience at CERN
  Prototyping character: winding layout very close to that of IAXO toroidal design.
10 m
70 cm

## Slide 88: BabyIAXO magnet
Technical in-depth review of magnet design successfully passed at DESY PRC already in 2020.
Now ongoing adaptations derived from difficulties to procure Al-stabilized SC cable:
  Original cable not usable
  Potential Russian providers not available
  Need to re-activate know-how in industry.
  New review planned for end of year
Request for quotations & tendering started for some subsystems.
Critical item, causing delays.

## Slide 89: BabyIAXO optics
2 detection lines in BabyIAXO with different solutions:
Hybrid approach for custom BabyIAXO optic
Inner part Al-foil or segmented glass optic
Outer part cold-slumped Willow-glass technology
First coating test (10 & 30 nm Ir) on NuSTAR flight glass and Willow glass satisfactory agreement with expectations
   Henriksen et al, Appl. Opt. 60 (2021)
Design of support structure and vessel to hold, co-align and calibrate both underway
XMM Flight Spare XRT
Engineering model sent to DESY, actual optic currently at PANTER (Munich). MPE/PANTER formally joined IAXO.
ESA letter received in 2019. Now operational requirements and loan agreement in preparation
Calibration at PANTER scheduled soon

## Slide 90: B-resilient transmons using graAl
DQ
  Magnetic field resilient superconducting quantum circuits with granular aluminium, A. Théry et al. submitted to PRL‘23
Rabi-like drive at finite B-field
T=20mK
Preliminary results from
T. Kontos’ group
(ENS-Paris)
90

## Slide 91: Qubit-based Single Photon Detector (SPD)
Dixit et al. Searching for dark matter with a superconducting qubit, Phys. Rev. Lett. 126
Other SC devices/layouts possible (*)
Problem: transmons are supersensitive to B-fields!
91

## Slide 92: Potential impact in high-freq RADES setup
SPD
dark count rate
+ single-photon counter
+ reasonable tunability
Other parameters conservative – current RADES numbers:
V ~ 0.03 liters
Q ~ 104
B ~ 9 T
Time per -step = 2 h
Total effective exposure time = 800 days (can be distributed in a few cavities)
DQ

## Slide 93: Magnonics for tuning
DQ
  Magnetic crystals (e.g. YIG or GdVO4) can modify the mode geometry and frequency in a B-dependent way
  Varying B to tune cavity: avoid messy and challenging mechanical systems! And maybe increase range?
  Challenge: how to implement without affecting Q or mode coupling
  Plan B: we go back to mechanical tuning
Preliminary results from
T. Kontos’ group
(ENS-Paris)
93

## Slide 94: RADES groups
MPP-Munich
CAPA-Zaragoza
JGU-Mainz
CERN
ICCUB, Barcelona
IFIC, Valencia
TRIUMF, Vancouver
UPCT, Cartagena
ITA, Zaragoza
OAN, Yebes
LSC
ENS-Paris
KIT
Aalto
+ IFAE (P.Forn) via QRADES
Large expertise in axion haloscopes and related know-hows
“Quantum tech” experts
via DarkQuantum

## Slide 95: Low frequency: pushing BabyIAXO to SQL
Unprecedented magnetic volume
Available to axion community
We need:
  Ultra-cryogenics for unorthodox size and dimensions: challenging but possible.
  SQUID-based quantum-limited amplifier
2 x 10-m long 70-cm diameter magnet bores
First scaled-down prototype built and tested:

## Slide 96: Enhanced sensitivity prospects
Benchmark “QCD axion” model band
From our recent RADES@BabyIAXO paper:
+ cryogenics
+ quantum-limited readout
DQ

## Slide 97: BabyIAXO complementary technologies
Gridpix
MMC: Metallic Magnetic calorimeters
SDD: Silicon Drift Detectors
TES: Transition Edge senstors
Beyond baseline, “high precision” detectors
  Better threshold & energy resolution
  Design and material optimization ongoing in all fronts
  Background studies with different shielding configurations
  DALPS project (French ANR)
ERC-StG (2020)
M.Meyer
To understand bkg in TES

## Slide 98: Technical coordination at DESY
Site: HERA South Hall, former ZEUS detector hall: 43 x 25m
Support and Drive System: Reusing (parts of) CTA MST Prototype from Berlin.
Technical coordination and project office very active, WBS, PBS, …

## Slide 99: BabyIAXO: beyond baseline
BabyIAXO as a generic axion(-like) facility
BabyIAXO constitutes a great infrastructure that can be used to target other physics goals beyond Primakoff solar axions:
Other (non-Primakoff) solar axion production mechanisms
Axions from SN
Dark Matter axions: haloscope setups inside the BabyIAXO bores
Other WISPs: hidden (dark) photons, chameleons, …
post-Discovery “precision” physics

## Slide 100: Other solar axion sources
In addition to Primakoff, “ABC axions” may be x100 more intense… but model-dependent.
Non-hadronic “ABC” Solar axion flux at Earth
JCAP 1312 008
axions
* if the axion couples with the electron ()
(non hadronic axion)
Primakoff
“ABC” axions (*)

## Slide 101: Other solar axion sources
Via axion-nucleon couplings: monochromatic lines from nuclear transitions:
  E.g. 14.4 keV axions emitted in the M1 transition of Fe-57 nuclei, MeV axions from 7Li and D(p;g)3He nuclear transitions or Tm-169. Di Luzio et al. 2111.06407
More recently proposed: photons interacting with macroscopic solar B-fields. e.g. Guarini et al. 2010.06601
axions
longitudinal and transversal plasmons conversion.
Depend on !
TP depend on too
Depend on solar B-field. Poorly known but constrained: