## Slide 1
Progress on the P2 Basket
, on behalf of the CEA/IRFU/P2 Basket Group
(1)CEA/IRFU/Université Paris – Saclay
Wednesday, 07 January 2026
P2 Collaboration Meeting

## Slide 2: The P2 Basket Group
DEDIP (Département d'Électronique des Détecteurs et d'Informatique pour la Physique):
S. Anvar, E. Casalotti, A. Demonti, M.-M. Diop, A. Gairot (Internship student), C. Goblin, M. Kebbiri, I. Mandjavidze, P. Mas, B. Moreno, F. Prunes, B. Rapp, N. Salse, M. Vandenbroucke, H. Le Provost
DPhP (Département de Physique des Particules) :
M. Boonekamp, L. Chevalier, M. Gailliard (PhD Student), P.-F. Giraud, A. Kallitsopoulou (Post-Doc)
DIS (Département d’Ingénierie Systèmes) : S. Cazaux, P. Charon, T. Lebrun

## Slide 3: P2 @ Mainz - Recap
P2 Forward angle measurement
Electrons scattered within 25º<θ<45º
Focused with a solenoidal magnetic field 0.7 T
Measured with Cherenkov counters
Scattering rate of ~ 100 GHz
Signal () dominated by
  For ~ 1% stat precision
  10000h  4x1018 electrons
Beam energy 50 -150 MeV
But the internal structure of the proton contributes to bringing systematic uncertainties to P2 measurement
Notes: The parity-violating scattering cross section asymmetry, APV, dominated by the weak charge of the proton, 𝑄𝑊𝑝=1−4sin2 θ𝑊.
Given the scattering rates mentioned above, a measurement of 𝑄𝑊𝑝with ~1% relative statistical precision can be achieved in 10000 hours

## Slide 4: P2 @ Mainz - Recap
P2 Backward angle measurement
P2 + BASKET
Electrons scattered within 120º<θ<160º
Scattering rate of ~ 100 MHz
1000h  1014 electrons
Larger angles  100 x larger
Dominated by the proton form factors instead of
Once constrained
  NO limit for the forward angle P2 result
Not “extra physics” — it is essential to unlock the full precision of P2
Notes: The parity-violating scattering cross section asymmetry, APV, is about 5x10-8 in this configuration, and dominated by the weak charge of the proton, 𝑄𝑊𝑝=1−4sin2 θ𝑊.
Given the scattering rates mentioned above, a measurement of 𝑄𝑊𝑝with ~1% relative statistical precision can be achieved in 10000 hours, and yields a precision in the weak mixing angle of δsin2θW ~ 0.0003, which competes with that of the best e+e- measurement results from LEP and SLC.

## Slide 5: P2 @ Mainz - Recap
P2 Backward angle measurement
P2 + BASKET
Experimental advantages
  Manageable event rate
  Allows event-by-event tracking (unlike forward P2 in integrating mode)
    Reconstruct: scattering angle momentum, vertex position
    Validate: Energy loss models in LH2 target, radiative corrections, background and acceptance effects
Notes: Impact on systematics
Reduces uncertainty from axial/strange form factors by factor 5–10
Lowers their contribution to Qᵂᵖ uncertainty to ~0.2%
Ensures P2 reaches its precision goal on sin²θ₍W₎

## Slide 6: Toward the P2-Basket Implementation
3. Detectors(IRFU/DEDIP/DPhP)
  Bulk Micromegas
  Frame and Drift electrode
  HV and Gas circulation
1. Mechanics (IRFU/DIS)
  Chapeau
  Target Mask
  Vacuum Shielding (in collaboration with DEDIP)
  Detector Support
2. Physics(IRFU/DPhP)
  Simulation
    Signal acceptance
    Background
  Online Tracking
  Reconstruction
4. Electronics (IRFU/DEDIP)
  Frond-end
  Back-end (Supervisor/Software)
  Service (BT/Interlock)
  Low voltage

## Slide 7
Mechanics

## Slide 8: Mechanics – 2025 Design
fwd. meast bkwd. meast
Chapeau
Chapeau
  Includes membrane and beam tube extension
    Challenges on the design:
      Main flange and membrane difficult to shape and solder
      Difficult integration (little margin)

## Slide 9: Mechanics – 2025 Design
fwd. meast bkwd. meast
Chapeau
Chapeau (Finalized)
  Change on the shape of the main flange (“stairs”)
  Shorter cylinder
    Simulation studies (M. Gailliard) shown better acceptance with closer detector planes
    Shorter membrane
      Carbon fiber
      Can be purchased separately
      Simplifies integration
      Facilitates the Target/Mask design

## Slide 10: Mechanics – 2025 Design
fwd. meast bkwd. meast
Shieldings
Vacuum shielding (Finalized)
    Two designs to connect to the rails
    24 aluminum frames; 10 lead sheets/frame
      Total weight ~ 700kg including screws
Integration strategy
    Purchase material + water-jet cutting of basic elements
    Assembly on site (Saclay and/or Mainz)
Notes: Why do we need the water-jet cutting approach?

## Slide 11: Mechanics – 2025 Design
fwd. meast bkwd. meast
Target & Target mask
Target Mask & Target (Not Started)
    Complex interface with target support
    Depended on the chapeau design (due to limited available space)
    With the updated design of the Chapeau the objects can now move as a single system!
    Challenge: Interface and hooks still need to be defined
Latest design step files can be found here : https://seafile.rlp.net/library/16a6740c-1a99-4435-acd7-2c98f5eea8bf/P2/
Notes: Is the plan to move the target for the forward and backward measurements? Will they be taken place separately?

## Slide 12: Planning 2026
Strategy: separate contracts for the different elements
Chapeau : T4 2026 - T2 2027
  Timeline: Call for tender end Feb  contract early summer 2026  construction few months (TBC)  updated design review with NTG needed
Membrane : T3 2026
  Design finalized, company identified, quote available
Vacuum chamber shielding : T3 2026 (installed first)
  Design finalized, contacts established, quote available
Target mask : T4 2026 (installed second)
  Simple design, interface with target support to be defined (maybe dedicated meeting soon?)
Beam tube extension : T3 2026
  Standard beam tube & flanges + bellows to absorb the small movements (Coordination with MESA foreseen)
Notes: What Is NTG

## Slide 13
Physics

## Slide 14: Optimization of the signal acceptance
Target
det2 det1 det0
300mm
z=500mm
zDet0=-2500mm
3 parameters to optimize
    Distance between detectors
    Position of closest to target detector
    Magnetic field scaling ( 0.7 T is the max value)
Work done by M. Gaulliard
Observables
    Fraction of elastic electrons that produce a 3-plane track (3Hits coincidence)
      Combinatorial background events included in the total number of events on this analysis
Notes: Why the chapeau is outside? Is it really? Is only the membrane in vacuum and the rest is supported outside? Target (slide 2 on the google slides, it seems to me that its all inside a vaccume chamber)
In the simulation is it one detector per plain? Do we include the detector per pad response? And how does the optimization goes
Instead of absolute rate(number of 3-hit events per second), we maximize:
(3-hit elastic e⁻ rate) / (total e⁻ rate)
This:
suppresses background sensitivity
isolates geometrical and magnetic effects
is robust against luminosity assumptions

## Slide 15: Optimization of the signal acceptance
3 parameters to optimize
    Distance between detectors
    Position of closest to target detector
    Magnetic field scaling ( 0.7 T is the max value  100%)
Work done by M. Gaulliard
Observables
    Fraction of elastic electrons that produce a 3-plane track (3Hits coincidence)
      Combinatorial background events included in the total number of events on this analysis

## Slide 16: Optimization of the signal acceptance
3 parameters to optimize
    Distance between detectors
    Position of closest to target detector
    Magnetic field scaling ( 0.7 T is the max value  100%)
The smallest possible distance between the det planes gives the best efficiency for any B field
300mm  Hardware limit
Work done by M. Gaulliard
Observables
    Fraction of elastic electrons that produce a 3-plane track (3Hits coincidence)
      Combinatorial background events included in the total number of events on this analysis
Notes: Instead of absolute rate, we maximize:
(3-hit elastic e⁻ rate) / (total e⁻ rate)
This:
suppresses background sensitivity
isolates geometrical and magnetic effects
is robust against luminosity assumptions

## Slide 17: Optimization of the signal acceptance
3 parameters to optimize
    Distance between detectors
    Position of closest to target detector
    Magnetic field scaling ( 0.7 T is the max value  100%)
Observables
    Fraction of elastic electrons that produce a 3-plane track (3Hits coincidence)
      Combinatorial background events included in the total number of events on this analysis
Further backward from the target @ 70% of B the best det. efficiency
Output of Simulation
    Distance between detectors  300 mm
    Distance closer to target  -2700 mm
Work done by M. Gaulliard
Notes: → zDet0 = -2700m, B 70% (further backward) best relative 3hits rate
→intermediate config. can still be interesting (more stats, different scattering angle distrib.)

## Slide 18: Optimization of the signal acceptance
3 parameters to optimize
    Distance between detectors
    Position of closest to target detector
    Magnetic field scaling ( 0.7 T is the max value  100%)
Observables
    Fraction of elastic electrons that produce a 3-plane track (3Hits coincidence)
      Combinatorial background events included in the total number of events on this analysis
Further backward from the target @ 70% of B the best det. efficiency
Output of Simulation
    Distance between detectors  300 mm
    Distance closer to target  -2700 mm
Work done by M. Gaulliard
Resolution estimation
Scattering angle  σθ = 4 degrees
Z vertex  σz = 133 mm
Notes: → zDet0 = -2700m, B 70% (further backward) best relative 3hits rate
→intermediate config. can still be interesting (more stats, different scattering angle distrib.)
Here we focus on the 3-hit fraction as a purity-driven metric; optimizing the absolute rate favors different configurations and provides complementary acceptance, which will be addressed in follow-up studies
Optimizing for clean track fraction and optimizing for total statistics lead to different preferred detector configurations. By shifting the detector position and magnetic field within the allowed range, we can access complementary acceptances, which is interesting from a physics point of view.

## Slide 19
Detectors

## Slide 20: Minimization of X-ray background
Detector technology
    Micromegas detectors
    Suitable for low material budget applications
    Large area coverage
    Radiation hard
    Good spatial/energy resolution ~ 150 μm / 15%
Mylar
Readout Kapton
Mesh
Mylar
Drift
[Giomataris et al., NIM A 376 (1996) 29]
Geant4 simulation
    X-ray beam generated in an Ar/C4H10 gas envelope with a MM detector included
    Drift electrode  Drift Gap (3.25 mm) Ar/C4H10(90:10)  Mesh  Ampl. Gap(128um) Ar/C4H10(90:10)  Cu (50um)  FR4(150um)  Cu 50um
Notes: → zDet0 = -2700m, B 70% (further backward) best relative 3hits rate
→intermediate config. can still be interesting (more stats, different scattering angle distrib.)

## Slide 21: Minimization of X-ray background
Detector in P2 and in the simulation
    Metallic Micromegas with readout pad structure
    Readout structure of 1 cm □ pads
    (corresponding to 1280 per module)
Construction material can affect the background
    Drift electrode material effect
    Mesh Geometry effect
120 µm Mylar drift electrode
60 µm mesh interwire
offers 11% reduction
Condition: at least 1 e- is produced & reach an active gas region
Work done by M. Gaulliard
Notes: → zDet0 = -2700m, B 70% (further backward) best relative 3hits rate
→intermediate config. can still be interesting (more stats, different scattering angle distrib.)

## Slide 22: Comparison with Experimental data
spectrum of xray in full P2 simulation, received by closest-to-target Micromegas
X-ray Beam Measurements
    Soft x-ray beam of 15-100 keV energy range
    SOLEIL synchrotron @ Ormes de Merisiers (France)
    Two 10x10 cm2 detector prototypes
    Germanium / Silicon Drift  Detector reference measurement for energy calibration
Good agreement @ 30, 40, 100 keV (already satisfactory for the P2 energy range)
Work done by M. Gaulliard

## Slide 23: Detector Production (Size 1 Prototypes)
Production on site
    Challenges in the bulking process:
      Max size with respect to the machine size
      Change in the photoresist material available (needed for the bulking process)
      Bulking process and degradation of the raw PCB material
    Key challenges identified; mitigation strategies in progress
    Bulking process
    Drift electrode assembly
    Connector soldering

## Slide 24: Detector Testing
Cosmic Bench in Saclay
    Two outer 60x60 cm2 scintillator with four 50x50 cm2 Micromegas trackers
    Characterization of prototypes in low muon rate environments
    Efficiency measurements / Homogeneity of response
Work done by G. G. Veyrac & A. Gairot

## Slide 25: Detector Testing
Particle Beams @ CERN SPS H4 Beamline
  Highly energetic muons (80-150GeV) and pions of 80 GeV
  Shared TB campaign with EIC group of CEA
  Three 10x10 cm2 small scale prototypes
  One Size one prototype
  Gas Mixture : Ar/CO2/Iso (95:3:2) (non-flammable)
  Detector characterization measurements using different particle types
  Rate performances evaluated, mainly for the electronics
P2_G
P2_1
P2_3
banco ref tracker
beam direction
P2_3

## Slide 26: Highlighted Results (Analysis ongoing)
  Stable detector performance in a range of rates from few kHz up to 2MHz with muons and pions
  Stable operation also of the dedicated frond end /back end electronics tested with different protection boards

## Slide 27: Planning 2026
Simulations
  Understand and Finalize SOLEIL Analysis (low energy problem)
  Physics Fit of for backward measurement with pseudo-data
  Online Tracking
  Pattern recognition and Lookup Table (3 channels →truth values) & its hits matching logic need to be implemented in FPGA
Detector Performances
  Prioritize the detector development process
  Set the plan for detector integration/validation/commissioning
  Detector testing in magnetic field
  Finalize the analysis framework for the test beam data
Notes: I don’t really understand the two last objectives of the simulation part

## Slide 28
Electronics

## Slide 29: Readout architecture
Machine interface Clock, synchro
Frontend on detector
180 VMM Hybrids  60 per plane
Backend in cavern
12 AXKU040 boards
15 hybrids per backend
5m
100m
Supervisor in control room
e.g. EK-VCK190 board
10 GE optical
High-speed optical Data & control
Ethernet network
PC cluster
Data & control
Electrical : data & control

## Slide 30: Frontend Status
Frontend production
  200 VMM Hybrids delivered and validated in-house on Irfu test-bench
    196 accepted with not more than 2 bad channels per 128-channel hybrid
    4 hybrids replaced by SRS Technology
  Hybrid classification data base under construction
    ID, malfunctioning channels, best performance configuration parameters …
Frontend protection circuit studies
  Goal: Improve deadtime after detector discharges and achieve robust channel protection
  2 add-on schemes devised standing 600 V sparks
    bulky (higher safety margin)
    compact (lower safety margin)
  Both degrade S/N by ~15%
  Both improve deadtime ~4 times
  Enough knowledge to design frontend adaptation board
VMM Hybrid
NUP4114
1M
470p
VMM 0
Chan X
10
ProtStage DC
1M
ProtStage AC
470p
BAV99
BAV99
TP

## Slide 31: Backend Status
Backend
  FW and SW of the commercial AXKU040 board extended to support
    16 frontends
    Separate data and control Ethernet networks
    10G Ethernet for data links
  Prototype backend-frontend interface board developed
  Slow-control software
    Main functions for scripting hardware configuration and running data acquisition ready
    Data model extended to support 8 sub-networks of 16 Fec boards each containing 16 hybrids (full system: 262K channels)

## Slide 32: Low voltage powering
Low voltage power distribution
  TDK Lambda LV power modules for frontend and backend electronics
  6 m cable harness devised based on commercial shielded cables
  Performance validated with the nominal load of 10 frontends
    Power-up sequence tested – final-scale scheme under elaboration
Portable test bench with backend, PS, switch and frontend for radiation tolerance assessment
LV power supply
LV power supply
Hybrids
Backend

## Slide 33: Irradiation Tests
Radiation tolerance studies
  Expected radiation doses after 3 months of operation
    Frontend : ~40 krad and 6x1011 1 MeV neq / cm2 – space-grade
    Backend : ~4 krad and 3x1011 1 MeV neq / cm2 – high neutron flux
  Irradiation tests in A1 hall @ MAMI
    Overwhelmingly intensive : beam current (20 mA?)
    Frontend and backend installed on beam pipe close to beam dump
      Including neutron flux monitoring nBLM detectors
    Controlling electronics installed in “safe” area behind shielding blocks
  Estimated received dose : ~1 Mrad
  Parts of acquisition started to become inaccessible
    Even in the “safe” zone
  Neutron fluence to be understood from simulations
    Unfortunately nBLM acquisition failed
  Damage level to be evaluated when access to hardware be possible

## Slide 34: Planning 2026
Validate system readout on 1/6 of the tracker
    2027 : production, construction, validation, commissioning
Frontend
    Develop, validate and produce 50 detector interface boards with protection circuits
Backend
    Enrich firmware with cross-backend and supervisor isochronous communication links
    Produce backend-frontend interface boards
Supervisor
    Make supervisor board choice
    Develop supervisor-machine interface board
    Develop run-control part of the supervisor firmware

## Slide 35: Planning 2026
System
    Understand radiation and magnetic field related issues
      May have important consequences for backend electronics whereabouts
    Finalize LV distribution system
    Devise and validate frontend cooling
    Developpe software and firmware versions of on-line track-finding algorithms
Software
    Pursue run-control framework development
    Simplified GUI for operating the system
    Monitoring visualizations
    Run management including run conditions

## Slide 36: Thank you
CEA SACLAY
91191 Gif-sur-Yvette Cedex
France
alexandra.kallitsopoulou@cea.fr

## Slide 37
Back up

## Slide 38: Optimization of the signal acceptance
Observables
    Fraction of elastic electrons that produce a 3-plane track (3Hits coincidence)
      Combinatorial background events included in the total number of events on this analysis
Output of Simulation
    Distance between detectors  300 mm
    Distance closer to target  -2700 mm
Resolution estimation
    Scattering angle  σθ = 4 degrees
    Z vertex  σz = 133 mm
Work done by M. Gaulliard
Notes: → zDet0 = -2700m, B 70% (further backward) best relative 3hits rate
→intermediate config. can still be interesting (more stats, different scattering angle distrib.)

## Slide 39: Frontend production
200 VMM hybrids have been received on 7/Feb/2025
  In-house production validation on Saclay test-bench (next page)
Acceptance criteria
  Not more than 2 bad channels per 128-channel Hybrid
  “Bad” hybrids to be replaced by SRS Technology
Outcome
  196 accepted VMM hybrids
  4 hybrids replaced by SRS Technology
    To be tested on Saclay test-bench
  Frontends classified
    Number of channels, “best-performance” configuration parameters
    On-going : excel sheet to be replaced by a data base

## Slide 40: Saclay production validation test bench
Backend
LV power for
Hybrid and Backend
LV power for
charge injector
Charge injector
Hybrid
Protections

## Slide 41: Frontend protection

## Slide 42: Frontend protection studies
VMM hybrids feature on-board per-channel protection circuit
  Overvoltage diodes followed by an AC coupling capacitor
  Non-optimal to recover metallic detector efficiency after discharge
  Requires an extra protection circuit to be robustly safe
Study add-on protections to overcome the weakness
  Exercise with dedicated “killer” circuit and real detectors
  Check S/N degradation
  Check deadtime decrease
  Develop a flexible cascade-able board to check different protection types
Make the choice for detector-frontend adaptation board design
  Robust, compact, acceptable S/N degradation
VMM Hybrid
NUP4114
1M
470p
VMM 0
Chan X
10
ProtStage DC
1M
ProtStage AC
470p
BAV99
BAV99
Killer
1n
HV
From -1V to -600V
TP
ProtStage board
“Killer”
A test configuration example with cascaded ProtStages and Killer

## Slide 43: Frontend protection studies
2 possible add-on circuits identified
  Bulky : less than ± 6V peak residual voltage at the entry of the VMM Hybrid
  Compact : less than -20 V / +10 V residual voltage at the entry of the VMM Hybrid
  Both survive 600 V discharges
  Both degrade S/N by ~15%
  Both improve deadtime ~4 times
Frontend adaptation board with “bulky” circuits if space limitation permits
60 ms
600 ms
Mesh potential : on-board protections only
Mesh potential : with additional protections
Coherent
Killer & detector
measurements
Detector measurements coherent with simulation
Expected

## Slide 44: Protection studies
1 additional AC-coupled BAV99 diode stage
  Asymmetric excursions exceeding -20 and +10V
  All 4 tested channels died under -600V discharges
1 additional BAV99 diode stage + 10Ω resistor
  Asymmetric excursions lower than -20 and +10V
  All 7 tested channels survived -600V discharges
2 additional BAV99 diode stages
  Symmetric +/- excursions < 5V
  All 7 tested channels survived -600V discharges
Chart: Averaged residual voltage @ hybrid input
| -10 | -100 | -200 | -300 | -400 | -500 | -600
1-stage | -2.9825 | -7.51 | -11.16 | -14.44 | -17.0025 | -20.065 | -22.7875
1-stage | 1.92 | 3.8925 | 6.03 | 7.425 | 9.2125 | 10.3425 | 10.47
1-stage+10Ω | -2.2943 | -5.5057 | -7.98 | -10.1786 | -11.9414 | -13.8757 | -15.6429
1-stage+10Ω | 1.2271 | 2.7514 | 4.0557 | 5.39 | 6.5857 | 7.3729 | 7.6114
2-stage | -2.0367 | -2.79 | -3.15 | -3.5086 | -3.828 | -4.2 | -4.3914
2-stage | 1.6983 | 2.2314 | 2.68 | 3.2914 | 3.76 | 4.046 | 4.09
All killed
All killed

## Slide 45: Radiation immunity

## Slide 46: Frontend test configuration
Dose estimate for ±0.5m around the beam : 20 rad /h
Dose monitor to be installed on the frontend
20 m
Negligible radiation area in the hall
Adapted radiation area in the hall
Counting room
Time | TID (krad) | Grade
Hour | 0.02 | Commercial
Day | 0.5 | 
Month | 14 | 
1 000 h | 20 | Rad tolerant (space)
3 months | 43 | 
6 months | 86 | 
9 months | 130 | 
Year | 173 | 
10 000 h | 200 | Rad hard

## Slide 47: Backend test configuration
Dose estimates at 50 cm to 1m from ground : 2 rad / h
Dose monitor to be installed on the backend
20 m
Negligible radiation area in the hall
Adapted radiation area in the hall
Counting room
Time | TID (krad) | Grade
Hour | 0 | Commercial
Day | 0.1 | 
Month | 1.4 | 
1 000 h | 2 | 
3 months | 4 | 
6 months | 9 | 
9 months | 13 | 
Year | 17 | 
10 000 h | 20 | Rad tolerant

## Slide 48: The objects to irradiate
Each require a single 220V mains outlet
Dimensions of nBLM neutron detectors to be taken into account when placing the objects in the hall
Integrated backend
2-4 krad < 10 krad
~1011 1MeV neq / cm2
Integrated frontend
20-40 krad < 100 krad
~1011 1MeV neq / cm2
220
360
120
490
460
120

## Slide 49: The objects in the safe area
To be added :
  Scope and HV PS for nBLM detectors
  A PC + screen
Integrated setup with
Backend for irradiated frontend
Frontend for irradiated backend
Backend
Frontend
700
300
200
380
200
380

## Slide 50: Low Voltage Power Supply testbench with 10VMM
Configuration:
Z10-40 -> 2,2 V IP: 192.168.0.50
Z10-40 -> 3,3V IP: 192.168.0.51
Z20-40 -> 12V IP: 192.168.0.70
When Alinx power ON, voltage@TDK output:
  [2,2V]: 2,17V / 12,65A
  [3,3V]: 3,3V / 2,43A
Voltage measurement:
Power suppy TDK output:
  [2,2V]: 2,64V /13,53A
  [3,3V]: 3,30V /1,35A
Power suppy bus bars:
  [2,2V]: 2,17V
  [3,3V]: 3,26V

## Slide 51
LVPS Testbench: Power supply 10 VMM Ref power supply: TDK Lambda Z10-40
2,2V
2,2V
GND
3,3V
Bus Bars
3,3V
Shut off control
Number | VMM | Current for 2,2V | Current for 3,3V
1 | 4529 | 1,48 A | 0,13A
2 | 4389 | 1,47A | 0,13A
3 | 4360 | 1,49A | 0,12A
4 | 4015 | 1,64A | 0,13A
5 | 4096 | 1,31A | 0,13A
6 | 4321 | 1,19A | 0,12A
7 | 4342 | 1,51A | 0,12A
8 | 4346 | 1,49A | 0,12A
9 | 4024 | 1,75A | 0,13A
10 | 4021 | 1,37A | 0,12A
 | Total | 14,84A | 1,23A

## Slide 52: LVPS Testbench – Rise time measurement with 10 VMM
Rise time for 2,2V: 965,7 µs
Rise time for 3,3V: 536,9 µs

## Slide 53: LVPS Testbench – No glitch !
Rise time for 2,2V: 965,1 µs
Rise time for 3,3V: 555,4 µs

## Slide 54
HDMI 1m cable, 25 times measurements
Voltage C1: 3,31V, time rise : 1,78 ms and no glitch with 200ms timebase
Voltage C2: 2,3 V, time rise 808,87 µs and no glitch with 200ms timebase
SNR Testbench: Rise time measurement with VMM Hybrid Ref power supply: TDK Lambda Z10-40

## Slide 55
HDMI 1m cable, 25 times measurements
Voltage C1: 3,31V on power supply
Voltage C2: 2,7 V on power supply
SNR Testbench: Rise time measurement with VMM Hybrid without sense Ref power supply: TDK Lambda Z10-40

## Slide 56
HDMI 1m cable, 25 times measurements
Voltage C1: 3,31V on power supply
Voltage C2: 2,2 V on power supply
SNR Testbench: Rise time measurement with VMM Hybrid with sense Ref power supply: TDK Lambda Z10-40