## Slide 1: Scintillating Bubble Chambers
Status of SBC-LAr10 & SBC-SNOLAB Carter Garrah
MI Annual Meeting – Queen’s University, Kingston
July 28, 2026

## Slide 2
Bubble Chambers
MI Annual Meeting 2026
Carter Garrah
Threshold detectors using superheated target fluids a
Sufficient local energy deposition (Erecoil > QSeitz) yields vaporization: bubbles ! (acoustic/pressure + visual signal) a
Process is highly β and 𝛾 insensitive
1
3
1
2
2

## Slide 3
Why Liquid-Noble Bubble Chambers?
Carter Garrah
Freon target: a
  Purely threshold detectors (no energy information) a
  Become sensitive to β and 𝛾 at low-thresholds
Liquid-noble target: a
  Scintillation signal a
  Improved β and 𝛾 suppression observed at low thresholds
Pico C3F8 Ionization Model LXe SBC Sensitivity
Freon ER Limits
Xenon ER Limits
Phys. Rev. D 111, 032002 and Universe 2023, 9(8), 346
MI Annual Meeting 2026

## Slide 4
The 1st SBC: XeBC Demonstration Chamber
Carter Garrah
CAMERA (VISUAL)
ACOUSTIC
SCINTILLATION
First demonstration with a 30-g bubble chamber with a liquid xenon target; single event readout for x3 sensory channels
MI Annual Meeting 2026
Phys. Rev. Lett. 118, 231301

## Slide 5
Inner Chamber Schematic
SiPMs
Piezo
Camera View Ports
CF4
Liquid Argon
Pressure Vessel
Vacuum Jacket
SBC: Current 10-kg Detector Design
Carter Garrah
x2 near-identical SBC detectors:
  SBC-LAr10 @ Fermilab
  SBC-SNOLAB
Active Fluid: 10 kg LAr doped with 𝒪(10 ppm) Xe
100 eV nuclear recoil threshold target
Chamber operated at 130 K and 30 psi with CF4 cryogenic hydraulic fluid
Diagram Credit: Ezri Wyman
MI Annual Meeting 2026

## Slide 6
SBC: A Tale of Two Chambers
Carter Garrah
~300 cm
SBC-LAr10 (Fermilab)
SBC-SNOLAB
MI Annual Meeting 2026

## Slide 7
SBC: Sensory Equipment
Carter Garrah
Three key sensory components to an SBC chamber for acquiring particle information
1
2
Cameras (x3)
Piezoelectric Transducers (x8)
Silicon Photo- Multipliers (SiPMs) (x32-48)
Bubble Event Location + Visual Trigger
Acoustic Bubble Data + Particle Identification
Scintillation Light + Energy Information
3
MI Annual Meeting 2026

## Slide 8
SBC-LAr10 @ Fermilab
Carter Garrah
  First of the two identical detectors being developed near-simultaneously
  Physics goals:
    Detector gamma calibration
    Engineering prototyping for SNOLAB
    Potential reactor CEνNS studies
SBC-LAr10 @ MINOS Hall
MI Annual Meeting 2026

## Slide 9
SBC-LAr10: Current Status
Carter Garrah
Sample Volume Pressure Trace
Camera Trigger
Acoustic Signal (Start)
  First operational runs now complete!
  6 months of stable operation; simultaneous bubble nucleation + scintillation observed
  Analysis of gamma calibration data is on-going (testing electron recoil sensitivity)
  Publication expected this autumn (stay tuned!)
MI Annual Meeting 2026

## Slide 10
More of SBC-LAr10 @ Fermilab
Carter Garrah
MI Annual Meeting 2026

## Slide 11
SBC-LAr10: Tri-Camera Setup
Carter Garrah
Cam 1
Cam 2
Cam 3
Simulated Camera Images Showing all Three Chamber Views
Credit: Gray Putnam Rendered with Mitsuba Python library
MI Annual Meeting 2026

## Slide 12
SBC-LAr10 Sample Camera Streams
Carter Garrah
Sample Single Bubble from SBC-LAr10
MI Annual Meeting 2026

## Slide 13
SBC-LAr10 Sample Camera Streams
Carter Garrah
Sample Multi-Bubble from SBC-LAr10
MI Annual Meeting 2026

## Slide 14
SBC-LAr10 Hamamatsu SiPMs
Carter Garrah
SBC Preliminary
SBC Preliminary
1 PE
2 PE
3 PE
4 PE
5 PE
SiPM Pulse Fitting
Semi-populated SBC-LAr10 copper SiPM panels with Hamamatsu VUV4s (32 total)
MI Annual Meeting 2026

## Slide 15
SBC-LAr10 Piezoelectric Sensors
Carter Garrah
Example Acoustic Signal from SBC-LAr10
MI Annual Meeting 2026

## Slide 16
SBC-SNOLAB
Carter Garrah
  Second detector, currently being developed here at Queen’s University!
  Physics goals:
    WIMP / particle dark matter search
    Background mitigation through improved detector shielding + SNOLAB’s natural overburden
SBC-SNOLAB
MI Annual Meeting 2026

## Slide 17
SBC-SNOLAB: Current Status
Carter Garrah
MI Annual Meeting 2026
Have passed SNOLAB’s TDR and IRR processes; ready for installation on-site to begin!
Pressure vessel + vacuum jacket already at SNOLAB (right)
Awaiting final detector components (e.g., fluid panels) before installation
DAQ/Sensor development on-going (more on that in a bit…)

## Slide 18
More of SBC-SNOLAB
Carter Garrah
MI Annual Meeting 2026

## Slide 19
SBC-SNOLAB: Custom FBK VUV HD3 SiPMs
Carter Garrah
(Photos Credit: G. Sweeney)
FBK VUV HD3 Silicon Chip Wafer
Wire Bonds
MI Annual Meeting 2026

## Slide 20
FBK SiPM Testing Plans
Carter Garrah
Hamamatsu VUV4
(Test) FBK VUV HD3
~50 FBK SiPMs fabricated at TRIUMF
Recently acquired a set of SiPM-FE-Rev1-A multi-channel amplifiers from nEXO group
Testing/Characterization Plans:
  Currently assembling small testing chamber for operating 48+ SiPMs
  Clean-room tests @ vacuum for operational testing + I-V curves
  Potential in-gas/liquid testing (TBD)
Testing out SiPM electronics with VUV4s to prep for FBKs!
H. Hawley-Herrera et al 2024 JINST 19 T08003
MI Annual Meeting 2026

## Slide 21
SBC-SNOLAB: Camera System
Carter Garrah
Arducam OV281 Webcam
Current Tasks: a
Implementing timing control of tri-camera setup through our PLC
Camera model selection:
  Baslers (0.4 MP ace acA720-290gm)
    Stronger PLC compatibility (industrial cameras via GigE)
    Hot! (sub-50℃ casing temperature)
  Arducams (1 MP OV281 UVC Webcam)
    Used for SBC-LAr10 (MIPI variant)
    Less heat dissipation
Analysis Tasks:
  Bubble position (x, y ,z) reconstruction
  Trigger algorithm testing for speed (< 10 ms processing) and efficacy
Basler Ace GigE Cameras
MI Annual Meeting 2026

## Slide 22
Carter Garrah
SiPMs
Piezos
Cameras
CF4
Liquid Argon
Pressure Vessel
Vacuum Jacket
SBC-SNOLAB: Data Acquisition Unification
PLC Beckhoff CX5140 PC (10 ms cycle)
  SBC-LAr10’s sensory systems and electronics operate on numerous (13!) independent machine clocks
  We believe that we can do better with SBC-SNOLAB: 1 PLC-controlled clock
PLC: Programmable Logic Controller
- PC with I/O terminal cards for interfacing with various equipment (RTDs, pressure sensors, etc.) that can perform cyclical logic computations during detector operation
1
2
3
MI Annual Meeting 2026

## Slide 23
SBC-SNOLAB: Data Acquisition Unification
Carter Garrah
The reality of working with PLCs looks something like this…!
MI Annual Meeting 2026

## Slide 24
The Future of SBC and Conclusions
Carter Garrah
  Fermilab chamber operational runs are now complete; analysis on-going!
  SBC-SNOLAB is progressing; TDR phase II & IRR complete + preparing for above-ground assembly
  Eventual future plans for scaling to a ton-scale detector with potential for ν-floor sensitivity
MI Annual Meeting 2026

## Slide 25
Thank You for Listening!

## Slide 26: End Slide