## Slide 1: NESSA: NEutron SourceS at UppSAla A versatile neutron facility for detector physics, activation studies and SEE research
Sandipan Dawn
Sandipan.dawn@physics.uu.se
15th Nordic Meeting in Nuclear Physics

## Slide 2
Presentation Outline
NESSA: Facility Overview
Present Beamlines:
    14 MeV mono-energetic neutrons based on D-T reaction.
    Tandem Accelerator based Neutron facility for selected ranges of neutron energies.
Associated Detector Systems.
Monte Carlo simulations.
Current Experimental Program.
Future Research Directions.
NESSA Team
S. Pomp (PI), G. Ericsson, M. Lantz, E. Arnqvist, L. Hägg, S. Jarl Holm., & S. Dawn

## Slide 3
TSL : A world class high energy neutron beam for basic research: Closure in 2013 left a major gap in Swedish neutron physics infrastructure — the gap NESSA now fills
The Neutron Physics Legacy at Uppsala — and the Gap NESSA Fills
TANDEM Laboratory Ion beams for materials research.
The Fast Reflectometer for Extended Interfacial Analysis (FREIA) for the ESS facility
TANDEM
TSL
FREIA

## Slide 4
NESSA facility at Ångström Laboratory, Uppsala
Initiated in 2013*.
Commissioned in November 2025.
Sodern Genie 16™ Model.
Door, dose and ventilation interlocks for Radiation Safety.
Flux and dose rate monitoring from outside control station.
*H. Sjostrand et al.; Total Monte Carlo Evaluation for Dose Calculations, RPD, 2013

## Slide 5: Key Technical Specifications of the Neutron Generator
Peak neutron yield: 4.7 × 10⁸ n/s/4π sr
Tritium inventory (2018): 120 GBq
Maximum achievable thermal flux at 3.5 cm from target (Closest User Position: CUP)
Operating modes: continuous (DC) and pulsed
Pulsed mode (current-limited): minimum achievable pulse: 10 µs
Pulse timing controlled via proximity box; external trigger compatible
151mm
70mm
CUP

## Slide 6: Principal Components of the D-T Neutron Generator
Gas replenisher: regulated D-T fuel supply.
RF ion source: generates D-T plasma.
HV accelerating stage: 40–120 kV.
Tritiated target (Ti-T): emits 14.1 MeV neutrons.
Both source and target use an equimolar D:T mixture (50:50).
proton
neutron

## Slide 7: Neutron Flux: Measurement Parameters and Notation
Parameter Definitions:
RRep — Gas replenisher resistance (mΩ). controlling gas pressure and D-T fuel flow.
VHV — Applied high voltage (kV). governs ion beam energy and thus neutron yield.
Itube — Tube current (µA). directly proportional to the neutron production rate.
At 120 KV- VHV , 80 µA- Itube & 1670 mΩ- Rrep
Y=4.4 x 108 n/s.

## Slide 8: Associated Detector Systems and Instrumentation
Micro-fission chamber (µFC) for real-time beam flux monitoring — both ²³⁵U and ²³⁸U variants available.
NaI(Tl) & LaBr₃ scintillators for prompt gamma-ray spectroscopy.
EJ-301 liquid scintillator for fast-neutron detection and n/γ discrimination.
High Efficiency HPGe system for gamma spectrometry.
WENDI extended energy neutron dose-rate meter
Fission Chambers and Liquid scintillators placed in closed user position
Building up the lead castle for HPGe in NESSA

## Slide 9: ⁹³Nb Activation Foil Dosimetry and Flux Monitoring
93Nb(n.2n)92mNb
93Nb is one of the most suitable elements for absolute yield measurements via neutron activation.
93Nb(n,2n)92mNb  934.44 keV γ with 99.15 % branching ratios.
σ ~ 0.457 barn at 14 MeV.
100% isotopic abundance

## Slide 10: Absolute Neutron Yield from ⁹³Nb(n,2n)⁹²ᵐNb Activation Foil
Calibrated values during commissioning is 4.4 x 108 n/s.
Source degrades over time (6 years old)
Uncertainty from HPGe counting is only statistical uncertainty.
Y = (4.33 ± 0.36) × 10⁸ n/s

## Slide 11: Monte Carlo Modelling of the complete beamline
Major Monte Carlo codes have been used to reconstruct complete NESSA geometry and detector responses.
Geant4. FLUKA. MCNP. PHITS & SERPENT.
Activation analysis of different structural materials, air activation.
Neutron Spectrometry and dosimetry at different irradiation positions.
Intercomparison of different physics models, cross-section libraries and Monte Carlo codes.
3D reconstruction of NESSA facility
Reconstruction of HPGe detector

## Slide 12
Simulated Neutron Fluence
Neutron Fluence Map in NESSA bunker using PHITS
Characterization of Neutron fluence and spectra through out the beam hall.
Maximum flux at CUP is 2.46 x 106 n/cm2/sec.
Important for detector characterization. activation analysis and safety report.

## Slide 13
Characterization of Neutron Spectra
Location / Energy Range | Fluence (1/cm²) | % | Notes
CUP Location |  |  | 
Thermal (<10 eV) | 2.76E+03 | 0.14 | Room-return thermal
10 eV - 100 keV | 5.78E+03 | 0.28 | Epithermal region
Fast (≥100 keV) | 2.03E+06 | 99.58 | Primary D-T (~14.1 MeV)
FCIB Location |  |  | 
Thermal (<10 eV) | 2.14E+03 | 25.06 | Room-return thermal
10 eV - 100 keV | 1.91E+03 | 22.40 | Epithermal region
Fast (≥100 keV) | 4.49E+03 | 52.53 | Primary D-T (~14.1 MeV)
Room back-scattering components are significant due to relatively compact geometry.
At certain irradiation positions. it can be up to 50%.
Important for detector calibration and response studies.

## Slide 14
uFC location experiment | coating | σavg(b) | Measured count rate (cps) (*) | Calculated rate (MCNP) ( = 65%) | Calculated rate (PHITS) ( = 65%)
CUP* | 235U | 2.45 | 34.16 | 36.1 (+5.7%) | 33.10 (-3.1%)
CUP* | 238U | 1.15 | 10.20 | 15.6 (+53%) | 14.4 (+41%)
FCIB ** | 235U | 92.00 | 2.213 | 2.224 (+0.5%) | 2.060 (-6.9%)
FCIB** | 238U | 0.36 | 11.01x10-3 | 8.6010-3 (-22%) | 7.6910-3 (-30%)
* CUP is about 4 cm from the neutron emitting target
** FCIB is about 130 cm from the neutron emitting target
Fission Chamber response in NESSA
Ericsson. G.. Pomp. S.. Hägg. L.. & Dawn. S. (2026). Development of a Neutron Field Monitoring System for the DT Neutron Generator Facility NESSA
Fission chamber in irradiation positions
R235/R238 is the spectral index

## Slide 15
Gamma Ray in the neutron field: Simulation Results
Type
Nuclide
Reaction
γ Energy (MeV)
T½
Source in NESSA
PROMPT
¹H
¹H(n.γ)²H
2.223
—
PE shielding. thermalised n
PROMPT
¹²C
¹²C(n.n'γ)
4.439
—
Borated PE. organic material
PROMPT
¹⁶O
¹⁶O(n.n'γ)
6.129 / 6.917
—
Concrete walls. air in hall
PROMPT
⁵⁶Fe
⁵⁶Fe(n.n'γ)
0.847 / 1.238
—
Iron plug. collimator wall
DELAYED
¹⁶N
¹⁶O(n.p)¹⁶N
6.129 / 7.115
7.1 s
Concrete & air; dominates post-beam dose
DELAYED
²⁴Na
²⁷Al(n.α)²⁴Na
1.369 / 2.754
14.96 h
Al in structural material
Prompt (during beam-on)
Delayed (post beam-off. activation)
Production of Prompt and Delayed gamma due to neutron activation.
Plays important role in radiation protection.
An important resource for activation studies, beam characteristics, gamma detector response.
SHORT-LIVED minutes — hours
Isotope
T½
Reaction
γ (keV)
V-52
3.74 min
V-51(n,γ)
1434.1 keV
Al-28
2.24 min
Al-27(n,γ)
1778.9 keV
Mg-27
9.46 min
Al-27(n,p)
843.8 keV
C-11
20.4 min
C-12(n,2n)
511.0 keV
Mn-56
2.58 h
Fe-56(n,p)
846.8 keV

## Slide 16
Gamma Ray in the neutron field
Dose rate near the closest user position can reach 10 Sv/h.
Wide distribution of energies. Can reach up to 10 MeV.
Dose rate out side bunker is < 1µSv/h
Distribution of gamma dose rate in source plane using PHITS
Simulated Prompt γ spectra at CUP using PHITS

## Slide 17
Liquid Scintillator in Pulse Mode : Die-Away Phase
Important application in studying Die-Away phase in nuclear disarmament
Neutron Generator in Pulse Mode
n/γ discrimination
neutron
gamma

## Slide 18
Major Goal of NESSA: studying electronics damage like Single Event Error/Upset(SEE).
Direct implication in Space Science. Reactor Electronics. Aviation Safety.
Irradiated two chip configurations (Linear Feedback Shift Register and Fast Fourier Transform)
Observed single bit-flip errors in program memory requiring automatic reconfiguration.
Error rates scaled dramatically with resource utilization: FFT (86% chip utilization) suffered ~10 x more errors in comparison to LFSR design.
Error cross-section has been studied with G4SEE Monte Carlo simulation code.
Studying SEE and Electronics Damage at NESSA
Irradiation of electronic chips at NESSA
Evaluation of SEE cross-sections as a factor of critical charge using G4SEE simulation

## Slide 19: 115/113In +14 MeV neutron: Initial Results
¹¹⁵In reactions (95.7% abundant):
(n,2n)¹¹⁴ᵐIn — threshold 10.4 MeV, 49.51 d, 190.27 keV —absolute yield calibration reaction: 1210 ± 71 mb
(n,γ)¹¹⁶ᵐIn — thermal capture, 54.29 min, 1097/1293 keV — the room-return thermal contribution: Simulation benchmark
(n,n')¹¹⁵ᵐIn — threshold 0.34 MeV, 4.486 h, 336 keV — inelastic threshold detector : T½ = 4.353 ± 0.224 h.
¹¹³In reactions (4.3% abundant):
(n,2n)¹¹²In — threshold 9.2 MeV, dual isomers at 156.5 617.5 keV — IYR measurement

## Slide 20
¹¹³In(n,2n) Isomeric Yield Ratio — Decay Scheme & Measurement
Decay Scheme
¹¹³In + n (E_n ≈ 14.7 MeV)
(n,2n)
¹¹²ᵐIn
T½ = 20.67 min
¹¹²ᵍIn
T½ = 14.97 min
γ: 156.5 keV
IT (99%)
γ: 617.5 keV
⚠ ¹¹²Ag interferes
617.5 keV overlap
115In(n,α)
IYR = Yᵐ / Yᵍ (pure ground-state yield)
Measurement & Analysis Chain
1
Irradiation at NESSA D-T beam
Foil in 14.7 MeV neutron beam
Y ≈ 4.3×10⁸ n/s (⁹³Nb calibration)
2
HPGe Spectroscopy
156.5 keV (¹¹²ᵐIn) + 617.5 keV (¹¹²ᵍIn + ¹¹²Ag)
Timed series: cool, count, repeat
3
Bateman ODE Solver (Python)
Source-term equations for all phases:
irrad. → cooling → counting; Ag-112 deconvolution
4
Geant4 Validation
Full geometry simulation of HPGe + foil;
efficiency, self-absorption, angular distribution
5
IYR Extraction
R = A₁₅₆ / A₆₁₇_corrected
Statistical + systematic uncertainties
112gIn
112mIn
112Ag

## Slide 21
¹¹³In(n,2n) IYR — Results at 14.7 MeV & Cross-Checks
Measured IYR (Yᵐ / Yᵍ): 3.82 ± 0.47
**first measurement at NESSA
¹¹²Ag: T½ = 3.13 h, γ 617.5 keV
Produced via ¹¹⁵In(n,α) (~2.7 mb)
Bateman ODE system solved numerically
Time series fitting separates ¹¹²In from ¹¹²Ag component
Correction: ~8% on ground-state yield
Geant4 Validation
HPGe detector geometry fully modelled.
Foil self-attenuation at 156 & 617 keV.
Simulated peak efficiencies agree with IAEA source calib.
G4Radioactivation used for cascade verification.
Intercomparison of HP, INCLXX, QGSP_BIC, FTFP_BERT physics model.
Luo et al., 2017, Nuclear Science and engineering, Volume 188

## Slide 22
Complementary Neutron Beam facility at Tandem Laboratory at Uppsala University.
Proton beam up to 10 MeV energies can be achieved.
Several targets have been tested for neutron production
Target | Primary (p.n) reaction | Q (MeV) | Eth (MeV)
Be | ⁹Be(p.n)⁹B | −1.85 | 2.06
LiF | ⁷Li(p.n)⁷Be | −1.64 | 1.88
V | ⁵¹V(p.n)⁵¹Cr | −1.53 | 1.56
Mn | ⁵⁵Mn(p.n)⁵⁵Fe | −1.02 | 1.04
Mo | ⁹⁸Mo(p.n)⁹⁸Tc | −2.47 | 2.50
Zn | ⁶⁸Zn(p.n)⁶⁸Ga | −3.72 | 3.78
Fe | ⁵⁶Fe(p.n)⁵⁶Co | −5.35 | 5.44
B | ¹¹B(p.n)¹¹C | −2.76 | 3.02
C | ¹³C(p.n)¹³N | −3.00 | 3.24
5 MV 15SDH-2 Pelletron facility for Neutron production

## Slide 23
8MeV proton on different targets
Chart: Neutron yield (n / proton)
| Be | LiF | V | Mn | Mo | Zn | SS | Fe
6 MeV | 0.000506 | 0.000365 | 0.000239 | 0.000166 | 1.7e-05 | 1.2e-05 | 5e-06 | 1.1e-05
7 MeV | 0.000779 | 0.000497 | 0.000415 | 0.000374 | 4.2e-05 | 5.4e-05 | 1.9e-05 | 1.2e-05
8 MeV | 0.001068 | 0.000591 | 0.000627 | 0.000549 | 0.000131 | 0.00014 | 7.4e-05 | 1.9e-05
Experimental vs Simulated Neutron yield at various proton energies.
Experimental measurements are extrapolated from Neutron Dose rate meters and activation foil measurement.
Simulations for low Z, low proton energies
Depends heavily on Physics models, cross section libraries.
Target | Measurement (n/s/nAmp) | Simulation (n/s/nAmp)
Be | 1.03 x 1007 | 1.33x 1007
LiF | 7.56 x 1006 | 7.38x 1006
V | 8.25x 1006 | 7.83x 1006
Mn | 1.11x 1007 | 1.01x 1007
Mo | 2.16x 1006 | 1.64x 1006
Zn | 2.16x 1006 | 1.76x 1006

## Slide 24
3 Major Reaction Channels with highest Neutron Yield
9Be(p,n)9B
7Li(p,n)7Be
1H(7Li,n)7Be
3 Major Neutron producing targets.
Quasi Monoenergetic neutron of various energies are available.
Possibilities to study inverse kinematics
Chichester, David L.. "Production and applications of neutrons using particle accelerators." , Nov. 2009. https://doi.org/10.2172/1169209

## Slide 25: Future Developments in NESSA
Optimal moderator configuration under study
Thermalized Beam line
Rabbit system for activated samples
Goal :T1/2< 10 sec.

## Slide 26
Procurement of High Yield D-T Generator – 1 x 1010 n/s : 20 X increase.
  Funded by Swedish Energy Agency.
  Procurement under process.
Tandem Laboratory: More Standardized and dedicated neutron beam line with multiple energies and angular distribution.
Establishment of reference neutron fields and cross calibration with established facilities.
NESSA in 2026-2027

## Slide 27: Summary
NESSA: being built as an intermediate-level, complete neutron beamline facility to serve the full spectrum of neutron physics research.
  Absolute neutron yield calibrated: Y = (4.33 ± 0.36) × 10⁸ n/s via ⁹³Nb activation
  First SEE measurement confirmed: Neutron-induced bit-flip errors observed in chips — NESSA is operational for electronics irradiation.
  Fission chamber response validated: R₂₃₅/R₂₃₈ spectral index measured;
  First nuclear data result from NESSA: ¹¹³In(n,2n) isomeric yield ratio measured — IYR = 3.82 ± 0.47 at 14.7 MeV, first measurement at this facility.
NESSA is open, and we would be genuinely glad to collaborate, share beam time, and do good science together.

## Slide 28: Thank you & Question??