## Slide 1
Quantum Sensors for Fundamental Physics
Oxford 10/16/2018
Ion Storage Group
, Boulder
Trapped-Ions, Precision Measurements and Optical Clocks
D. B. Hume, S. M. Brewer, J. S. Chen, C. W. Chou, E. Clements, A. M. Hankin, D. J. Wineland, J. C. Bergquist and D. R. Leibrandt
Notes: 1
Thanks for the introduction

## Slide 2: Outline
Ions, Ion traps,
Tests of fundamental physics
2. Single-ion optical clocks
  Al+ vs Hg+ at NIST
  Al+ vs optical lattice clocks
3. Useful quantum techniques
  Quantum logic spectroscopy
  Correlation spectroscopy

## Slide 3: Trapped Ions
Quantum-limited experiments
Long interaction times
Small relativistic shifts
Small perturbation from EM fields
Hans Dehmelt
A “Single Atomic Particle Forever Floating at Rest in Free Space”
Hans Dehmelt 1988 Phys. Scr. 1988 102
+ Strong, controllable interactions between ions
Charged
Notes: Hans Dehmelt led some of the pioneering work on trapped ions and on optical clocks
Had a love of naming things Geonium, Sapfaris, Gertie
Good summary of the strength of trapped ions

## Slide 4: Trapped Ion Species
Elementary particles (e-, e+,…)
Composite particles (p, p, …)
Atomic ions
  Singly-ionized (Ca+, Al+, Yb+, …)
  Highly-charged (Ar14+ ,…)
  229Th nucleus
Molecular ions
  CaH+, N2+, HD+, AlH+, …
  Biological molecules
Macroscopic particles
  Water droplets, dust, …
https://www.nist.gov/pml/periodic-table-elements
https://science.energy.gov/hep/

## Slide 5: Ion Traps
Penning Trap
EBIT (Electron Beam Ion Trap)
Linear
Paul Trap
Linear:
Blade Wafer Planar
https://www.mpi-hd.mpg.de/pfeifer/page.php?id=90#figure02
Features:
Deep trapping, typ. 300K – 10000 K
Well-controlled environment
- UHV conditions
- Small and/or stable EM fields
- Low temperature
Ion cooling
- Laser cooling
- Resistive cooling
- Buffer gas cooling
Spherical:
RF confining fields
Space charge
High B field
https://quantumoptics.at/en/research/quantum-information.html

## Slide 6: Precision Tests of Fundamental Physics
Quantum mechanics
Linearity
Randomness
Bell’s inequalities
Heisenberg limit
Relativity
Local position invariance
Lorentz invariance
Equivalence principle
Gravitational redshift
Standard model
g-factor measurements
Mass measurements
Tests of quantum electrodynamics
Electron electric-dipole moment
Proton radius
Variation of fundamental constants ()
Dark matter searches
Parity non-conservation
Isotope shifts, King-plot non-linearities
Anomalous forces, interactions (spin- dependent, spin-independent)
If you want to find the secrets of the universe, think in terms of energy, frequency and vibration. – Nikola Tesla (disputed)

## Slide 7: Precision Tests of Fundamental Physics
Quantum mechanics
Linearity
Randomness
Bell’s inequalities
Heisenberg limit
Relativity
Local position invariance
Lorentz invariance
Equivalence principle
Gravitational redshift
Standard model
g-factor measurements
Mass measurements
Tests of quantum electrodynamics
Electron electric-dipole moment
Proton radius
Variation of fundamental constants ()
Dark matter searches
Parity non-conservation
Isotope shifts, King-plot non-linearities
Anomalous forces, interactions (spin- dependent, spin-independent)
If you want to find the secrets of the universe, think in terms of energy, frequency and vibration. – Nikola Tesla (disputed)
Frequency vs. theory Gabrielse

## Slide 8: Precision Tests of Fundamental Physics
Quantum mechanics
Linearity
Randomness
Bell’s inequalities
Heisenberg limit
Relativity
Local position invariance
Lorentz invariance
Equivalence principle
Gravitational redshift
Standard model
g-factor measurements
Mass measurements
Tests of quantum electrodynamics
Electron electric-dipole moment
Proton radius
Variation of fundamental constants ()
Dark matter searches
Parity non-conservation
Isotope shifts, King-plot non-linearities
Anomalous forces, interactions (spin- dependent, spin-independent)
If you want to find the secrets of the universe, think in terms of energy, frequency and vibration. – Nikola Tesla (disputed)
Frequency vs. time
Godun Wednesday 11:55
Gill Wednesday 9:35

## Slide 9: Precision Tests of Fundamental Physics
Quantum mechanics
Linearity
Randomness
Bell’s inequalities
Heisenberg limit
Relativity
Local position invariance
Lorentz invariance
Equivalence principle
Gravitational redshift
Standard model
g-factor measurements
Mass measurements
Tests of quantum electrodynamics
Electron electric-dipole moment
Proton radius
Variation of fundamental constants ()
Dark matter searches
Parity non-conservation
Isotope shifts, King-plot non-linearities
Anomalous forces, interactions (spin- dependent, spin-independent)
If you want to find the secrets of the universe, think in terms of energy, frequency and vibration. – Nikola Tesla (disputed)
Frequency vs. Spatial orientation
T. Pruttivarasin et al. Nature 517, 592 (2015)

## Slide 10: Precision Tests of Fundamental Physics
Quantum mechanics
Linearity
Randomness
Bell’s inequalities
Heisenberg limit
Relativity
Local position invariance
Lorentz invariance
Equivalence principle
Gravitational redshift
Standard model
g-factor measurements
Mass measurements
Tests of quantum electrodynamics
Electron electric-dipole moment
Proton radius
Variation of fundamental constants ()
Dark matter searches
Parity non-conservation
Isotope shifts, King-plot non-linearities
Anomalous forces, interactions (spin- dependent, spin-independent)
If you want to find the secrets of the universe, think in terms of energy, frequency and vibration. – Nikola Tesla (disputed)
Frequency vs. Applied Fields
W. B. Cairncross et al., Phys. Rev. Lett. 119, 153001 (2017)

## Slide 11: Outline
Ions, Ion traps,
Tests of fundamental physics
2. Single-ion optical clocks
  Al+ vs Hg+ at NIST
  Al+ vs optical lattice clocks
3. Useful quantum techniques
  Quantum logic spectroscopy
  Correlation spectroscopy

## Slide 12: Clock Tests of Fundamental Physics
Quantum mechanics
Linearity
Randomness
Bell’s inequalities
Heisenberg limit
Relativity
Local position invariance
Lorentz invariance
Equivalence principle
Gravitational redshift
Standard model
g-factor measurements
Mass measurements
Tests of quantum electrodynamics
Electron electric-dipole moment
Proton radius
Variation of fundamental constants ()
Dark matter searches
Parity non-conservation
Isotope shifts, King-plot non-linearities
Anomalous forces, interactions (spin- dependent, spin-independent)
If you want to find the secrets of the universe, think in terms of energy, frequency and vibration. – Nikola Tesla (disputed)

## Slide 13: Principle of Optical Atomic Clocks
Atomic System
Clock frequency:
≈1015 Hz
11:00 am
Femtosecond Laser
Frequency feedback ~0.1 Hz
Drive atomic resonance ~0.1 s
Ultrastable Laser
Notes: Optical clocks based on dipole-forbidden transitions in atoms and ions (high Q)
100000 x higher frequency than microwave clocks
Rely on fs comb laser

## Slide 14: Clock Performance
Stability
Average fractional frequency variations
Typically characterized by the Allan deviation:
()
Accuracy
Systematic uncertainty in clock frequency.
Two types of shifts
  Field shifts e.g. Zeeman shift and black body shift
  Motional shifts e.g. Relativistic Doppler
Notes: Atomic clocks are characterized by two main performance characteristics
  Accuracy is referred to in statements like “this clock won’t gain or lose a second in 1 million years”
  Stability refers to statistical variation in the transmitted clock frequency
Define v, c and k
Discuss Q (high frequency!), SNR and 1/sqrt(tau)

## Slide 15: Historical Clock Accuracy

## Slide 16: 199Hg+ system
Spherical Paul Trap
Cryogenic environment (4 K)‏
High sensitivity to variation in the fine structure constant
2D5/2
2P1/2
2S1/2
Diddams et al., Science 293, 825 (2001)
T. Rosenband, et al. Science 319, 1808 (2008)
Notes: The Hg+ is trapped in a spehrical paul trap, kept in criogenic (liquid He) evironment. This evironment provides the required vacuom level for a long ion lifetime (it can be as long as many moths) and also a low BBR shift for the clock. This a picture of the trap, show on a cent coin a schematicof the dewars and a photo of the trap chamber, with the imaging lens to collect the fluorescence. This is lurencence image of the single ion

## Slide 17
27Al+ Atomic System
1S0
3P0 =267.43 nm, t = 21 s
3P1 =266.99 nm, t = 300 ms
Insensitive to trapping fields
Small Stark shift from blackbody radiation
Light mass Relativistic shifts
Two-ion quantum logic techniques with for cooling, state preparation & clock readout [1]
[1] D. J. Wineland et al.,
Proc. 6th Symp. Freq. Stds. and Metrology, 361 (2001)
= 167 nm,  = 1.5 GHz
1P1
INACCESSIBLE
Schmidt et al., Science 309, 749 (2005)
Notes: 1. Several steps in single ion spectroscopy, laser cooling, state prep, probe clock transition, detect

## Slide 18: Al+/Hg+ Comparison
×2
×2
Hg+
199Hg+
1126 nm laser
1070 nm
laser
×2
×2
27Al+
9Be+
27Al+
fiber
fiber
fb,Al
m frep+ fceo
fb,Hg
n frep+ fceo
1.052 871 833 148 990 438 ± 5.5 x 10-17
1.9x10-17
2.3x10-17
T. Rosenband, et al. Science 319, 1808 (2008)
Hg-systematic | 
Al-systematic | 
statistical | 
Hg-systematic | 
Al-systematic | 
statistical | 

## Slide 19: Measuring with Optical Clocks
Sensitivity coefficients determined based on atomic structure calculations
[1] V. A. Dzuba and V. V. Flambaum Phys. Rev. A 77, 012515 (2008)
Atom, transition | 
199Hg+, | - 3.0 [1]
27Al+, | + 0.0079 [2]
171Yb+, | + 0.88 [1]
171Yb+, | - 5.95 [3]
171Yb, | + 0.31 [4]
Atom, transition | 
 | - 3.0 [1]
 | + 0.0079 [2]
 | + 0.88 [1]
 | - 5.95 [3]
 | + 0.31 [4]
[2] E. J. Angstmann, et al., Phys. Rev. A 70, 014102 (2004)
[3] V. A. Dzuba, V. V. Flambaum, M. V. Marchenko Phys. Rev. A 68, 022506 (2003)
Relativistic effects determine sensitivity of clock transitions to
[4] V. A. Dzuba, V. V. Flambaum, Can. J. Phys. 87 15 (2009)

## Slide 20: Al+/Hg+ Comparisons
ΔR x 1015
/year
/year
10-16

## Slide 21: Boulder Atomic Clock and Optical Network
Free Space Frequency Transfer
Fiber Frequency Transfer
1156 nm
X 2
1069 nm
Ti:Sapph
Al+
Yb
Sr
X 2
X 2
534 nm
267 nm
578 nm
698 nm
1540 nm
X 2
Er:Fiber
770 nm
NIST
JILA
1.5 km

## Slide 22: The Teams
Al
David Leibrandt
David Hume
Samuel Brewer
Jwo-Sy Chen
Aaron Hankin
Ethan Clements
Combs
Scott Diddams
Tara Fortier
Holly Leopardi
Yb
Andrew Ludlow
Kyle Beloy
William McGrew
Xiaogang Zhang
Robbie Fasano
Stefan Schafer
Daniele Nicolodi
Sr
Jun Ye
John Robinson
Eric Oelker
Dhruv Kedar
Sarah Bromley
Lindsey Sonderhouse
Colin Kennedy
Tobias Bothwell
Free Space
Nathan Newbury
Laura Sinclair
JD Deschenes
Isaac Khader
Martha Bodine
Timescale
Jeff Sherman
Jian Yao
Notes: Big group
Also Dave Wineland and John B.
Aaron, Ethan and James

## Slide 23: Frequency Ratio Measurements
Al clock stability
1.3x10-15 @ 1s
Yb/Sr stability
3.1x10-16 @ 1s
> 70 % up-time for all clocks

## Slide 24: Ratios Day by Day
FAl/FSr
FYb/FSr
FAl/FYb

## Slide 25: Dark Matter as an Ultralight Particle
WIMP
Axion
100
1012
1024
Mass eV
10-12
10-24
Dilaton dark matter
Fuzzy dark matter
Wave dark matter
Ultralight bosonic dark matter
Ultralight virialized fields
…
de Broglie wavelength shorter than size scale of a galaxy
Bosonic (as many as 10100 particles in a single mode)
Density: ~0.3 GeV/cm3
Acts like a scalar field oscillating at the Compton frequency
Coherence time ~106 x Oscillation period
Dark photon
If it is an ultralight particle, what we DO know:

## Slide 26: Ultralight Dark Matter Constraints
See also: Tilburg et al., PRL 115, 011802 (2015) and Hees et al., PRL 117, 061301 (2016)

## Slide 27: Outline
Ions, Ion traps,
Tests of fundamental physics
2. Single-ion optical clocks
  Al+ vs Hg+ at NIST
  Al+ vs optical lattice clocks
3. Useful quantum techniques
  Quantum logic spectroscopy
  Correlation spectroscopy

## Slide 28: Quantum Logic Spectroscopy
Typical mode frequencies: 2.7 – 7.2 MHz
Monroe et al., PRL 75, 22, 4011 (1995)
Diedrich et al., PRL 62, 4, 403 (1989)
Notes: At the current Raman beam detuning (50 GHz), we estimate that the Stark shift due to the continuous cooling beams will be about -4x10-17.
We have since added 900 MHz Raman beams, which should reduce the Stark shift to approximately -1x10-18.

## Slide 29: Al+ quantum-assisted readout
Cool to motional ground-state with logic ion
Depending on Al+ clock state, add one vibrational quantum via Al+
Detect vibrational quantum with logic ion
Mean = 1.3
Mean = 6.9
Probability
Photon counts
D. B. Hume, et al.
PRL 99, 120502 (2007)
D. J. Wineland, et al.
Proc. 6th Symp. Freq. Stds. and Metr. (2001)
P.O. Schmidt, et al.
Science 309, 749 (2005)
T. Rosenband, et al.
PRL 98, 220801 (2007)
QND
27Al+ 1S0
27Al+ 3P0
Photon counts

## Slide 30: Generalizing to New Atomic Systems
Applications
  Variations of fundamental constants (α, μ)
  Parity Nonconservation
  Electron EDM
  Comparing with astrophysical data
  The ideal clock?
  The ideal qubit?
State detection that does not depend on details of the atomic structure
Off-resonant interactions for projective detection
Broadband source for spectroscopy

## Slide 31: ``Quantum Jumps´´ between Zeeman States
Hume PRL, 107, 243902 (2011)
Coherent state amplitude:

## Slide 32: 40CaH+: Test bed for Molecular Ion Spectroscopy
Room temperature, in electronic ground state
M. Abe et al., Chem. Phys. Lett. 521, 31 (2012)
J
0
1
2
3
1S, v = 0
J
0
1
2
3
Rotation sublevels
J
0
1
2
3
-1/2
m
+1/2
+3/2
+5/2
-7/2
-5/2
-3/2
+7/2
H nuclear spin 1/2
 1.1 % population in each sublevels at 300 K
~0.6 THz

## Slide 33: Coherent Spectra from a Single Molecule
11 kHz
13 kHz
Projective
State Preparation
Experiment Pulse
Detection
J = 1
J = 2
Optical Pumping
Summary: Quantum logic spectroscopy
“Logic ion” used for:
  Cooling
  State initialization
  Detection
Flexible
Sensitive
Suitable for many precision experiments with exotic species
Chou et al., Nature 545, 203 (2017)

## Slide 34: Correlation Spectroscopy: Projection Noise Limit
Oscillation frequency
Atom number
Free-evolution period
Total measurement duration
Free evolution period (i.e. Ramsey probe time) limited by laser coherence
Idea: probe two ions simultaneously with same laser
  Laser noise is common mode
  Simultaneous measurements insensitivity to noise during dead-time
Free evolution,
Detection
Chou, et al., PRL 106, 160801 (2011)
Chwalla et al., App. Phys. B 89 483 (2007)
Marti et al., PRL 120, 103201 (2018)

## Slide 35: 2 atom Ramsey experiment
Free evolution,
Detection
1S0
1S0
3P0
3P0
Clock 1
Clock 2
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 36: 2 atom Ramsey experiment
Free evolution,
Detection
Free evolution,
Detection
1S0
1S0
3P0
3P0
Clock 1
Clock 2
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 37: 2 atom Ramsey experiment
Detection
Free evolution,
Detection
1S0
1S0
3P0
3P0
Clock 1
Clock 2
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 38: 2 atom Ramsey experiment
Free evolution,
Detection
1S0
1S0
3P0
3P0
Clock 1
Clock 2
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 39: 2 atom Ramsey experiment
Free evolution,
Detection
1S0
1S0
3P0
3P0
Clock 1
Clock 2
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 40: 2 atom Ramsey experiment
Free evolution,
Detection
1S0
1S0
3P0
3P0
Clock 1
Clock 2
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 41: Correlation Spectroscopy between 2 Clocks
Ca+/Al+
Mg+/Al+
Active magnetic field servo
Active path stabilization
UV optical fiber
UV optical fiber
Chou, et al., PRL 106, 160801 (2011)
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 42: UV Optical Coherence at 1 s
T = 1 s
T = 0.05 s
Within laser coherence time
T = 1 s
Laser – Atom coherence lost
Atom – Atom coherence observed in correlations
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 43: Correlation Spectroscopy Stability
Previous Al-Al measurement stability
50X reduction in averaging time!
Yb/Sr stability
Summary: Correlation spectroscopy
One atoms acts as a “local oscillator” probing another
Can be done with “off-the-shelf” and/or transportable laser systems
Suitable for many clock experiments
  Geodesy
  Frequency ratio measurements
  Frequency vs. …
Notes: Huntemann et al., PRL 113 210802 (2014)
Derevianko et al., Nat. Phys. 10 933 (2014)

## Slide 44: Trends in Trapped Ion Experiments
Expansion of quantum control and precision measurement to new previously inaccessible systems (low, medium and high energies)
  new atomic systems, molecules, antimatter, highly-charged ions
Precision measurements adopting techniques from quantum information processing
  Quantum-enhanced metrology, dynamical decoupling, quantum logic spectroscopy
Identifying new targets for precision measurements in ion traps for fundamental physics
  Lorentz invariance, dark matter, King-plot nonlinearities,. . .
T Pruttivarasin et al. Nature 517, 592-595 (2015)
H. Nagahama et al., Nat. Comm. 8, 14084 (2017)
Schmoeger et al. Science 347, 1243 (2015)

## Slide 45
Thanks!
David Leibrandt
David Wineland
Sam Brewer
Jim Bergquist
James Chou
Jwo-Sy Chen
Ethan Clements
Aaron Hankin
Tom Hardy
NIST, Boulder, Colorado

## Slide 46: Backup Slides

## Slide 47: CaH+ Optical Pumping
J = 1, B = 0.36 mT
-1/2
+1/2
+3/2
-3/2
m

## Slide 48: CaH+ Optical Pumping
J = 1, B = 0.36 mT
-1/2
+1/2
+3/2
-3/2
m

## Slide 49: Dark Matter
Galactic Rotation Curves
Gravitational Lensing
Large-Scale Structure Formation
Multiple, consistent lines of evidence indicate predominance of dark matter over normal matter
No direct observation on Earth

## Slide 50: Dark Matter as an Ultralight Particle
WIMP
Axion
100
1012
1024
Mass eV
10-12
10-24
Dilaton dark matter
Fuzzy dark matter
Wave dark matter
Ultralight bosonic dark matter
Ultralight virialized fields
…
de Broglie wavelength shorter than size scale of a galaxy
Bosonic (as many as 10100 particles in a single mode)
Density: ~0.3 GeV/cm3
Acts like a scalar field oscillating at the Compton frequency
Coherence time ~106 x Oscillation period
Dark photon
If it is an ultralight particle, what we DO know:

## Slide 51: Searching for Dark Matter with Clocks
Ultralight (1x10-25 – 10 eV) dark matter particles act like a field φ
Coupling to Standard Model Particles
Atom, transition | 
199Hg+, | - 3.0
27Al+, | + 0.0079
171Yb+, | + 0.88
171Yb+, | - 5.95
171Yb, | + 0.31
87Sr, | +0.06
Atom, transition | 
 | - 3.0
 | + 0.0079
 | + 0.88
 | - 5.95
 | + 0.31
 | +0.06
A. Arvanataki et al.,Phys. Rev. D 91, 015015 (2015)
Y. V. Stadnik and V. V. Flambaum, Phys. Rev. Lett. 115, 201301 (2015)
A. Derevianko and M. Pospelov., Nature Phys. 10, 933 (2014)
Y. V. Stadnik and V. V. Flambaum, PRA 93, 063630 (2016)
Notes: Value of the frequency ratio changes depending on the amplitude of the field

## Slide 52: Dark Matter Field Coupling to
Leads to oscillation of the value of α, at the Compton frequency
Amplitude of the oscillation dR depends on:
  Dark matter density ρDM
  Coupling coefficient de

## Slide 53: Other work in the Ion Storage Group
Trap RF
waves
sapphire substrate
Quantum information processing
Penning Trap Experiments
Molecular Spectroscopy
Tan et al., PRL 117, 060505 (2016)
Ospelkaus et al., Nature 476, 181 (2011)
Chou et al., Nature 545, 203 (2017)
Gilmore et al., PRL 118, 263602 (2017)
Bohnet et al., Science 352, 6291 (2017)

## Slide 54: Al+ Clock Uncertainty Budget
Sources | Fractional Uncertainty (10-18) |  | 
 | Shift | Uncertainty | Previous clock
Time-dilation: Excess micromotion | -4.7 | 0.6 | -9.0(6.0)
Time-dilation: Secular motion | -1.8 | 0.3 | -16.3(5.0)
BBR shift | -2.6 | 0.3 | -9.0(3.0)
Cooling light shift | 0.0 | 0.0 | -3.6(1.5)
Quadratic Zeeman shift | -925.9 | 0.6 | -1079.9(0.7)
Linear Doppler shift | 0.0 | 0.2 | 0.0(0.3)
Clock light shift | 0.0 | 0.2 | 0.0(0.2)
Background gas collision | 0.0 | 0.3 | 0.0(0.5)
AOM phase chirp | 0.0 | < 0.1 | 0.0(0.2)
Total | -935.0 | 1.0 | -1117.8(8.6)

## Slide 55: Frequency vs. Theory
Experiment
  Single electron in a Penning trap
Hanneke et al., Phys. Rev. Lett. 100, 120801
Theory
  Taking α from independent measurements, this is a test of QED
  Alternately, assuming calculated coefficients and corrections from QED, this is a measurement of α
Example: Measurement of the electron magnetic moment

## Slide 56: Test of Lorentz Invariance
Frequency vs. Spatial Orientation
T. Pruttivarasin et al. Nature 517, 592 (2015)
Use a decoherence free subspace of 2 Ca+ ions for long probe times

## Slide 57: Electron EDM
Frequency vs. Applied Fields
W. B. Cairncross et al., Phys. Rev. Lett. 119, 153001 (2017)
- HfF+ ions in an octupole ion trap
- Electric field in molecule enhanced from 10 V/cm to 23 GV/cm