## Slide 1: Accelerator Test-Beam Capabilities at BNL
12/1/2021
Mark Palmer
Snowmass Instrumentation Frontier Topical Group 9 Meeting
Accelerator Science & Technology Office

## Slide 2: The Brookhaven Accelerator Complex
NSLS-II
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
(s)PHENIX
Electron lenses
Polarized Jet Target
RF
Electron cooling
EBIS
BLIP
SRF
TPL
ATF
Diverse Accelerator Complex: e- a ions
Accelerator-based SC User Facilities: RHIC (NP), NSLS-II (BES), ATF (ARDAP)
Laboratory-operated User Facilities: Tandem Van de Graaff, NASA Space Radiation Laboratory (NSRL) Brookhaven Linac Isotope Producer (BLIP)
Future Capabilities Being Developed: Electron-Ion Collider (NP) High Energy Effects Test (HEET) Facility @AGS
Complex supports a broad range of beam test options

## Slide 3: Overview of Beam Test Capabilities
Will provide a brief overview of BNL beam test capabilities:
Proton/Ion Facilities
  Tandem Van de Graaff
  BLIP a NSLS-II Materials Analysis
  NSRL (see Mike Sivertz’ talk for more details)
  Emerging AGS options (HEET)
Electron Facilities
  ATF
  NSLS-II
How to connect to BNL beam test resources

## Slide 4: Tandem Van de Graaff

## Slide 5: Tandem van de Graaff Capabilities
Ions Available at Tandem
Target Irradiation Beamline

## Slide 6: Brookhaven LINAC Isotope Producer - BLIP

## Slide 7: Targetry Studies: BLIP & NSLS-II
Courtesy Nick Simos

## Slide 8: BLIP Irradiation Capabilities
Multiple proton energies 66-200 MeV
Beam current (165µA +) Beam rastering
Typical RUN cycle (December – July)
Operates in tandem with Isotope production and RHIC
(no dedicated beam time needed)
Fully operational hot cell laboratory & infrastructure Availability of nuclear instruments/technical expertise Can operate as neutron spallation source
Mode I: Irradiation with BNL Linac protons (up to 200 MeV)
Position A
Position B
Beam
Mode II: Target endstation as a Neutron Source
Fusion spectrum similarities

## Slide 9: Irradiation Damage Experiments
Aim: reach proton fluence levels that approach threshold or operational goal
Target Array in Beam

## Slide 10: Nano-structured Fe-based Coatings on Steel
BNL studies demonstrated the remarkable ability of nano-structured coatings to remain amorphous under intense proton irradiation.

## Slide 11
  CZT crystals
SiO2: LHC 0-degree calorimeter
  Rare-earth magnets
  Ferrofluidics
  Performance Degradation of Ferrofluidic Feedthroughs in a Mixed Irradiation Field
FF static torque vs. the inverse of displacement time (1/td) following rotational speed cycles up to 5,000 rpm

## Slide 12: NASA Space Radiation Laboratory (NSRL)
See also next talk by Mike Sivertz

## Slide 13: NASA Space Radiation Laboratory (NSRL)
Started in 2003, simulates galactic radiation for human space flight
  Heavy ion beams from AGS Booster
  Electron Beam Ion Source (EBIS) provides all necessary ion beams
  New laser ion source for EBIS allows for rapid species switching to simulate energy and species spectrum of deep space radiation field
Additional uses of NSRL
  Radiation effects studies (rapidly growing demand for satellite electronics testing)
  R&D of ion beam cancer treatment
  Agreement with NASA in place for non-NASA users (“non-designated user facility”)

## Slide 14: AGS Future Possibilities: HEET

## Slide 15: Proposed High Energy Effects Testing Beamline - HEET

## Slide 16: HEET Overview
Large range of beam energies (e.g., 40 -2000 MeV/n Fe21+ions)
Large number of available ion species (e.g., H to U [Z = 1 to 92] and more)
Fast energy change (minutes)
Fast switching of ions (minutes)
3D Uniform Beams
  Square uniform beam sizes from 1 cm2 to 400 cm2
Pencil beams on the scale of 1 cm rms (Smaller also possible)
Many operational similarities to NSRL (next talk by M. Sivertz)
If approved, could be online in 3-4 years

## Slide 17
Courtesy: K. Brown

## Slide 18: Electron Capabilities: ATF & NSLS-II

## Slide 19: Accelerator Test Facility
Primary mission is development of advanced accelerator and laser concepts
High brightness electron beam available for a range of
18-75 MeV electrons, 1 mm emittance
~10 pC - 3 nC bunch currents
Periscope body
Azimuth Motor
Narrow angle camera, camera optics, rad- protected 20M Pixel CMOS detector
Tilt mirror
Star camera assembly
CMOS CMV20000 detector
Adjustable Aperture Diamond Detector Applied Diamond, Inc.
NASA’s New Frontier’s Homesteader Program, APIC concept component testing

## Slide 20: Challenges of Connecting Scales: Materials in Extreme Conditions
How do we connect irradiation outcomes with the material properties?

## Slide 21: Synergies with the BNL Accelerator Complex
Collider Complex
ID 28 (XPD) Beamline
NSLS II Synergy

## Slide 22: How to Connect to BNL Beam Capabilities

## Slide 23
https://www.bnl.gov/accelerators/

## Slide 24: Thank you for your attention!