## Slide 1: Overview of SARAF Israel Mardor Soreq Nuclear Research Center
Joint SARAF & WIS TPC Mini-Workshop
Weizmann Institute of Science, 19/02/2026

## Slide 2: SARAF – Soreq Applied Research Accelerator Facility
To enlarge the experimental nuclear science infrastructure and promote research in Israel
To develop and produce radioisotopes for bio-medical applications
To modernize the source of neutrons at Soreq and extend neutron-based research and applications
Notes: 2

## Slide 3
SARAF I 2010 - 2019
Commissioning
A. Nagler, Linac2006 K. Dunkel, PAC 2007 C. Piel, PAC 2007 C. Piel, EPAC 2008 A. Nagler, Linac 2008 J. Rodnizki, EPAC 2008 J. Rodnizki, HB 2008 I. Mardor, PAC 2009 A. Perry, SRF 2009 I. Mardor, SRF 2009 L. Weissman, DIPAC 2009 L. Weissman, Linac 2010 L. Weissman, JINST 2018
Operation
D. Berkovits, Linac 2012 L. Weissman, RuPAC 2012 A. Kreisel, Linac 2014 L. Weissman, WAO 2014 L. Weissman, JINST 2014 L. Weissman, JINST 2015
 | MeV | mA
p | 4 | 1 CW
p | 2 | 2 CW
d | 5.6 | 1*10%
d | 3 | 1.1 CW

## Slide 4
SARAF Phase-I compact neutron source
LiLiT technical reports
S. Halfon et al.: ARI 69 (2011) 1654 AIP 1525 (2013) 511 RSI 84 (2013) 123507 RSI 85 (2014) 056105 ARI 88 (2014) 238 M. Paul et al.: PoS (2014) 059 J. RNC (2015)
LiLiT 2.0
The Liquid Lithium jet Target LILIT
1010 – 1012 n/sec

## Slide 5: SARAF-I nucleosynthesis research program
status | Collaboration HU-SARAF- | Detection technique | Target
M. Tessler et al., PLB 751, 418 (2015) | - | spec | natZr(n,g)
M. Tessler et al., PRC 105, 035801 (2022) | - | spec | 69,71Ga(n,g)
R. N. Sahoo et al., PRC 109, 025808 (2024) | - | spec | natCe(n,g)
S. Pavetich et al., PRC 99, 015801 (2019) | Goethe U Frankfurt –Dresden-Rossendorf-ANU | g spec + AMS | 23Na35,37Cl(n,g)
Under analysis | ANU-ANL | AMS | 92Zr(n,g)
L. Weissman et al., PRC 96, 015802 (2017) | U. Seville | g spec | 208Pb(n,g)209Pb
A. Shor et al., PRC 96, 055805 (2017) | JRC IRMM Geel | a + b + g spec | 209Bi(n,g)210gBi
M. Tessler et al., PRC 104, 015806 (2021) | ANL - Goethe U - U. Bern | g + b spec + MOT atom trap | 78,80,84,86Kr(n,g)
M. Tessler et al., PRL 121, 112701 (2018) | ANL - Goethe U | AMS + g spec | 36,38,40Ar(n,g)
C. Guerrero et al., PRL 125, 142701 (2020) | U. Seville-PSI-CERN | spec | 171Tm(n,g)
C. Guerrero et al., PLB 797, 134809 (2019) | U. Seville-PSI-CERN | spec | 147Pm(n,g)
Benchmark and higher precision
Noble gases
Radioactive
targets
Michael Paul, Hebrew University of Jerusalem
M. Paul et al.,
EPJA (2019) 55: 44
Notes: 5

## Slide 6
Parameter | Value | Comment
Ion Species | Protons/Deuterons | a, M/q ≤ 2
Energy Range | 1.3(2.6) – 35(40) MeV | p(d), Variable energy
Energy Spread | ~60 keV r.m.s. | At 40 MeV
Current Range | 10 nA – 5 mA | CW (176 MHz)
Pulsed Mode | 0 – 200 kHz | Single 1 nsec pulses  variable macro-pulses
Beam Size | 1 mm – few cm | Transverse plane, 2D Gaussian
Emittance | 0.2 p∙mm∙mrad | Transverse
Maintenance | Hands-On | Very low beam loss
Phase-II design N. Pichoff et al., IPAC 2019
radiation and isotopes
1) fast particles
3) applications
2021
target
2) nuclear reaction
Phase-I finished operation in October 2019. It was built to test, characterize and prove the novel technologies
SARAF II – A Superconducting Versatile LINAC
2009 - 2019
NEW lattice under construction
2020
Up to 200 kW beam power

## Slide 7
N. Pichoff et al., IPAC 2018 and IPAC 2019
SARAF Phase-II Superconducting RF linac
HWR 
 Solenoid
In operation since 2008
STATUS:
All CM’s are at SARAF
2 installed
2 being assembled

## Slide 8
Beam line
Ga pipes
EMP
Ga tank
Ga-Oil heat exchanger
Lead wall
Target chamber
Target room
Basement
Lifting system
Lead shielding for removing the system
Oil-water heat exchanger
Ga tank for maintains
GaLiT
Galium Indium Liquid Target

## Slide 9
GaLiT chamber and nozzle
Thermocouples
Foil and Wire
Ga Trap
Nozzle
View port
Thermocouples
Fiber optic

## Slide 10: SARAF II – building
Nov. 11th, 2019
SARAF-I
SARAF-II
Notes: 10

## Slide 11: SARAF II – building
Nov. 11th, 2019
SARAF-I
SARAF-II
Notes: 11

## Slide 12: SARAF II – Installations on site
RFQ
MEBT
CM1
CM4
Accelerator
Beam line #1
GaLiT
GaIn liquid target

## Slide 13
CW Fast Neutrons
Target | Liquid gallium-indium jet
Beam power | 200 kW CW (5 mA ∙ 40 MeV)
Maximum neutron yield | 1015 n/sec

## Slide 14: Neutron Yield results
A. Kreisel et al., Eur. Phys. J. A 59, 185 (2023)

## Slide 15: Neutron flux downstream of GaLiT target
Power density on GaIn target: ~2 kW/cm2 (similar to IFMIF-DONES) on a 2 cm2 spot
For highest flux, place sample of interest as close as possible to the neutron source
FLUKA simulation of n flux from GaIn,
from 40 MeV deuterons at 5 mA
(normalized to measured yield), averaged over a 5×5 cm2 area downstream of the target
GaIn target location

## Slide 16: Neutron flux downstream of GaLiT target
Most efficient to place sample on target backplate
Distance from neutron source: ~1-2 cm
Flux at SARAF: 2-3×1013 n/cm2/s/5mA
Only ~1 order of magnitude less than IFMIF-DONES, for small samples
IFMIF-DONES
Y. Qiu et al., Jour. Nucl. Eng. 3, 385 (2022)
SARAF

## Slide 17: Research plans with CW fast neutrons
Cryogenic Stopping Cell (CSC)
Long irradiation pipe
Fast short irradiations (Rabbit)
CSC Vacuum
CSC Beam line
Manipulator
Beam dump room top view
GaLiT)
BL #1

## Slide 18: Expected Fission Product Yields
Expected separated fission product rates (FP/sec)
after the MR-TOF-MS
Ratio of SARAF II expected rates to FRIB

## Slide 19
Thermal neutron source
Target | Liquid gallium-indium jet
Moderator | Light water
Reflector | Beryllium and polyethylene
Beam power | 200 kW CW (5 mA ∙ 40 MeV)
Thermal camera flux | 4×105 n/cm2/sec at L/D=250
Diffractometer | ~106 n/cm2/sec at exit port
Fast Internal irradiation station | Via pneumatic transfer, ~1012 n/cm2/sec
Development port | ~106 n/cm2/sec at exit port
Long internal irradiation station | ~1012 n/cm2/sec

## Slide 20
Time of Flight (ToF)
Targets | Solid Li or LiF
Average beam power | Up to 200 W (DC~10-3) (5 mA ∙ 40 MeV)
Beam structure | Down to 1 nsec bunches at 200 kHz
Neutron flight path length | 18 m
Epithermal neutrons | 
Moderator | Polyethylene
Neutron flux | ~104 n/cm2/sec at 10 m from target
Fast neutrons - ‘white’ spectrum | 
Target thickness | ‘Thick’ target (~25 mm)
Neutron rate from at target | ~1012 n/sec
Fast neutrons – quasi-mono-energetic | 
Target thickness | 1.5 mm
Ion beam | Protons up to ~30 MeV
Neutron spectrum | Ion beam energy ± 1 MeV (with low tail)
Neutron flux | ~1010 n/sec/sr

## Slide 21: Neutron spectra comparison
SARAF, NFS:
Thick Li targets

## Slide 22: Neutron spectra comparison
Neutron spectra from
thin light targets at
NFS@SPIRAL2,
GANIL, France
NFS:
Neutrons For Science
X. Ledoux et al.,
First beams at neutrons for science
Eur. Phys. Jour. A 57:257 (2021)

## Slide 23
ALEX target room
    Additional future ideas under development for this area:
    A target station for isotope production
    Radiation damage studies via ion beams
Target | Liquid lithium jet target (LiLiT 2.0)
Target thickness | 1.5 mm (suited for p/d of a few MeV)
Epithermal neutron rate | 1010 n/sec at 10’s keV
Fast neutron rate | 1012 n/sec at a few MeV

## Slide 24: The Science at SARAF (Phases I, II)
Searches for Beyond Standard Model Physics (abn of 6He, 23Ne, etc.)
Nuclear Astrophysics (s-process cross sections, r-process input)
Exploration of Exotic Nuclei (low z and fission products)
High Energy Deuteron and Neutron Induced Cross Sections (up to En ~ 50 MeV)
Material Research (Gen-IV, transmutation, fusion, blistering)
Neutron Based Therapy (Boron neutron capture therapy)
Development of New Radiopharmaceuticals (Diagnostics and Therapy)
Accelerator based neutron imaging (thermal and high energy)
Positron Annihilation Spectroscopy
And maybe also – neutrino physics (well-defined, pulsed, high energy, and )
I. Mardor et al., "The Soreq Applied Research Accelerator Facility (SARAF) – Overview, Research Programs and Future Plans", Eur. Phys. Jour. A 54, 98 (2018)
I. Mardor et al., "Opportunities for high-energy neutron- and deuteron-induced measurements for fusion technology at the Soreq applied research accelerator facility (SARAF)", Front. Phys. 11:1248191 (2023)

## Slide 25: Summary and Outlook
Soreq NRC is constructing SARAF as a versatile facility for the communities of applied and basic research and development
Scientific programs g at SARAF I educated graduate students and generating scientific results that are published and presented in international conferences
The high current of SARAF II, with our high-power irradiation targets, may constitute a world competitive neutron facility at various beam structures and energies
SARAF II accelerator, beam lines 1,2 and two GaLiT targets to be installed in 2026
First thermal neutron images are planned for the end of 2027
Subsequent irradiation stations in the TOF hall are planned by the end of the decade
SARAF is open to new collaborators and contributions. We look forward to research proposals and letters of intent