## Slide 1
TPC detector at SARAF
Motivation for TPC detector at SARAF
The proposed detector scheme
Specific cases for the first “easy” experiment

## Slide 2
Reactions with the charged particles products
(n,p), (n,a), (n,d), (n,3He),(n,f)
Possible experimental schemes:
Passive activation: irradiation with consequent off-line activity measurement
work for some cases with appropriate reaction products
Solid State Nuclear Track Detectors: irradiation with consequent off-line processing
and track analysis
Charge particle detectors arays: large vacuum chamber, large detector array
Gas detectors: gas detector with thin target in active volume or gas as the target
(active target)
Off –line, “low-tech”
measurements
Advantages– high rate-
close locations
On –line, “high-tech”
Measurements
Far distance locations
TOF beam lines

## Slide 3
Example: Simple gas detector 16O(n,a)12C
16O(n,a)
background
including 16O
from16O(n,el)
Measurement of 12C(a,n)16O via reverse reaction 16O(n,a)12C (reciprocity)
Ionization chamber with oxygen rich gas (active target)
  En Ea Eel. Recoil
  7.1 2.3-4.7 0-1.5 very good signal to noise
  2.5 0-0.25 0-0.6 at astrophysical relevant region
  the signal will be buried in the noise
In this very important case, it is evident that
more sophisticated detector is required for the reaction
measurement at En <3 MeV measurement.

## Slide 4
Time Projection Chamber gas detector
drift field
oxygen rich gas
amplification gap
anode
readout anode
n
a
12C
drift field
n
16O
amplification gap
anode
readout anode
The detector readout provide the X-Y projection of the reaction tracks
The time collection provides the Z component
Advantages:
100 % efficiency
Complete 3D reconstruction of events
Relative simplicity and relative cost efficiency
Deep knowledge of gas properties:
drift velocities, survival rate, lateral diffusion, amplification process, fluorescence
amplification system
read out system
x
y
z
oxygen rich gas

## Slide 5
tracks target
neutron
pulse
shield/collimator
thin
target
fast PMTs,
primary light
proton
pulse
drift
field
amplification gap/anode
secondary light
production
target
cathode
Optical readout system
Experimental scheme at SARAF

## Slide 6
Fast TimePix cameras
Taken from F. Brunbauer presentation

## Slide 7
The prospective experiments
Measurements0 | Neutron range | Motivations | Importance | Comment
7Be(n,a)a | Astrophysics | 7Li underproduction in Big Bang | Very High | Requires a thin radioactive 7Be target of high activity. Experimental background due to the target
17O(n,a)14C | Astrophysics | Bottleneck for heavy element synthesis in non standard big bang models | High | Possibility to use “active target” mode. Need enriched 17O gas
16O(n,a)13C | 3-5 MeV | Indirect measurement of 13C(a,n)16O – the main source of neutrons for S-process. Also understanding He production in nuclear fuel (High Priority Request) | Very High | Possibility to use “active target” mode
25Mg(n,a)22Ne |  | Indirect measurement of 22Ne(a,n)25Mg - source of stellar neutrons |  | 
26Al(n,p)26Mg 26Al(n,a)26Na | Astrophysics | Understanding of abundance of 26Al, an important probe of stellar evolution | High | Need to obtained target with rare 26Al isotope (PSI)
General (n,a) | 0.1-10 MeV | Study of stellar photodisintegration reaction (g,a) via (n,a) | High | 
p(n,g)d | Astrophysics | Big Bang first reaction | Very high | Important for epithermal neutrons
(n,f) | 0.01-10 MeV | Anisotropy in fission, some High Priority Request reactions | High | Require thin actinide targets

## Slide 8
“Easy” cases for the first experiments
10B(n,a)7Li reaction
Thin enriched Boron target
10B(n,a)7Li is very well studied reaction up to 3 MeV
The cross-section is very high for low neutron energy: 3840 b for thermal, ~10 b for 10 keV, 2 b for 100 keV
Two final particles a and 7Li – unambiguous identification from tracks
Relatively high alpha a/7Li energy
The test with boron target will be used for understanding device in the whole operational range
Fission reactions
Thin actinide target
Energy arbitrage: fission products ~ 100 MeV>> elastic recoils energy
Fission cross-section is high > 1 b
Two final particles – unambiguous identification from tracks
It would be very beneficial to perform the first tests at with thermal
neutrons at Soreq research reactor

## Slide 9
Interest in fission reaction data
Fission discovered in 1938
Is it still any interest in fission ?
Approximately 20 % of HPRL reactions are fission

## Slide 10
First reports on “exotic” fission events:
long-range alphas in 1947
  Experiments with photographic emulsion soaked with Uranium salts
  After irradiations with neutrons exotic events are visualized
  From the track it is concluded that light fragment is LRA
  t/b ~ 2 10-3
  LRA is emitted by ~ 90 deg, collinearity of heave fragment is slightly broken
Long Range Alpha (LRA)
Tsien San-Tsiang et al.,
Phys. Rev.71,382 (1947)

## Slide 11
Binary fission
Ternary fission
Naive picture

## Slide 12
More exotic tracks
M. L. Muga al , Phys. Rev. 121 270 (1961) and others
Ternary fission
with short range light particle
tripartition
Ternary fission
with roughly equal mass fragments
true ternary fission
Long range alpha

## Slide 13
Tsien San-Tsiang et al, Nature 1947
Some evidence on quaternary fissions tracks in the pioneering papers from 1947
The ratio of exotic to binary events t/b ~ 3 10-3, q/b~ 3 10-4
In the later publication, much lower ratios t/b <10-5, q/b< 10-7
Tsien San-Tsiang et al, Phys. Rev 1947
More exotic tracks (quaternary fission)

## Slide 14
Discrepancy in the literature
Over two decades a few studies were done to obtain ratio of ternary to binary fission
These included experiments with nuclear emulsions , counting method (ionization chambers and solid state detectors)
and radiochemical methods
Reported large discrepancy in results over four orders of magnitude.
Example:
  Stonner&Hilman, Phys. Rev 1966 –radiochemical measurements
  compared to Muga, Phys. Rev. Lett. 1963 – counting experiment
Muga 1963
Stonner&Hilman 1966
upper limits

## Slide 15
Measurements at ILL reactor (Grenoble)
5 1014 n/cm2/s
Measure light products from neutron-induced fission
Consider these nuclei as a product of ternary fission

## Slide 16
ILL results ternary fission
Von Oertzen &Nasirov

## Slide 17
Fission spectrum as a function of neutron energy

## Slide 18
Other people also look into it
Only one image of ternary fission event taken by a modern
detector found in the literature

## Slide 19
Location for experiment
TOF
GALIT

## Slide 20
neutron line
GALIT beam dump: neutron source
Neutrons go to sky – long range many 10s -100 meters
Low neutron scattering on the surrounding:
  Good for experiments
  Good for radiation safety
  No need for neutrons dumps
BEAM

## Slide 21
Fission experiments at different locations
Assumptions:
high quality fissile target: ~ 300 ug/cm2 on thin carbon, 1018 atoms/cm2
1 barn fission cross-section
SARAF : “nominal” proton beam - 5 mA peak current, 35 MeV
Location | TOF thin target 10 m from the target | TOF thick target 10 m from the target | GALIT BD ~ 6 m from the target | Soreq reactor diffractometer line
Neutron spectrum | White spectrum | Epithermal | White spectrum | Thermal neutrons
Max Duty Cicle | 5 ·10-4 | 8 ·10-4 | 1 | Continuous beam
Max flux n/s/cm2 | 106 | 104 | 108 | 104
Fissions (Hz) | ~10 | ~0.1 | ~1000 | ~0.1

## Slide 22
Summary
TPC detector at SARAF significantly expand the spectrum of prospective measurements
at SARAF (n,p), (n,a), (n,d), n,t), (n,3He), (n,f) reactions
Neutron induced fission reaction – is an “easy” case for the detector commissioning
Exotic fission is the scientific bonus –
It would be very interesting observe ternary events (LRA, tripartition, true ternary)
Even more interesting quaternary event
After first observation one can consider possibility of systematic studies of
exotic fission modes
Possible locations: Soreq reactor – initial test debugging the detector, proof of principle
TOF beam lines – systematic studies, TOF experiments
GALIT – look into exotic fission modes

## Slide 23
Spare slides

## Slide 24
Herbert Diehl and Walter Greiner. Theory of ternary fission in the liquid drop model. Nuclear Physics A229 (1974) 29-46.

## Slide 25
Fission experiment
Need to obtain high quality targets:
~ 300 ug/cm^2 on thin carbon
Taking 1018 atoms/cm2 in target
10 n/cm2/burst neutron density in target
100 kHz burst rate (high rate mode)
1 barn fission cross-section
We obtain fission events rate of the order of 10 Hz
We estimate the rate of background to be ~ event/burst 100 kHz
There is a hope that 2-3 orders difference in energy would allows
to suppress the background
The best case would be fissile target (fission at En<<1 MeV), so low
energy neutrons could be used. This is further increase the
difference between signal and background

## Slide 26
ILL results, quaternary fission
R. Hentschel et al., Nucl. Phys. A 571 (1994) 427
Experiment :
Actinide target
Cold neutrons beam
Two multiwire chambers and PIN diodes array
for multiparticle coincidences
Observed:
Ternary events
Quaternary events involving:
t+t - 10-9/f
a+t - 10-8/f
a+a – 10-7/f
Difficulty to distinguish between simultaneous (or “true”) and sequential
(or “pseudo”) quaternary decays.

## Slide 27
Neutron induced charge particle measurements:(n,p), (n,a), (n,f)
Main requirement for a detector:
  timing resolution (ns) for TOF use
  ability to work at high pulse frequency (200 kHz, potentially 1 MHz)
  reasonable energy resolution (< 50 keV)
  high detection efficiency for charge particles (>50 %)
  low background sensitivity (elastic scattering, (n,p), (n,a) on detector material)
  extraction information on reaction kinematic
  robustness and relative simplicity
  cost effective
  versatile
It seems there are two possibilities:
1. gas detector
2. segmented solid state detector array
For these proposal we consider the gas detector option only:
1. expertize of the WI group
2. gas detector seems to be the better option (not discussed here in details why)

## Slide 28
First reports on “exotic” fission events:
long-range alphas in 1947
Tsien San-Tsiang et al., Phys. Rev.71,382 (1947)
Experiment with ionizing chamber
  ~ 16 MeV alphas detected from fissile target
  irradiated by neutrons
  Alphas from alpha decays chain (4-8 MeV) are blocked by absorbers
  One long range alpha (LRA) per 250-500 fissions
  (t/b)=2-4 10-3
Experiments with photographic emulsion soaked with Uranium salts
  After irradiations with neutrons exotic events are visualized
  From the track it is concluded that light fragment is LRA
  t/b ~ 2 10-3
  LRA is emitted by ~ 90 deg, collinearity of heave fragment is slightly broken

## Slide 29
More exotic tracks from photographic emulsion soaked with fissile salt (U, Th)
M. L. Muga al , Phys. Rev. 121 270 (1961)
Some evidence on short range light particle
Some evidence on true ternary fissions (similar masses)