## Slide 1
Introduction: A bit on Optical TPCs

## Slide 2
The Time Projection Chamber is a detector concept invented by Dave Nygren in the 70’s
Primary interactions leave a cloud of electrons drifted by a uniform field to a readout plane able to record x,y ionization charge as a function of time
Knowing the drift velocity knowledge, one can “project the time” and reconstruct the z coordinate  3D reconstruction
The basics: From TPC to OTPC
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
[1] D. R. Nygren, Origin and development of the TPC idea, NIM A, 2018 doi:10.1016/j.nima.2018.07.015
Optical/Electroluminescent TPCs:
Include light readouts: the drifting electrons are accelerated near the readout plane in order to yield electroluminescence (EL)  track photo-imaging
Using an array of photosensors (PMTs, SiPMs)
Or use optical lenses and cameras outside of the main volume
Illustration taken from LCTPC website

## Slide 3
Advantages: - Avoiding electronic-related challenges - One single integrated imaging device commercially available - Great spatial resolution - Low cost (for million-scale pixels)
Limitations: - Limited framerate (not an issue for rare event searches) - Readout noise (massively improved over the last decade) - No direct access to (x,y) time information (only 2D flattened view)
OTPCs with traditional cameras (and some examples)
“Warsaw” OTPC (2007)
Nuclear decay imaging
CCD camera + PMT for timing
CYGNO
Directional DM searches at LNGS
Orca Quest cameras + PMTs
Developing negative ion
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
Migdal
Migdal effect: an electron and a nuclear recoil sharing common vertex

## Slide 4
TimePix3 chip bump-bonded with a light sensitive silicon sensor
Photons convert to electrons in the silicon, then accumulated on a pixel until a threshold is reached  pixel registers a hit (x,y,t)
TimePix3 also gives the time-over-threshold which is a proxy for amount of light
TimePix-based camera offers 3D tracking and calorimetry with a single integrated device
Caveat: not single-photon sensitive  requires intensifier with fast phosphor
OTPC with TimePix-based camera with Ariadne
Phosphor screen
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 5
Results from a prototype Optical TPC at WIS: a milestone towards a detector at SARAF-II
R. Felkai, M. Borysova, L. Moleri, J. Pienaar, D. Vartsky, A. Breskin, I. Mor, L. Weissman and S. Bressler
19th February SARAF&WIS TPC mini-workshop

## Slide 6
Soreq Applied Research Accelerator Facility (SARAF) will upgrade its neutron beamline: higher beam energy (~30 MeV), higher current (5 mA)
Pulsed fast neutrons with a broad energy spectrum  Time-of-Flight (ToF) energy tagging
Relevant to studying neutron-induced reactions in the fields of astrophysics, civil nuclear engineering...
Motivation for an OTPC at SARAF-II
SARAF-II layout
Needs a versatile detector
Optical Time Projection Chambers (OTPCs) are gas detectors that provide nearly 4π acceptance and event-by-event tracking
Primary scintillation (S1) and electroluminescence (S2) enable 3D reconstruction of the final state
PID from range and dE/dx
Single versatile detector: tunable gas/pressure to optimize the performance to specific reactions
CF4 is a molecular gas emitting light in the near-UV and in the visible: compatible with modern scientific cameras
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 7
Prototype at Weizmann
Electron transport, charge amplification, electroluminescence and imaging
Test-bench for novel imaging techniques
This talk
Project roadmap
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 8
Prototype at Weizmann
Electron transport, charge amplification, electroluminescence and imaging
Test-bench for novel imaging techniques
This talk
Multi-purpose detector
Scaled up geometry (20 cm drift length)
Tunable pressure (10 mbar up to 1 bar)
Modular design
Project roadmap
In progress
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 9
Prototype at Weizmann
Electron transport, charge amplification, electroluminescence and imaging
Test-bench for novel imaging techniques
This talk
Commissioning + Physics
Simulations:
- Neutron background
- Reaction products
Early runs: Collimated nuclear reactor neutron flux on Boron-10 targets
Multi-purpose detector
Scaled up geometry (20 cm drift length)
Tunable pressure (10 mbar up to 1 bar)
Modular design
Project roadmap
In progress
In progress
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 10
TPC configuration
Baseline gas mixture: Ar:CF4 95:5 at 1 bar (constant flow)
Field cage: Stack of copper-clad FR4 (∼ 5 cm max drift length)
4 woven mesh electrodes (500 µm pitch, 50 µm ⌀, 81% T): - 1 drift cathode, 1 drift anode and 2 amplification anodes
A broadband PMT behind the cathode (sensitive to S1)
Orca-Quest2 camera with ultra-fast lens behind a fused silica viewport
Low activity (30 Bq) Am-241 source placed behind the drift cathode
Prototype assembled at Weizmann
Setup views
Example of a PMT signal at moderate amplification
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
S1
S2

## Slide 11
Prototype assembled at Weizmann
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
Source

## Slide 12
Direct measurement from preamp rise time (drift-only)
Two ways to compute the electron drift velocity: - Charge signal rise time (drift-only) on the drift anode - Extrapolation of the anti-correlation between S2 delay and S2 duration These methods take advantage of the alphas being emitted from behind the drift cathode
Electron transport in the drift region
S2 delay wrt S1 (Δt) vs S2 duration (drift field of 200 V/cm)
Knowing the drift velocity is required to convert drift time into distance
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
Explain signal shape

## Slide 13
Direct measurement from preamp rise time (drift-only)
Electron drift velocity Vs Drift Field
Two ways to compute the electron drift velocity: - Charge signal rise time (drift-only) on the drift anode - Extrapolation of the anti-correlation between S2 delay and S2 duration
These methods take advantage of the alphas being emitted from behind the drift cathode
Electron transport in the drift region
S2 delay wrt S1 (Δt) vs S2 duration (drift field of 200 V/cm)
Working value: 77 mm/µs at 200 V/cm
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 14
Light Yield Vs Gain
Charge gain:
Charge sensitive preamplifier connected to the second anode
Drift field at 200 V/cm, gap spacing 1.6 / 3 / 4.6 mm
Collected charges normalized to that obtained in drift-only/collection
Detector performance
Light yield:
Integrate baseline-subtracted PMT waveform
Convert to absolute yield using Ar/CF4 secondary emission spectrum [1], PMT QE and solid angle
[1] F. M. Brunbauer, Applications of gas scintillation properties in optically read out GEM-based detectors, PhD. Thesis, 2018
Gain Vs Amplification Field
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 15
Detector performance: 2-gap operations
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
Charge

## Slide 16
3D alpha tracks projection

## Slide 17
CMOS camera: 9.4MPixels, 4.6 µm pitch  18.841 mm × 10.598 mm
Extremely low readout noise (0.4 e- rms in standard, 0.3 e- rms in quiet)
Rolling shutter, readout time 8.3 ms and expmin 7.6 µs  120 FPSmax
QE up to 85% @ 460 nm
Orca Quest 2
Quantum Efficiency of sensors + secondary emission spectrum of Ar:CF4
Free running mode (with CoaXPress)
Photon number resolving output
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
From the manufacturer
Poisson λ = 2

## Slide 18
CMOS camera: 9.4MPixels, 4.6 µm pitch  18.841 mm × 10.598 mm
Extremely low readout noise (0.4 e- rms in standard, 0.3 e- rms in quiet)
Rolling shutter, readout time 8.3 ms and expmin 7.6 µs  120 FPSmax
QE up to 85% @ 460 nm
Orca Quest 2
Quantum Efficiency of sensors + secondary emission spectrum of Ar:CF4
Free running mode (with CoaXPress)
Photon number resolving output
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
From the manufacturer
Poisson λ = 2
Poisson λ = 3
From the manufacturer

## Slide 19
Global exposure timing output of the camera (TTL) connected to the oscilloscope
Event selection: only one event per time window and within TTL
This is a workaround for the rolling shutter of the camera coupled with USB readout limitations (we are upgrading to CoaXPress)
Camera setup and synchronization with the PMT
Camera signal output in coincidence with PMT-recorded S2
Image focused on the second and third anodes
View of the camera in front of the detector
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 20
Short movie (a tribute to Satyajit Ray)
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 21
PMT timing
Images are rebinned 8 x 8 to improve S/N (scale of 0.35 mm/px8x8)
Main assumption is a linear mapping between the track profile (camera) and the emission time (PMT)
3D Track Projection
Image processing
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 22
Short term limitations (can be fixed):
Frame rate is too low (USB) which forces idle time of the camera in free running mode (event loss)
3D Track Projection
3D projection
Long term limitations (intrinsic):
2D frame + PMT signal is challenging in multi-track events
Frame rate limit of 120 Hz (hard limit), minimum exposure of 8 ms (lossless) likely too coarse for beamline experiments
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026

## Slide 23
TimePix-based camera
1. The OTPC prototype achieved:
Establishing and validating methods of signal acquisition and processing
Performance mapping in Ar:CF4 95:5 at 1 bar
3D track projection with camera+PMT
Understanding hardware limitations and informing the design of the next-generation detector
Conclusion and outlook: From Prototype  Beamline-ready OTPC
2. Work in progress:
Test GEM+mesh performance and hexagonal etched meshes with different stacking geometries
Microphysics studies
Demonstrate novel ways of achieving 3D tracking
Compare these novel ways with more classical 3D tracking done by TimePix-based camera and the camera+PMT method described previously
3. Beamline-ready multi-purpose detector:
Commissioning the detector
Performance mapping of different gas mixtures at various pressures
Physics run with a neutron beam provided by a nuclear reactor
Source of the image: Medipix collaboration website
Ryan Felkai, SARAF&WIS TPC mini-workshop, 19th February 2026
Next talks covering these topics!

## Slide 24
Thank you!