## Slide 1: Israel Research Reactor 1 – IRR-1
Joint SARAF-WIS TPC mini workshop 19/02/2026
Dr. El’ad N. Caspi
Head, Nuclear Physics Division, Soreq-NRC

## Slide 2: The first reactor in Israel

## Slide 3: Nuclear physics division - SNRC

## Slide 4: Some history of Soreq Nuclear Research Center
Founded in 1958 as a research center of the Israeli Atomic Energy Commission (IAEC) with the main goal to operate the first Israeli reactor.
1958 – This is where it all started
1959 – Building the reactor

## Slide 5: Some history of Soreq-NRC
Given to Israel by President Eisenhauer as part of Atoms for Peace program.
Went critical on June 1960.
Supervised by the IAEA.
1959

## Slide 6: IRR-1 – Basic Characteristics
Open pool reactor
MTR (Materials Testing Reactor) type fuel
HEU – 93%
Fork type control rods – Ag, In, Cd
Light water moderator and coolant
  Primary cooling cycle – Mineral less water 650 m3/h
  Secondary cooling cycle – Soft water 1100 m3/h
Graphite reflector

## Slide 7: General schematics
Irradiation tubes
Core lattice
Flapper
Fuel rods
Ionization chambers

## Slide 8: General schematics

## Slide 9: Research stations
Three operational tubes:
  Thermal neutron camera (radial tube)
  Thermal neutron diffractometer (radial tube)
  Thermal neutron chamber (radial tube)
Pneumatic Rabbit Irradiation System
“Direct” access to the core from the pool

## Slide 10: Thermal neutron diffractometer
PG monochromator  = 2.421Å
∆d/d = 1.6% @ 3Å (medium resolution)
Cu monochromator  ≈ 1Å
∆d/d = 1.4% @ 3Å (medium resolution)
14 3He detector multi-detector (45.5o)
2 = 5o – 130o
Q = 0.23 – 4.7Å-1 @  = 2.421Å (Q ≈ 0.55 – 11.4Å-1 @  = 1Å)
T = 10 – 300K
~105 n/cm2/s

## Slide 11: KARL – select papers

## Slide 12: Thermal neutron camera
L/D = 250
Maximum object size 40 x 40 cm2
Average time of exposure ~ 30 min
~106 n/cm2/s

## Slide 13: IRR-1 “applications”
Materials science
NDT for industry and IAEC
Activation analysis
Neutron detectors calibration and QA
Radiation damage
Experimental reactor physics
Nuclear Safeguard
Education in reactor and nuclear physics

## Slide 14: How to ask for a beam-time
Must collaborate with SNRC scientist
Nuclear Physics Division approval (both Reactor Manager or Division Head)
Safety approval
Final scheduling by reactor manager or Chief Operation Engineer