## Slide 1: Beam-Beam Interaction with Longitudinal Impedance, local RF Cavity
Y. Zhang, N. Wang
Workshop on the Circular Electron-Positron Collider, EU Edition 2019
Oxford, UK, April 15 - 17, 2019

## Slide 2: Beam-Beam Parameter at CEPC & LEP2
the damping rate per beam-beam interaction
CEPC-H
CEPC-W
CEPC-Z
http://tlep.web.cern.ch/content/accelerator-challenges
R. Assmann
CDR

## Slide 3: Bunch Current Limit @ Higgs
CDR
Bunch lengthening is considered instead of longitudinal wake force
Maximum limit ~ 0.12

## Slide 4: Tune Scan
The error bar shows the turn-by-turn luminosity difference.
0.61,
Higgs
X-Z instability @(0.535,0.61)
K. Ohmi and etal., DOI:10.1103/PhysRevLett.119.134801
CDR

## Slide 5: Higgs: Higher Luminosity (1904)
Qx=0.555
Qy=0.610
Luminosity = 5e34
SR Beam Power = 30MW
Ne=17e10
Maximum Beam-Beam Parameter: ~0.11
Lower : 1.5mm->1mm
Lower : 1.21nm -> 1.89nm
Ne: 15e10 -> 17e10

## Slide 6: Crosstalk between Beam-Beam Interaction & Collective Effect
Bunch lengthening caused by impedance => Gaussian Approximation
In the conventional case, it is fine since the longitudinal dynamics is not sensitive to the beam-beam interaction
In CEPC/FCC, the beamstrahlung effect will also lengthen the bunch
It is self-consistent to consider the longitudinal wake field and beamstrahlung

## Slide 7: Crosscheck of Longitudinal Impedance (W/O Beam-Beam)
Ne=20e10,
Higgs-CDR,
With CDR impedance budget
Elegant vs IBB

## Slide 8: Collision with Longitudinal Impedance: the 1st sight (Higgs, CDR)

## Slide 9: Check of with impedance
A. Chao, “Physics of Collective Beam Instabilites in High Energy Accelerators”

## Slide 10: Dependence on Horizontal Tune
CDR, Ne=20e10
The optimized working point with impedance is shifted closer to half integer.

## Slide 11: Moment Evolution w/ impedance
Ne=20e10
Coherent vertical oscillation and transverse blowup

## Slide 12: Moment Evolution w/o impedance
Ne=20e10
No coherent vertical oscillation and No transverse blowup

## Slide 13: Moment Evolution w/ impedance
Ne=20e10
Optimized working point could suppress the coherent oscillation and transverse blowup.

## Slide 14: Horizontal Tune Scan (w/ impedance, 1904)
Qy=0.610
Ne=17e10

## Slide 15: Beamstrahlung lifetime (Qx=0.550)
15e10
17e10
14e10
16e10
w/ impedance, 1904

## Slide 16: 2D Tune Scan with Impedance (Ne=17e10, 1904)
0.005
Optimized Working Point: (0.550, 0.590)

## Slide 17: Crab-Waist Strength with Impedance (Ne=17e10, 1904)
Optimized CW strength ~0.85
Notes: Cw = 0.85

## Slide 18: Performance vs zero bunch current length
Higher RF Voltage:
It is no use for luminosity performance after beam-beam limit is reached
It is expected we could collide with lower bunch current and achieve similar beam-beam parameter.
It could help us increase the RF bucket height and the width of stable working point space.

## Slide 19: Different Bunch Population with Local RF Cavity (Sin-Wave)
RF Voltage = 1.176GV * 2
Longitudinal direction is unstable when

## Slide 20: Horizontal Tune: Local RF Cavity
RF Voltage = 1.176GV * 2
NE=17e10
LINEARIZED Cavity
Sin-Wave Cavity
0.545-0.549 is stable in linearized approximation
From 0.543-0.553 is always unstable in non-linearized case, due to serious bunch lengthening
Is it real physics or some bug of code
If it depends on the initial bunch distribution? Bootstraping(By D. Shatilov) is a must?

## Slide 21: Higher RF Voltage Local RF Cavity (nonlinear): Qx
RF Voltage = 1.294GV * 2
With higher RF Voltage, there exist one stable working point @0.552

## Slide 22: Different initial bunch distribution Local RF Cavity (nonlinear)
RF Voltage = 1.294GV * 2
RF Voltage = 1.176GV * 2
NE=17e10
Stable Collision:
Width：0.004
Stable Collision:
Width：0.006
Start with equilibrium distribution obtained without impedance and with smooth approximation in arc
Higher RF Voltage -> Wider Stable Working Point Space

## Slide 23: More times simulation with same parameter Local RF Cavity (nonlinear)
RF Voltage = 1.176GV * 2
The longitudinal instability does not always occur in the simulation!
Repeat the simulation 3 more times with same parameters
Ne=17e10, Qx=0.547
Notes: Hrf1176-Qx547-ne17-zlongit, 90t, 稳定，ibb3-slice-190409,
Hrf1176-qx547-ne17-zlongit-190411, 再重复计算一遍 @190411，20：34
Hrf1176-qx547-ne17-zlongit-190411-1，再重复计算一遍 @190411，20：34
Hrf1176-qx547-ne17-zlongit-rf190411，再重复计算一遍 使用rf190406 @190411，20：39

## Slide 24: Discussion on the Impedance Effect
Starting collision with “pure” zero-bunch current distribution(SR equilibrium, without bunch lengthening caused by impedance) means very strong beam-beam interaction() and may occasionally excite high energy photon(beamstrahlung) which lead the e+ or e- exceeding the RF bucket.
It is supposed that the particles exceeding the RF bucket are not reasonably treated (by interpolation) in the current beam-beam code. That’s why the “instability” is triggered in the longitudinal distribution.
It will be checked if the scenario is right in the following days.

## Slide 25: Higgs: 80%, 100%, 120% impedance
The beam-beam performance is not sensitive to longitudinal impedance budget.

## Slide 26: Higgs, Unequal Longitudinal impedance
The performance is not sensitive to the asymmetry of the longitudinal impedance

## Slide 27: =1.5mm->1mm (Solenoid: 3T -> 2T)
With same beam current,
smaller +weaker solenoid, luminosity increase by a factor of two.
bunch population increase from to , luminosity increase about 20%.
Z, CDR

## Slide 28: Z with longitudinal impedance
Bunch Lengthening and Energy Spread w/o Collision
CDR, Ne=12e10

## Slide 29: Direct Collision: Z with impedance
Transverse Blowup
Vertical Coherent Oscillation

## Slide 30: Bootstrapping Collision: Z with impedance
Transverse Blowup
Vertical Coherent Oscillation

## Slide 31: Discussion & Summary
The longitudinal impedance has been considered at CEPC
The performance of Higgs is not sensitive to the impedance
The stable working point has been shifted by the impedance. The cause need to be explained
The “bootstrapping” method is a good choice in the simulation considering local RF cavity, otherwise the very strong collision may lead particle exceeding RF bucket.
It seems the performance of Z would be sensitive to the longitudinal impedance. More parameter scan will be done in near future.

## Slide 32
Backup Slides

## Slide 33: CEPC CDR Parameters
 | Higgs | W | Z（3T） | Z（2T）
Number of IPs | 2 |  |  | 
Beam energy (GeV) | 120 | 80 | 45.5 | 
Circumference (km) | 100 |  |  | 
Synchrotron radiation loss/turn (GeV) | 1.73 | 0.34 | 0.036 | 
Crossing angle at IP (mrad) | 16.5×2 |  |  | 
Piwinski angle | 3.48 | 7.0 | 23.8 | 
Number of particles/bunch Ne (1010) | 15.0 | 12.0 | 8.0 | 
Bunch number (bunch spacing) | 242 (0.68s) | 1524 (0.21s) | 12000 (25ns+10%gap) | 
Beam current (mA) | 17.4 | 87.9 | 461.0 | 
Synchrotron radiation power /beam (MW) | 30 | 30 | 16.5 | 
Bending radius (km) | 10.7 |  |  | 
Momentum compact (10-5) | 1.11 |  |  | 
 function at IP x* / y* (m) | 0.36/0.0015 | 0.36/0.0015 | 0.2/0.0015 | 0.2/0.001
Emittance ex/ey (nm) | 1.21/0.0024 | 0.54/0.0016 | 0.18/0.004 | 0.18/0.0016
Beam size at IP sx /sy (m) | 20.9/0.06 | 13.9/0.049 | 6.0/0.078 | 6.0/0.04
Beam-beam parameters x/y | 0.018/0.109 | 0.013/0.123 | 0.004/0.06 | 0.004/0.079
RF voltage VRF (GV) | 2.17 | 0.47 | 0.10 | 
RF frequency f RF (MHz) (harmonic) | 650 (216816) |  |  | 
Natural bunch length z (mm) | 2.72 | 2.98 | 2.42 | 
Bunch length z (mm) | 4.4 | 5.9 | 8.5 | 
HOM power/cavity (2 cell) (kw) | 0.46 | 0.75 | 1.94 | 
Energy spread (%) | 0.134 | 0.098 | 0.080 | 
Energy acceptance requirement (%) | 1.35 | 0.90 | 0.49 | 
Energy acceptance by RF (%) | 2.06 | 1.47 | 1.7 | 
Photon number due to beamstrahlung | 0.082 | 0.050 | 0.023 | 
Beamstruhlung lifetime /quantum lifetime* (min) | 80/80 | >400 |  | 
Lifetime (hour) | 0.43 | 1.4 | 4.6 | 2.5
F (hour glass) | 0.89 | 0.94 | 0.99 | 
Luminosity/IP L (1034cm-2s-1) | 2.93 | 10.1 | 16.6 | 32.1
*include beam-beam simulation and real lattice

## Slide 34: CEPC New Parameters
 | Higgs | W | Z（3T） | Z（2T）
Number of IPs | 2 |  |  | 
Beam energy (GeV) | 120 | 80 | 45.5 | 
Circumference (km) | 100 |  |  | 
Synchrotron radiation loss/turn (GeV) | 1.68 | 0.33 | 0.035 | 
Crossing angle at IP (mrad) | 16.5×2 |  |  | 
Piwinski angle | 3.78 | 8.5 | 27.7 | 
Number of particles/bunch Ne (1010) | 17.0 | 12.0 | 8.0 | 
Bunch number (bunch spacing) | 218 (0.76s) | 1568 (0.20s) | 12000 (25ns+10%gap) | 
Beam current (mA) | 17.8 | 90.4 | 461.0 | 
Synchrotron radiation power /beam (MW) | 30 | 30 | 16.5 | 
Bending radius (km) | 10.7 |  |  | 
Momentum compact (10-5) | 0.91 |  |  | 
 function at IP x* / y* (m) | 0.33/0.001 | 0.33/0.001 | 0.2/0.001 | 
Emittance ex/ey (nm) | 0.89/0.0018 | 0.395/0.0012 | 0.13/0.003 | 0.13/0.00115
Beam size at IP sx /sy (m) | 17.1/0.042 | 11.4/0.035 | 5.1/0.054 | 5.1/0.034
Beam-beam parameters x/y | 0.024/0.113 | 0.012/0.1 | 0.004/0.053 | 0.004/0.085
RF voltage VRF (GV) | 2.4 | 0.43 | 0.082 | 
RF frequency f RF (MHz) (harmonic) | 650 (216816) |  |  | 
Natural bunch length z (mm) | 2.2 | 2.98 | 2.42 | 
Bunch length z (mm) | 3.93 | 5.9 | 8.5 | 
HOM power/cavity (2 cell) (kw) | 0.58 | 0.77 | 1.94 | 
Energy spread (%) | 0.19 | 0.098 | 0.080 | 
Energy acceptance requirement (%) | 1.7 | 0.90 | 0.49 | 
Energy acceptance by RF (%) | 3.0 | 1.27 | 1.55 | 
Photon number due to beamstrahlung | 0.104 | 0.050 | 0.023 | 
Beamstruhlung lifetime /quantum lifetime* (min) | 30/50 | >400 |  | 
Lifetime (hour) | 0.22 | 1.2 | 3.2 | 2.0
F (hour glass) | 0.85 | 0.92 | 0.98 | 
Luminosity/IP L (1034cm-2s-1) | 5.2 | 14.5 | 23.6 | 37.7
*include beam-beam simulation and real lattice