## Slide 1: CEPC MDI
Sha Bai
for CEPC MDI group
Workshop on the Circular Electron-Positron Collider, EU Edition 2019,
Oxford, April 15-17, 2019.
2019-04-16

## Slide 2: Outline
MDI layout and IR design
IR Superconducting magnets
Synchrotron radiation
Beam loss background
Collimator design
HOM absorber
RVC
Mechanics and assembly
IP BPM
Summary

## Slide 3: MDI layout and IR design
The accelerator components inside the detector without shielding are within a conical space with an opening angle of cosθ=0.993.
The e+e- beams collide at the IP with a horizontal angle of 33mrad and the final focusing length is 2.2m
Lumical will be installed in longitudinal 0.95~1.11m, with inner radius 28.5mm and outer radius 100mm.
The Machine Detector Interface (MDI) of CEPC double ring scheme is about 7m long from the IP
The CEPC detector superconducting solenoid with 3T magnetic field and the length of 7.6m.
With Detector solenoid
Without Detector solenoid
~cryostat in detail

## Slide 4
Without tungsten shield.
The design of interaction region
The inner diameter of the beryllium pipe is 28mm with the length of 7cm.

## Slide 5
Superconducting QD coils
Single aperture of QD0
(Peak field 3.2T)
Magnet | Central field gradient (T/m) | Magnetic length (m) | Width of Beam stay clear (mm) | Min. distance between beams centre (mm)
QD0 | 136 | 2.0 | 19.51 | 72.61
Room-temperature vacuum chamber with a clearance gap of 4 mm
Rutherford NbTi-Cu Cable
IR Superconducting magnets
Iron option for QD0 is investigated.
*10-4
Two options w/o iron yoke.

## Slide 6
Superconducting QF coils
One of QF1 aperture
(Peak field 3.8T)
Magnet | Central field gradient (T/m) | Magnetic length (m) | Width of Beam stay clear (mm) | Min. distance between beams centre (mm)
QF1 | 110 | 1.48 | 27.0 | 146.20
Room-temperature vacuum chamber with a clearance gap of 7 mm
Rutherford NbTi-Cu Cable
IR Superconducting magnets
There is iron yoke around the quadrupole coil for QF1. Since the distance between the two apertures is larger enough and there is iron yoke, the field cross talk between two apertures of QF1 can be eliminated.
n | Bn/B2@R=13.5mm
2 | 10000
6 | 1.08
10 | -0.34
14 | 0.002
Integral field harmonics with shield coils（×10-4）

## Slide 7
Bzds within 0~2.12m. Bz < 300Gauss away from 2.12m
The skew quadrupole coils are designed to make fine tuning of Bz over the QF&QD region instead of the mechanical rotation.
Solenoid compensation
Specification of Anti-Solenoid
3T & 7.6m
Anti-solenoid | Before QD0 |  | Within QD0 |  | After QD0
Central field（T） | 7.2 |  | 2.8 |  | 1.8
Magnetic length（m） | 1.1 |  | 2.0 |  | 1.98
Conductor (NbTi-Cu, mm) | 2.5×1.5 |  |  |  | 
Coil layers | 16 | 8 |  | 4/2 | 
Excitation current（kA） | 1.0 |  |  |  | 
Inductance（H） | 1.2 |  |  |  | 
Peak field in coil (T) | 7.7 | 3.0 |  | 1.9 | 
Number of sections | 4 | 11 |  | 7 | 
Solenoid coil inner diameter (mm) | 120 |  |  |  | 
Solenoid coil outer diameter (mm) | 390 |  |  |  | 
Total Lorentz force Fz (kN) | -75 | -13 |  | 88 | 
Cryostat diameter (mm) | 500 |  |  |  | 

## Slide 8: SC magnet prototype
3D model and field simulation of QD0
Mechanical and stress analysis of QD0 are in progress
Specifications on superconductor strand and cable:
Strand:
NbTi/Cu, 0.5mm in diameter,
Cu/Sc=1.3, Filament diameter < 8μm,
@4.2K, Ic≥340A@3T，Ic≥280A@4T，Ic≥230A@5T.
Rutherford Cable:
Width: 3mm, mid thickness: 0.93 mm,
keystone angle: 1.9 deg, No of stands: 12.
Ordered: NbTi/Cu Strand, Rutherford Cable.
Stress after assembled
Stress after cool down to 4.2K

## Slide 9: Detector magnet yoke decrease
Shape and size comparison: purple part is the coil, red part is the yoke.
 | CEPC original | CEPC 3 layers yoke | Smaller coil & 1 layer yoke
Central field (T) | 3 | 3 | 3
Diameter of coil (mm) | 7200 | 7200 | 6800
Length of coil (mm) | 7606 | 7606 | 7238
Barrel yoke inner diameter (mm) | 8800 | 9000 | 8400
Barrel yoke outer diameter (mm) | 14480 | 12200 | 9600
Total length of yoke (mm) | 13966 | 11600 | 9200
Weight of barrel yoke (t) | 6122 | 1608 | 1125
Weight of each end cap (t) | 3419 | 678 | 405
Total weight of yoke (t) | 12573 | 2874.5 | 1935
The original design of detector magnet has a very thick yoke. Reduces the thickness and total weight by 70% and 85% w.r.t the original design.
Benefits: weight reduced to ¼, cost reduced a lot.
End cap edge reduced to 4.6m from IP, supporting system design easier.
Combined field distribution of anti-solenoid and detector solenoid magnet meets the design requirements.

## Slide 10: Synchrotron radiation
Lumical inner radius restrict and three mask position (4.2m, 1.93m, 1.51m), SR photons in 1.11m are limited. SR power at mask~large.
SR from FD and reflection part from mask in 1.11m region，~mW power.
SR from last bend upstream hit beam pipe: QF1~3.1W, L(QF1~QD0)~36.1W, QD0~2.8W, L(lumical~QD0)~28W. Water cooling structure needed.
No SR photons within 10 directly hitting or once-scattering to the detector beam pipe.
Collimators cut beam to 13. SR photons generated from 10 to 13 will hit downstream of IR beam pipe, once-scattering photons not go into detector beam pipe but goes to even far away from the IP region.
SR photons from final doublet quadrupoles will not damage the detector components and cause background to experiments.
SR from
last bend upstream
SR from FD

## Slide 11: SR from solenoid combined field
Horizontal trajectory will coupled to the vertical.
Due to the sol+anti-sol field strength quite high, maximum~4.24T, transverse magnetic field component is quite high.
SR from vertical trajectory in sol+anti-sol combined field should be taken into account.

## Slide 12: SR critical energy and power distribution
Chart: Vertical SR critical energy distribution
| 0 | 0.04 | 0.08 | 0.119999999999999 | 0.16 | 0.2 | 0.23999999999999899 | 0.28000000000000003 | 0.32 | 0.35999999999999899 | 0.4 | 0.44 | 0.47999999999999898 | 0.52 | 0.56000000000000005 | 0.59999999999999898 | 0.64 | 0.68 | 0.71999999999999897 | 0.76 | 0.8 | 0.83999999999999897 | 0.88 | 0.92 | 0.95999999999999897 | 1 | 1.04 | 1.08 | 1.1200000000000001 | 1.1599999999999899 | 1.19999999999999 | 1.23999999999999 | 1.28 | 1.32 | 1.36 | 1.3999999999999899 | 1.43999999999999 | 1.47999999999999 | 1.52 | 1.56 | 1.6 | 1.6399999999999899 | 1.6799999999999899 | 1.71999999999999 | 1.76 | 1.8 | 1.84 | 1.8799999999999899 | 1.9199999999999899 | 1.95999999999999 | 2 | 2.04 | 2.08 | 2.12
 | 476.8875 | 476.7598 | 476.598 | 476.4017 | 476.1658 | 475.8913 | 475.5693 | 475.2015 | 474.7741 | 474.2904 | 473.7298 | 473.0934 | 472.3541 | 471.5026 | 470.5092 | 469.3499 | 467.951 | 466.2951 | 464.2191 | 461.6718 | 458.3253 | 454.0383 | 447.8626 | 439.4827 | 425.9427 | 405.416 | 365.6503 | 294.4639 | 137.9872 | -114.4776 | -375.0867 | -534.3286 | -622.1913 | -668.1842 | -670.3139 | -662.1203 | -666.816 | -665.6555 | -665.5305 | -668.0885 | -670.1539 | -670.481 | -668.2044 | -662.2664 | -650.5145 | -627.8949 | -586.7504 | -523.0915 | -451.2375 | -377.8699 | -275.3793 | -138.9724 | -31.467 | 4.2445
Maximum: 670keV
Chart: Vertical SR power distribution
| 0 | 0.04 | 0.08 | 0.119999999999999 | 0.16 | 0.2 | 0.23999999999999899 | 0.28000000000000003 | 0.32 | 0.35999999999999899 | 0.4 | 0.44 | 0.47999999999999898 | 0.52 | 0.56000000000000005 | 0.59999999999999898 | 0.64 | 0.68 | 0.71999999999999897 | 0.76 | 0.8 | 0.83999999999999897 | 0.88 | 0.92 | 0.95999999999999897 | 1 | 1.04 | 1.08 | 1.1200000000000001 | 1.1599999999999899 | 1.19999999999999 | 1.23999999999999 | 1.28 | 1.32 | 1.36 | 1.3999999999999899 | 1.43999999999999 | 1.47999999999999 | 1.52 | 1.56 | 1.6 | 1.6399999999999899 | 1.6799999999999899 | 1.71999999999999 | 1.76 | 1.8 | 1.84 | 1.8799999999999899 | 1.9199999999999899 | 1.95999999999999 | 2 | 2.04 | 2.08 | 2.12
 | -15.7 | -15.7264 | -15.7157 | -15.7028 | -15.6872 | -15.6693 | -15.6478 | -15.6237 | -15.5958 | -15.5636 | -15.5276 | -15.4854 | -15.4368 | -15.3814 | -15.3166 | -15.2409 | -15.1508 | -15.0434 | -14.9099 | -14.7461 | -14.5341 | -14.2627 | -13.8775 | -13.3626 | -12.5528 | -11.3711 | -9.2503 | -5.999 | -1.3174 | -0.90672 | -9.7342 | -19.7532 | -26.7844 | -30.8905 | -31.0876 | -30.3328 | -30.7636 | -30.6571 | -30.6461 | -30.8808 | -31.0722 | -31.1034 | -30.8914 | -30.3456 | -29.2776 | -27.2764 | -23.8192 | -18.931 | -14.0873 | -9.8787 | -5.2466 | -1.3362 | -0.068508 | -0.0012465 | -0.055061
Maximum: 31W

## Slide 13: SR from solenoid combined field
SR sector is focused in a very narrow angle from
-116urad to 131urad
SR will not hit Berryllium pipe, and not background to detector.
SR will hit the beam pipe ~213.5m downstream from IP
Water cooling is needed.
Berryllium pipe

## Slide 14: Beam loss Backgrounds at CEPC
Beamstrahlung
IP1
IP3
Beam Lost Particles
Energy Loss > 1.5%
(energy acceptance)
Radiative Bhabha
scattering
242 bunches
Revolution frequency: 2997Hz
particles/Bunch
L:
Beam-Gas
Scattering
Beam-Thermal photon
scattering

## Slide 15: CEPC beam lifetime
 | Beam lifetime | others
Quantum effect | >1000 h | 
Touscheck effect | >1000 h | 
Beam-Gas（Coulomb scattering） | >400 h | Residual gas CO，10-7Pa
Beam-Gas（bremsstralung） | 63.8 h | 
Beam-Thermal photon scattering | 50.7 h | 
Radiative Bhabha scattering | 74 min | 
Beamstrahlung | 80 min | 

## Slide 16: Loss particles due to RBB & BS
For RBB, most the events lost in the detector immediately. A few particles with high energy will lost near the IP after one revolution for a small energy loss.
For BS, energy spread distribution close to the energy acceptance, the beam loss particles not appeared in the downstream of first turn.
Compared to the one turn’s tracking, more particles get lost in the upstream region of the IR.
Although pretty large fraction of events lost in the downstream region, the radiation damage for detector component is tolerable.
The events lost in the upstream region are more dangerous for they are likely permeate into the detector components, even with the small flying angle respect to the longitudinal direction considered.
Collimators are needed.
Chart: turns
downstream | 6827 | 287 | 52 | 2 | 0 | 0 | 2 | 0 | 0 | 0 | 2 | 4 | 3 | 3 | 0 | 1 | 2 | 7 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
upstream | 366 | 388 | 123 | 272 | 197 | 99 | 31 | 13 | 5 | 70 | 302 | 258 | 654 | 100 | 93 | 49 | 112 | 59 | 37 | 79 | 117 | 66 | 15 | 5 | 2 | 0 | 21 | 74 | 74 | 123 | 47 | 32 | 8 | 16 | 13 | 16 | 12 | 30 | 13 | 7
Chart: turns
downstream | 0 | 1803 | 375 | 13 | 3 | 0 | 0 | 5 | 0 | 2 | 19 | 28 | 12 | 7 | 2 | 5 | 8 | 37 | 13 | 8 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 2 | 1 | 0 | 2 | 4 | 2 | 1 | 1 | 1 | 0
upstream | 2335 | 2503 | 697 | 1424 | 1100 | 534 | 196 | 58 | 30 | 312 | 1553 | 1373 | 3414 | 489 | 537 | 263 | 639 | 294 | 196 | 348 | 530 | 325 | 102 | 30 | 25 | 11 | 84 | 355 | 377 | 680 | 270 | 141 | 43 | 101 | 48 | 48 | 116 | 150 | 48 | 18

## Slide 17: Collimator design
Beam stay clear region: 18 x+3mm, 22 y+3mm
Impedance requirement: slope angle of collimator < 0.1
To shield big energy spread particles, phase between pair collimators: /2+n*
Collimator design in large dispersion region: =
name | Position | Distance to IP/m | Beta function/m | Horizontal Dispersion/m | Phase | BSC/2/m | Range of half width allowed/mm
APTX1 | D1I.1897 | 2139.06 | 113.83 | 0.24 | 356.87 | 0.00968 | 2.2~9.68
APTX2 | D1I.1894 | 2207.63 | 113.83 | 0.24 | 356.62 | 0.00968 | 2.2~9.68
APTX3 | D1O.10 | 1832.52 | 113.83 | 0.24 | 6.65 | 0.00968 | 2.2~9.68
APTX4 | D1O.14 | 1901.09 | 113.83 | 0.24 | 6.90 | 0.00968 | 2.2~9.68
Chart: RBB loss upstream vs horizontal collimator half width
| 9 | 8 | 7 | 6 | 5
no vertical collimator | 2001 | 1658 | 1046 | 149 | 0
y=3.3mm | 1486 | 1249 | 789 | 111 | 0
y=3mm | 1385 | 1170 | 739 | 99 | 0
Chart: BS loss upstream vs horizontal collimator half width
| 9 | 8 | 7 | 6 | 5
no vertical collimator | 10280 | 8486 | 5436 | 909 | 0
y=3.3mm | 7681 | 6462 | 4160 | 682 | 0
y=3mm | 7116 | 5988 | 3842 | 609 | 0
Only horizontal collimator are selected, vertical collimators are not needed.
Vertical collimators are usually placed very close to the beam, no vertical collimators to avoid transverse mode coupling instability.

## Slide 18: Beam-Gas bremsstrahlung and Beam-Thermal photon scattering loss particles
Without collimators
With collimators
The lost particles has been reduced to a very low level with collimators, especially in the upstream of the IP, can be accepted by the detector.
Although the beam loss in the downstream of the IP is still remained, the radiation damage and the detector background are not serious, since the direction is leaving the detector.
Beam-Gas bremsstrahlung
Beam-Thermal photon scattering

## Slide 19
Wake Integration type : Indirect Interfaces
Simulated wake length : 1000 mm
Wake shift x : 0 mm
Wake shift y : 0 mm
Wake-Loss-Factor : 1.403765e-001 V/pC
Entry interface at z-coordinate: -3.851471e+002 mm (grid-index: 102)
Exit interface at z-coordinate : 3.851471e+002 mm (grid-index: 4681)
Collimator impedance

## Slide 20: Synchrotron radiation at collimator
Bend
Collimator
beam
Synchrotron radiation from the upstream bending magnet in the ARC can contribute to the heat load of the collimators.
SR hit collimators: critical energy~357keV, power~7.7kW.
SR uniform distribution in horizontal plane and Gaussian distribution in vertical plane.
Total vertical angular divergence of SR photon beam~ 8.52urad.
Horizontal plane
Vertical plane

## Slide 21: Collimator design structure
Beam
Cooling water entrance
Cooling water exit
Movable baffle
Transition spring sheet
Considering the collimation section, the movable baffle can not protrude the step between the vacuum pipe and the collimator section. The vacuum pipe in the collimator section transits from elliptical section to rectangular section.
During the moving process of the movable baffle, the spring sheet is always pressed on the baffle to realize the gradual transition of the moving process.
Structural design and refinement (including machinery, vacuum, etc.); drive scheme design (drive, control, etc.); material selection (considering physical requirements, heat dissipation, strength, etc.); finite element simulation (thermal-structural).

## Slide 22: HOM absorber
HOM absorber design refer to FCC, under development
Distance from IP is around 70cm just before the crotch point, no space conflict with RVC and IP BPM.
Impedance
HOM at crotch point（z~±700mm）
HOM frenquency 10GHz, close to cut-off frequency (decided by beam pipe aperture).
HOM power ~3kW.
This mode is trapped mode.
HOM absorber is needed，water cooling system considered.
Synchrotron radiation from Final doublet magnets and reflection part from mask，~mW power.
SR resistance acceptable for HOM absorber

## Slide 23: IR mechanics assembly
Helicoflex
IR mechanics assembly typical point is remote vacuum connection.
The sealing point is 6m away from the operation point.
Ultrahigh vacuum sealing, Helicoflex.
RVC head and drive gear
cutaway view of RVC head
RVC tail/handwheel structure
Cutaway view of moving part

## Slide 24: IR mechanics assembly
CEPC MDI Lumical and accelerator components conflict in both position and alignment accuracy has been fixed: Lumical can be separated into 2 parts, one part with high precision installed and aligned with Be vacuum chamber, the other part 50~100kg can be installed and aligned with cryostat. And can be calibrated with IP BPM(<1um), Be pipe installed with detector.
IP
Detector
SC magnet and cryostat
RVC
Lumical main part
Lumical high accuracy part
Beam pipe

## Slide 25: IR mechanics assembly
1：IP beam pipe and detector(VX. Silicon) assembly in TPC and aligned, Lumical high accuracy part installed with detector beam pipe.
2：Cryostat with SC magnet installed on supporting system, SC magnet relative to supporting system pre-aligned in room temperature. Lumical IPBPM assembly with RVC，and aligned。
3：components in the second step with supporting system move to the setting position.
4：Beam pipe one side connected with cryostat using RVC. SC magnet aligned. Alignment accuracy ~30um.
5：Repeat the 2~4 step in the other side. Yoke installed.
6：technical detection，alignment, completed.

## Slide 26: IP BPM
Considering response time and calibration difficulty, two 4 button electrodes BPM at each side of CEPC IR is adopted.
Most of CEPC IR beam pipe are cylinder or conic, only the part from 70cm to 95cm is special shape.
There is a bellows for the requirements of installation in the crotch region, located about 0.7 m from the IP. IP BPM will be installed at 80cm from the IP in the double pipe part.
Beam pipe size：diameter 18.74mm
Bunch length：2.68mm
Single bunch charge：24nC

## Slide 27: 4 button electrodes BPM
Electromagnetic field at electrodes
Electrodes signal(bunch length 2.68mm)
Due to the short bunch length, signal has many resonance hump, signal amplitude proportional to the bunch charge.
Signal intensity can be satisfied by CEPC MDI requirement.

## Slide 28: 4 button electrodes BPM
4 button electrodes structure
4 button electrodes size
Electrode diameter:11.4mm
Inner conductor diameter: 6mm
Electrode pole to beam line:19.4mm
Space conflict for the inside two buttons
Monitoring the time when two beams arrive at the collision point, it is better to be consistent strictly.
Looking for solutions

## Slide 29: Summary
The finalization of the beam parameters and the specification of special magnets have been finished. The parameters are all reasonable.
The detector solenoid field effect to the beam can be compensated.
The most importance beam loss background is radiative Bhabha scattering and beamstrahlung for the Higgs factory.
Collimators are designed in the ARC which is about 2km far from the IP to avoid other backgrounds generation. Beam loss have disappeared in the upstream of IP for both Higgs and Z factory.
HOM of IR beam pipe has been simulated, water cooling and synchrotron radiation were considered and HOM absorber is under design.
Synchrotron radiation and impedance are taken into account for collimators, collimator machanics structure preliminary designed.
RVC preliminary design finished, next step will go to experiment and review meeting.
Mechanics assembly procedure is finalized with detector group.
IP BPM under design.

## Slide 30
Thanks