## Slide 1: CLARA Commissioning and First Friendly User Experiments
Mark Johnson*, Deepa Angal-Kalinin, James Jones and Thomas Pacey, on behalf of the CLARA Team
mark.johnson@stfc.ac.uk
deepa.angal-kalinin@stfc.ac.uk

## Slide 2: Outline
1. Introduction to CLARA
Accelerator overview, layout, and beam parameters
2. Commissioning Highlights
Commissioning timeline and key physics measurements
3. First User Experiments
Science themes, and an overview of the experiments
Below: Lancaster Castle

## Slide 3: Introduction
CLARA is a 250 MeV high-brightness electron beam facility at STFC Daresbury Laboratory (UK)
CLARA will deliver high-quality, ultra-short electron bunches to a wide variety of user experiments
The CLARA front end (~35 MeV) was previously operated as a successful user facility until 2022
The accelerator has recently undergone commissioning after installation of a major upgrade (2022 – 2025)
J.A. Clarke et al., JINST 9 T05001 (2014)
D. Angal-Kalinin et al., PRAB 23, 044801 (2020)
E.W. Snedden et al., PRAB 27, 041602 (2024)
Parameter | Low Charge | High Charge
Repetition Rate [Hz] | 1 - 100 | 
Bunch charge [pC] | 5 | 250
Bunch length [fs] | 50 | 100
Energy spread [%] | < 1 | < 5
Spot Size at IP [μm] | 20 | 100
Norm. Emittance [μm] | 2.0 | 5.0
Above: Design CLARA beam parameters for user experiments
Below: Simplified schematic showing the layout of the CLARA accelerator

## Slide 4: CLARA Front End Layout
The CLARA front end was successfully operated as a separate user facility (2018 – 2022)
D. Angal-Kalinin et al., PRAB 23, 044801 (2020)
Example Technical System | CLARA Front End (35 MeV)
RF Structures | 2
Magnets | 22
Diagnostic Systems | 13
Vacuum Gauges and Pumps | 57

## Slide 5: CLARA Layout
Example Technical System | CLARA Front End (35 MeV) | CLARA (250 MeV)
RF Structures | 2 | 7
Magnets | 22 | 77
Diagnostic Systems | 13 | 65
Vacuum Gauges and Pumps | 57 | 109

## Slide 6: CLARA FEBE Layout
Example Technical System | CLARA Front End (35 MeV) | CLARA (250 MeV) | CLARA FEBE (250 MeV)
RF Structures | 2 | 7 | 7
Magnets | 22 | 77 | 126
Diagnostic Systems | 13 | 65 | 94
Vacuum Gauges and Pumps | 57 | 109 | 155
First experiments in the Full Energy Beam Exploitation (FEBE) user area took place in early 2026

## Slide 7
CLARA Installation
View of the CLARA bunker in 2024, looking out from the accelerator’s front end towards Linac 2 and Linac 3

## Slide 8: FEBE User Area on CLARA
The Full Energy Beam Exploitation (FEBE) beamline includes a dedicated user area in a separately-shielded enclosure
Two large (~2 m3) experimental chambers can be configured for a wide range of experiments (both in air and under vacuum):
  Novel acceleration,
  Advanced diagnostics,
  New radiotherapy modalities,
A 120 TW laser will be available in late 2026, for applications requiring synchronized photon and electron beams
E.W. Snedden et al., PRAB 27, 041602 (2024)
Beam Direction

## Slide 9: FEBE Laser System
The FEBE laser is based on a commercial system (Amplitude Arco) system running at 5 Hz and 120 TW
Combining the CLARA electron beam with high-power laser pulses will provide access to unique experimental regimes
Potential applications include:
  Inverse Compton scattering (ICS) studies,
  Laser wakefield acceleration (LWFA)
Laser Parameter | Value
Wavelength [nm] | 800
Energy per pulse [J] | 2.6
Pulse duration (FWHM) [fs] | 23
Beam size at waist [μm] | 30
Peak laser intensity [W cm-2] | 6.5 x 1018
Normalised vector potential | 1.75
Above: Laser system installed in a room above the FEBE hutch
Left: Estimated laser properties at the FEBE interaction point for a co-linear geometry
Laser transport into the FEBE area is currently being installed. Commissioning expected to be complete by Autumn 2026.

## Slide 10: A Look Back…
Since July 2025:
  Successful upgrade to Cs2Te cathode
  Dielectric wakefield structure commissioned
  Extensive beam dynamics studies
  Beam transport to FEBE user area
  X-band (4th harmonic) cavity delayed until Q3 2026
  First user experiments
Tom Pacey Talk “First High Energy Beam from the CLARA Electron Accelerator and Commissioning Progress”
IOP PAB 2025
✅
✅
✅
✅
✅

## Slide 11: Commissioning Timeline
Jan. 2025
March 2025
May 2025
July 2025
Sep. 2025
Nov. 2025
Jan. 2026
March 2026
The majority of CLARA commissioning was completed in 2025, often in parallel with RF conditioning and/or FEBE installation work
A machine development (MD) period is currently underway, for detailed optimisation of the beam parameters
Technical Commissioning with Beam
Beam to FEBE
Shutdown
User Experiments
RF Conditioning (from 2024)
January 29th, 2026 First beam delivered to user experiments
April 2nd, 2025 First 250 MeV beam
September 8th, 2025 First 250 pC beam after Cs2Te cathode installation
June 27th, 2025 First bunch compression

## Slide 12: Beam Images (250 pC)
1 mm
3 mm
5 mm
1 mm
2 mm
2 mm
2 mm

## Slide 13: Cs2Te Photocathodes
Caesium telluride (Cs2Te) photocathodes for CLARA were developed in-house at Daresbury
Installation of the first Cs2Te cathode (Sept. 2025) facilitated an increased bunch charge up to 250 pC
Stable effective quantum efficiency (QE) of ~10% measured under operational conditions in the CLARA gun
Laser energy now available for longitudinal pulse shaping in future
Above: Photocathode surface, with
Cs2Te coating on the active area
Left: Typical QE measurement for a CLARA photocathode
Molybdenum Cathode Plug
Cs2Te Coating

## Slide 14: Emittance Measurements
Emittance measurements are based on quadrupole scans throughout the CLARA beamline
We routinely achieve emittances of < 1 μm in the low-energy (35 MeV) section immediately after the CLARA injector
Work is ongoing to mitigate emittance growth, which is most likely due to transverse wakefields in the linac cavities
Beam Setup (250 pC) | Horizontal Normalised Emittance [μm]
Post-injector (35 MeV) | 0.7
Uncompressed (250 MeV) | 2.3
Compressed (250 MeV) | ~5.0
Above: Results of a typical quadrupole scan in the low-energy section after the CLARA injector Left: Emittance measurements for a 250 pC compressed beam. High-energy measurements were made immediately after the final linac

## Slide 15: Phase Space Tomography
We also use generative Machine Learning (ML) for high resolution measurements of the transverse phase space
The ML technique accurately reconstructs the beam’s charge distribution, including any substructure
The method provides an accurate representation of the beam that can be used for analysis of user experiments
R. Roussel et al., PRL 130, 145011 (2023)
R. Roussel et al., PRAB 27, 094601 (2024)
Above: 4D transverse phase space, reconstructed for an uncompressed
30 pC beam immediately after the final linac
Left: Diagram showing the generative phase space reconstruction (GPSR) method for reconstructing a charge distribution from experimental data

## Slide 16: Longitudinal Dynamics
100 pC
The CLARA lattice allows measurement and manipulation of the beam’s longitudinal phase space:
  Variable bunch compressor (VBC)
  Transverse deflecting cavity (TDC)
  Passive dielectric dechirper
The 250 pC CLARA beam can be compressed to a minimum RMS bunch length of ~150 fs
Commissioning of the fourth harmonic cavity will facilitate highly compressed beam modes
Above: Animation showing measurements of the longitudinal phase space for different VBC offsets
Left: Measured RMS bunch length as a function of VBC offset

## Slide 17: Longitudinal Space Charge
During commissioning, we noticed a strong modulation of the beam energy spectrum near maximum bunch compression
Recent experimental studies revealed that the effect is caused by strong longitudinal space charge (LSC)
LSC is driven by a current spike at the head of the bunch, which forms due to its non-linear longitudinal phase space.
The effect has been reproduced in start-to-end simulations, and can be mitigated with the fourth harmonic cavity
Above: Simplified diagram showing the effect of LSC on the CLARA beam. Adapted from Yasutome et al. (2026)
K. Yasutome et al., in Proc. IPAC26, THO3T03 (2026)
Above: Spectrometer images showing the energy spectrum of the 250 MeV CLARA beam near maximum compression
pz
y
CSR modulation
LSC modulation
Observed at any bunch charge between 5 – 250 pC

## Slide 18: Passive Wakefield Structure
A passive wakefield structure has been installed in the final section of CLARA (250 MeV/c)
The device uses wakefields excited by the beam itself to manipulate the longitudinal phase space. It can be used as a:
  Dechirper to remove correlated energy spread,
  Streaker to infer the time structure of the bunch
Commissioning of the device as a dechirper has demonstrated:
  Reduction of the beam energy spread,
  Preservation of the transverse emittance
T. Overton et al., in Proc. IPAC26, WEP6091 (2026)
Beam Direction
Motion control for variable DLW gap
Planar dielectric lined waveguides (DLW)
Above: Passive wakefield structure installed on the CLARA beamline
Left: Measurements of energy spread as a function of dechirper gap, for a 250 pC beam

## Slide 19: Beam Stability
The CLARA electron beam benefits from stable operation across a wide range of timescales:
  Shot-to-shot jitter (10 - 100 Hz),
  Recovery from an RF trip (seconds)
  Slow drifts (minutes to hours),
  Reproducibility between shifts (days)
Multiple CLARA users gave feedback indicating that their experiments would not have been possible without this stability
Above: Video showing the 250 MeV/c CLARA beam in a spectrometer line. The beam recovers from an RF trip within a few seconds.
“The stability and beam quality at CLARA is… comparable to other state-of-the-art facilities”
“The working point provided excellent stability compared to similar facilities”
“The robust and stable beam allowed for rapid irradiation [of samples]”
– Anonymised User Feedback

## Slide 20: Software and Machine Learning
Most high-level CLARA software is based on CATAP, a python-based middle layer that simplifies interactions with the accelerator hardware
A simulation-based digital twin has recently been deployed on CLARA, for online modelling of the accelerator and setup optimization
CLARA is an ideal test facility for machine learning (ML) and artificial intelligence (AI). Many applications are in development:
  Photoinjector laser pulse shaping
  Magnet hysteresis modelling,
  Reinforcement learning,
  Virtual diagnostics,
  Agentic control,
M. King et al., arXiv:2509.19794 (2025)
A.D. Brynes et al., arXiv:2604.19101 (2026)
J. Jones et al., in Proc. IPAC26, WEV6003 (2026)
Above: Web interface for the simulation-based CLARA digital twin

## Slide 21: User Science Themes
Medical Applications
Compact Accelerators
Advanced Diagnostics
AI for Accelerators
Laser Based Accelerators
Examples:
Virtual diagnostics,
Reinforcement learning optimisation
Examples:
FLASH dosimetry,
VHEE beam delivery,
Radiobiology studies
Examples:
Optical Transition Radiation (OTR),
Coherent Transition Radiation (CTR)
Examples:
Beam driven plasma acceleration,
Active plasma lenses
Examples:
Laser-plasma acceleration,
Inverse Compton scattering
After FEBE Laser
Commissioning
(Q3 2026)
Planned Friendly User Run (Q2 2026)
First Friendly User Run (Q1 2026)

## Slide 22: Comparison with European Facilities
 | CLARA | ARES | CLEAR | FLUTE | PITZ | SPARC Lab
Accelerator Components R&D | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
Beam Diagnostics R&D | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
Novel Acceleration (DWA, DLA) | ✔ | ✔ |  |  |  | 
Novel Acceleration Using High Power Lasers (PWFA, LWFA*, THz) | ✔ |  |  |  |  | ✔
Radiation Sources |  |  |  | ✔ | ✔ | ✔
Plasma Lens Development | ✔ |  | ✔ |  |  | 
VHEE FLASH Radiotherapy | ✔ |  | ✔ |  |  | 
Other Medical Applications |  | ✔ |  | ✔ |  | 
Irradiation Experiments† |  |  | ✔ |  |  | 
* External injection into laser wakefield acceleration (LWFA) † Excluding radiotherapy applications
Updated from IPAC23 talk: “Electron Beam Test Facilities for Novel Applications”
D. Angal-Kalinin et al., in Proc. IPAC23, MOZG1 (2023)

## Slide 23: Friendly User Programme
The first CLARA user experiments took place between January – April 2026
Experiments were specifically selected to:
  Deliver high-impact science,
  Cover a wide range of science themes,
  Build on successful experiments at other facilities,
  Exploit the full capabilities of the CLARA accelerator,
  Complement ongoing commissioning work
Below: Map showing the home institutes of the first CLARA users

## Slide 24: Optical Transition Radiation (OTR)
Experiment involved measurements of the transverse beam optics, using an OTR target located after the FEBE hutch
Aimed to characterize the resolution of single-shot emittance measurements, made via an optical pepper pot technique
The FEBE beamline was used to:
  Benchmark OTR measurements against quadrupole scans,
  Deliver specific Twiss parameters to the OTR target
Lead Investigator: J. Wolfenden (Liverpool University)
Spatially Coherent OTR Beam Size < 50 μm at 250 pC
OTR target
Periscope
Light box with optical paths for:
Direct imaging of OTR light
OTR imaging via a multi-lens array (MLA)
Direct
MLA

## Slide 25: Coherent Transition Radiation (CTR)
Lead Investigator: W. Kuropka (DESY ARES)
Experiment aimed to demonstrate a CTR-based compression diagnostic for ultra-short (< 10 fs), low charge (< 5 pC) beams
Signals were measured with several photodiodes, mounted next to a CTR target just before the FEBE hutch
Minimized the bunch length by adjusting the VBC R56 to maximize the CTR signal at short wavelengths
Delivered ultra-short electron bunches: ≲ 5 fs duration at ~3.5 pC

## Slide 26: Medical Applications
CLARA is a valuable test facility for new radiotherapy methods using very high energy electrons (VHEE)
Simulation studies have indicated that CLARA can deliver FLASH dose rates (> 40 Gy/s) to the FEBE user area
FLASH dose rates are of interest due to evidence that they deliver similar tumour control while sparing healthy tissue
The VHEE’25 workshop was held at Daresbury in Sept. 2025
D. Angal-Kalinin et al., Front. Phys. 12, 1496850 (2024)
Above: Participants of the VHEE’25 workshop
See Roger Jones’ talk about VHEE radiotherapy after the coffee break
Left: Visualisation of Monte Carlo dose rate calculations with the 250 MeV CLARA beam

## Slide 27: VHEE Scatterers
Lead Investigator: M. Dosanjh (Oxford University and CERN)
C. Robertson et al. NIM A 1082, 170943 (2026)
The first in-air experiment carried out in either of the FEBE experimental chambers
Aimed to generate large (~1 cm), uniform beam profiles suitable for Very High Energy Electron (VHEE) radiotherapy
Successfully produced uniform beams at energies up to 250 MeV, using various scatterer configurations
Builds on previous work with 200 MeV beam at CLEAR (CERN)
Top Right: Photo of the experimental setup inside the second FEBE chamber
Bottom Right: Analysis of RCF films showing uniform electron beam profiles
Conical Scatterers
Collimator
Water Phantom
Beam Direction

## Slide 28: VHEE Cell Irradiation
Lead Investigator: R.M. Jones (Manchester University)
Dosimetry studies to establish the electron beam parameters required to achieve FLASH dose rates (> 100 Gy/s) at CLARA
Experiment will study cell survival and DNA damage after VHEE irradiation at conventional and FLASH dose rates
Builds on previous studies at CLARA, ARES (DESY) and CLEAR (CERN)
K.L. Small et al., Sci. Rep 11, 3341 (2021)
D. Angal-Kalinin et al., Front. Phys. 12 1496850 (2024) K. Small et al., NIM B 565, 165752 (2025)
Above: Photo of the experimental setup inside the FEBE chamber
Left: Video showing delivery of the CLARA electron beam to samples held in a 96-well cell plate
European first: VHEE FLASH irradiation of cancer cells (A549 lung adenocarcinoma) with the 250 MeV electron beam
96-Well Cell Plate
Beam Axis
10 mm
See talk by Kristina Small at 11:20 today

## Slide 29: Plasma Acceleration - Goals
Lead Investigator: R. D’Arcy (Oxford University)
The HALHF Collaboration plan to explore concepts for novel accelerator staging (for high energy) and repetition rates (for high luminosity) at CLARA
  Plan benefits from unique, flexible, modular infrastructure
  To be carried out in a multi-year phased approach
Experimental goals (this beam time):
  Prove plasma-accelerator infrastructure at CLARA, and generate plasma with a discharge capillary
  Drive a plasma wake with the CLARA beam Goal: Generate GV/m (decelerating) fields
  Focus CLARA beams with an active plasma lens Goal: Generate >100 T/m (focussing) fields
Above: Plasma cell in the FEBE experimental chamber
Left: First (argon) plasma generation
arXiv:2503.19880

## Slide 30: Plasma Acceleration - Results
All goals achieved!
  ~GV/m electric fields
  ~150 T/m magnetic fields
Next steps (in subsequent beam times)
  Novel interstage optics scheme (for staging of plasma-accelerated beams)
  Plasma acceleration of bunch trains with HALHF properties (~10 ns separation, 100 Hz)
  Energy-mapping studies and high average power plasma sources
Lead Investigator: R. D’Arcy (Oxford University)
Courtesy of C.A. Lindstrøm
Milestone: First beam-driven plasma “accelerator” in the UK, and the first active plasma lensing at CLARA
See talk by Meg Savage Tuesday at 11:15

## Slide 31: Future Plans
CLARA is delivering high-brightness electron beams to high-impact user experiments
More milestones are expected over the coming months…
  Commissioning of the fourth harmonic cavity,
  120 TW laser transport into the FEBE hutch,
  First experiments combining the CLARA electron beam and FEBE laser
Further user experiments, involving machine learning and the FEBE laser, are planned for later this year
Above: Fourth harmonic cavity installed on the CLARA beamline
Left: 120 TW laser installed in a room above the FEBE hutch

## Slide 32
Thank You for Listening!
Questions are Very Welcome
CLARA at IPAC26
TUP3075 | In-situ cathode measurements (A. Pollard)
TUP3076 | Dark current measurements (F. Jackson)
WEV6003 | High-level software (J. Jones)
WEP6091 | Dechirper commissioning (T. Overton)
WEP6092 | Phase space tomography (M. Johnson)
WEP6104 | High-level RF interfaces (N. Joshi)
WEP6171 | Automated RF conditioning (M. King)
THP2100 | Compression and linearisation (J. Jones)
THP2143 | Cs2Te cathode production (H. Churn)
THP2144 | High-power RF conditioning (A. Gilfellon)
www.ipac26.org/prepress