## Slide 1
Terahertz techniques for advanced accelerators
Morgan T. Hibberd
Ernest Rutherford Fellow
morgan.hibberd@manchester.ac.uk

## Slide 2
Outline
The accelerator spectrum
What can terahertz offer?
Progress in terahertz acceleration
Our terahertz acceleration research at the Cockcroft Institute
  Sources and dielectric-lined waveguides
  Bunch compression, bunch trains and temporal locking
  External injection into plasma wakefields – can we solve this challenge?
  Upcoming THz experiments on CLARA
Summary
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
1

## Slide 3
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Advanced accelerators
Radio
Microwave
Infrared
Ultraviolet
X-Ray
Gamma
3 GHz
10 cm
Visible
12 GHz
25 mm
375 THz
800 nm
8 THz
40 µm
0.4 THz
750 µm
0.2 THz
1.5 mm
Terahertz
0.1 THz
3 mm
2 THz
150 µm
X-band
mm-wave
Terahertz-driven
RF
AWAKE
PWFA
LWFA
Dielectric laser accelerators
2

## Slide 4
Radio
Microwave
X-Ray
Gamma
Terahertz
Radio-frequency
Laser plasma wakefield
Infrared
Ultraviolet
Visible
1000x
Higher frequency
Higher accelerating gradient
Smaller accelerator
Advanced accelerators: Laser-driven plasma wakefield acceleration
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
3
Notes: RF 3 GHz 10 cm (LHC 400 MHz)
X band 12 GHz 25 mm
Mm-wave: 0.1 THz 3mm
AWAKE: 0.2 THz 1.5 mm
THz : 0.4 THz 750 um
PWFA 2 THz 150 um
LWFA: 8 THz 40 um
DLA 375 THz 800 nm

## Slide 5
Radio
Microwave
X-Ray
Gamma
Terahertz
Radio-frequency
Laser plasma wakefield
Infrared
Ultraviolet
Visible
Advanced accelerators: Laser-driven plasma wakefield acceleration
Terahertz
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
3
Notes: RF 3 GHz 10 cm (LHC 400 MHz)
X band 12 GHz 25 mm
Mm-wave: 0.1 THz 3mm
AWAKE: 0.2 THz 1.5 mm
THz : 0.4 THz 750 um
PWFA 2 THz 150 um
LWFA: 8 THz 40 um
DLA 375 THz 800 nm

## Slide 6
What does terahertz offer?
Electron bunch
<1 ps
Energy gain
Energy loss
Multi-cycle
THz pulse
fTHz = 0.4 THz
RF
>2 GV/m
to match
THz
20 MV/m
TRF > 300 ps
TTHz = 2.5 ps
fRF = 3 GHz
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Advantages of THz accelerators
High electric field strengths
Laser and THz pulse shaping
Laser timing synchronisation
Compact mm-scale structures
Optimal frequency for manipulation
Laser-driven sources of terahertz (THz) radiation
Frequency range between RF/microwave and infrared (lasers)
Exploit advantages from both technologies
Terahertz dielectric-lined waveguide structure
4

## Slide 7
A decade of terahertz acceleration
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Selected examples
E. A. Nanni et al. Nat. Commun. 6, 8486 (2015)
C. Kealhofer et al. Science 352, 429-433 (2016)
D. Zhang et al. Nat. Photonics 12, 336-342 (2018)
D. Ehberger et al. Phys. Rev. Appl. 11, 024034 (2019)
S. Li et al. Nat Commun. 14, 6596 (2023)
J. Ying et al. Phys. Rev. X 15, 021095 (2025)
Sub-relativistic electron beams
Acceleration
Streaking
Compression
Focusing
Photoemission
Electron guns
5

## Slide 8
A decade of terahertz acceleration
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Selected examples
E. Curry et al. Phys. Rev. Lett. 120, 094801 (2018)
L. Zhao et al. Phys. Rev. Lett. 122, 144801 (2019)
M.T. Hibberd et al. Nat. Photon. 14, 755-759 (2020)
E.C. Snively et al. Phys. Rev. Lett. 124, 054801 (2020)
H. Tang et al. Phys. Rev. Lett. 127, 074801 (2021)
H. Xu et al. Nat. Photon. 15, 426-430 (2021)
X.Q. Yu et al. Nat. Photon. 17, 957–963 (2023)
Z.P. Li et al. Phys. Rev. Lett. 134, 075001 (2025)
Relativistic electron beams
Acceleration
Streaking
Compression
Jitter suppression
Bunch trains
Spin-polarization
6

## Slide 9
3.18 mm
3.25 mm
Field confinement boosts accelerating gradient
Create longitudinal fields for acceleration
Velocity-matching with the dielectric lining
Coupler entrance
Our approach: Terahertz dielectric-lined waveguides
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
L. Nix et al., Phys. Rev. Accel. Beams 27, 041302 (2024)
O. Apsimon et al. Phys. Rev. Accel. Beams 24, 121303 (2021)
V. Georgiadis et al., App. Phys. Lett. 118, 14 (2021)
7
1200 μm
575 μm
695 μm
Dielectric lining (top and bottom)
Laurence Nix
PDRA
Poster: Advances in coupling schemes for terahertz-driven electron beam manipulation
Joseph Bradbury
PDRA
Talk: Terahertz
transverse streaking for femtosecond diagnostics
Filip Peczek
PhD student
Poster: Machine learning for terahertz waveguide design

## Slide 10
+ more wafers
Terahertz sources: Periodically-poled lithium niobate wafer-stacks
Terahertz acceleration: Terahertz sources
Mosley et al. Opt. Express. 31 4041 (2023)
Narrowband frequency matched to dielectric-lined waveguide
Cryo-cooling boosts THz field and provides frequency tuning
Large-area sources for high-power laser systems
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
8
Patrick Dalton
PhD student
Poster: Optimisation of a lithium niobate wafer narrowband THz source for driving THz accelerators
Dalton et al. Appl. Phys. Lett. 125, 141101 (2024)
Dalton et al. Opt. Lett. 51, 5-8 (2026)

## Slide 11
30 mm
Time
Energy
Single compressed bunch
Time
Energy
Multi-cycle modulation
Time
Energy
Micro-bunch train
Time
Energy
Long injected bunch
Time
Energy
Short injected bunch
Time
Energy
Sub-cycle chirping
PPLN source
THz phase shear plate
Drive laser
5.5 MeV
35.5 MeV
Magnetic dogleg
THz pulse
CLARA
3 GHz RF linac
2 m
Magnetic chicane compressor (modelled)
THz beam profile
Terahertz acceleration: Experiments on CLARA @ Daresbury Laboratory
Dielectric-lined waveguide
RF accelerator as bunch injector
Laser-generated THz for energy modulation
Simulate magnetic compression of THz-induced chirp
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
M.T. Hibberd et al. Terahertz control of relativistic electron beams for femtosecond bunching and laser-synchronized temporal locking. arXiv:2508.20685
9

## Slide 12
Energy gain (acceleration)
Energy loss (deceleration)
Energy gain/energy loss
(de-chirping/chirping)
Multi-cycle narrowband THz pulse
Short
electron bunch
Different interaction depending on injection timing of the electron bunch relative to the THz field
We have precise femtosecond control using an optical delay stage on the THz drive laser
Long chirped electron bunch
Energy gain/energy loss (modulation)
Time
-ve
+ve
Field
Terahertz-driven acceleration and manipulation
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
10

## Slide 13
Sub-cycle acceleration and manipulation: For bunch compression
THz-driven chirping followed by magnetic compression
THz off
Acceleration
Deceleration
Chirping
15 fs rms
400 fs rms
Measured
Modelled
Injected bunch
Compressed bunch
Modelled
Measured
With improvements to the THz and bunch parameters
 sub-10 fs bunches with >kA peak currents achievable
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Modelled compression
Bunch charge = 2.5 pC
M.T. Hibberd et al. arXiv:2508.20685
11

## Slide 14
Multi-cycle energy modulation: For bunch train generation
Ultrashort micro-bunch trains with picosecond spacing
Can’t be done with conventional RF techniques
Tunable spacing using THz frequency or R56
Can be used as a longitudinal bunch diagnostic
Peak width provides direct measurement of slice uncorrelated energy spread
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Energy modulation (over-modulated)
Magnetic compression
Micro-bunch trains
Energy modulation (matched chirp)
THz injection phase scan
Increase THz field
M.T. Hibberd et al. arXiv:2508.20685
12

## Slide 15
Laboratory reference frame
Electron-to-laser temporal locking
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
THz drive laser reference frame
M.T. Hibberd et al. arXiv:2508.20685
Bunches are “temporally locked” to the THz fields and the THz drive laser
Improvements required to push towards the femtosecond scale
Lased-based accelerator applications
FEL pump-probe experiments
Ultrafast electron diffraction
Compton scattering for strong-field QED
External injection into LWFA
13

## Slide 16
Terahertz-driven “acceleration”
External injection of electrons into a laser-driven plasma wakefield
RF-based accelerator
CLARA (250 MeV electrons)
Laser-driven plasma wakefield
Poor beam quality
Maintains high beam quality
Combines 3 accelerator technologies
THz “bridge” between RF and LWFA
Laser
Combining technologies: Solving the LWFA external injection problem
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
14

## Slide 17
Combining technologies: Solving the LWFA external injection problem
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
THz waveguide
CLARA/FEBE @ Daresbury Laboratory one of only a few facilities in the world with this capability
Plasma cell
Diagnostics
Combine 250 MeV electron beam with 100 TW laser system
15

## Slide 18
Aras Amini
PhD student
Terahertz-assisted LWFA external injection
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
A. Amini et al. Controlling external injection in laser-plasma accelerators with terahertz frequency bunch manipulation. arXiv:2604.16059
Start-to-end simulations for high-quality GeV beams
Electron bunch from CLARA RF linac
THz-driven energy modulation/chirping
Magnetic chicane compression
Injection, transverse matching and acceleration in LWFA
RF linac
Time
Density
Density
Time
Dielectric-lined waveguide
Drive laser
THz pulse
THz off
THz on
Jitter >100 fs rms
< 10 fs rms
>70 fs rms
THz off
Energy
Shots
THz on
Plasma channel
Electron bunch
Magnetic chicane
1
2
3
Poster: Sub-10 fs synchronization in laser-plasma accelerators with THz frequency bunch manipulation
16

## Slide 19
Terahertz-assisted LWFA external injection: THz compression and temporal locking
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
S2E model of CLARA beam
Gaussian bunch
S2E model
Gaussian
Initial bunch parameters | S2E | Gaussian
Charge (pC) | 5 | 5
Energy (MeV) | 230 | 250
Bunch length (fs rms) | 189 | 120
Transverse size (μm) | ≈ 50 | ≈ 50
Uncorrelated energy spread (keV) | 22 | 20
Norm. emittance (mm mrad) | 0.23 | 0.3
Arrival time jitter (fs rms) | 100 | 100
At LWFA injection point | S2E | Gaussian
Charge (pC) | 5 | 5
Energy (MeV) | 229.8 | 249.9
Bunch length (fs rms) | 8.5 | 5.9
Transverse size (μm) | ≈ 3-4 | ≈ 3-4
Energy spread (%) | 0.4 | 0.31
Norm. emittance x/y (mm mrad) | 0.82/0.94 | 0.6/0.3
Arrival time jitter (fs rms) | 8.0 | 3.7
After THz compression and temporal locking
A. Amini et al. arXiv:2604.16059
17

## Slide 20
Terahertz-assisted LWFA external injection: Plasma injection and acceleration
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Emittance and energy spread along the plasma for:
Optimal and sub-optimal injection (only 12.3 fs offset)
Growth in εny
Growth in energy spread
Injection timing critical at the sub-10 fs level
Maintain low emittance (< 1 um) and energy spread (< 1%)
Laser parameters | 
Wavelength | 800 nm
Pulse energy | 2 J
Waist size | 30 μm
Pulse length FWHM | 25 fs
Plasma parameters | 
Plasma density (on-axis) | 1x1017 cm-3
Ramp-up/down length | 5.5 λβ
Plateau length | 9 cm
εnx
εnx
εny
A. Amini et al. arXiv:2604.16059
18

## Slide 21
Terahertz-assisted LWFA external injection: High quality GeV beam
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
No THz control (RF-manipulated bunches)
Large energy jitter ≈ 20% rms
Dominated by relative arrival time jitter (> 70 fs rms)
With THz control (S2E beam) Median energy spread ≈ 1.1% rms Energy jitter reduced to ≈ 2.2% rms
With THz control (Gaussian beam) Median energy spread ≈ 0.30% rms
Energy jitter reduced to ≈ 0.29% rms
THz controlled injection enables high quality beams
Reduce energy jitter by 1-2 orders-of-magnitude
A. Amini et al. arXiv:2604.16059
19

## Slide 22
Upcoming THz experiments on CLARA
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
First experimental demonstration of THz compression and temporal locking in September
THz waveguide
Plasma cell
Diagnostics
20

## Slide 23
Upcoming THz experiments on CLARA
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
First experimental demonstration of THz compression and temporal locking during September beam-time
20
THz
EOSI
Laser
Longitudinal bunch diagnostics are critical
  Transverse deflecting cavity (TDC) for full longitudinal phase-space (LPS) measurement
  Electro-optic spectral interferometry (EOSI) for bunch profile and arrival time jitter (relative to the laser)
Samuel Norman
PhD student
Talk: Electro-optic spectral interferometry bunch profile monitor
S. Norman et al. Proc. 14th International
Beam Instrumentation Conference
(IBIC 2025), Liverpool, UK, 2025 WEPCO40

## Slide 24
Upcoming THz experiments on CLARA
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
21
Experimental goals
Single and multi-bunch trains
Bunch compression and synchronisation at 10 fs level
First component for external LWFA injection
Experimental design and preparation underway
New laser beamline
New THz source chamber
New interaction chamber
Christopher Shaw
PDRA
CLARA electron beam
To chicane
To EOSI

## Slide 25
Summary
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference
Laser-based THz acceleration offers unique advantages for compact high-frequency bunch control
Ultrashort bunch compression and tunable micro-bunch trains
Towards femtosecond-scale electron-to-laser temporal-locking
Provide “bridge” between conventional and plasma wakefield technologies
Solve challenge of external injection into LWFA for high quality GeV beams
THz
LWFA
RF
M.T. Hibberd et al. Terahertz control of relativistic electron beams for femtosecond bunching and laser-synchronized temporal locking. arXiv:2508.20685
A. Amini et al. Controlling external injection in laser-plasma accelerators with terahertz frequency bunch manipulation. arXiv:2604.16059
22

## Slide 26
Terahertz Acceleration Group @ The Cockcroft Institute
www.thzag.uk
Academic leads
Morgan Hibberd Steven Jamison
Darren Graham Graeme Burt
Rob Appleby Rosa Letizia
PDRAs
Laurence Nix
Christopher Shaw
Joseph Bradbury
Dan Lake
Sergey Siaber
Connor Mosley
Rohit Kumar
PhDs
Aras Amini
Patrick Dalton
Filip Peczek
Sam Norman
Ryan McGuigan
Thomas Wilson
Xi Luo
Beatriz Higuera Gonzalez Vasileios Georgiadis
Oliver Finlay
Alisa Healy
Additional collaborators
Ed Snedden James Jones Laura Corner
David Walsh Lewis Reid
Tom Pacey
Thank you for your attention
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference

## Slide 28
Single-cycle THz pulse
vg = 0.585c
vp = 0.999c = ve
at 0.4 THz
Multi-cycle THz pulse
Normal waveguide has TM11 accelerating mode
Phase-velocity vp > c  Can’t match to particle bunch velocity
Dielectric-lined waveguide has LSM11 accelerating mode
Phase-velocity vp = c at specific frequency  Can match particle velocity
Envelope travels at the group velocity
Carrier wave travels at
the phase velocity
Narrowband much better!
Less dispersion
Phase-velocity matched
Strong interaction
Broadband not good
Lots of dispersion
Phase-slippage
Weak interaction
Terahertz acceleration: Accelerating structures
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference

## Slide 29
Electromagnetic waves typically propagate with transverse electric and magnetic fields
Due to finite size, they also have longitudinal components
Can enhance longitudinal component by focusing a radially-polarised beam
Radially-polarised THz can be different to generate
S Winnerl et al. New J. Phys. 14 103049 (2012)
Can we use a simpler mode?
Terahertz acceleration: Longitudinal fields
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference

## Slide 30
y
z
x
DLW
LSM11 mode
Electric field (a.u.)
1
0
Dielectric
lining
Vacuum
aperture
y
z
Free-space
TEM01 mode
Copper
walls
Longitudinal cross-section of the DLW
Electron propagation
+
_
+
_
Electron propagation
TEM01 free-space mode  LSM11 waveguide mode
Transverse fields off-axis (deflect particles)
Longitudinal fields on-axis (accelerate particles)
Terahertz acceleration: Waveguide modes
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference

## Slide 31
quasi-TEM01
TEM00
PTFE
phase-shifter plate
THz beam
Make the correct mode using a “phase-shifter”
Terahertz acceleration: Waveguide modes
THz camera image of TEM01 mode at entrance to waveguide
Measured THz electric fields showing 180º phase change between top and bottom
Dr Morgan Hibberd | Terahertz techniques for advanced accelerators | PAB 2026 Conference