## Slide 1: Third Harmonic Cavity Design for the Electron-Ion Collider
IOP PAB 2026
30th June 2026
S. Toole s.j.toole@lancaster.ac.uk
G. Burt, Z. Conway, R. Rimmer

## Slide 2
Motivation for an Electron-Ion Collider
1
Figure 1: Evolving understanding of proton spin origin. (Left) proton was composed of three valence quarks, with total spin ½. (Right) proton contains quarks, as well as a gluonic sea of quark-antiquark pairs; the total spin is composed of that of the elementary spins2.
1“Lipkin, Harry J. 1988. “Flavor Symmetry, EMC Results and the Spin Content of the Proton.” Physics Letters. B 214 (3): 429–33; 2White Paper on the Electron-Ion Collider in Preparation for the NSAC Long Range Plan.” 2023
In 1988, deep inelastic scattering (DIS) experiment revealed valence quarks contribute less than 30% of proton spin1
Valence quark spin
Protons, were thought to derive their ½ spin primarily from their constituent valence quarks, uud
Quark and gluon orbital angular momentum
Gluon spin

## Slide 3: The Electron Ion Collider
2
The existing 3.4km rings of the Relativistic Heavy Ion Collider are used to build:
3Bnl.gov. (2017). The EIC Machine., Satogata, T. (2023). 4EIC Parameter List Summary. [online] EIC.JLAB. Available at: https://eic.jlab.org/Documents/EIC-General/EIC_ParameterList.pdf.
Hadron Storage Ring (HSR): storing polarised protons at energies 41-275 GeV.
Electron Storage Ring (ESR): storing polarised electrons at energies 5 GeV -18 GeV.
Rapid-Cycling Synchrotron (RCS): a pre-injector to accelerate polarised electrons from 200MeV to 5 GeV-18 GeV4.
Two interaction regions
Parameter | e- | p+
Beam energy [GeV] | 10 | 275
Beam current [A] | 2.5 | 1
Spin polarisation [%] | ≥70 | 
Luminosity [1034cm-2s-1] | 1 | 
Beam parameters operating at maximum luminosity4.

## Slide 4
Coherent Electron Cooling
5COHERENT ELECTRON COOLING PHYSICS FOR THE EIC. doi:https://doi.org/10.18429/JACoW-IPAC2024-THYD1 6Ratner, D. (2013). Microbunched Electron Cooling for High-Energy Hadron Beams. Physical Review Letters, 111(8). Bergan, W.F., Mayes, C., Wang, N. and Stupakov, G. (2024).
18 - 275 GeV
50 - 150 MeV
Heavy ions do not have an intrinsic damping mechanism to counteract emittance growth when subjected to long stores in collider rings
Emittance growth occurs due to: Intra Beam Scattering → Degrades luminosity
Vertical emittance grows from to in 2 hours5
External fast cooling mechanism required to counteract this6
3
A future upgrade

## Slide 5: Cooling at the EIC
4
Latest schematic – 20227
7Wang, E, W Bergan, F Willeke, S Benson, K Deitrick, Thomas Jefferson, C Mayes, D Douglas, C Gulliford, and N Taylor. n.d. “ELECTRON ION COLLIDER STRONG HADRON COOLING INJECTOR and ERL.
Two stage amplification with chicanes
Kicker
Modulator
Hadron Chicane
e- to ERL
P+
p+ to HSR

## Slide 6: Cooling at the EIC
5
7Wang, E, W Bergan, F Willeke, S Benson, K Deitrick, Thomas Jefferson, C Mayes, D Douglas, C Gulliford, and N Taylor. n.d. “ELECTRON ION COLLIDER STRONG HADRON COOLING INJECTOR and ERL.
Primary electron cooler accelerating cavities
Third harmonic cavities

## Slide 7: Energy Recovery Linacs & BBU
6
Beam accelerated by SRF cavities
2. After use, beam is recirculated back to cavities with phase difference
3. Beam is decelerated, returning its energy back to cavities
Limits maximum operable beam current
Compromises complete energy recovery
ERL operation
Beam Break Up Instability
Bunch enters cavity off axis
Deflecting HOM is excited
Bunch experiences transverse kick
Bunch returns to cavity with larger transverse offset
Bunch receives another transverse kick
Bunch decelerated, HOM energy grows
Positive feedback loop
Deflecting modes must be sufficiently damped

## Slide 8: Motivation for Third Harmonic Cavities
8Byrd, J.M., Baptiste, K., De Santis, S., Kosta, S., Lo, C.C., Plate, D., Rimmer, R.A. and Franks, M. (2000). Design of a higher harmonic RF system for the Advanced Light Source. Nuclear Instruments and Methods in Physics Research Section A: Accelerators, Spectrometers, Detectors and Associated Equipment, [online] 439(1), pp.15–25. doi:https://doi.org/10.1016/s0168-9002(99)00892-x.
7
Cooler electron bunch length is 4-5 cm, occupying 36 degrees of 591 MHz RF voltage
Curved electron bunch
Poor cooling efficiency
Bunch head, centre, and tail see different voltages
Causes curved bunch
1st harmonic
1st harmonic + 3rd harmonic
Total voltage is flat across bunch centre linearity restored
1st harmonic
1st + 3rd harmonic

## Slide 9
8
591MHz SRF 5-cell cavity module for the ERL cooler10
9 Rimmer, R. (2021). An Overview of RF Systems for the EIC. JaCoW. doi:https://doi.org/10.18429/JACoW-IPAC2021-MOPAB385 10Rimmer, R. and Daly, E. (2022). CAVITY AND CRYOMODULE DEVELOPMENTS FOR EIC. JaCoW. doi:https://doi.org/10.18429/JACoW-eeFACT2022-WEXAS0101
1773MHz Cavities: The Spec
Parameter | Value
Frequency [MHz] | 1773
V 5-cell [MV] | 6.33
 | 2.77
[mT/MV/m] | 5.54
[MV/m] | 15.4
Parameter | Value
Frequency [MHz] | 1773
V 5-cell [MV] | 6.33
 | 2.77
 | 5.54
 | 15.4
Electron beam current in cooler is 100 mA : HOM impedance is a major issue
Minimum aperture radius, : 30 mm
  Maximise HOM propagation by lowering cut-off frequency
All SRF cavities adopt maximum allowable surface fields of 40 MV/m (Epk) and 80 mT (Bpk)9 - 19 MV provided to 3 cavities, 6.33 MV per cavity
5-cells per cryomodule, three cryomodules
How large can the aperture be while satisfying cavity specification?
Notes: [1]
R. Rimmer et al., “CAVITY AND CRYOMODULE DEVELOPMENTS FOR EIC * OVERVIEW OF SRF SYSTEMS FOR EIC.” Accessed: Nov. 14, 2024. [Online]. Available: https://accelconf.web.cern.ch/eefact2022/papers/wexas0101.pdf
High current ERL beams are susceptible to multibunch instabilities arising from Higher Order Modes (HOMs). Operating at 100mA, the ERL benefits from reduced short range wakefields due to large beamholes reducing impedance.
Optimisation of SRF cavities considers limits imposed by thermal breakdown (), field emission, and multipacting (while maximising the accelerating gradient ( for a given stored energy (.
[1]
R. Rimmer et al., “CAVITY AND CRYOMODULE DEVELOPMENTS FOR EIC * OVERVIEW OF SRF SYSTEMS FOR EIC.” Accessed: Nov. 14, 2024. [Online]. Available: https://accelconf.web.cern.ch/eefact2022/papers/wexas0101.pdf
High current ERL beams are susceptible to multibunch instabilities arising from Higher Order Modes (HOMs). Operating at 100mA, the ERL benefits from reduced short range wakefields due to large beamholes reducing impedance.
Optimisation of SRF cavities considers limits imposed by thermal breakdown (𝐵_𝑝/𝐸_𝑎𝑐𝑐), field emission, and multipacting (𝐸_𝑝/𝐸_𝑎𝑐𝑐) while maximising the accelerating gradient (𝐸_𝑎𝑐𝑐) for a given stored energy (𝑄_0).

## Slide 10: Single Cell Optimisation
9
1. Epk/Eacc – surface electric field required to produce
2. Bpk/Eacc – surface magnetic field required to produce
3. R/Q – how efficiently RF energy is transferred to beam
CAVITY OPTIMISATION GOALS
Inductive region
Capacitive region
Cavity geometry is optimised by balancing competing objectives
Notes: Limitations of manual optimisation:
Cavity geometry produces conflicting RF objectives
Improving one figure of merit often degrades another
Difficult to manually produce a vast, exotic set of non-dominated solutions

## Slide 11
10
Multi-Objective Optimisation
Cavity design requires simultaneous optimisation of conflicting objectives
Design objectives:
Candidate geometries
A design is Pareto-optimal if one objective cannot be improved without degrading another.
30 mm
35 mm
40 mm
Multi-objective genetic algorithm is used to identify a set of Pareto-optimal geometries satisfying objectives
Each point is an individual design candidate from the optimisation process, where cell elliptical parameters were varied with increasing aperture radius.
Notes: Multi-objective optimisation proves time consuming it is difficult to manually produce a set of non-dominated solutions to explore the design space
Optimisation of SRF cavities considers limits imposed by thermal breakdown (), field emission, and multipacting (while maximising the accelerating gradient ( for a given stored energy (.
Pareto optimisation anual design space exploration and producing a set of non-dominated, varied solutions is a challenging, time demanding task for thousands of simulations – particularly when they are conflicting!
Multi-objective optimisation proves time consuming it is difficult to manually produce a set of non-dominated solutions to explore the design space
Optimisation of SRF cavities considers limits imposed by thermal breakdown (𝐵_𝑝/𝐸_𝑎𝑐𝑐), field emission, and multipacting (𝐸_𝑝/𝐸_𝑎𝑐𝑐) while maximising the accelerating gradient (𝐸_𝑎𝑐𝑐) for a given stored energy (𝑄_0).
Pareto optimisation anual design space exploration and producing a set of non-dominated, varied solutions is a challenging, time demanding task for thousands of simulations – particularly when they are conflicting!

## Slide 12
11
Each 5-cell configuration satisfies
Field Flatness ≥98%
Transit Time Factor ≥ 0.7
Evenly distributed surface fields across all cells (close to 1:1)
Trapped Mode Analysis
TE11 above cut-off
TE11 below cut-off
Propagation region
Trapping region
Beampipe radius sets TE11 cut-off frequency
TE11 cut-off frequency in circular waveguide
Initial studies of dipole behaviour begins with a standard 5-cell structure
cavity aperture radius = beampipe radius
Lowest HOM frequency is trapped within all candidates
30 mm
35 mm
40 mm
All cavity candidates require a larger beampipe to propagate dipoles
Propagation region
Notes: Enlarged beampipes can decrease the TE11 cut-off below the TE111 resonance, at the cost of moving the TE111 resonance closer to the TM010 frequency
This increases the difficulty in sufficient HOM suppression without coupling to the TM010 mode

## Slide 13
11
Trapped Mode Analysis
Using a larger beampipe requires an optimised ‘lip’ transition between cavity and beampipe
Beampipe
Cavity
Lip
propagation
trapping
example
Maximum aperture limited by:​
Evanescent decay of TM010 mode into beampipe​
TM010 cut-off​
Cavity sandwiched between 591 MHz cavities –beampipe will have to taper down
Notes: Enlarged beampipes can decrease the TE11 cut-off below the TE111 resonance, at the cost of moving the TE111 resonance closer to the TM010 frequency
This increases the difficulty in sufficient HOM suppression without coupling to the TM010 mode

## Slide 14: Baseline HOM Spectrum
12
4.1-4.4 GHz band: high impedance and
~5.3 GHz: single high impedance monopole
2 GHz band: high impedance modes
Narrowband damping
Requires broadband damping
BLA configuration based on beampipe optimised for TM010 trapping (

## Slide 15: Lowest Dipole Frequency Propagation
2
Beampipe cut-off
HOM propagation
HOM trapped
Key Takeaway
Lip radius determines whether the first dipole is trapped or propagates
  Using a smaller lip increases dipole frequency to push above cut-off
30 mm and 32 mm lip shows promise for damped however,
and impedance dipole response to lip radius 2.0GHz – 5.4 GHz must be evaluated
13
Beampipe cut-off frequency
Lip radius defined from beamline axis

## Slide 16: Mode Trapping in Bottleneck Geometry
14
A huge impedance improvement GHz band with larger lip
Improvement in of 2 GHz band dipoles
Same improvement seen with 4 GHz band
Balanced behaviour, but outweighed by a…

## Slide 17: End Cell Optimisation for Dipole Damping
15
First Dipole Passband
4 GHz Dipole Bands
End cell length
~4.15 GHz band favours longer end cell
2 GHz bands: smaller end cell length favours
4 GHz bands: longer end cell length improves both and impedance
We require broadband damping of and impedance, with stronger impedance weighting for BBU longer end cell preferred

## Slide 18: Beam Break-Up Instability
16
Minimum beam current to drive regenerative beam break up for each cavity11 (Ib= 100 mA)
Threshold currents calculated using cavity , HOM frequency, and lattice recirculation optics (
All modes stable at operating current
11 S. Sentiyaz (2025) BBU Parameters for EIC-ERL, Private communication,
High impedance modes
Horizontal Dipole Polarisation,
Vertical Dipole Polarisation,
High impedance modes
Smallest threshold current is 2A, x20 safety margin

## Slide 19: Waveguide Consideration
17
Beampipe absorber shows good promise for damping dipole modes
however,
In a recirculatory machine, available beamline real estate is limited
Beamline absorber requires warm section
Requires more space
BLA – CAV – WG
Can adding a waveguide provide equivalent or improved HOM damping than a BLA?
Break rotational symmetry → introduce hybrid modes → complex WG system
Local field enhancement around beampipe-WG interface
Multipacting
Possible configuration
WG – CAV – WG

## Slide 20
18
Summary
Developed 5-cell 3rd harmonic cavity for EIC cooler
Optimised end-cell and cavity-beampipe geometry for built-in HOM damping
All BBU threshold currents at least 1 order of magnitude above
Evaluate if a waveguide provides improved damping for optimisation of space utility
Perform thermal simulations of BLA with ferrite HOM loads
Change of direction – coaxial coupler for EIC crab cavity
Future Work

## Slide 21: Thank you for listening
IOP PAB 2026
S. Toole s.j.toole@lancaster.ac.uk
G. Burt, Z. Conway, R. Rimmer
19

## Slide 22: Back-up Slides
IOP PAB 2026
S. Toole s.j.toole@lancaster.ac.uk
G. Burt, Z. Conway, R. Rimmer
20

## Slide 23
21
Multipacting in the Beampipe
Figure 10: Electron evolution starting from a homogenous distribution of 1000 electrons as a function of rising EP surface fields on 5-cell cavity with no lip optimisation. Nb (2K) SEY curve: 300˚C bakeout.
Operating
Parameter | Value
 | 1.5
 | 0.8
Impact energy at first crossover [eV] | 75
Maximum impact energy [eV] | 300
Initial number of electrons | 1000
Parameter | Value
 | 1.5
 | 0.8
Impact energy at first crossover [eV] | 75
Maximum impact energy [eV] | 300
Initial number of electrons | 1000
Table X: SEY parameters of high purity Nb following 300˚C bakeout.
Multipacting field levels
Unoptimised lip (cavity-beampipe interface)

## Slide 24
22
1Sergey Belomestnykh, and Valery Shemelin. 2008. “Multipacting-Free Transitions between Cavities and Beam-Pipes.” Nuclear Instruments and Methods in Physics Research Section a Accelerators Spectrometers Detectors and Associated Equipment 595 (2): 293–98. https://doi.org/10.1016/j.nima.2008.05.041
It is energetically favourable for electrons to exist in a local electric minima due to the associated lower potential , which attracts electrons
‘Calm corners’ are eliminated by encouraging electron drift in the direction of the decaying field.
Figure 12: (top) Blend at beampipe-lip transition region of 0mm, 12.5mm, and 25mm (bottom) Elimination of electric field minima at MP location.
Miller force
Diagnosing MP in the Beampipe

## Slide 25
23
BBU ERL Parameters
Cavity | Energy [MeV] |  | Energy [MeV] | 
1st | 25.052 | -2.40998727 | 25.025 | 5.47015190
2nd | 26.462 | -1.79034846 | 26.462 | 4.32234179
3rd | 27.899 | 0.9118264 | 27.889 | 3.61400521
4th | 29.336 | 2.89340006 | 29.336 | 3.77933567
Cavity | Energy [MeV] |  | Energy [MeV] | 
1st | 25.052 | -2.40998727 | 25.025 | 5.47015190
2nd | 26.462 | -1.79034846 | 26.462 | 4.32234179
3rd | 27.899 | 0.9118264 | 27.889 | 3.61400521
4th | 29.336 | 2.89340006 | 29.336 | 3.77933567
Revolution time = 2.526298722343194e-06 s

## Slide 26
24
EIC DIS data
x -fraction of proton momentum carried by a struck quark or gluon (Bjorken scaling variable)
- negative squared four momentum transfer carried by the exchanged virtual photon during scattering event
Achieving this region requires maximising total available energy at collision point