## Slide 1
Muhammad Raharsya Andiva1, Chenxi Zhao2, Qinghua Lei1, and Martin Ziegler3
1 Department of Earth Sciences, Uppsala University, Sweden
2 CCTEG Coal Mining Research Institute, Beijing, China
3 Federal Office of Topography, Mont Terri Underground Rock Laboratory, St-Ursanne, Switzerland
Numerical simulation of damage evolution around the PF/PF-A experiment borehole in faulted Opalinus Clay
Federal Office of Topography
Federal Nuclear Safety
Inspectorate ENSI

## Slide 2: Numerical modelling strategy
2
Ventilation and resaturation
Short-term (hours to days)
Long-term (months to years)
Free surface creation
Mechanical unloading
Stress redistribution
Rock mass deformation
Damage evolution
…
Pore pressure diffusion
Poroelasticity
Saturation evolution
Suction
Swelling
Creep
Damage
…
Geomechanical modelling
Hydromechanical modelling
Drilling
Not to scale

## Slide 3: PF/PF-A experiment
Jaeggi (2019)
Martin and Loew (2021)
Located in Mont Terri Rock Laboratory
1 experiment borehole
6 monitoring boreholes
Structurally-controlled overbreaks
Martin and Loew (2021)
3

## Slide 4: Overbreak pattern (shortly after drilling)
Zhao, Lei, Ziegler, Loew (2024) IJRMMS

## Slide 5: Model setup (geomechanical model)
Fracture network reconstruction
Numerical model construction
5
Zhao, Lei, Ziegler, Loew (2024) IJRMMS
Generated using Fracman
Simulated using 3DEC

## Slide 6: Simulation results
Displacement field
Stress field
6
Zhao, Lei, Ziegler, Loew (2024) IJRMMS

## Slide 7: Simulation results
7
Zhao, Lei, Ziegler, Loew (2024) IJRMMS

## Slide 8: Simulation results
Base case: with fractures and fault zone; Case A: with fractures but without fault zone
Case B: with fault zone but without fractures; Case C: without fault zone and fractures
8
Zhao, Lei, Ziegler, Loew (2024) IJRMMS

## Slide 9: Simulation results
Base case: with fractures and fault zone; Case A: with fractures but without fault zone
Case B: with fault zone but without fractures; Case C: without fault zone and fractures
9
Zhao, Lei, Ziegler, Loew (2024) IJRMMS

## Slide 10: Simulation results
Acute intersection angle (10 deg) between fault zone and borehole
Stronger overbreaks, more new cracks and squeezing ground behaviour are observed
Zhao, Lei, Ziegler, Loew (2024) IJRMMS
10

## Slide 11: Simulation results
Acute intersection angle (10 deg) between fault zone and borehole
Stronger overbreaks, more new cracks and squeezing ground behaviour are observed
Zhao, Lei, Ziegler, Loew (2024) IJRMMS
11

## Slide 12
Start of ventilation phase
End of ventilation phase
After ~3 years of resaturation
Ventilation
Resaturation
Borehole relative humidity and temperature evolution
Evolution of overbreaks along the experiment borehole
Long-term overbreak evolution in the PF-A experiment
Resaturated

## Slide 13
Matrix
Fault zone
Secondary fractures
Experiment borehole
Solid deformation
Poroelasticity 
Damage 
Swelling
Fracture deformation
Creep
Plasticity
Fluid flow
Unsaturated and saturated flow
Model setup (hydromechanical model)
Simulated using COMSOL

## Slide 14
Start of ventilation
End of ventilation
Start of resaturated
End of resaturated
Variation of unsaturated zone
L = 4 m
0.5 m
Preliminary simulation results
RH
Unsaturated zone evolution

## Slide 15
Preliminary simulation results
Damaged zone evolution
1
2
3
1
2
3

## Slide 16: Next step plan (hydromechanical modelling)
16
Generating new DFN with conditioned simulation.
Adjusting parameters based on the current updates from the lab team.
Benchmarking of key model components.
Validation against experimental observation data (e.g. strain measurements, overbreak pattern and evolution).
Use the model to understand the interplay and relative importance of different processes (suction, swelling, poroelasticity, creep, etc.) in driving time-dependent overbreak and damage evolution.

## Slide 17: Concluding remarks
17
A 3D framework has been developed to simulate progressive failure around the PF/PF-A borehole in faulted Opalinus Clay
The geomechanical model captures short-term damage and overbreak formation, highlighting the effects of fault zone and fracture networks
The hydromechanical model incorporates realistic hydraulic boundary conditions and coupled processes including unsaturated flow, swelling, suction, and damage
Future work will extend the framework to drift-scale modelling
Acknowledgement
We are grateful for the financial support from Swisstopo, ENSI, BGR, ETH, and Uppsala University
Federal Office of Topography
Federal Nuclear Safety
Inspectorate ENSI

## Slide 18
18

## Slide 19: Backup slides
19

## Slide 20: Overbreak pattern along the experiment borehole
Zhao, Lei, Ziegler, Loew (2025) IJRMMS

## Slide 21: Constitutive models
Crack growth driven by tensile or shear failure
Bilinear Mohr-Coulomb criterion
21
Zhao, Lei, Ziegler, Loew (2025) IJRMMS

## Slide 22
Ventilation
Resaturation
RH during ventilation between 62 and 74 %
Time-dependent rock desaturation
Resaturation from 07/2022
Since 01/2024, the experiment borehole is at >95 % RH
The unsaturated zone was observed at a distance of 15–21 cm from the tunnel.
The boundary condition for the tunnel in the model was set based on observed relative humidity data.
Borehole relative humidity and temperature evolution
Ziegler et al. 2025

## Slide 23
Evolution of induced cracks and breakouts
Ziegler et al. 2025
New cracks and breakouts developed during the ventilation period and grew extensively during the resaturation period.
a = before the ventilation start
b = halfway through the ventilation period
c = end of ventilation period
d = after resaturation ramp
e = end of resaturation period

## Slide 24
Mechanical equilibrium
Total stress
Damage
Swelling
Fracture deformation
Richard’s equation (matrix)
Richard’s equation (fracture)
Brooks-Corey retention model
Fracture permeability
Governing equations

## Slide 25
Unsaturated zone
Chart: Unsaturated zone length (m)
| Start of Ventilation | End of Ventilation | Start of Resaturation | End of Resaturation
Average | 0.05878 | 0.067487 | 0.047831 | 0.04592
Maximum | 0.40669 | 0.65177 | 0.30491 | 0.28738

## Slide 26
Evolution of damage
Aperture evolution mostly driven by the suction effect.
Damage integration along borehole is almost constant along the borehole during the ventilation and resaturation period.