## Slide 1: Unidad de Física Nuclear Básica (FNB) del CNA: actividades en IABA
J. Espino, B. Fernández, J. P. Fernández-García, J. Ferrer, J. Gómez-Camacho, C. Guerrero, T. Rodríguez-González and J.M. Quesada
PhD students: A. Vegas, J. Bartolomé-Sarsa and G. Auñón
Others: C. Muñoz, A. Reina@CERN + former PhD students M.A. Millán-Callado @PTB, P. Pérez-Maroto@CERN
Dpto. Física Atómica, Molecular y Nuclear (FAMN), Universidad de Sevilla, 41012 Seville, Spain
Centro Nacional de Aceleradores (CNA), 41092 Seville, Spain
1st IABA meeting, Madrid 10/3/2026

## Slide 2
Introduction of the group

## Slide 3: Introduction of the group
Composition:
J. Espino, B. Fernández, J. P. Fernández-García, J. Ferrer, J. Gómez-Camacho, C. Guerrero, T. Rodríguez-González and J.M. Quesada
PhD students: A. Vegas, J. Bartolomé-Sarsa and G. Auñón
Others: C. Muñoz, A. Reina@CERN + former PhD students (M.A. Millán-Callado @PTB, P. Pérez-Maroto@CERN)
Research lines:
Nuclear reaction measurements and instrumentation at CNA and international laboratories (INFN-LNS, ISOLDE, TRIUMPH,, …)
Neutron reaction measurements and instrumentation at CNA and international laboratories (n_TOF, NFS, HZDR, CLPU, PTB, JRC-MONNET, …)
Funding
Plan Nacional AEI (…., PID2024, …) y regionals (last in 2018)
Infraestructuras ICTS and AEI
Planes de Recuperación, Transformación y Resiliencia (MRR)
EC projects: CHANDA, EUROLABS, ARIEL, SANDA, OFFERR and APRENDE
Education and Learning
Masters: Interuniversitario en Física Nuclear + Erasmus Mundus en Física Nuclear + Tecnologías Físicas para la Medicina y la Biología
HiSPANoS School on the Production, Detection and Use of Neutrons [2022, 2026]
Basic Training School on Accelerator Applications in Nuclear Physics (BTS25) [2025]
Most of the FNB Unit

## Slide 4
Overview of work carried out at international facilities

## Slide 5: Overview of work carried out at international facilities

## Slide 6
Previous and planned work at CNA / CMAM:
nuclear reactions at FNB beam line

## Slide 7: Nuclear reactions at FNB beam line of CNA
Setup validation
Currently: collaboration with ASFIN (LNS-INFN)
Collaboration with the ASFIN group to measure α – α in coincidence from 6Li(4He,2H)8Be.
Relative energy distribution centred in 91 keV (8Be dissociation energy).
Coincidence measurements capability.
Measurement of 6Li+12C reaction around Coulomb Barrier (4.5 MeV).
Fragment separation capability with telescopes.
Determination of excitation function and angular distribution for different reaction channels.
New setup!
- New 40 cm3 Aluminium chamber reaction.
- Large active area (50cm2) segmented (20, 40 and 500 µm) & PAD (300 µm) detectors.
2H
4He
1H
91 keV
¹²C(⁶Li,⁴He)¹⁴N
¹²C(⁶Li,²H)¹⁶O
Next: 9Be + 12C measurement
Experiment with beam energies around the Coulomb barrier (7 MeV) at CNA and ¿CMAM?
Reaction fragments and coincidences measurements.

## Slide 8: Magnetron-Sputtering to make solid-gas targets for CNA and CERN
Industrially well established
Large areas feasible
Wide range of substrates
Control of microstructure
Control of composition
Gas
element
Gas
element
Gas
element
Gas
element
solid
matrix
Self supported Si-He target
Many of the isotopes of interest in nuclear (and neutron) reactions correspond to geaseous elements, which poses a serious problem.
=> A solution is to “grow” samples that incorpórate the gas into the sustrate in sufficient amounts, which has been demosntrated by our group and now at CNA we will be able to make such targets for nuclear physics experiments at CNA, CERN/ISOLDE, TRIUMPH, LNS, etc.
Magnetron Sputtering
UNIVEX 250 for RF sputtering by Leybold

## Slide 9
Previous and planned work at CNA / CMAM:
neutron (in/out) reactions at CNA HiSPANoS
Research lines of CNA
Collaborations with other groups (besides MANY)

## Slide 10: HiSPANoS neutron beam line at CNA
Time domain: Continuous & Pulsed (1 MHz, 2 ns)
Energy domain:
  Thermal via moderated 9Be(p,n) → 25 meV
  Epithermal via 7Li(p,n) → 1-100 keV
  Fast monoenergetic via 2H(d,n) → 2,5 to 5 MeV
  Fast white beam via 9Be(d,n) → 1 to 10 MeV

## Slide 11: Measurements of 30 keV Maxwellian Averaged Cross Sections (MACS30keV)
P. Pérez-Maroto et al., Neutron activation as benchmark for cross section evaluations: Demonstration through the MACS of 50Cr for nuclear technology applications, Physics Letters B 862 (2025)
The 7Li(p,n) reaction at 1912 keV produces neutrons similar to those of the s-process: a 30 keV Maxwell-Boltzman distribution
CNA research line for the exploitation of MACS activation measurements:
2025: 50Cr for nuclear technology applications
2026: 59Co, 109Ag, 186W and 232Th within EC-APRENDE
(requested by the International Reactor Dosimetry and Fusion File IRDFF-II)
2027: Short–lived isotopes with the HiSPANoS/CERN-NEAR CYCLIC
→ Nuclear astrophysics
→ Nuclear technology

## Slide 12: Production and use of thermal neutrons
Thermal neutron beams are key to many applications of science and industry.
Situation in Spain
Experimental fission reactors (JEN-1, ARGOS) dismanteled decades ago. [Ffield=1013, Ffield=109 n/cm2/s]
UPM opperates an Am/Be moderated neutron source
CIEMAT has designed a new Am/Be moderated neutron source
CANS represent a intermediate solution in terms of flux
[Ffield=---, Ffield=102 n/cm2/s]
CNA HiSPANoSthermal: Ffield=107, Fbeam@50cm=104 n/cm2/s
→ in between reactors and radioactive sources
Prospects:
Thermal XS
Neutron-imaging
NAA (heritage & industry)
Detector characterization
….

## Slide 13: Measurements of (a,n) reactions within MANY (via activation)
Activation if radioactive
AMS always
Neutron counting
Neutron ToF spectroscopy
PaAA
Validation with 27Al(a,n)30P

## Slide 14: Measurements of (a,n) reactions within MANY (via activation)
Activation if radioactive
AMS always
Neutron counting
Neutron ToF spectroscopy
PaAA
14N(a,n)17F @9 MeV
Nitrogen often used as inert buffer gas and present in some plastics
→ discrepancies between two only measurements at 7-10 MeV
Issues: N is gas + N compounds are insulators
Ti and Ge candidates for fusion diagnostics by foil activation Bonheure et al., Fusion Engineering and Design 88 (2013) 533

## Slide 15: Measurements of (a,n) reactions within MANY via neutron spectroscopy
Neutron counting
Neutron ToF spectroscopy
PaAA

## Slide 16: Measurements of (a,n) reactions within MANY via neutron spectroscopy
Neutron counting
Neutron ToF spectroscopy
PaAA
5 Li-glass 2”x0,5” detectors for epitermal neutrons (1-800 keV)
5 EJ309 5”x2” detectors for fast neutrons (500 keV to 15 MeV)
New ion source
(2 → 20 mA)
New buncher
(DT=2ns)
After demonstrating the fasibility of (a,n) ToF specroscopy, we’ve waited three years to become fully productive and realiable
By end of 2026:
Our own array of detectors, compatible with MONSTER
A 16 channel 12 bits digitizer (old one was 8 channels, 10 bits)
A high performance buncher a beams (2 ns)
A high intensity ion source for a beams (from 2 to 20 mA)
Detector calibration and methodology validated at PTB (Sc.V)
A high performance and well trained PhD student

## Slide 17: Collaborations with research groups & industry (besides MANY activities)
Characterization of concrete for shielding @IFMIF-DONES
The construction of IFMIF-DONES requires efficient shielding to neutrons, for which new concrete compositions are being developed.
Transmission measurements with fast monoenergetic neutron beams are carried out to validate the GEANT4 Monte Carlo calculations.
Mutagenesis for improved crops
Kaki buds were irradiated with fast neutrons in a range 0,1 to 1 Gy, achieveing the LD=50 @ ~1Gy.
Fast neutrons
Now the fruit trees are monitored at ANECOOP facilities in Valencia.
37Ar production for dark matter
Irradiation of CaO powder for 5h with 3×1010n/sr/s from Be(d,n) at 1.2 µA:
Demonstration of TREX-DM reaching O(10eV) thresholds, at the level of single-electron ionization in Ar.
40Ca(n,a)37Ar (t1/2=35d)
37Ar source: EK=2,8 keV, EL=270 eV
J. Castel et al., JCAP (2026)
Innovative SiC neutron detector
Response of the detector thermal neutrons
(LiF convcerter)
M. Pérez et al., NIM-A 1069 (2024)
50mm thick p-n diode built in a 4H-SiC wafer
The CSIC-IMB-CNM have developed their own technology of solid-state SiC radiation. When loaded with 10B, 6LiF and PE converters, become suitabile for thermal/fast neutron detection.

## Slide 18: Collaborations with research groups & industry (besides MANY activities)
RPC based neutron detectors
Resistive Plate Chambers (RPCs) are simple, cheap and good timing (sub-ns) and spatial resolution.
A new design with 10B neutron converter is under development at LIP and has been tested successfully at HiSPANoS.
Irradiation of electronics
A.C Vilas-Bôas et al., Journal of Integrated Circuits and Systems (2026)
At CNA there is a well established program on Radiation-to-Electronics (R2E) using MeV photons (60Co from RadLab) and ions (3 MV tandem and 18 MeV cyclotron).
SEUs candidate in a FPGA irradiated with fast neutrons for 1 h.
n-sensitivity of CERN detectors
The measurement of (n,g) reactions at the CERN n_TOF facility requires radiation detectors insensitive to neutrons. They are made of C6D6 and can be mounted on carbon fiber housings.
Conventional and innovative (SiPM, lower volumes), have been recently tested against epithermal neutrons at HiSPANoS.
In addition:
Neutron imaging
(USC and Neutron Insights)
Fission s(f,n) with MGAS
(NTUA via EC-EUROLABS)
- Quenching of Skipper CCD
(UBA via EC-EUROLABS)
- Radiobiology with neutrons
(U. Lisboa via EC-OFFERR)
- NAA of roman coins
(USE and IAPH)
and more.

## Slide 19
Thank you
This work has receieved funding from Plan Complementario de I+D+i de Astrofísica y Física de Altas Energías (MRR) ASTRO21/1.3/3 project and from Agencia Estatal de Investigación (AEI) through PID2021-123879OO, PID2024-155965OB-I00 and EQC2024-008842-P