## Slide 1
CMAM for Nuclear Physics
10th March 2026
Gastón García

## Slide 2
Accelerator, beamlines
Nuclear Physics BLs
Pulsed beam
Contents

## Slide 3
Accelerator
Emax=Eext+VT·(q+1)·e
E1 (MeV)=1·VT·e
E2 (MeV)=q·VT·e
q= charge state
Eext =Vext·1·e
Ion sources
High stability (ripple below 1E-5)
Four sources:
Duoplasmatron: He
2 x pulsed duoplasmatron (He and H)
Sputtering: Solid targets, many beam species used & molecular beams posible, energy 10´s of MeV

## Slide 4
Beamlines
Nuclear
physics
BL
External
μBL
Implantation
BL (+fs laser)
Internal
μBL
Standard
BL
ERD-TOF
BL

## Slide 5
Nuclear Physics: NUC-30 & NUC-45º beamlines
5

## Slide 6
NUCLEAR BeamLines

## Slide 7
4‑axis collimator slits.
F-cup
X/Y Z scanner
Collimator <>
NUC30 Upgrade 2026

## Slide 8
Computer controlled Rotary target developed for NUC-45
remotly & automatic change of different targets and F-cup without breaking vacuum
automatic cyclic change in/off beam and current measurement.
Rotatory target holder
teflon (pos. 2127)
graphite (pos. 1474)
nylon (pos. 871)
NUCLEAR BeamLines R&D
Target for:
Minibelen & GARRY
Target for Monster

## Slide 9
Summary status of NUC BLs
NUC30 needs some refurbishment, but is a flexible tool for NUC experiments
NUC45 has very limited diagnostics and strong optics limitations, but is very flexible for ad-hoc setups

## Slide 10
Pulsed beam
Ion sources
Continuous beam
Chopper
Chopped bunch
Cumpressed bunch
Buncher

## Slide 11
Pulsed beam: phase space
E
E
E
t
t
t
E
t
t
t
After chopper
After buncher
After some drift space
After optimum drift space

## Slide 12
Pulsed proton beam
Latest commissioning: (17/02/2026)
NUC-45: FWHM ≈ 2 ns
0o degrees: FWHM < 1.5 ns
Commissioning on NUC-45: (27/01/2026)
27Al(p,γ)28Si
Beam energy: 4 MeV
FWHM ≈ 3.26 ns

## Slide 13
Pulsed alpha beam
Commissioning on NUC-45: (29/01/2026)
27Al(α,γ)30Si
Beam energy: 6.5 MeV
FWHM ≈ 5.3 ns

## Slide 14
Pulsed beam with protons optimized (Δt < 2 ns) Pulsed beam for alphas limited to Δt ~ 5ns Most likely explanation is dispersive contribution of magnet at large angles (30-45deg) Investing efforts in understanding better these limitations
Pulsed beam: status