## Slide 1: Drift Properties of Noble Gases in Negative Ion Drift TPCs
Elizabeth Tilly – Wellesley College
Work carried out during PhD at the University of New Mexico
CPAD – OCtober 2026
et117@wellesley.edu

## Slide 2: Directionality for Rare-Event Searches
S. Vahsen et al Annu. Rev. Nucl. Part. Sci. 2021. 71 189-224 [2102.04596 (arxiv.org)]

## Slide 3: Noble Gases as Targets
Gaseous He, Ar, Xe and CF4 for WIMP DM searches
  J.F. Castel et al. JINST 19 C05029 (2024)
  F.D. Amaro et al. Particles 4 343-353 (2021)
  S.E. Vahsen et al. (2020) arxiv:2008.12587
  C. Deaconu et al. Phys. Rev. D 95 122002 (2017)
  K. Nakamura et al. JINST 7 C02023 (2012)
Gaseous Xe for neutrinoless double beta decay
  K. Mistry, D. R. Nygren, (2025) arxiv:2512.19290
  I.G. Irastorza et al. JCAP 01 033 (2016)
Gaseous He, Ar, Xe, CF4 in Migdal Effect searches
  D. Yi et al. Nature 649, 580–583 (2026)
  H.M. Araújo et al. (MIGDAL collaboration), Astropart. Phys. 151 102853 (2023)
  K.D. Nakamura et al. PTEP 1 013C01 (2021)
Gaseous Ar in collider-based neutrino experiments
  R.M. Amarinei, et al. JINST 18 P12001 (2023)
  A. Abed Abud, et al. (2022) arXiv:2203.06281
And the list goes on…
Far from a comprehensive list…

## Slide 4: Negative Ion Drift Low-Pressure Gas TPCs
Amplification Plane
Cathode
+V
-V
(2) Ionization electrons are captured according to
forming negative ions
(1) Recoiling particle ionizes gas creating track
(3) As charge cloud drifts, it is diffused with a characteristic
(4) In order to amplify, the ions must be stripped of their electrons
(5) Resulting track is read out via optical or charge readout
Lower diffusion
Longer Tracks
Better Directional Resolution

## Slide 5: Advantages of Negative Ion Drift (NID)
CF4
CF4+CS2
CF4
CF4+CS2
Gains for these tracks are on the order of 105!
Notes: Comparable gas gains but the light is lower so the G is a good estimate using two gGEMs like in MIGDAL ** mention MPII

## Slide 6: Thermal Drift
At low electric fields, ions are nearly in thermal equilibrium with the gas. As a consequence:
  Diffusion width evolves according to the following
  Mobility is constant with E/P
At higher fields (i.e. more energetic systems):
  Mobility and diffusion are larger at higher fields
  Diffusion becomes axially dependent
= drift velocity, = mobility, = Electric Field, = ion charge, = thermal energy, = drift length, = diffusion width
Electric Field
σ
E-field
Plots created using desmos.com

## Slide 7: Optimizing/Testing Different Gas Mixtures
GOAL: Explore gas mixtures with high quantities of the target gas maintaining negative ion benefits
Target Gases: Xe, Ar, He, CF4 NID gases: SF6 and CS2
  Of interest to Migdal searches, Directional Dark Matter searches, Neutrino Studies, etc
Properties of interest for Noble Gas NID TPCs:
  Diffusion = Track broadening from stochastic motion within the gas  NID is narrower
  Mobility = Proportionality constant between drift velocity and field  NID is slower
  Gain = Stable operation and amplification capability  electron stripping is required for avalanche amplification in NID but NID gases increase stability
  Attachment Length = Mean distance before electrons are captured in the gas  Must have short attachment length

## Slide 8: The Detector
N.S. Phan et al 2017 JINST 12 P02012
** THGEM we used is 400 um thick and has 10x10 cm active area, a pitch of 0.5mm, and a hole diameter of 0.3mm
**

## Slide 9: Relative Gains
Peak lies at 5.9 keV
Strongly electronegative SF6 and CS2 ions must be stripped before amplification
CS2-based mixtures had higher gains, in general, than SF6-based mixtures
20% for CS2 and 25% for SF6
Stable operation resolving 5.9 keV peak from 55Fe with as little as 3 Torr SF6 and 5 Torr CS2!
All numbers in labels are in Torr
All numbers in labels are in Torr
Notes: Pitch 0.5mm hole diam 0.3mm

## Slide 10: Laser-based Measurements
60 cm
55Fe
N2
RFI Signal induced by Laser firing  t0
Signal from charge cloud  ta
Current [au]
19+1 Torr Xe+SF6
SF5-
SF6-

## Slide 11: Mobility
  N and No are gas density in detector and at STP, vd is drift velocity, E is Electric Field
Mobilities are roughly 2 orders of magnitude lower than in the pure noble gases
Many minority species were noted with mobilities around ~10-20% of the primary species
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED* () | NID ()
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Preliminary
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/

## Slide 12: Mobility
  N and No are gas density in detector and at STP, vd is drift velocity, E is Electric Field
Mobilities are roughly 2 orders of magnitude lower than in the pure noble gases
Many minority species were noted with mobilities around ~10-20% of the primary species
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED* () | NID ()
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Mobility at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 188 | 0.77
Ar | 50 | 325 | 1.64
He | 200 | 796 | 9.03
Preliminary
12
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/

## Slide 13: Waveform Shape
Fitting Functions Used to model Diffusion width, σ (and attachment length, λ = 1/L)
Gaussian:
Exponentially Modified Gaussian:
Step + Gaussian:
Current [au]
Current [au]
Current [au]

## Slide 14: Longitudinal Diffusion
  D’L is longitudinal diffusion coefficient used by Garfield and Magboltz. It relates to the normal Diffusion coefficient, D, by
Diffusion can be suppressed by ~ an order of magnitude with as little as 1 Torr SF6 or 5 Torr CS2
In many cases it’s nearly thermal!
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED D’long* () | NI D’long ()
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
14
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/
Preliminary

## Slide 15: Attachment Length in CS2 Mixtures
Attachment could only be measured in a subset of the data
CS2 + Ar and CF4 mixtures had large attachment lengths!
Consequences of high attachment for tracking detectors:
Exponentially modified waveforms along drift axis
“Mixed Drift” waveforms if drift length too short
  Leads to waveform distortion
  Leads to mixed gain for ED and NID components of the waveform
Preliminary

## Slide 16: Conclusions
Negative ion drift properties in mixtures of Xe, Ar, He, and CF4 with either SF6 or CS2 have been measured with very low partial pressures of the NID component
Stable gain for Fe-55 peak noted in many of the mixtures
Diffusion was suppressed by ~1 order of magnitude
Mobility was slowed by 2 orders of magnitude
In some cases, attachment length could also be measured!
Special thanks to my collaborators on this project:
Dinesh Loomba and Drew Gibson and the UNM group
Fermilab/DOE
GIRA Award
Awarded to E.Tilly
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) | ED D’long* () | NI D’long ()
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
Diffusion Coefficient at 600 V/cm and 3 Torr SF6 |  |  | 
Gas | Ptotal (Torr) |  | 
Xe | 20 | 941 | 165
Ar | 50 | 1143 | 154
He | 200 | 1063 | ~77
* S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/

## Slide 17: Backups

## Slide 18: Notable Papers Regarding NID
C.J. Martoff et al 2000 NIMA 440 335 (https://doi.org/10.1016/S0168-9002(99)00955-9)
  The original NID Paper
N.S. Phan et al 2017 JINST 12 P02012 (https://doi.org/10.1088/1748-0221/12/02/P02012)
  Established SF6 as an ideal NID gas
J.B.R. Battat et al 2017 AstroPart Phys 91 65 (https://doi.org/10.1016/j.astropartphys.2017.03.007)
  DRIFT Experiment results using minority NI species to fiducialize leading to 54 day zero-background run

## Slide 19: The Future of these studies
Paper coming soon!
Development of a novel low-pressure NI TPC
  10cm x 10cm 2D strips at 200 μm pitch
    Gas Electron Multiplier (GEM) at 140 μm pitch to amplify the signal from the tracks
  Front-end electronics assembled, adapted, tested and characterized with collaborators at Boston University
Alex Madorsky
Lila Smith
Ed Kearns

## Slide 20: Light Yield in NID
Courtesy of D. Loomba RD51 Collab. Meeting 6/14/22

## Slide 21: Minority Species Area
Preliminary
Charge Ratio is defined as the area under the minority peak divided by the area under the primary peak

## Slide 22: Measuring Electron Energy
Under a very simple assumption:
We can use the area ratios to get approximate electron energies (pre-capture)
  Note: different electronegativities mean these two species probably have different gains
    Thus, this is more likely an upper limit on the energy
Preliminary

## Slide 23: Dealing with Water
Small amounts of water in detector lead to ‘water-shelves’ on left side of waveform
Compromises measurement of minority area and diffusion sigma of main peak
Include 1 or 2 step functions in fit:
  For minority area:
  For main peak diffusion:

## Slide 24: Exponentially Modified Gaussian
λ = mean free path of attachment (i.e. attachment length)
σ = diffusion
Fit Residuals
Fits well at all measured
Has a fairly small ‘good-fit’ region

## Slide 25: Negative Ion Species Cross Sections
Standard capture and dissociation process for SF6:
Standard dissociation processes for CF4:
CS2 likely forms NI in a similar process as SF6.
I. Iga, M. V. V. S. Rao, S. K. Srivastava, and J. E. Nogueira, Z. Phys. D 24, 111 (1992).
L. G. Christophorou, J. K. Olthoff, Int. J. of Mass Spectrom. 205 (1) 27–41 (2001)

## Slide 26: Select Averaged Waveforms with Attachment
40 + 10 Torr Ar + CS2
40 + 5 Torr CF4 + CS2

## Slide 27: Energy Resolution
Preliminary
Preliminary

## Slide 28: Aside: Attachment in CF4
By measuring the exponential portion of the waveform, we reconstruct measured attachment to within 80%
L. G. Christophorou, J. K. Olthoff, M. V. Rao, J. Phys. Chem. Ref. Data 25, 1341–1388 (1996)
S. Biagi (1995). https://magboltz.web.cern.ch/magboltz/
Preliminary
Preliminary

## Slide 29: Bridging the Gap Between Exponential Fit and EMG
Exponential fits on CF4 waveforms reproduced Christophorou’s recommended attachment length to within 8%
Measurements made in Ar+CS2 found very good agreement between exponential and EMG fits 
EMG fits were chosen instead of exponential fits in order to measure both attachment and diffusion width
  Exponential fits could not be verified on waveforms with
    This region falls roughly in our EMG ‘good-fit’ region, thus it was straightforward to use EMG results