## Slide 1: 4D Fabric: a NIFTY solution to 4D Pixel Detectors
21.10.26
Timon Heim, Graham Anderson, Rebecca Carney, Caleb Ceravolo (UW), Maurice Garcia-Sciveres, Deion Fellers, Alexis Mulski - LBNL

## Slide 2
CPAD 2026
Drivers
Goal: develop 4D Pixel detector readout chip technology
Aiming to add O(50ps) timing precision to Pixel detectors
Leverage work done in LDRD in FY22/23, specifically Big Rock AFE
Exploring collaboration with SLAC/FNAL
Co-design with detector simulation -> directly understand physics performance impact
  ECRP (FY26-FY30)
Goal: develop Pixel detector readout chip technology with on-chip intelligent networks
Improve on classic column based readout by implementing mesh networking
Emerging intelligence from simple routing rule set
Looking for scalable architecture to full reticule size or even to wafer level
  NIFTY (FY26-FY28)
Goal: develop Pixel detector readout chip technology suitable for direct deposition of thin film sensors
Awards 28nm shuttle run in December 2026
4mm by 4mm size
Can receive full 12” wafers
Enables: industrialization of process at wafer scale
  CMOS + X

## Slide 3
CPAD 2026
The Compromise
Removal of high precision timing removes major analog work not feasible before Dec 2026
Digital-on-top design flow is foundation to all future developments
Emphasis on scalable and modular digital architecture to serve future chip versions and increase design iteration speed
Goal: develop a Pixel detector readout chip in 28nm CMOS for a December 2026 submission
4mm by 4mm chip size, 50um by 50um pixel pitch -> 64 x 64 pixel matrix
No high-precision timing, no TDC -> 25ns time stamp but using high speed AFE
Pixel Matrix organized in 8 x 8 pixel cores, cores organized in network mesh, cores flat synthesized as digital sea with analog islands
Triggered readout with up to 40MHz trigger rate (streaming), ~12us buffering
Digital-on-top design flow, verification with cocoTB, co-design against ATLAS ITK and MAIA (Muon collider) simulation
  4D Fabric - Chip “PixCanvas”

## Slide 4
CPAD 2026
Traditional Readout Architecture
Pixel Matrix organized in columns of Cores (8x8 pixels) (e.g ITkPix is 48 by 50 cores)
Cores interconnected only within column (up/down)
One shared column bus for data transmission to end-of-column buffer
Token bus to arbitrate usage of column bus and return of token signals all hits from one event have been read
One core column processes only one trigger at a time in chronological order, different core columns can work on different triggers
2-stage Core column concentrator reads events in order from end-of-column buffer -> event building
Pro: highly optimized, low latency data transfer, built-in event building
Con: single point failure can affect large number of pixels, no load balancing
…

## Slide 5
CPAD 2026
NIFTY Architecture
Cores connected in 2D Mesh (shown here NSEW mesh)
End-of-column concentrators become the “root” of the network, cores try to route data towards any root
EOC concentrators are followed by a fully connected layer to events buffers
  We are evaluating if need intermediate laters for routing or timing reasons
Each event buffer collects data from one specific time-slice as informed by the trigger table
Event buffers are each connected to their own data output
Configuration is injected at the root level by the config generator
Trigger
Table
EOC
Concentrator
Event Buffer
Networked
Core Matrix
8x8
Config
Generator

## Slide 6
CPAD 2026
Core Block Diagram
RD53 Core Layer
8x8 Pixel Digital Core
4 Pixel Region
2x2 Analog Front-End
ToT Memory
4x LE
4x TE
Timestamp Memory
16x
Data
Readout
Control
Rd Token
+ Trig ID
+ Timestamp
Rd Token
Trig ID
Timestamp
Stripped digital Core from RD53 - ITkPixV2
ToT of Hits is saved with associated timestamp
Trigger of timestamp marks data to be readout
16 x 4 Pixel Regions read out through common data bus arbitrated through token
2x2 Analog Island
50um x 50um pitch
Original RD53 Layout, PixCanvas Analog Island size might vary
Flat synthesized
Digital logic
400um
400um
Analog Front-End design from Pebbles chip, see talk about it at CPAD 2023!

## Slide 7
CPAD 2026
Core Block Diagram
RD53 Core Layer
Trig ID
Timestamp
Network Core
Data from RD53 Core
Data from NSEW Neighbors
Data to NSEW Neighbors
Crossbar
Memory
(5 deep)
Arbiter
Router
Status Info from NSEW Neighbors
Network Core interfaces with NSEW Neighbors
Can receive data on all edges at the same time
  Underlying RD53 core acts as 5th input
Send data only on one edge at a time
Interface is bidirectional, S & W operate in positive edge domain, while N & E operate in negative edge domain
Memory acts as FIFO
Router contains intelligence to know where to route data, receives status info (e.g. buffer fill status, data acknowledge) of neighboring cores
  Performs failure detection of neighbors
Configuration also received via network
Data contains some information related to routing to avoid loops
Overall goal: make core as autonomous as possible, to avoid single core malfunction from impacting others
Config
Trigger Queue

## Slide 8
CPAD 2026
Toy Sim
Sources: random, ATLAS ITk simulation, MAIA simulation
One data packet loaded into network layer per cycle (packet can hold up to 4 pixel hits)
Emulating triggering by random sampling
  Data Generation
Each Core can transmit one data packet on one edge each cycle
Each can receive from all incoming edges (including its own pixels) at the same time
No back-pressure mechanism, data is simply dropped if network buffer overflows
Each Core has finite memory
  Networking
Each Core has an individual router
Router decides on which edge to transmit data for every cycle
Router knows which edges have smaller, larger, or equal distance to the root nodes
Router has information about buffer status from connected nodes
  Routing
Play with it yourself:
https://nifty.lbl.gov/www/simulation/
Can simulate static failures and temporary failures
Any data routed into a failed core will be dropped
Data generated in failed core not counted
  Failures
Simulation written in such a way that we can optimize each component with machine learning
Currently though: fixed a lot of parameters to reduce phase space
Some constraints from physical layout
  Optimization
Framework also used for NIFTY-LArPix development! See talk by Rebecca and poster by Deion!

## Slide 9
CPAD 2026
Heat Map: Data Generated
ATLAS ITk Layer 0 u=200
No global structure, random
Can contain some structure at pixel level (clustering)
Only simulate “triggered” data, random trigger with configurable average frequency
  ATLAS Data
No global structure, random
Can contain some structure at pixel level (clustering)
Only simulate “triggered” data, random trigger with configurable average frequency
  Future Collider Data

## Slide 10
CPAD 2026
Topology Choice
  2D Mesh
  Diagonal Mesh
  Hexagonal Mesh
  Octagonal Mesh

## Slide 11
CPAD 2026
Heat Maps
  2D Mesh
  Diagonal Mesh
  Hexagonal Mesh
  Octagonal Mesh

## Slide 12
CPAD 2026
Topology Comparison

## Slide 13
CPAD 2026
Heat Maps II
No static failures

## Slide 14
CPAD 2026
Heat Maps III
15% static failure (beige cores)

## Slide 15
CPAD 2026
Heat Maps IV
15% static failure (beige cores)

## Slide 16
CPAD 2026
Core Tiling and Topology
Real estate for core interconnects limited by overlap. Interconnect density limited
2D Mesh topology:
Idea for hex topology:
Only half or less the space available for interconnects
Less space for network connections might be ok, as we have to send additional signal vertically!
Core needs to build around analog pixel island (2x2). Other than square geometry could be possible but might come at cost of routing density

## Slide 17
CPAD 2026
Core RTL Status
Have rudimentary Networked Core written in RTL and interfaced with stripped RD53 core
Writing verification at the same time as developing RTL
Full verification run as part of CI, produces automatic coverage reports* and documents RTL hierarchy
Some issues trying to accelerate simulation with e.g. ventilator due to aggressive clock gating to reduce power
3x3 Core simulation still runs fast enough to for CI (O(min)), while larger networks are feasible for milestones
Current focus: transition from open source tooling (Icarus) to licensed tools (Questasim) to generate better coverage reports & integrate design in digital-on-top flow
RTL GitLab Page:
Automatic generation of documentation, verification, and reports through continuous integration
Core 1
Core 2
Core 3

## Slide 18
CPAD 2026
End of Chip Logic - Event Building
One per core column
Pushes data to intermediate layer depending on Trigger ID
  Roots
Concentrates data from specific trigger ID
Memory depth will depend on number of event buffers and Clk speed
Could have multiple layers if intermediate buffers to overcome routing/timing constraints
  Intermediate Layer
At time of trigger is assigned an event ID (specific trigger time)
Only collects data from that specific event ID
Event is considered complete, after no data has been received for X number of cycles
Data for events that cannot be assigned an event buffer will be dropped
  Event Buffer
Time to wait after last data fragment has been received:
Total time to collect event:
Exact number of concentrators, intermediate layers, and event buffers depends on expected hit rate and wanted trigger rate.
RTL should be parametric to adapt/scale easily!
Push
Event
Buffer
Event
Buffer
Push
Pull
Round-Robin
Trigger
Table
Intermediate
Event Buffer
N-deep
1-deep
N = number of
EOC concentrators

## Slide 19
CPAD 2026
Summary & Plans
4D Fabric project aims to ultimately develop fully fletches 4D Pixel detector technology
Intermediate stepping stone: PixCanvas chip to build scalable digital architecture for pixel readout chips → the “fabric”
Toy simulation framework helped guiding design choices or clearly points towards potential future improvements
RTL and verification are progressing well → Now have enough meat to tackle digital-on-top design flow
Analog designs to be leveraged from past 28nm submission
  Recently started working on adding new analog elements (Bias DACs) with University of Hawaii
December 2026 submission will be tight, but does not seem completely unreasonable … stay tuned
Next iteration will aim at adding high precision timing into the design → add the “4D” to the “fabric”
  Will need to tackle some major challenges, but network topology also opens new opportunities
Special shoutout to Graham and Caleb who did most of this work during a SULI internship and will continue as undergraduate researchers:
Poster by Caleb

## Slide 20
Backup
CPAD 2026

## Slide 21
CPAD 2026
The Overarching Goal
High temporal resolution (<30ps)
High spatial resolution (<25um)
99% detection efficiency
Low Power/Low Mass
Extreme readout bandwidth
On-chip data processing
Extreme radiation tolerance
Wafer-scale detectors
  4D Pixel Detectors
  for next-gen Colliders
Scalable Network
Architecture
Digital-on-top
Design Flow
PixCanvas
…
Thin Film
Sensors
TBD
On-chip
PLL
TDC
System
Integration
4D
Analog Front-End
28nm CMOS
Pebbles/
Metarock
I/O Drivers
On-chip
Bias Generation

## Slide 22
CPAD 2026
Router Optimization
Ranks edges by score, picks the lowest score
Score = distance to root + buffer status
  Simple Router
Ranks edges by score, picks the lowest score
Score = distance to root + W * buffer status
Weight W to be optimized
  Smart Router

## Slide 23
CPAD 2026
Topology Comparison II
# of cycles from data entering network smaller = better
Sigma of number of packets routed by each root
smaller = better
Number of packets routed out / total number of packets higher = better
# of cycles from data entering network minus min. Number of hops
smaller = better
Gen period -> smaller = more data

## Slide 24
CPAD 2026
Topology Comparison III
# of cycles from data entering network smaller = better
Sigma of number of packets routed by each root
smaller = better
Number of packets routed out / total number of packets higher = better
# of cycles from data entering network minus min. Number of hops
smaller = better

## Slide 25
CPAD 2026
Failure Detection
To reduce logic/power use data to test neighboring cores
Means protection cannot be perfect, but identification circuit becomes trivial
Core B “acknowledge” transmission of data to the original source of the data Core A, if Core A does not receive acknowledgment -> disables transmission to Core B for some period of time
Tests for multiple failures at the same time:
  Data from Core A does not arrive in Core B
  Core B does not save data correctly
  Core B is “noisy” and flooded with other data
  Core B cannot send data onwards
  How to identify dynamic failures?
Single Event Effects (SEE) can upset logic and cause abnormal behavior until reset
Physical damage to chip can manifest in temporary failures lasting from single event to failed until reset
  Source of temporary failures?
Core A
Core B
Data is generated in Core A
Core A routes Data to Core B
Core A starts countdown timer, Core B saves data
Core B routes data to next core & sends acknowledge to Core A
Core A receives acknowledgment in time and edge to Core B stays enables

## Slide 26
CPAD 2026
Failure Detection
To reduce logic/power use data to test neighboring cores
Means protection cannot be perfect, but identification circuit becomes trivial
Core B “acknowledge” transmission of data to the original source of the data Core A, if Core A does not receive acknowledgment -> disables transmission to Core B for some period of time
Tests for multiple failures at the same time:
  Data from Core A does not arrive in Core B
  Core B does not save data correctly
  Core B is “noisy” and flooded with other data
  Core B cannot send data onwards
  How to identify dynamic failures?
Single Event Effects (SEE) can upset logic and cause abnormal behavior until reset
Physical damage to chip can manifest in temporary failures lasting from single event to failed until reset
  Source of temporary failures?
Core A
Core B
Data is generated in Core A
Core A routes Data to Core B
Core A starts countdown timer, Core B saves data
Core B routes data to next core & sends acknowledge to Core A
Core A receives acknowledgment in time and edge to Core B stays enables

## Slide 27
CPAD 2026
Failure Detection
To reduce logic/power use data to test neighboring cores
Means protection cannot be perfect, but identification circuit becomes trivial
Core B “acknowledge” transmission of data to the original source of the data Core A, if Core A does not receive acknowledgment -> disables transmission to Core B for some period of time
Tests for multiple failures at the same time:
  Data from Core A does not arrive in Core B
  Core B does not save data correctly
  Core B is “noisy” and flooded with other data
  Core B cannot send data onwards
  How to identify dynamic failures?
Single Event Effects (SEE) can upset logic and cause abnormal behavior until reset
Physical damage to chip can manifest in temporary failures lasting from single event to failed until reset
  Source of temporary failures?
Core A
Core B
Data is generated in Core A
Core A routes Data to Core B
Core A starts countdown timer, Core B saves data
Core B routes data to next core & sends acknowledge to Core A
Core A receives acknowledgment in time and edge to Core B stays enables

## Slide 28
CPAD 2026
Failure Detection
To reduce logic/power use data to test neighboring cores
Means protection cannot be perfect, but identification circuit becomes trivial
Core B “acknowledge” transmission of data to the original source of the data Core A, if Core A does not receive acknowledgment -> disables transmission to Core B for some period of time
Tests for multiple failures at the same time:
  Data from Core A does not arrive in Core B
  Core B does not save data correctly
  Core B is “noisy” and flooded with other data
  Core B cannot send data onwards
  How to identify dynamic failures?
Single Event Effects (SEE) can upset logic and cause abnormal behavior until reset
Physical damage to chip can manifest in temporary failures lasting from single event to failed until reset
  Source of temporary failures?
Core A
Core B
Data is generated in Core A
Core A routes Data to Core B
Core A starts countdown timer, Core B saves data
Core B routes data to next core & sends acknowledge to Core A
Core A receives acknowledgment in time and edge to Core B stays enables

## Slide 29
CPAD 2026
Failure Detection
To reduce logic/power use data to test neighboring cores
Means protection cannot be perfect, but identification circuit becomes trivial
Core B “acknowledge” transmission of data to the original source of the data Core A, if Core A does not receive acknowledgment -> disables transmission to Core B for some period of time
Tests for multiple failures at the same time:
  Data from Core A does not arrive in Core B
  Core B does not save data correctly
  Core B is “noisy” and flooded with other data
  Core B cannot send data onwards
  How to identify dynamic failures?
Single Event Effects (SEE) can upset logic and cause abnormal behavior until reset
Physical damage to chip can manifest in temporary failures lasting from single event to failed until reset
  Source of temporary failures?
Data is generated in Core A
Core A routes Data to Core B
Core A starts countdown timer, Core B saves data
Core B routes data to next core & sends acknowledge to Core A
Core A receives acknowledgment in time and edge to Core B stays enables
Core A
Core B

## Slide 30
CPAD 2026
Expanding into the 4th Dimension
Skipping high timing precision is necessary to accommodate tight submission deadline
But once digital architecture has been put together and digital-on-top flow been exercised should have a great foundation to expand into 4th dimension
We want to keep focussing on the digital architecture and use the new network architecture to enable features not easily possible in traditional readout
  “Sub-event” building: data could be sorted by time in smaller increments than bunch crossings -> Some time slices should be more interesting than others (e.g. at Muon Collider), also serves as type of compression
  Data prioritization: could teach Router for favor some data over other data in case bandwidth is limited, e.g. via a cluster shape based analysis that could distinguish signal from background
  Adaptive synchronization: in case a global detector synchronization to O(30ps) is not easily achievable, each chip could try to “re-time” itself based on information from its own data or neighbors

## Slide 31
CPAD 2026
CMOS + X
https://nw-ai-hub.org/sites/default/files/media/file/28nmshuttle-townhall-webinar-slides-mar-2026.pdf

## Slide 32
CPAD 2026
Digital-on-top Design Flow

## Slide 33
CPAD 2026
RD53 Readout Architecture

## Slide 34
CPAD 2026
Title Text

## Slide 35
CPAD 2026
Film on Readout Chip
Goal: deposit sensor material onto CMOS Pixel readout chip to enable low mass and highly scalable Pixel detectors
Allows independent readout chip and sensors development
LDRD in FY24/25 to investigate thin film sensors using facilities available at LBNL:
  Semiconductor Detector Lab (SDL)
  Molecular Foundry
  UC Berkeley Nanolab
Primary sensor materials investigated:
  a-Si: known caveats but should yield functioning detector
  IGZO (Indium Gallium Zinc Oxide): very high electron mobility and can theoretically yield equivalent amount of electron/hole pairs than crystalline silicon
  Film on Readout Chip (FORC)
Three prong investigation:
  1. Identify suitable materials and understand required processing/stackup
  2. Understand and test constraints of direct deposition on CMOS chips
  3. Test industrialization and scalability of process
Do currently not have functioning prototype
Had to learn a lot of material science, many of steps we want to do are unorthodox (>1um thick layers, substrates, deposition constraints)
Very close to hopefully first working a-Si prototype
Some more work needed for IGZO due to more complicated material stackup/processing
  Status