## Slide 1: In-pixel machine learning in the presence of silicon detector noise By: Ben Weiss on behalf of the Smartpixels group Cornell University – bw539@cornell.edu
CPAD – 21 October 2026
Notes: Funding Acknowledgement?

## Slide 2: Pixel Granularity VS Data-rate
Si-pixel tracking in high–luminosity colliders requires
ultra-high resolution that strains bandwidth
Intelligent front-ends relieve the burden
on triggers downstream by beginning
reconstruction at the source
FCC-hh:
Muon Collider:
Notes: Event display pic HL LHC Muon collider ED, include lindsey slide 2 in backup at least

## Slide 3: Enter Smartpixels!
Smartpixels goal: embed small NNs on Si-pixel ASIC readout chips that perform pre-trigger data refinement at the collision rate.
pT filtering and regression of track geometry from a single Si-layer
  Advantage: track parameter readout does not scale with granularity!
Extreme-edge implementation targeting CMS Phase 3 conditions
SmartPix ROC bonded to pixel
Digital NN
Analog readout
Predictions:
- High vs. low pt?
- Hit position
- Track angle
Pixelated charge
L1 Trigger
@ 40 MHz

## Slide 4: Smartpixels Datasets
Incident pion kinematics taken from real CMS data. Sensor charge collection simulated with PixelAV.
16x16 pixel array
50µm x 12.5µm pixel pitch
20 timesteps (200ps appart)
Subset available on Zenodo
500k-4M events/dataset
Dataset production work by Danush Shekar, Morris Swartz
π
Si
Pixels

## Slide 5: Noise in a Si-pixel frontend
Raw charge + σN = 80e Noise
Si-pixel noise sources include thermal excitations, leakage current, irradiation…
This study assumes noise sampled from gaussian with µ=0, σ=σN
Detailed simulation of FE response presented in Harshul Gupta’s talk
Simulated irradiation studied in SmartPixels filter.
Standard denoising approach:
impose a 3-5σN threshold
Noise estimated in https://arxiv.org/pdf/2510.07485
TNo Noise =
[0, 30, 845]
T80e Noise =
[248, 668, 1663]
Last TS First TS
Estimated noise contributions |  |  | 
σTh | ENC | ENC w/ 0.5 GRad | Total σN
45e | 40e | 55e | ~78e
Notes: Enc is 55 without radiation at -40c (Sec. 4.4)

## Slide 6: 3 regression algorithms considered
Increasing # of operations
Latent Space
<4x4x5>
Seperable Conv2D
Conv2D
Latent Space
<20x64>
Large MLP
Small MLP
x Proj.
y Proj.
Dense
Dense
2D images
Latent Space
<16>
Small MLP
Multi-head Attention
X 4
Patch Encoder
SlimMLP
Params: 2,179
HLS: 0.34 mm2
SlimConv2D
Params: 1,682
HLS: 0.28 mm2
Transformer Params: 705K
Output: {x,y,β}
Output: {x,y,β}
Output: {x,y,ɑ,β}+10 Covariances
2D images
2D images
MLP
Encoder Network
Dencoder Network
Notes: Switch graphic to include transformer

## Slide 7: Regression in the presence of noise
Base deployable network performance competes with non-ML techniques but both fail with a small amount of injected noise
Retraining with noise recovers performance but barely reaching sub-pixel accuracy
Networks here use ADC thresholds assuming no noise… Can we optimize these?
Base performance
Retraining with noise
x pitch
y pitch

## Slide 8: Soft Quantization: Optimize FE in training
Choice of 2-bit ADC thresholds matters! Treat these as trainable parameters.
First network layer: Smooth step function with trainable step location.
Annealed slowly for optimization stability
SQ Technique and animation by Arghya Das https://arxiv.org/abs/2602.15946v3

## Slide 9: SQ thresholds and regression results
Soft Quantization naturally sets the lowest threshold to roughly 3xσN
SQ drastically improves regression performance
Can we go further?
  Can charge information
bellow σN be reintroduced by denoising?
Threshold 0
Threshold 1
Threshold 2
SQ improves regression
x pitch
y pitch

## Slide 10: In pixel denoising
Denoising Goal: recover the cluster shape according to σN = 0 thresholds.
Raw charge collected +noise
Denoised 2-bit image
w/ Th(σN =0e):
[0e, 30e, 845e]
Denoise & digitize

## Slide 11: In pixel denoising – SQAutoEncoder
1. Train each encoder to denoise using an AutoEncoder architecture
LS
Soft Quant.
Raw charge collected + σN noise
Classification
Encoder
Large Decoder
Denoised 2-bit image
w/ Th(σN =0e):
[0e, 30e, 845e]

## Slide 12: In pixel denoising – SQAutoEncoder
1. Train each encoder to denoise using an AutoEncoder architecture
LS
Soft Quant.
Raw charge collected +noise
Classification
MLP
x, y, β
Soft Quant.
Encoder
LS
Encoder
Large Decoder
2. Freeze the encoder
and retrain the
regression MLP
The MLP now operates on a LS rich with charge shape information below σN!
Denoised 2-bit image
w/ Th(σN =0e):
[0e, 30e, 845e]

## Slide 13: SQAutoEncoder Pixel Categorization accuracy
All SQ AutoEncoder architectures achieve high denoised pixel categorization accuracy, even well bellow σN
Note: 90% of denoised pixels are 00
Comparison to accuracy with standard digitization scheme in backup!

## Slide 14: SQAutoEncoder: Denoising and regression
So, can we go further?
A little bit, but only with a more complex on-chip algorithm
SlimMLP performance degrades with SQAutoEncoder
  Denoising may shift the learning objective too far from the regression task
  Future work: multi-objective training

## Slide 15: Conclusions
Si-Pixel detector noise degrades on-ASIC ML track parameter regression, but performance is recoverable with ML tricks.
Intelligent front-ends offers a route towards tracking in HL environments.
Even a simple noise model on a Si-AFE destroys track geometry predictions.
Retraining the on-chip network improves performance. Optimizing ADC thresholds in the training loop helps even more.
It is possible to further improve regression using a denoising autoencoder to enrich some network layers with information below the noise floor.
  Currently this technique only works with a more sophisticated network on-chip.

## Slide 16: The Smartpixels group!
Fermi National Accelerator Laboratory: Abhijith Gandrakota, Benjamin Parpillon, Chinar Syal, Douglas Berry, Farah Fahim, Gauri Pradhan, Giuseppe Di Guglielmo, James Hirschauer, Jennet Dickinson, Lindsey Gray, Nhan Tran, Ron Lipton
Cornell University: Jennet Dickinson, Ben Weiss
Johns Hopkins University: Dahai Wen, Morris Swartz, Petra Maksimovic
Northeastern University: Nick Manganelli
Northwestern University: Manuel Blanco Valentin
Oak Ridge National Laboratory: Aaron Young, Shruti R. Kulkarni
Purdue University: Mia Liu, Arghya Das
University of Chicago: Karri DiPetrillo, Carissa Kumar, Emily Pan, Rachel Kovach-Fuentes, Aidan Nicholas, Eliza Howard, Eric You
University of Colorado Boulder: Jannicke Pearkes, Ricardo Silvestre
University of Illinois Chicago: Corrinne Mills, Danush Shekar, Jieun Yoo, Mohammad Abrar Wadud
University of Illinois Urbana-Champaign: Mark S. Neubauer, David Jiang
University of Kansas: Alice Bean

## Slide 17: SQAutoEncoders (MLP, Conv2D, XFormer)
Given a cluster with 80e gauss. noise added, how well can each model predict denosied pixel values
Average pixel categorization accuracy
Denoised pixel values defined by Xformer optimized SQ thresholds with no added noise:
  TIdeal = [0e, 30e, 845e]
  TReal = [231e, 637e, 1592e]\

## Slide 18: Non-ML performance
Using 80e thresholds ->
(but SQ ML models)
Optimized thresholds -> by noise

## Slide 19: ASIC synthesis
Established pipeline to translate quantized python level model to RTL design
hls4ml converts QKeras model to C++
Catapult HLS converts C++ to RTL
Estimates model footprint (mm2), power consumption
Feedback for python optmization
Full precision Python model
QKeras: quantized model
hls4ml:
C++
CatapultHLS:
RTL design
Tapeout!
Credit: Giuseppe Di Guglielmo

## Slide 22: Filtering algorithm
Classifies high vs low momentum particles with ~0.2 GeV threshold
13x21 pixel array with 2-bit quantization on front end charge
Dense network trained on y-projection of charge cluster images
4 Bit quantization of weights & biases
Credit: Jieun Yoo et al 2024. https://doi.org/10.1088/2632-2153/ad6a00
input (14) <2>
Notes: Geometry and irradiation comparisons from danush?

## Slide 23: Filtering algorithm performance
Credit: Danush Shekar, Jennet Dickinson
Retrainable to endure irradiation:
%
%
Multiple geometries (0.2 GeV thresh.):
Notes: Highlight reprogramability

## Slide 24: New Prototype SmartPixels ROIC
Newest Smartpixels TSMC 28 nm chip hosts per-pixel charge injection and programmable network for classifier.
2 sets of 8x32 pixel arrays (2 ADC vers.)
ADC+DNN consumes ~6 µW/pixel @ 40 MS/s
Credit: Benjamin Parpillon, Anthony Badea
Spec. | Value | Units
Parameters | 4652 | w+b
DNN+ADC area | ~0.2 | mm2
Total area | ~1.6 | mm2
Clock frequency | 40 | MHz
Latency | 50 | ns
1mm
ADC v1
ADC v2
Notes: Power consumption assumes 1hit/mm^2, within 1mW/cm^2 budget 1.6 mm2 ASIC chip. A TSMC CMOS 28

## Slide 25: Chip testing efforts
FPGA based setup to communicate with the smartpixels ROIC
Spacely+Caribou+Peary
ASIC on eval. board
Test routines developed to measure:
Power consumption
Pixel S-curves
DNN programing/ predictions on chip
Credit: Benjamin Parpillon, Anthony Badea
True pT [GeV]
Fraction predicted high pT (>0.2GeV)
Notes: Ask anthony about turn on curve!!!

## Slide 26: Regression Alg. design space exploration
Current development to reduce model size for hardware implementation
On ASIC, generally:
Conv2D>Conv1D>Dense
Reducing # of operations

## Slide 28: Regression ROIC synthesis estimates

## Slide 29: Data rates at the LHC
Compact Muon Solenoid (CMS) Pixel detector
~Raw O(TB/s)
YouTube’s total average streaming data rate*
~O(TB/s)
*Very rough estimate, YouTube streams ~60B hrs/year
Triggers
HL LHC: 5x data rate
≈
!!!