## Slide 1: ADMX Overview and Run Status
On Kim
University of Washington
CPAD 2026 Workshop
October 21st, 2026

## Slide 2
Dark Matter
(inferred)
Matter
Image: NASA, ESA, CSA, STScI, CXC; Science: James Jee (Yonsei University, UC Davis), Sangjun Cha (Yonsei University), Kyle Finner (Caltech/IPAC)
Dark Matter Problem
Strong Problem
Neutron
10 orders of magnitude!
Electric dipole moment
Axion

## Slide 3: Axion–Photon Coupling
Axion decays into two photons:
For a μeV-scale QCD axion, spontaneous two-photon decay lifetime is far longer than the age of the Universe.

## Slide 4: Axion–Photon Coupling
Instead, we can convert axions into photons in a strong static magnetic field.
x
External static magnetic field
Inverse Primakoff process

## Slide 5: Microwave Cavity Haloscope
A high-Q microwave cavity resonantly enhances axion–photon conversion [PRL 51,1415 (1983)].
Since we don’t know the axion mass a priori, the cavity must be tunable.
x
Tuning rod

## Slide 6
7.6 T magnet with a roughly 0.6 m bore diameter, 1 MJ stored energy.
ADMX “insert”
Cavity and tuning rod

## Slide 7: Parameter Space
(ADMX) PRL 135, 191001 (2025)
is axion–photon coupling constant.
Benchmark QCD axion models: KSVZ and DFSZ.
Current physics target: achieve DFSZ sensitivity for about 1.0–1.4 GHz range.
To reach the DFSZ sensitivity, we must know the signal power and noise fluctuation level precisely.
Goal
ADMX

## Slide 8: Signal Power
On cavity resonance, the expected axion signal power is approximately,

## Slide 9: Signal Power
On cavity resonance, the expected axion signal power is approximately,
Large, strong magnet
Form factor (mode overlap) Axion couples most strongly to TM010 mode in ADMX setup.
(Loaded) quality factor stored energy / lost energy per cycle.
The antenna coupling is assumed to be around 2.
Detector parameters
TM010
TM011
Input model parameters

## Slide 10: Signal Power
On cavity resonance, the expected axion signal power is approximately,
The signal power corresponds to only 10–20 photons per second.
How can we reduce the noise fluctuations to this signal scale?
Noise fluctuation,
Signal power, / bin

## Slide 11: Noise
Dicke radiometer equation:
For a single scan, we have DFSZ signal-to-noise ratio (SNR) of:
Reliable exclusion or discovery requires substantially higher SNR. Combine statistics to increase SNR
System noise temperature: ~0.6 K
Resolution bandwidth: 100 Hz
Integration time: 100 s

## Slide 12: Cold RF Chain
The cold RF chain effectively looks as follows:
The cavity physical temperature and the added noise of the first stage amplifier are the dominant factors that determine the system noise temperature.
Circulators
1st stage amplifier: Josephson Parametric Amplifier (JPA)
Cavity
Noise source
2nd stage amplifier: HFET (HEMT)
Listen to Kieran’s talk (next talk) for more details on our JPA and noise calibrations

## Slide 13: Challenges
Magnet quench (Jan. 2026)
magnetized the JPA. After repair and other upgrades, data taking in June 2026.
Hot cavity
Cavity effective temperature appears hotter than the temperature sensor. Typically indicates hot-rod problem.
Noise model discrepancy
Discrepancies between the noise model and the SNRI measurements can be due to the cavity–JPA interaction.
Fixed
Working on model analysis and upgrade planning

## Slide 14: Data Taking
Each scan follows this sequence:
Cavity characterization
JPA calibration and tuning
Digitization
Tuning
• Measure cavity resonance, Q-factor, antenna coupling
• Monitor mode crossing
• Measure SNRI
• Periodically re-bias JPA
• 100-second digitization
Tuning rod steps
Cavity frequency
• Tune the cavity resonance
VNA reflection
SNRI vs. bias current

## Slide 15: Preliminary Result
Highlighting our first frequency interval: 1250–1270 MHz.
Assuming axion constitute the entirety of the local dark matter (DM) halo, and at a DFSZ coupling, we excluded the DM density (previously) 0.49 GeV/cm3 (now) 0.22 GeV/cm3.
Preliminary
Published in 2025 (not quite DFSZ)

## Slide 16: Looking Forward: Run-2A
We will have four cavity array to search for higher frequency.
Cavity and 4K teststand at Fermilab.
Ongoing: commissioning of amplifier chain and dark photon search.
Run-1D
(1.0–1.4 GHz)
Run-2A
(1.4–2.0 GHz)
Magnet bore
Rod
Cavity
Piezoelectric (rotary) actuator
Stepper motor array
@Fermilab

## Slide 17: Summary
ADMX searches for axion dark matter at the DFSZ sensitivity.
  Microwave cavity resonator(s) as our coherent detector.
  Employs quantum amplifier package (such as JPA) to achieve quantum-limited noise.
Currently, we are taking data over 1.0–1.4 GHz range ensuring the DFSZ sensitivity.
The next run (2A) will be using four cavity array to maximize the signal power in a given volume.
Thank you for your attention!

## Slide 18
ADMX Collaboration Meeting (May 2026) @ UW
This work is supported by U.S. Department of Energy through Awards No DE-SC0009800, No. DE-SC0009723, No. DE-SC0010296, No. DE-SC0010280, No. DE-SC0011665, No. DEFG02-97ER41029, No. DE-FG02-96ER40956, No. DE-AC52-07NA27344, No. DE-C03-76SF00098, No. DE-SC-0022148 and No. DE-SC0017987. Fermilab is a U.S. Department of Energy, Office of Science, HEP User Facility managed by Fermi Research Alliance, LLC (FRA), under Contract No. DE-AC02-07CH11359. Additional support was provided by the Heising-Simons Foundation and by the Lawrence Livermore National Laboratory LDRD office. PNNL is a multi-program national laboratory operated for the U.S. DOE by Battelle Memorial Institute under Contract No. DE-AC05-76RL01830. UWA and Swinburne participation is funded by the ARC Centre of Excellence for Engineered Quantum Systems and CE170100009, Dark Matter Particle Physics, CE200100008. The Sheffield group acknowledges support from the UK Science and Technology Facilities Council (STFC) under grants ST/ T006811/1 and ST/X005879/1. CRB is supported by DOE Office of Science, High Energy Physics, Early Career Award (FWP 77794 at PNNL). Chelsea Bartram acknowledges support from the Panofsky Fellowship at SLAC. John Clarke acknowledges support from the U.S. Department of Energy, Office of Science, National Quantum Information Science Research Centers.
Acknowledgements

## Slide 19: Backup

## Slide 20: Noise Calibration
We heat a noise source and measure output power versus source temperature.
The narrowband JPA must be retuned with frequency. Repeating a full thermal calibration at every setting is impractical.
Noise source temperature
Power
Noise source
Amplifier
*Details of ADMX noise calibration can be found in [PRD 111, 092012 (2025)]
Calibration example

## Slide 21: Signal-to-Noise Ratio Improvement (SNRI)
We measure the SNR improvement with the JPA on versus off.
SNRI is dB in this example
Already-calibrated (broadband)

## Slide 22: Strong Problem
QCD Lagrangian admits the -odd term:
It introduces a nonzero neutron electric dipole moment (nEDM):
The 2020 neutron EDM measurement gives [PRL 124, 081803 (2020)]:
It implies
But is a dimensionless angular parameter, whose natural domain is . The Standard Model does not provide an explanation for this small value.
Strong problem: Why is the physical -violating angle so small?

## Slide 23: The Peccei-Quinn Solution
Spontaneous breaking of the Peccei–Quinn symmetry introduces the axion field , making the effective CP angle dynamical [PRL 38,1440 (1977)].
can take any value when universe is hot enough, but after the QCD transition, the axion “rolls down” the potential and relaxes toward zero and oscillates about the minimum.
axion field
Before QCD transition
After QCD transition
Adapted from Sci. Adv. 8, eabj3618 (2022)

## Slide 24: Axion Dark Matter
Axions can be produced nonthermally as coherent field oscillations.
  Negligible initial momentum cold
  Extremely weak interactions long-lived
  Adequate misalignment (or topological defects) observed DM abundance
Under standard cosmological assumptions, QCD axion dark matter naturally lies in the eV–sub-meV regime.
1 eV 240 MHz, turning the search into a measurement of an oscillating field of a “microwave” frequency.
Adapted from Sci. Adv. 8, eabj3618 (2022)
Hot universe, massless axion
Axion acquires mass and becomes CDM

## Slide 25: Receiver Chain
The digitizer records a band containing the cavity feature and its idler image produced by the JPA.
Cold
Warm
Mixing
Digitizer
Local oscillator
JPA
Cavity
Idler
1 MHz digitized bandwidth
Cavity feature
+150 kHz offset from the JPA resonance

## Slide 26: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion

## Slide 27: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion
Cavity (signal) band
Apply data-quality cuts and retain the kHz band around the cavity resonance.

## Slide 28: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion
We conventionally estimate the receiver baseline with a Savitzky–Golay smoothing filter.
Define the fractional excess :
This procedure could attenuate the narrow axion signal.
Can a physical baseline model preserve more of the axion signal?

## Slide 29: Feed-forward Model: Cavity
The temperature contrast sets whether the cavity feature is a peak or a dip.
Input noise:
Cavity
Near-perfect reflector (), off-resonance
Near-perfect absorber (), on-resonance (near critical coupling, )
( is the cavity reflectance)
Cavity output:
Cavity band

## Slide 30: Feed-forward Model: JPA
The JPA mixes the signal and idler bands, producing a mirrored cavity feature.
A hotter cavity reproduces the broad cat-ear structure in the forward model.
Input noise:
Cavity
JPA output:
Cavity band
JPA
idler

## Slide 31: Hot Cavity
A cavity hotter than the input noise source can produce a peak, but the cavity sensor reads a lower temperature.
Noise source temperature sensor
Cavity temperature sensor

## Slide 32: Hot Rod
A simple hypothesis: poor thermalization leaves the tuning rod hotter than the cavity walls.
Tuning rod (no temp. sensor)

## Slide 33: Hot Rod
A simple hypothesis: poor thermalization leaves the tuning rod hotter than the cavity walls.
To test for excess cavity noise, we recorded JPA-off spectra at several antenna couplings.
Tuning rod (no temp. sensor)

## Slide 34: Hot Rod
The fit suggests an effective cavity-mode temperature 0.1 K above the sensor reading.
Fit model uses:
sensor

## Slide 35: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion
Normalize the fractional excess by the expected DFSZ signal power, including the cavity response.

## Slide 36: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion
A roughly 1 kHz halo signal spans about ten 100 Hz bins.
Apply the standard halo model lineshape kernel () as a matched-template fit
Fitted significance

## Slide 37: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion
Combine overlapping fitted spectra at each physical frequency using inverse-variance weights:
We search the grand spectrum for significant excesses.

## Slide 38: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion
Rescan targets include excess-power candidates and frequencies with insufficient sensitivity.
  Most of the time, large excess candidates are statistical flukes.
  Rescan (take more data) around candidates.
Persistent excesses receive dedicated follow-up checks. It can be
  Blind synthetic axion injection (SAG).
  Ambient RF interference (RFI).
  Or axion!
Test whether the excess follows the expected axion response.
  Reduce axion power .
  Change cavity mode to TM011 form factor is near-zero.
  Identify or remove source of RFI.
  SAG turned off.

## Slide 39: Analysis Pipeline
DQC-passed raw spectra
Baseline removal
Response and DFSZ normalization
Axion lineshape fit
Grand spectrum
Candidate rescan
Discovery or exclusion
Assume a local axion density 0.45 GeV/cm3.
Set a 90% credible upper limit with a flat prior in nonnegative signal power.
Published Run-1D Part 1 result, PRL 135, 191001 (2025)

## Slide 40
Adapted from 10.5281/zenodo.3932430 by C. O’Hare

## Slide 42
PRL 135, 191001 (2025)

## Slide 45: System Noise Calibration
Hot load
mK attenuator
1. Hot load: connected by the RF switch. 2. mK attenuator (new in Part 2): no switch needed. The concept worked!
Notes: Before I show our most recent noise calibration data, let me quickly recap our noise sources.
We call them the hot load attenuator and the mK attenuator.
The hot load can be connected through the RF switch and replaces the cavity.
The measurement is reliable and stable—but operating the RF switch is a bit of a hassle and takes time.
In Part 2, we introduced the mK attenuator noise source in the bypass line.
No switch is needed, and the concept has worked pretty well.