## Slide 1: High-Purity Germanium Detectors for the LEGEND experiment
Aparajita Mazumdar
On behalf of the LEGEND Collaboration
Postdoctoral Research Associate
University of North Carolina at Chapel Hill
jita@unc.edu
Coordinating Panel for Advanced Detectors 2026,
Seattle, October 20, 2026

## Slide 2: High-purity Germanium detectors (HPGe)
Core detector technology used in g-ray spectroscopy, studying nuclear structure and nuclear reactions
passivated surface
p+
n+
holes
electrons
Applied high voltage
High-purity Ge
(Impurities < 1010/cm3)
Signal read-out
Schematic (Planar Geometry)
HPGe
NaI
Ref
g peaks resolved using HPGe detectors but not in NaI
Semiconductor diode detector operated in reverse bias
Excellent energy resolution

## Slide 3
Evolution of the detector geometry
passivated surface
p+
n+
Planar
Semi-Coaxial (“Coax”)
Point Contact
Simple geometry
Difficult to scale to large masses
Large Mass
Uniform Electric Fields
Capable of discriminating based on the event topology
Latest designs have a large mass
Variants of the technology exist from the 1960s, yet the designs continue to improve today!

## Slide 4
Signal formation in Germanium detectors
Shockley-Ramo theorem (for a single charge q)
Instantaneous induced charge
Weighting Potential
Coax detector
D. Hervas, Ph.D. thesis
Weighting Potential
Laplace’s equation with artificial boundary conditions: Signal electrode at 1V, others set to 0V
Our signal: Integrated induced charge due to drift of electrons and holes

## Slide 5
Charge waveform
Current (Smoothed derivative of charge waveform)
Acceptance window
Acceptance window
Point contact detectors are sensitive to the event topology
Pulse Shape Discrimination
Same energy but different values for the maximum amplitude of the current pulse!

## Slide 6
p+ : O(100 nm) thick, Boron implantation
n+ : O(1mm) thick, Lithium diffusion.
Events in the FCCD are energy-degraded “slow” pulses.
Charge collection near the surface
Not typically used for charged a/b spectroscopy, yet excellent for studying internal bb decays
“slow”
“normal”

## Slide 7
The search for Neutrinoless Double Beta Decay
2nbb
0nbb
Yet to be observed!
Detector = Source, high detection efficiency for electrons
76Ge enrichment of >90% possible
Highly radiopure
Excellent energy resolution
(𝐅𝐖𝐇𝐌 ~ 𝟎.𝟏% @ 𝑄𝛽𝛽 )
HPGe excellently suitable
𝑄𝛽𝛽 = 2039 keV
Smoking gun evidence of the Majorana nature of n
Summed energy of electrons

## Slide 8
LEGEND-200
LEGEND-200
Up to 200 kg of enrGe detectors
Uses GERDA infrastructure in Hall A, LNGS
Operational since 2023
Goals:
  1 tonne . yr of exposure
  Background ~ 2 x 10-4 cts / (keV . kg . yr)
  > 1027 yr 30 – 70 meV
Designed to be quasi-background free at every phase
Readout electronics
HPGe
LEGEND-1000
Next phase
1000 kg of enrGe detectors
Uses new infrastructure in Hall C, LNGS
Goals:
  10 tonne . yr of exposure
  Background ~ 10-5 cts / (keV . kg . yr)
  > 1028 yr 10 – 20 meV
Bare HPGe operated in LAr
with strong Compton Suppression

## Slide 9
HPGe detector Production
Crystal growth
Electric Field and Pulse
Shape Simulations
Geometry optimization
Detector produced
Time
Collaborative process between LEGEND and vendor
Average detector mass improved over time
After production, detector characterized by LEGEND.
LEGEND IC Detector Mass

## Slide 10
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Column1 | 14.7 | 19 | 22.1 | 86.7
Property | Coax | BEGe | PPC | IC
Point contact | NO | YES | YES | YES
Small passivated surface | YES | YES | NO | YES
Typical detector mass | 2.5 kg | 0.7 kg | 1 kg | 2-4 kg
LEGEND-200 HPGe
Configuration for Mar ’23 – Feb ’24 Physics Data taking
14.7 kg
19.0 kg
22.1 kg
86.7 kg
Point contact detectors are
  Capable of event topology-based discrimination
  Have low noise
Small passivated surface detectors
  Operate stably in the LAr
Increased detector mass
  Reduced background by means of reducing non-active components (cabling, copper rods, etc)
Detector characterization
Stability monitoring
Systematics Studies
(combined fit from
GERDA, Majorana
and LEGEND-200)
T1/2 (0𝜈ββ) >1.9 x 1026 yr (90% CL)
mββ < 70 -200 meV
Leading limit for 76Ge, Published in PRL
Inputs to the final result
Phys. Rev. Lett. 136, 022701

## Slide 11
~0.1% FWHM at Qββ
Stable energy observables
Monitored Weekly calibrations performed using 228Th
Second order variations tracked in time
Data set partitioned according to stability
Excellent energy resolution
Calibration
Energy resolution
https://arxiv.org/abs/2605.22479; Accepted in EPJ C

## Slide 12
Single site event
(0nbb/2nbb)
ACCEPTED
Multi site event
(g)
REJECTED
Low A/E
p+ surface event
(a)
REJECTED
High A/E
n+ surface event
(42K/42Ar)
REJECTED
Low A/E
Low A/E: multi-site rejection, n+ surface event rejection
High A/E: p+ surface event rejection
LQ replaces high A/E as surface cut for detectors with large passivated surfaces.
Special PSD Cuts developed for Coax detectors.
A/E = max(current)/energy
PSD in LEGEND-200
Late Charge (LQ) : slow component above the rising edge after 80% of charge is collected, i.e., the area above the waveform
n+ surface
(42K/42Ar)
REJECTED
Single site (0nbb/2nbb)
ACCEPTED
p+ surface
(a)
REJECTED

## Slide 13
u
v
w
x
0nbb signal
2nbb
Singly Compton Scattered
Double escape peak (DEP)
e-
e-
e-
e-
e+
e-
e-
u
v
w
x
Escaping 511 keV
Escaping 511 keV
Incoming g
Incoming g
Compton scattered g
‘Detector’
Single-site proxies
Single-site proxies
Single site
Multi site
Stable PSD observables:
Monitored with weekly 228Th calibrations.
Data set partitioned according to stability.

## Slide 14: PSD Systematics
Detector type | Efficiency at Qbb
IC | 84.3 ± 3.0 %
BEGe | 81.1 ± 3.9 %
PPC | 85.0 ± 4.5 %
Coax | 76.0 ± 5.7 %
Eff of PSD cuts at 0nbb
Eff of MSE and surface cuts at 208Tl DEP
Time stability
Energy-dependent
effects
Uncertainty due to noise
Geometric difference between DEP and 0nbb
Special calibration sources such as 56Co are useful to characterize the systematics arising from calibration procedure biases.
IC detectors have a high signal efficiency.
Papers in preparation

## Slide 15
Cuts applied on spectrum:
  data cleaning + muon veto + multiplicity cut
  Pulse Shape Discrimination:
    Surface a and b backgrounds highly suppressed
    ~60% suppression of Compton background at Qββ
  Complementarity with the LAr cut
Surviving Compton background
a background suppressed
42K
40K
208Tl
212Bi
Powerful background mitigation!
Background rejection performance of the PSD cut
208Tl
214Bi
Background estimation window
After ALL cuts
BLINDED

## Slide 16
Current Status
142 kg of LEGEND-200 HPGe acquired physics data Mar’23 – Feb’24 and showed excellent performance.
Across the entire detector array, a combined average resolution of (2.47 ± 0.08) keV at Qββ is achieved.
Energy calibration and systematics publication accepted in EPJ C (https://arxiv.org/abs/2605.22479)
PSD papers in preparation
First LEGEND-200 background index and 0nbb result published in Phys. Rev. Lett. 136, 022701
After maintenance period, redeployment of 138 kg detectors in July 2025
Future Plans
Potential improvements to PSD to further reject the 42K surface events.
Improved FCCD measurements and n+ layer modelling in simulations
Better understanding of the low energy backgrounds, to pursue other novel physics beyond the Standard Model.
LEGEND-1000 will employ IC detectors with an average mass of 3 kg!
Conversion of PPC, Coax and underperforming detectors to IC

## Slide 17
Thank you for your attention
LEGEND Collaborator Dr. David C. Radford
with a large Germanium detector

## Slide 18
MAJORANA DEMONSTRATOR (MJD): The best E,
2.52 keV
GERDA:
The lowest BI,
cts/(keV . kg . yr)
LEGEND combines the best technologies from MJD and GERDA + new innovations!
Improved exposure and technology!
> Half a century of research
Suitability of HPGe detector technology
Phys. Rev. Lett. 136, 022701 (LEGEND-200 + MJD + GERDA result)

## Slide 19
Signal formation
in point contact detectors
Point
Contact
Geometry
Largest contribution to the signal as charge drifts near the p+ contact (typically hole dominated)

## Slide 20
Artificial Neural Network
Method developed for Coax detectors, which do not have a point contact style geometry.
Rise time cut
p+ contact events in Coax detectors are rejected using a cut based on the pulse risetime. Similar method to GERDA Phys. J. C 82, 284 (2022)
Replaces the high A/E cut as a surface event cut in detectors with a large passivated surface (PPCs)
PSD cuts developed for Coax detectors
n+ surface
(42K/42Ar)
REJECTED
Single site (0nbb/2nbb)
ACCEPTED
p+ surface
(a)
REJECTED
Late Charge (LQ)
Is quantified by the slow component above the rising edge after 80% of charge is collected, i.e., the
area above the waveform.
Targets slow charge re-release events, which originate from the passivated and n+ surfaces.
These events are energy degraded and can add to the background in the region of interest.
Other PSD

## Slide 21
Time
Energy resolution of ICPC is overall constant even when the mass increases.

## Slide 22: Data in the region of interest
208Tl
214Bi
unblinded
208Tl
214Bi
Blinded
Background estimation window: 1930 – 2190 keV
  Excluded g lines at 2104 (208Tl) and 2119 keV (214Bi)
  9 events
    + 2 events AFTER unblinding = 11 surviving events
  2 Datasets
    Golden (48 kg . yr) : unblinded for Neutrino ’24
    BIgolden cts/(keV . kg . yr)
    Silver (13 kg . yr) : mainly COAX (worse background rejection)
    BIsilver cts/(keV . kg . yr)
Comparable to GERDA