## Slide 1: RTLswarm: Simulating Detector Readout at Scale
CPAD October 22, 2026
Kalindi Gosine, Yuan Mei
The University of Texas at Arlington

## Slide 2: Single ASIC to entire detector readout
ASIC Network
DUNE Module
ASIC design
Fabrication
Analog front-end design
Digital design (RTL)
Analog front-end design
Digital design (RTL)
Layout & Synthesis
Register Transfer Level (RTL) code models synchronous digital circuits. It is written in a Hardware Description language like Verilog which is then synthesized into physical chip gates.
Notes: What does it take to instrument an entire detector with an ASIC-based readout?
You’re now talking about anywhere from tens to hundreds of thousands of individual ASIC sensing elements.
If you’re in a cryogenic environment a top concern for you is how do you extract the information from thousands of ASICs.
One way you can minimize the number of output points is by having ASICs communicate with each other in a network, routing data towards a smaller number of “sink” ASICs which are then transmitted out of the detector.
By designing ASICs with digital circuitry to pass data towards this sink node, you’ve now coupled your single ASIC behavior to the behavior of a

## Slide 3: Designing at two scales simultaneously
Individual ASIC
RTL will define the protocol for how chips communicate with each other
Single chip RTL validation can be done in SystemVerilog testbenches & any of the existing RTL simulators (Synopsys, Verilor, Cadence Xcelium, …)
Network scale readout
Finite buffers & limited link bandwidth
How do nodes use these resources when traffic contends for them?
Flow control, routing decisions, and synchronized hardware protocols couple the nodes
  A local RTL design choice produces network-scale congestion, latency, or data-loss behavior.
Integrated-circuit fabrication is costly, time-consuming, and difficult to correct after production. Designers must be able to study the behavior of that source design at all scales before committing it to hardware.
simulation +
iteration

## Slide 4: What is RTLswarm?
RTLswarm is a distributed, parallel simulator for networks of RTL-defined ASICs
RTL-accurate: simulates the actual synthesizable RTL of each ASIC
Network-scale: simulates interconnected ASICs operating concurrently
Cycle-accurate: preserves digital clock-cycle behavior across the network

## Slide 5: Parallel RTL evaluation
RTLswarm uses Verilator build the RTL-defined core of a chip process
Verilator translates SystemVerilog behavior into an executable C++ model
RTLswarm runs an instance of that model for each chip process
Each chip process is mapped to one CPU for parallel evaluation
Digital design (RTL)
Digital design (C++)
one chip process
to
one CPU

## Slide 6: Network communication
Coordinates the RTL simulation stepping and data passing between nodes in lockstep
Communication between chip processes is done via an open source messaging library (NNG or Open MPI)
Distributed computing compatible, no shared memory between chip processes

## Slide 7: Preserving cycle accuracy across the network

## Slide 8: Configuring a network simulation
Changes to RTL can be quickly recompiled via Verilator and simulated
  Avoids the long FPGA compilation flow of synthesis, placement and routing
  Rapid A/B comparison between different RTL versions on the same scenario
Customizable scenarios
  stimulus to chips
  sending configuration data into the network from an external controller
Access to internal states within RTL at each tick, on all chip processes available through Verilator

## Slide 9
Two Tracks

## Slide 10
Network Config

## Slide 11: Performance & scaling
Run on a cluster from the Texas Advanced Computing Center (TACC)
Lockstep timing reduces throughput for larger network sizes despite parallel RTL evaluation

## Slide 12: Towards a digital twin: Integration with transistor-level analog front end
Analog front-end design
Digital design (RTL)
Each RTLswarm chip process hosts an ngspice analog frontend coupled to its Verilator-compiled RTL backend through the d_cosim interface.
Ngspice advances transistor-level circuitry with adaptive timesteps, while RTLswarm enforces precise synchronization at digital clock boundaries.
Analog outputs drive RTL inputs, and RTL control signals feed back into the analog circuit, preserving persistent mixed-signal state across clock cycles.
Goal: a full-ASIC digital twin combining transistor-level analog behavior, production RTL, and network-scale communication in one synchronized simulation.

## Slide 13: End-to-end detector simulation
Geant4 Physics Event
Resulting time-domain charge deposition at each ASIC location
Digital twin to ASIC
RTLswarm

## Slide 14: Availability & Acknowledgement
Check out RTLswarm here: https://github.com/snr-laboratory/snrlab-chip-network-sim/tree/main
Contact: kalindigosine@lbl.gov
Thanks to
LArPix Collaboration (Dwyer, 5:30PM, Auditorium)
NIFTY Collaboration (Carney, 5:50PM, Auditorium)

## Slide 15: Backup

## Slide 17: Multithreading

## Slide 18: Comparison to available network simulators
BookSim
Cycle-accurate network simulator
dedicated to studying network performance. Focused on the movement of flow-control units (flits) rather than bits. Concerned primarily with network information like queuing, arbitration, bandwidth, latency, congestion.
Simulates an abstraction of the node by modeling the routers, buffers, and channels.
Designed for large-scale network studies with abstract node models.
FireSim
Cycle-accurate FPGA-accelerated simulator for studying RTL-defined systems at scale. Concerned with system-level behavior, timing, and communication between simulated nodes.
The link between two nodes is modeled, capturing communication behavior without bit-level information.
Designed for cases where nodes are large RTL-defined computing blocks like SoCs (like data center modelling).