## Slide 1: The Electron-Ion Collider Project Status
May 20, 2026
Luisella Lari
EIC Project Manager transitioning to EIC Associate Director for Strategic Partnership
Sr. Scientist
IPAC’26 – the 17th International Particle Accelerator Conference

## Slide 2: What is the Electron-Ion Collider (EIC)?
What is the EIC?
A next-generation particle collider at Brookhaven National Laboratory
Collides electrons with atomic nuclei or protons
Acts as a precision microscope for studying quarks and gluons
Designed to answer how mass, spin, and nuclear structure emerge from the strong force (QCD)
Why electrons + ions?
Electrons probe structure cleanly and precisely
Protons/nuclei contain quarks and gluons
Polarized beams reveal spin and motion in 3D
2

## Slide 3: EIC Scientific Case Built Over Decades
2002
2007
2009
2013
2015
2018
2010
Gluons and the Quark Sea at High Energies
2012
“The science questions that an EIC will answer are central to completing an understanding of atoms as well as being integral to the agenda of nuclear physics today.” (National Academy of Sciences, 2018)
Major Nuclear Physics Facilities for the Next Decade
NSAC
March 14, 2013
2021
arXiv:2103.05419
2023
“We recommend the expeditious completion of the EIC as the highest priority for facility construction.” (Nuclear Science Advisory Committee, 2023)
EIC will be the only operating particle collider in the U.S. in the next decade/s.

## Slide 4: EIC Facility Requirements
Ultimate Performance Parameters
High Luminosity: L= 1033 – 1034cm-2sec-1
Highly Polarized Beams: 70%
Large Center of Mass Energy Range: Ecm = 28 – 140 GeV
Large Ion Species Range: protons – Uranium
Large Detector Forward Acceptance and Low-Background Conditions
Possibility to Implement a Second Interaction Region (IR)
4

## Slide 5: Accelerator Status at a glance
Reuse of RHIC Facility components
Valued at ~$2B
5
Polarized ion/proton source
Ion injection and initial acceleration systems – Linac (200 MeV), Booster (1.5 GeV), AGS (25 GeV)
Hadron Storage Ring (40-275 GeV) – HSR
Electron Pre-Injector (750 MeV linac)
Beam Accumulation Ring (750 MeV) – BAR
Electron Rapid Cycling Synchrotron (0.75 GeV – top energy) – RCS
Electron Storage Ring (5 GeV – 10 GeV) – ESR
Interaction Region(s) – IR
Hadron Cooling System

## Slide 6: EIC Infrastructure Project Scope
100% Design completed for the infrastructure around EIC/RHIC tunnel.
6

## Slide 7: Project Milestones
End 2026
~2035
e-hadron collisions
7
We are here today
CD-3a 2024
CD-1
CD-0
CD-3b 2026
CD-2/3
CD-4
Of infrastructure
around RHIC/EIC tunnel

## Slide 8
EIC Accelerator Challenges
Overview
8

## Slide 9: From RHIC to EIC
Protons: ~40 – 275 GeV
Electrons: 5 – 18 GeV
RHIC
RHIC
EIC
Ion species:
proton – Uranium
60% p polarization

## Slide 10: From RHIC (yellow ring) to EIC HSR
EIC HSR to be composed of existing arcs of the Yellow RHIC ring (remove unused magnets)
Insert sleeves coated with copper and amorphous carbon into superconducting magnet beam pipes to improve conductivity and reduce secondary electron yield (-> electron cloud)
Add new RF cavities
Add hadron cooling to create flat beam
Add crab cavities, new IR SC magnets
Add a collimation system
Add extra ‘snakes’
Actively Cooled Beam
Screen Material procurement
Tripled beam current, shorter bunch length, shorter bunch distance, ‘flat’ beams with small vertical emittance

## Slide 11: EIC Electron Storage Ring
Electron Storage Ring (ESR) consists of six FODO-cell arcs, and six straight sections (IRs)
High-intensity (28 nC), short (7 mm) bunches
add many interesting accelerator challenges
Circulating beam current ~2.5 A and the synchrotron
radiation power of ~10MW
EIC needs nearly constant (20 to 24 nm) emittance from
5 to 18 GeV for optimum luminosity, but equilibrium
emittance in an electron storage ring depends on beam energy.
We will use ‘super bends’ (reverse bends) for emittance
control below 10 GeV
36mm
80mm
Heater wire groove
BPM mount
Pump port

## Slide 12: Electron Injector
Function: Deliver electron bunches of up to 28 nC at a 1 Hz repetition rate for injection into the ESR at various energies of 5 – 10 GeV (upgradeable to 18 GeV).
RCS magnet assembly
Vacuum chamber: stainless steel, copper coated (50 um)
Polarized Electron Gun
1-nC, 30 Hz
RCS SRF Cavity, 591 MHz
Beam Accumulator Ring
750 MeV, 40 m
S-band linac, 750 MeV, 30 Hz, 1 nC single bunch
RCS
750 MeV – 18 GeV
28 nC, 1 Hz
85% polarization
1.4 km
Concept modeled after the ANL APS-U injector

## Slide 13: EIC - RF Systems
Crab Cavities (per IR) | HSR (Cavities/CMs) | ESR (Cavities/CMs)
197 MHz | 8/4 | –
394 MHz | 4/4 | 2/2
Bunch Splitting
3 49.2 MHz NCRF
4 98.5 MHz NCRF Capture & Accel
8 197 MHz NCRF
Low-Energy Cooler, IR02 -
16 197 QWR NCRF,
4 591 NCRF,
1 24 MHz NCRF,
And 1 591 MHz Deflecting Cavity
RHIC – 28 MHz acceleration cavity
4 24.6 MHz Capture & Accel Cavity, IR04
IR06
EIC LLRF DAC Clock for Crab Cavities
400 kW Solid State Amplifier
RCS
591 MHz 5-Cell Cavity Cryomodules
2 CMs
HSR NCRF – IR04
Electron Storage Ring & Hadron Storage Ring – IR10
591 MHz 800 kW 2 K
1-Cell Cavity Cryomodules
ESR = 8 CMs, 16 Cav
HSR = 2 CMs, 4 Cav

## Slide 14: IR6 (Crab Cavities)
Facilities
HPRF Amplifiers and Distribution
Crab Cavity Cryomodules
RF Controls
Crabbing System | Quantity
197 MHz HSR | 4 & 4
394 MHz HSR | 2 & 2
394 MHz ESR | 1 & 1
c/o: Karim Hamdi
Notes: Add extra verbiage on issues

## Slide 15
EIC IR Layout
High Luminosity:
  25 mrad crossing angle
  Small β* for high luminosity
  with limited IR chromaticity contributions
  Large final focus quadrupole aperture
  Machine Detector Interface
  Large detector acceptance
  Forward spectrometer
  No magnets within - 4.5 / +5 m from IP
  Space for luminosity detector, neutron detector, “Roman Pots”

## Slide 16: EIC IR layout
9 cryostats housing 11 cold masses (2 K)
  15 magnets (dipole, quadrupole, and combined-function)
    6 “cos-theta” magnets with Rutherford cables, 9 magnets fabricated with Direct Wind technique (DW)
RC-1
RC-2
RC-3
B0pF
FC-1
FC-2
FC-3
FC-4
B2pF
8 cryostats (4 per side) which contain the spin rotators (solenoids 8.5 T, 2K)
  2 long and 2 short per side
Interaction Region - Forward
Interaction Region – Rear
Interaction Region – Rear
Interaction Region - Forward

## Slide 17: EIC IR Superconducting Magnets
B2pF
Q1BpR-Q2eR
Q2pR-eDrift
Q1BpF-Q1eF
Q1ApF-eDrift
Q1ApR-Q1eR
B0ApF-eDrift
Q2pF-eDrift
Spin rotator
B0pF-Q0eF
B1pF-eDrif
B1ApF-eDrift
View from the IP
1 m
All magnets to the same scale

## Slide 18: The 41-GeV ‘bypass’
Sector 1 without and with the 41-GeV bypass line
This bypass provides access to the lowest EIC CoM energy, 29 GeV

## Slide 19: Low-energy Cooler Concept
DC Gun
400kV
e-
Laser
197 MHz
900 kW Beam Dump
16x 197 MHz
NCRF LINAC
extraction
injection
cooling
HSR
4x 591 MHz
NCRF correction Cavities
180° Dipole
Spectrometer
Quad
Cathode transport
Mu-metal shielding
24MHz
RF cavity
SC Quad
130 kW Beam Dump
Extraction line
Injector/linac
Test line
Solenoids
LEReC Cooling Solenoids
180°Dipole
(U-turn)
transport
PM
PM
PM
RF diagnostics line with Deflecting cavity
Injector test
e-
HSR
hadron
hadron
hadron
e-
RF diagnostic
Not to scale
IR2 layout
(all within the
existing RHIC
Tunnel)
150 m cooling section
24 GeV protons
12.5 MeV electrons

## Slide 20
20
The EIC facility is international in characters.
It will be built at BNL in Partnership with JLab, and collaborators around the world.

## Slide 21: Wolfram Fischer has been named co-chair of the Electron-Ion Collider Accelerator Collaboration
21