## Slide 1
○Mizuki Uenomachi1, Kenji Shimazoe2
1Kyoto University, 2The Univ. of Tokyo
2023.09.07
Evaluation of Compton recoil electron tracking capability of fine-pitch pixel silicon detector with a Monte Carlo simulation
13th International Conference on Position Sensitive Detectors

## Slide 2: Research Background
Compton imaging
Scatterer
Absorber
One of gamma-ray imaging techniques based on Compton scattering kinematics
Scattering angle information can be calculated from deposited energies in a scatterer and an absorber
No collimators required
Wide photon energy range for imaging
Wide field of view
Application
Astrophysics, Medical field, Nuclear field

## Slide 3: Research Background
Compton imaging in medical field
Nuclear Medicine
Heavy particle therapy
Detector
Gamma-rays
Radiopharmaceutical accumulation imaging
→Diagnosis, therapy
Detector
Gamma-rays
Prompt
Gamma-rays
Prompt gamma-ray imaging
M. Uenomachi et al., Sci. Rep., (2021):17933
A. Kishimoto et al., Sci. Rep., (2017): 2110
131I
85Sr
65Zn
4.4 MeV Prompt gamma imaging
S. Mochizuki et al., NIMA., (2019);936:43-45

## Slide 4: Research Background
Compton imaging in medical field
Nuclear Medicine
Heavy particle therapy
Detector
Gamma-rays
Radiopharmaceutical accumulation imaging
→Diagnosis, therapy
Detector
Gamma-rays
Prompt
Gamma-rays
Prompt gamma-ray imaging
M. Uenomachi et al., Sci. Rep., (2021):17933
A. Kishimoto et al., Sci. Rep., (2017): 2110
131I
85Sr
65Zn
4.4 MeV Prompt gamma imaging
S. Mochizuki et al., NIMA., (2019);936:43-45
Compton imaging is a promising method in medical field due to the wide energy range and collimator-less imaging
However, still in under research because of the low signal-to-background ration (SBR) caused by drawing a lot of Compton cones.

## Slide 5: Recoil electron tracking Compton imaging
Measurement of a recoil electron trajectory when a photon is Compton scattered in a scatterer
Constrains the radionuclide position on from a Compton conical surface to an arc surface
Conventional imaging
Electron tracking imaging

## Slide 6: Recoil electron tracking Compton imaging
Objective
Electron tracking Compton camera succeeded to be developed with gaseous detectors by Kyoto University Tanimori group for high energy gamma-ray astrophysics.
For medical imaging, semiconductor detector is ideal
However, the high spatial resolution (a few tens of µm) is required for electron tracking with a semiconductor detector
In this study, we developed a Compton imaging system with SOI (silicon on insulator) fine-pitch pixel sensor and GFAG scintillator detector for electron tracking Compton imaging

## Slide 7: SOI pixel sensor with 36 µm pixels
XRPIX7
608 x 384 pixel array
1 Pixel : 36 µm sq.
24.6 mm
15.3 mm
S/H Cap.
PGA
OUT BUF
DECODER & TRIGGER PROCESSOR
DECODER
&
TRIGGER PROCESSOR
Bias Gen.
21.9 mm
13.8 mm
Sensor information
- Chip size：24.6 mm x 15.3 mm
（Active area：21.9 mm x 13.8 mm）
- Pixel size：36 µm sq.
- Pixel number：608 x 384 (= ~233k)
- Sensor thickness：300 µm
Large area X-ray SOI sensor "XRPIX7”
Event driven mode → coincidence detection
Silicon on Insulator (SOI) technique → Monolithic circuit integrated silicon sensor

## Slide 8: Si-ASIC hybrid pixel sensor with 18 µm pixels
Sensor information
- Chip size (Si)：4.3 mm x 4.3 mm
- Sensor thickness：450 µm
- ASIC size : 5.0 mm x 5.0 mm
- Pixel size：18 µm sq.
- Pixel number：192 x 192 (= ~233k)
Hybrid pixel sensor → Si sensor coupled to pixel ASIC with 18 µm pixels

## Slide 9: Development of SOI-GFAG Compton camera
Scatterer1
Absorber1
Scatterer2
Absorber2
19 mm
35 mm
35 mm
19 mm
99mTc Source
XRPIX7 (scatterer)
GFAG detector (absorber)
99mTc source
140.5 keV Compton imaging
Experimental Setup
GFAG
SiPM

## Slide 10: A Monte Carlo simulation by geant4 toolkit
Simulation setup
Si detector
(same size of XRPIX7)
GAGG scintillator detector
(same size of XRPIX7)
300 µm
5 mm
GPS source
30 mm
17 mm
511 keV
1274.5 keV
(22Na gamma-rays)
100 M injection × 3 set

## Slide 11: A Monte Carlo simulation by geant4 toolkit
Data format
[event ID, track ID, parent ID, process name, detector name, deposit energy,
step start position (x,y,z) [mm] , step end position (x,y,z) [mm], momentum direction (x,y,z),
kinetic energy]
Recoil direction =
-
(x_end, y_end, z_end)
(x_start, y_start, z_start)
Si + GAGG Coincidence data

## Slide 12: 2D image of electron trajectory
511 keV
18 µm pixels
36 µm pixels
 | Coincidence events | 1-2 pixels event | 3 < pixels event
18 µm pixels | 8166 | 3220 | 4946
36 µm pixels |  | 1564 | 6602

## Slide 13: 2D image of electron trajectory
1274.5 keV
18 µm pixels
36 µm pixels
 | Coincidence events | 1-2 pixels event | 3 < pixels event
18 µm pixels | 1886 | 71 | 1815
36 µm pixels |  | 16 | 1870

## Slide 14: Estimation of 2D recoil direction
Pixel plane of Si detector
Estimation method of α angle
M. Kagaya et al., proceedings of 2021 IEEE NSS/MIC, (2021)
Deposited energy in a pixel
Vector of the adjacent pixel from start pixel

## Slide 15: Accuracy of 2D recoil direction
511 keV
18 µm pixels
36 µm pixels
Difference of simulated and calculated α angles [degree]
Mean : 33.5 deg
σ : 10.7 deg
Mean : 38.1 deg
σ : 15.3 deg

## Slide 16: Accuracy of 2D recoil direction
1274.5 keV
18 µm pixels
36 µm pixels
Difference of simulated and calculated α angles [degree]
Mean : 39.3 deg
σ : 11.6 deg
Mean : 40.7 deg
σ : 10.7 deg

## Slide 17: Electron Trajectory in XRPIX7
Energy [keV]
Energy [keV]
Row
Row
Column
Column
e-
e-
Recoil electron trajectories of 511 keV gamma-ray (22Na)
XRPIX7 could detect some of recoil electron trajectories of 511 keV gamma-ray.
For future work, we need to establish the method to extract the correct electron trajectory because XRPIX7 can measure only 2D trajectory.

## Slide 18: Summary and future works
We are developing SOI pixel detectors with pixel size of 36 µm
We also developed Si-ASIC hybrid sensor with pixel size of 18 µm
The Monte Carlo simulation by geant4 shows that the estimation accuracy of 2D recoil direction is not significantly improved by 18 µm measurements compared to by 36 µm measurements although the recoil trajectory can be measured more finely.
The estimation method of 3D recoil direction (B.C Plimley, UC Berckley Ph.D thesis, 2014) will be implemented
XRPIX7 can detect a recoil electron trajectory of 511 keV gamma-ray (but not full depletion)

## Slide 19
Thank you for your attention

## Slide 20: Basic performance of XRPIX7
740 eV
5.3 % (FWHM) @13.9 keV
Temperature : 0 deg
Vdet : -25V (not full depletion)
241Am spectrum of all pixels
13.9 keV
17.7 keV
20.8 keV
17.7 keV
20.8 keV
Gain correction